UN Office for Project Services

SMALL CONTRACT FOR SERVICES

Ref. RER/03/G31 (00034997)

2005 November - 2006 February

Director of Azecolab ___________________________ B.Suleymanov

______________ February 2006

Content

1	Introduction	3

1.1	Sampling and samples	3

1.2	Tasks for laboratory	4

2	Metods used	5

3	Results	6

3.1	Sediment characterization	6

3.2	Heavy metals	7

3.3	Alkanes	8

3.4	PAH	10

3.5	Pesticides	12

3.6	PCBs	13

List of figures

Fig. 1 Sampling points	3

List of tables

Tab. 1 Sampling point coordinates	3

Tab. 2 :Laboratory tasks	4

Tab. 3 Sediment  characteristics	6

Tab. 4 Heavy metal content	7

Tab. 5 Individual alkanes contents	9

Tab. 6 PAH content	10

Tab. 6 PAH content (continue)	11

Tab. 7 Pesticides content	12

Tab. 8 PCB content	13

Tab. 8 PCB content (continue)	14

# Introduction

## Sampling and samples

UNOPs had contracted Azecolab to carry out of laboratory analyses of sediments samples taken during Caspian Sea survey near the Azerbaijan coastline of Caspian Sea.

Fig. 1 Sampling points

Table 1 have indicate of the coordinates of the sampling points

| Sample ID | Lat | Long |
| --- | --- | --- |
| AZ1 | 38050’ | 49005’ |
| AZ2 | 38053’ | 9010’ |
| AZ3 | 38054’ | 49002’ |
| AZ4 | 38056’ | 49032’ |
| AZ5 | 38057’ | 49012’ |
| AZ6 | 38058’ | 49035’ |
| AZ7 | 39000’ | 49016’ |
| AZ8 | 39002’ | 49035’ |
| AZ9 | 39003’ | 49025’ |
| AZ10 | 39005’ | 49015’ |
| AZ11 | 39007’ | 49034’ |
| AZ12 | 39010’ | 49015’ |
| AZ13 | 39010’ | 49026’ |
| AZ14 | 39016’ | 49026’ |
| AZ15 | 39017’ | 49030’ |
| AZ16 | 39025’ | 49025’ |

Tab. 1 Sampling point coordinates

From each points Azecolab have received 2 samples, 1 for investigation of metals (in plastic cover), 2nd for investigation of organic (in metallic cover).

## Tasks for laboratory

Below table have indicated laboratory tasks for delivered samples.

| Sediment characterization | Sediment characterization (Extracted Organic Matter (EOM), Lipid content of the sediment, Grain Size of sediment , Organic Carbon of the sediment, Carbonate of the sediment) |
| --- | --- |
| HM | Suit of 20 elements (Ag , Al, As, Ba, Ca, Cd, Co, Cr, Cu, Fe, Hg, Li, Mn, Ni, Pb, Sb, Se, Sn, U, V, Zn) |
| Alkanes | OIL and oil products, Resolved aliphatics, Unresolved aliphatics, Total aliphatics ( n-C14-C34, n-C12, n-C13, n-C14, n-C15, n-C16, n-C17, n-C18, n-C19, n-C20, n-C21, n-C22, n-C23, n-C24, n-C25, n-C26, n-C27, n-C28, n-C29, n-C30, n-C31, n-C32, n-C33, n-C34, n-C35, n-C36, Pristane, Phytane |
| PAH | PAHs (Naphthalene, C1-naphthalenes, C2-naphthalenes, C3-naphthalenes, Acenaphthylene, Acenaphthene, Fluorene, C1-fluorenes, Dibenzothiophene, Phenanthrene, Anthracene, C1-dibenzothiophenes, C2-dibenzothiophenes, C3-dibenzothiophenes, C1-phenanthrenes, C2-phenanthrenes, C3-phenanthrenes, C4-phenanthrenes, Fluoranthene, Pyrene, Benz (a) anthracene, Chrysene, C1-chrysenes, C2-chrysenes, Benzo (b) fluoranthene, Benzo (k) fluoranthene, Benzo (e) pyrene, Benzo (a) pyrene, Perylene, Indeno [1,2,3-c,d] pyrene, Benzo [g,h,i] perylene, dibenz [a,h] anthracene |
| Pesticides | Chlorinated Pesticides (HCB ,  HCH,  HCH, Lindane,  HCH, pp' DDE, pp'DDD, pp'DDT, DDMU, opDDE, opDDD, opDDT, CisChlordane, TransChlordane, TransNonachlor, Heptachlor, Aldrin, Dieldrin , Endrin, HeptachlorEpoxide, Methoxychlor, AlphaEndosulfan, BetaEndosulfan, EndosulfanSulfate, Aroclor1254, Aroclor1260 |
| PCBs | PCBs (PCB 8, PCB 18, PCB 28, PCB 31, PCB 44, PCB 49, PCB 52, PCB 66/95, PCB 87, PCB 97, PCB 101, PCB 105, PCB 110/77, PCB 118, PCB 126, PCB 128, PCB 138, PCB 149, PCB 153, PCB 156, PCB 169, PCB 170, PCB 174, PCB 177, PCB 180, PCB 183, PCB 187, PCB 189, PCB 194, PCB 195, PCB 201, PCB 206, PCB 209 |

Tab. 2 :Laboratory tasks

# Metods used

Grain Size

Both Sieve and pipette methods were consecutive using for grain size test.

Carbonate content

HCL is added to the aliquote of sample. Till the end of CO2 realizing the mix is boiled and afterward is diluted. Aliquote of solution is titrated by base and carbonates are calculated as CaCO3 .

Total Organic Carbon

Organic C were determined by digestion with potassium dichromate and back-titrating with 0.2 M ammonium ferrous sulfate.

EOM

20 g of sample is ectracted with 20 ml of acetone and 50 ml of CCl4. Mix is filtrated and water is added into liquide for separation of organic part. Separated organic part are determined by gravimetric method.

% Lipid content

2 g of sample was extracted in mix of methanole-chloroform mix with phosphate buffering. After separation from water solvent also were separated in rotation system. Final stage are the separation of neutral lipids by chloroform in cilicate column and glucolipids by acetone and polar lipids by methanole.

Heavy metals

Aliquote of samples were degested at Ethos-Plus Microwave system and tested by using of Varian- Spectra AA 220FS and Perkin-Elmer Aanalyst 800 atom-absorbtion spectrometers.

238U content determination

Aliquote of samples were sealed for equilibrium and quantification were fulfilled at the Canberra HP Ge Gamma-Spectrometer.

Hydrocarbons- Alkanes

Soxlet extraction, clean up and Kuderna-Danish concentration were used for sample preparation. Analyses were implemented at the GC/FID Varian 3800. Additional clarification were fulfilled by using of the Saturn 2100T GC/MS and GC/MS TRACE DSQ in SIM mode.

PAH

Soxlet extraction, clean up and Kuderna-Danish concentration were used for sample preparation. Analyses were implemented at the Varian-Prostar HPLC with  Fluorescence detector. Additional clarification were fulfilled by using of the Saturn 2100T GC/MS.

Pesticides and PCBs

Soxlet extraction, clean up and Kuderna-Danish concentration were used for sample preparation. Analyses have implemented by using of the GC/ECD Varian 3800 and GC/MS TRACE DSQ in SIM mode.

# Results

## Sediment characterization

|  | Unit | AZ1 | AZ2 | AZ3 | AZ4 | AZ5 | AZ6 | AZ7 | AZ8 | AZ9 | AZ10 | AZ11 | AZ12 | AZ13 | AZ14 | AZ15 | AZ16 | Min | Max | Mean |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Grain Size - d>5 mm | % |  | 4.5 |  |  | 5.3 |  | 14 |  |  | 12 | 6 |  |  | 24.7 |  |  | 4.50 | 24.70 | 11.08 |
| Grain Size -2.5-5 mm | % |  | 0.3 |  |  | 1.4 |  | 3.9 |  |  | 2.8 | 2.3 |  |  | 8.6 |  |  | 0.30 | 8.60 | 3.22 |
| Grain Size -1-2.5 mm | % | 0.3 | 1.1 |  |  | 3.6 |  | 5.6 | 0.8 | 0.3 | 7.1 | 21.3 | 0.1 | 0.1 | 14.5 | 0.4 | 0.7 | 0.10 | 21.30 | 4.30 |
| Grain Size -500um-1mm | % | 0.1 | 1.3 | 0.6 |  | 1.9 |  | 2.8 | 0.9 | 0.4 | 5.5 | 23.4 | 0.1 | 0.8 | 7.6 | 0.1 | 0.5 | 0.10 | 23.40 | 3.29 |
| Grain Size -250-500 um | % | 0.1 | 1.1 | 1.5 |  | 1.7 |  | 1.2 | 1.2 | 0.3 | 1.7 | 11.6 | 0.4 | 1.8 | 5.4 | 0.3 | 0.8 | 0.10 | 11.60 | 2.08 |
| Grain Size -100-250 um | % | 7.6 | 12.3 | 10.5 |  | 50.6 | 0.2 | 59.9 | 3.8 | 1.8 | 52 | 8.8 | 3.3 | 4.1 | 14.9 | 13.1 | 4.4 | 0.20 | 59.90 | 16.49 |
| Grain Size -50-100 um | % | 5.5 | 6.7 | 23.8 | 0.2 | 4.6 | 0.6 | 6.2 | 2.8 | 4.2 | 8.2 | 4.6 | 2.2 | 6.6 | 3.7 | 13.6 | 8.8 | 0.20 | 23.80 | 6.39 |
| Grain Size -10-50 um | % | 28 | 18 | 20 | 30 | 10 | 32 | 2 | 38 | 36 | 8 | 6 | 42 | 38 | 8 | 40 | 38 | 2.00 | 42.00 | 24.63 |
| Grain Size -5-10 um | % | 12 | 16 | 14 | 10 | 4 | 22 |  | 12 | 16 | 1 | 4 | 12 | 14 |  | 14 | 14 | 1.00 | 22.00 | 11.79 |
| Grain Size -1-5 um | % | 38 | 20 | 12 | 34 | 10 | 28 |  | 24 | 24 | 1 | 4 | 28 | 24 | 6 | 6 | 16 | 1.00 | 38.00 | 18.33 |
| Grain Size -d<1 um | % | 8.4 | 18.7 | 17.6 | 25.8 | 6.9 | 17.2 | 4.4 | 16.5 | 17 | 0.7 | 8 | 11.9 | 10.6 | 6.6 | 12.5 | 16.8 | 0.70 | 25.80 | 12.48 |
| Grain Size -Sum Fines<50 um | % | 86.4 | 72.7 | 63.6 | 99.8 | 30.9 | 99.2 | 6.4 | 90.5 | 93 | 10.7 | 22 | 93.9 | 86.6 | 20.6 | 72.5 | 84.8 | 6.40 | 99.80 | 64.60 |
| Carbonate | % | 2.65 | 2.37 | 1.75 | 2.55 | 2.12 | 2.57 | 1.37 | 2.5 | 2.73 | 2.6 | 5.2 | 2.55 | 2.5 | 6.1 | 2.6 | 3 | 1.37 | 6.10 | 2.82 |
| Total Organic Carbon | % | 0.72 | 1.2 | 0.48 | 1.4 | 0.52 | 1.46 | 0.2 | 2 | 0.8 | 0.4 | 0.6 | 0.78 | 1.06 | 0.82 | 0.54 | 1.2 | 0.20 | 2.00 | 0.89 |
| Extracted Organic Matter | % | 0.27 | 0.22 | 0.1 | 0.55 | 0.3 | 0.46 | 0.24 | 0.48 | 0.26 | 0.2 | 0.36 | 0.25 | 0.56 | 0.4 | 0.38 | 0.42 | 0.10 | 0.56 | 0.34 |
| Lipid content of the sediment | % | 0.24 | 0.19 | 0.05 | 0.31 | 0.26 | 0.28 | 0.21 | 0.3 | 0.2 | 0.16 | 0.27 | 0.14 | 0.24 | 0.3 | 0.28 | 0.32 | 0.05 | 0.32 | 0.23 |

Tab. 3  Sediment  characteristics

## Heavy metals

|  | Unit | AZ1 | AZ2 | AZ3 | AZ4 | AZ5 | AZ6 | AZ7 | AZ8 | AZ9 | AZ10 | AZ11 | AZ12 | AZ13 | AZ14 | AZ15 | AZ16 | Min | Max | Mean |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Ag | ug/g | 0.083 | 0.091 | 0.076 | 0.08 | 0.083 | 0.069 | 0.071 | 0.085 | 0.048 | 0.094 | 0.066 | 0.072 | 0.092 | 0.059 | 0.058 | 0.041 | 0.04 | 0.09 | 0.07 |
| Al | ug/g | 66540 | 58180 | 64250 | 67430 | 33804 | 67080 | 57780 | 69870 | 63750 | 35600 | 33820 | 64620 | 61380 | 24690 | 61530 | 72400 | 24690 | 72400 | 56420 |
| As | ug/g | 5.26 | 9.51 | 7.74 | 9.19 | 6.35 | 7.86 | 8.49 | 8.83 | 9.37 | 6.04 | 4.45 | 8.14 | 7.21 | 1.84 | 8.05 | 5.32 | 1.84 | 9.51 | 7.10 |
| Ba | ug/g | 480.2 | 511.2 | 236.0 | 565.2 | 276.8 | 552.8 | 172.0 | 498.4 | 534.4 | 215.2 | 60.8 | 743.2 | 552.0 | 157.6 | 557.6 | 577.6 | 60.82 | 743.24 | 418.20 |
| Ca | ug/g | 2303 | 4625 | 2650 | 3329 | 3019 | 3374 | 9514 | 2545 | 2616 | 4676 | 3725 | 940 | 1235 | 4459 | 1218 | 2152 | 940 | 9514 | 3273 |
| Cd | ug/g | 0.131 | 0.129 | 0.095 | 0.142 | 0.103 | 0.115 | 0.097 | 0.111 | 0.104 | 0.082 | 0.096 | 0.29 | 0.109 | 0.148 | 0.107 | 0.122 | 0.08 | 0.29 | 0.12 |
| Co | ug/g | 17.09 | 16.84 | 18.37 | 16.76 | 19.81 | 16.91 | 18.53 | 15.31 | 16.53 | 21.49 | 7.78 | 17.76 | 15.55 | 7.93 | 18.13 | 16.23 | 7.78 | 21.49 | 16.31 |
| Cr | ug/g | 111.76 | 109.36 | 135.61 | 92.57 | 197.44 | 95.52 | 108.56 | 88.96 | 96.48 | 294.32 | 27.68 | 95.84 | 83.76 | 33.44 | 105.28 | 103.21 | 27.68 | 294.32 | 111.24 |
| Cu | ug/g | 49.03 | 48.12 | 55.81 | 52.59 | 36.22 | 52.61 | 34.03 | 51.41 | 52.79 | 36.04 | 27.41 | 62.19 | 52.63 | 28.58 | 54.39 | 52.41 | 27.41 | 62.19 | 46.64 |
| Fe | ug/g | 25106 | 23512 | 24779 | 25678 | 22765 | 26435 | 18538 | 26533 | 24062 | 25327 | 7515 | 26466 | 23101 | 8593 | 25101 | 22654 | 7515 | 26533 | 22260 |
| Hg | ug/g | 0.14 | 0.166 | 0.064 | 0.176 | 0.101 | 0.198 | 0.071 | 0.176 | 0.156 | 0.082 | 0.123 | 0.148 | 0.144 | 0.106 | 0.09 | 0.173 | 0.06 | 0.20 | 0.13 |
| Li | ug/g | 24.68 | 26.45 | 27.81 | 39.25 | 21.64 | 34.84 | 16.23 | 30.52 | 27.82 | 20.76 | 17.26 | 30.82 | 26.78 | 19.53 | 24.92 | 28.62 | 16.23 | 39.25 | 26.12 |
| Mn | ug/g | 764.1 | 755.3 | 787.9 | 743.4 | 814.2 | 737.1 | 804.6 | 654.3 | 719.1 | 693.4 | 372.1 | 825.7 | 714.9 | 392.1 | 786.8 | 717.9 | 372.1 | 825.7 | 705.18 |
| Ni | ug/g | 54.21 | 51.43 | 56.19 | 52.81 | 51.19 | 53.78 | 51.04 | 52.37 | 53.44 | 52.03 | 25.18 | 60.17 | 52.78 | 27.18 | 50.02 | 53.21 | 25.18 | 60.17 | 49.81 |
| Pb | ug/g | 20.24 | 19.81 | 15.38 | 22.52 | 15.29 | 22.62 | 13.23 | 21.94 | 18.51 | 13.87 | 12.82 | 19.44 | 17.52 | 11.87 | 16.95 | 18.43 | 11.87 | 22.62 | 17.53 |
| Sb | ug/g | 0.57 | 0.52 | 0.51 | 0.65 | 0.51 | 0.59 | 0.48 | 0.61 | 0.59 | 0.45 | 0.48 | 0.52 | 0.44 | 0.39 | 0.58 | 0.61 | 0.39 | 0.65 | 0.53 |
| Se | ug/g | 0.24 | 0.18 | 0.27 | 0.29 | 0.16 | 0.31 | 0.28 | 0.46 | 0.35 | 0.4 | 0.22 | 0.26 | 0.51 | 0.46 | 0.37 | 0.44 | 0.16 | 0.51 | 0.33 |
| Sn | ug/g | 0.63 | 0.79 | 1.62 | 0.93 | 0.59 | 0.94 | 1.58 | 1.83 | 0.82 | 1.18 | 0.85 | 1.34 | 1.29 | 0.73 | 0.9 | 1.03 | 0.59 | 1.83 | 1.07 |
| U | ug/g | 1.36 | 1.28 | 1.50 | 2.04 | 1.33 | 1.97 | 1.12 | 1.38 | 1.72 | 1.38 | 0.95 | 1.77 | 1.57 | 0.44 | 1.76 | 1.46 | 1.29 | 2.46 | 1.75 |
| V | ug/g | 108.92 | 98.24 | 101.05 | 103.90 | 128.36 | 120.32 | 112.16 | 106.12 | 101.31 | 144.43 | 58.47 | 102.08 | 95.07 | 52.56 | 88.16 | 93.92 | 52.56 | 144.43 | 100.94 |
| Zn | ug/g | 81.62 | 86.79 | 79.08 | 90.41 | 76.43 | 93.38 | 63.44 | 90.39 | 83.91 | 80.74 | 45.56 | 89.68 | 78.73 | 58.25 | 80.03 | 81.35 | 45.56 | 93.38 | 78.74 |

Tab. 4 Heavy metal content

## Alkanes

|  | Unit | AZ1 | AZ2 | AZ3 | AZ4 | AZ5 | AZ6 | AZ7 | AZ8 | AZ9 | AZ10 | AZ11 | AZ12 | AZ13 | AZ14 | AZ15 | AZ16 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Total aliphatics | ug/g | 21.67 | 4.93 | 0.56 | 96.33 | 22.74 | 63.94 | 6.97 | 67.56 | 50.40 | 11.03 | 23.00 | 48.92 | 82.81 | 20.89 | 26.19 | 50.71 |
| Resolved aliphatics | ug/g | 6.1 | 4.1 | 0.4 | 19.4 | 8.5 | 14.9 | 2.1 | 7.4 | 6.2 | 2.9 | 4.0 | 3.5 | 4.6 | 3.6 | 2.4 | 5.7 |
| Unresolved aliphatics | ug/g | 15.6 | 0.8 | 0.2 | 77.0 | 14.2 | 49.0 | 4.9 | 60.1 | 44.2 | 8.2 | 19.0 | 45.5 | 78.3 | 17.3 | 23.8 | 50.1 |
| Sum-C14-C34 | ng/g | 394 | 224 | 206 | 3088 | 711 | 1952 | 270 | 3394 | 3045 | 476 | 1237 | 1067 | 3497 | 961 | 1907 | 2117 |
| Pristane | ng/g | 662 | 795 | 589 | 322 | 560 | 320 | 401.3 | 0.71 | 0.12 | 1.00 |  | 0.74 | 0.37 | 0.32 | 0.10 |  |
| Phytane | ng/g | 305.0 | 337.0 | 272.0 | 102.0 | 221.0 | 95.0 | 156.2 |  |  |  |  |  |  |  |  |  |
| (Pr+Ph)/C18+C19) |  | 8.3 | 14.7 | 14.6 | 0.9 | 3.7 | 5.6 | 16.3 | 1.1 | 0.4 | 3.5 | 0.0 | 1.2 | 0.5 | 0.6 | 0.7 | 0.0 |

|  | Unit | AZ1 | AZ2 | AZ3 | AZ4 | AZ5 | AZ6 | AZ7 | AZ8 | AZ9 | AZ10 | AZ11 | AZ12 | AZ13 | AZ14 | AZ15 | AZ16 | Min | Max | Mean |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| n-C12 | ng/g |  |  |  |  |  | 13.0 | 3.1 |  |  |  |  |  |  |  |  | 99.5 | 3.1 | 100 | 39 |
| n-C13 | ng/g |  |  |  | 62.0 |  | 469.0 | 318.2 |  |  |  |  |  |  |  |  | 45.8 | 45.8 | 469 | 224 |
| n-C14 | ng/g | 60.0 |  |  | 60.0 | 73.0 | 142.0 | 112.4 |  |  |  |  |  | 1.5 | 5.9 |  |  | 1.5 | 142 | 65 |
| n-C15 | ng/g |  |  |  |  |  | 21.0 |  |  |  |  |  |  |  |  |  | 20.9 | 20.9 | 21 | 21 |
| n-C16 | ng/g |  | 8.0 |  | 91.0 | 11.0 |  | 3.6 |  |  | 2.9 | 15.8 |  | 384.0 | 262.7 | 38.5 |  | 2.9 | 384 | 91 |
| n-C17 | ng/g | 60.0 | 37.0 |  | 133.0 | 33.0 | 86.0 | 19.2 |  |  |  |  |  |  | 0.59 |  |  | 0.6 | 133 | 53 |
| n-C18 | ng/g | 36.0 | 22.0 | 18.0 | 235.0 | 15.0 | 40.0 | 6.3 |  |  |  |  |  |  |  |  |  | 6.3 | 235 | 53 |
| n-C19 | ng/g | 81.0 | 55.0 | 41.0 | 228.0 | 197.0 | 34.0 | 28.0 | 0.63 | 0.33 | 0.29 | 0.26 | 0.63 | 0.71 | 0.52 | 0.14 |  | 0.1 | 228 | 45 |
| n-C20 | ng/g |  |  | 16.0 | 237.0 | 21.0 | 47.0 |  | 134.50 | 81.4 | 86.5 | 164.6 | 147.8 | 204.4 | 125.3 | 33.4 | 202.6 | 16.0 | 237 | 116 |
| n-C21 | ng/g |  |  | 25.0 |  |  |  |  | 21.88 |  |  | 9.11 |  | 81.54 | 23.62 |  | 52.30 | 9.1 | 82 | 36 |
| n-C22 | ng/g | 14.0 |  |  | 206.0 | 1.0 | 55.0 | 2.5 | 211.44 | 141.8 | 77.3 | 140.4 | 159.0 | 341.8 | 118.5 | 25.3 | 332.3 | 1.0 | 342 | 130 |
| n-C23 | ng/g | 58.0 | 57.0 | 39.0 | 1499.0 | 103.0 | 1229.0 | 20.6 | 1418 | 547.4 | 178.7 | 151.1 | 29.8 | 468.0 | 303.0 | 106.4 | 531.5 | 20.6 | 1499 | 421 |
| n-C24 | ng/g |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| n-C25 | ng/g |  |  |  | 74.0 |  | 4.0 |  | 98.57 | 139.9 |  | 4.72 | 23.6 | 92.7 |  | 32.7 | 38.1 | 4.0 | 140 | 56 |
| n-C26 | ng/g |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| n-C27 | ng/g |  |  |  |  |  |  |  | 157.61 | 305.3 |  |  | 34.1 | 131.0 |  | 110.7 | 32.5 | 32.5 | 305 | 129 |
| n-C28 | ng/g |  |  |  |  |  |  |  |  | 95.1 |  |  |  |  |  |  |  | 95.1 | 95 | 95 |
| n-C29 | ng/g |  |  |  | 95.0 |  | 71.0 |  | 343.35 | 335.6 | 10.7 | 360.0 | 276.4 | 737.2 |  | 604.2 | 197.0 | 10.7 | 737 | 303 |
| n-C30 | ng/g | 50.0 | 23.0 | 19.0 | 80.0 | 42.0 | 76.0 | 37.4 | 594.30 | 534.8 | 56.7 | 240.1 | 172.1 | 608.5 | 54.4 | 472.2 | 352.8 | 19.0 | 609 | 213 |
| n-C31 | ng/g | 35.0 | 22.0 | 18.0 | 112.0 | 67.0 | 100.0 | 16.1 | 324.36 | 453.3 | 63.4 | 108.4 | 189.9 | 370.2 | 66.6 | 353.6 | 323.4 | 16.1 | 453 | 164 |
| n-C32 | ng/g |  |  |  | 17.0 |  | 18.0 | 0.0 | 31.97 | 237.2 |  |  |  |  |  | 31.3 |  | 0.0 | 237 | 56 |
| n-C33 | ng/g |  |  | 30.0 | 21.0 | 42.0 | 29.0 | 24.1 | 57.07 | 173.5 |  | 42.9 | 34.0 | 75.4 |  | 98.8 | 32.8 | 21.0 | 174 | 55 |
| n-C34 | ng/g |  |  |  |  | 106.0 |  |  |  |  |  |  |  |  |  |  |  | 106.0 | 106 | 106 |
| n-C35 | ng/g |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| n-C36 | ng/g |  |  |  |  |  |  |  |  | 43.4 |  |  |  | 22.00 |  |  |  | 22.0 | 43 | 33 |

Tab. 5 Individual alkanes contents

## PAH

|  |  | MDL | Min | Max | AZ-1 | AZ-2 | AZ-3 | AZ-4 | AZ-5 | AZ-6 | AZ-7 | AZ-8 | AZ-9 | AZ-10 | AZ-11 | AZ-12 | AZ-13 | AZ-14 | AZ-15 | AZ-16 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Naphthalene | ng/g | 0.5 | 1.26 | 4.21 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | 4.21 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | 1.26 | <0.5 |
| C1-naphthalenes | ng/g | 0.5 | 0.56 | 13.70 | <0.5 | <0.5 | 0.56 | <0.5 | <0.5 | 1.01 | 13.7 | 0.67 | <0.5 | 0.85 | <0.5 | <0.5 | <0.5 | <0.5 | 2.04 | <0.5 |
| C2-naphthalenes | ng/g | 0.5 | 0.72 | 25.50 | <0.5 | <0.5 | 1.05 | <0.5 | <0.5 | 1.89 | 25.5 | 1.25 | <0.5 | 1.59 | <0.5 | <0.5 | 0.72 | 0.83 | 1.7 | 0.94 |
| C3-naphthalenes | ng/g | 0.5 | 0.57 | 11.70 | <0.5 | <0.5 | 0.58 | <0.5 | <0.5 | 0.87 | 11.7 | 0.57 | <0.5 | 0.73 | <0.5 | <0.5 | <0.5 | <0.5 | 2.61 | <0.5 |
| Acenaphthylene | ng/g | 0.5 | 0.60 | 1.72 | 0.60 | <0.5 | <0.5 | 0.83 | <0.5 | 0.77 | <0.5 | <0.5 | 1.72 | <0.5 | 0.94 | 0.71 | 0.67 | <0.5 | <0.5 | <0.5 |
| Acenaphthene | ng/g | 0.5 | 0.61 | 0.73 | <0.5 | <0.5 | <0.5 | 0.73 | <0.5 | <0.5 | <0.5 | 0.61 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 |
| Fluorene | ng/g | 0.5 | 0.62 | 1.96 | 0.62 | <0.5 | 1.74 | <0.5 | <0.5 | 1.96 | <0.5 | 1.49 | <0.5 | 1.76 | <0.5 | <0.5 | 0.82 | 0.87 | 0.83 | 0.89 |
| C1-Fluorenes | ng/g | 0.5 | 0.56 | 1.71 | 0.58 | <0.5 | 1.28 | 0.72 | 0.56 | 1.71 | 0.88 | 1.60 | <0.5 | 1.28 | <0.5 | 0.64 | 0.63 | 1.15 | 0.75 | 0.72 |
| Phenanthrene | ng/g | 0.6 | 0.90 | 8.70 | 2.09 | <0.6 | <0.6 | 6.85 | 1.40 | 6.26 | 0.90 | 7.90 | 7.55 | 2.09 | <0.6 | 8.70 | 3.86 | 1.97 | 3.56 | 4.49 |
| C1-phenanthrenes | ng/g | 0.6 | 0.62 | 11.02 | 2.91 | <0.6 | 0.62 | 9.55 | 1.96 | 8.73 | 1.25 | 11.02 | 10.53 | 2.91 | <0.6 | 9.16 | 5.39 | 2.75 | 4.18 | 6.26 |
| C2-phenanthrenes | ng/g | 0.6 | 0.64 | 10.34 | 2.73 | <0.6 | 0.64 | 8.97 | 1.84 | 8.20 | 1.18 | 10.34 | 9.89 | 2.73 | <0.6 | 7.84 | 5.06 | 2.58 | 4.05 | 5.88 |
| C3-phenanthrenes | ng/g | 0.6 | 0.74 | 8.04 | 1.72 | <0.6 | <0.6 | 5.63 | 1.16 | 5.15 | 0.74 | 6.50 | 6.21 | 1.72 | <0.6 | 8.04 | 3.18 | 1.62 | 3.28 | 3.69 |
| C4-phenanthrenes | ng/g | 0.6 | 0.66 | 6.75 | 0.99 | <0.6 | <0.6 | 3.24 | 0.66 | 2.97 | <0.6 | 3.74 | 3.58 | 0.99 | <0.6 | 6.75 | 1.83 | 0.93 | 1.74 | 2.13 |
| Anthracene | ng/g | 0.5 | 0.69 | 4.27 | 1.54 | <0.5 | <0.5 | 3.05 | <0.5 | 2.85 | <0.5 | 3.43 | 2.93 | 0.74 | 0.93 | 4.27 | 1.58 | 0.69 | 2.32 | 1.93 |
| Dibenzothiophene | ng/g | 0.5 | 0.57 | 3.27 | 0.71 | <0.5 | <0.5 | 1.26 | 0.57 | 1.04 | <0.5 | 1.18 | 1.68 | <0.5 | <0.5 | 3.27 | <0.5 | <0.5 | 1.03 | <0.5 |
| C1-dibenzothiophenes | ng/g | 0.5 | 0.62 | 3.14 | 0.86 | <0.5 | <0.5 | 2.73 | 0.62 | 1.42 | <0.5 | 1.93 | 0.96 | <0.5 | <0.5 | 3.14 | 1.17 | 0.86 | 2.31 | 1.04 |
| C2-dibenzothiophenes | ng/g | 0.5 | 0.69 | 5.80 | 0.69 | 0.71 | <0.5 | 2.70 | 0.75 | 1.27 | <0.5 | 1.69 | 1.14 | 5.80 | 0.72 | 1.83 | 1.95 | 1.08 | 2.45 | 1.63 |
| C3-dibenzothiophenes | ng/g | 0.5 | 0.59 | 2.51 | 0.78 | <0.5 | <0.5 | 2.51 | <0.5 | 0.79 | <0.5 | 1.26 | 0.88 | <0.5 | <0.5 | 2.16 | <0.5 | 0.59 | 0.94 | 0.83 |
| Retene | ng/g | 0.6 | 0.70 | 1.31 | 1.31 | 0.82 | 0.70 | <0.6 | <0.6 | <0.6 | <0.6 | <0.6 | <0.6 | <0.6 | <0.6 | <0.6 | <0.6 | <0.6 | <0.6 | <0.6 |
| Fluoranthene | ng/g | 0.6 | 1.08 | 6.21 | 2.04 | <0.6 | <0.6 | 4.84 | 1.08 | 4.01 | <0.6 | 4.99 | 6.21 | 1.39 | 3.12 | 5.41 | 3.73 | 2.09 | 1.95 | 3.85 |
| Pyrene | ng/g | 0.6 | 0.83 | 5.73 | 3.54 | <0.6 | <0.6 | 5.54 | 1.12 | 4.03 | <0.6 | 5.73 | 0.83 | 1.29 | 2.34 | 3.17 | 4.98 | <0.6 | 4.47 | 4.72 |
| Cl-Pyrenes | ng/g | 0.6 | 0.63 | 3.17 | 2.53 | <0.6 | <0.6 | 1.86 | 0.86 | 3.17 | <0.6 | 1.28 | 0.63 | 1.07 | 1.25 | 2.04 | 2.91 | <0.6 | 3.14 | 1.73 |
| Benzo (c) phenanthrene | ng/g | 0.6 | 0.72 | 1.38 | 1.27 | <0.6 | <0.6 | 0.94 | 0.72 | 1.38 | <0.6 | 0.93 | <0.6 | 0.84 | <0.6 | <0.6 | 1.04 | <0.6 | <0.6 | <0.6 |
| Benzo (a) anthracene | ng/g | 0.4 | 0.67 | 4.10 | 2.14 | <0.4 | <0.4 | 3.77 | 0.67 | 2.77 | <0.4 | 4.00 | 4.10 | 0.74 | 1.70 | 0.94 | 3.09 | 1.04 | 1.07 | 3.26 |
| Chrysene | ng/g | 0.6 | 0.65 | 2.06 | 0.73 | <0.6 | <0.6 | <0.6 | <0.6 | <0.6 | <0.6 | 1.63 | 2.06 | <0.6 | 0.72 | <0.6 | 1.36 | 0.65 | 1.26 | 1.84 |
| C1-chrysenes | ng/g | 0.6 | 0.69 | 3.14 | 0.69 | <0.6 | <0.6 | <0.6 | <0.6 | <0.6 | <0.6 | 1.54 | 1.94 | <0.6 | 1.07 | <0.6 | 2.14 | <0.6 | 3.14 | 0.92 |
| C2-chrysenes | ng/g | 0.6 | 0.63 | 2.18 | 0.63 | <0.6 | <0.6 | <0.6 | <0.6 | <0.6 | <0.6 | 1.42 | 1.79 | <0.6 | 0.73 | <0.6 | 0.93 | <0.6 | 1.50 | 2.18 |

Tab. 6 PAH content

|  |  | MDL | Min | Max | AZ-1 | AZ-2 | AZ-3 | AZ-4 | AZ-5 | AZ-6 | AZ-7 | AZ-8 | AZ-9 | AZ-10 | AZ-11 | AZ-12 | AZ-13 | AZ-14 | AZ-15 | AZ-16 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Benzo (b) fluoranthene | ng/g | 0.5 | 0.53 | 4.21 | 1.51 | <0.5 | 0.56 | 3.61 | 0.69 | 2.70 | <0.5 | 4.21 | 2.23 | 1.07 | 0.98 | 1.42 | 2.33 | 1.10 | 0.53 | 2.37 |
| Benzo (k) fluoranthene | ng/g | 0.4 | 0.59 | 4.21 | 1.31 | <0.4 | 0.61 | 3.80 | 0.61 | 2.58 | <0.4 | 4.21 | 0.66 | 0.72 | <0.4 | <0.4 | 2.07 | 0.59 | <0.4 | 2.99 |
| Benzo (a) fluoranthene | ng/g | 0.5 | 0.58 | 1.18 | 0.83 | <0.5 | 0.76 | 0.93 | <0.5 | 0.92 | <0.5 | 1.18 | <0.5 | <0.5 | <0.5 | <0.5 | 0.58 | <0.5 | <0.5 | 0.93 |
| Benzo (e) pyrene | ng/g | 0.6 | 1.18 | 6.44 | 2.36 | <0.6 | <0.6 | 5.41 | 1.48 | 4.19 | <0.6 | 6.44 | <0.6 | 1.69 | 1.77 | 2.70 | 5.20 | 1.74 | 1.18 | 5.96 |
| Benzo (a) pyrene | ng/g | 0.5 | 0.52 | 2.85 | 1.38 | <0.5 | <0.5 | 2.84 | 0.52 | 2.13 | <0.5 | 2.85 | <0.5 | 0.59 | 0.72 | 0.89 | 2.11 | 0.74 | <0.5 | 2.48 |
| Perylene | ng/g | 0.5 | 0.58 | 9.58 | 6.6 | 0.79 | 1.08 | 9.58 | 2.10 | 8.65 | 0.58 | 5.24 | 1.42 | 2.96 | 4.81 | 0.77 | 7.65 | 0.79 | 3.06 | 8.74 |
| Indeno[1,2,3-c,d] pyrene | ng/g | 0.4 | 0.49 | 1.47 | 0.81 | <0.4 | <0.4 | <0.4 | 0.49 | 1.36 | <0.4 | 1.09 | 0.88 | 0.57 | <0.4 | <0.4 | 1.47 | <0.4 | <0.4 | 0.62 |
| Benzo [g,h,i] perylene | ng/g | 0.4 | 0.69 | 3.23 | 1.73 | <0.4 | <0.4 | <0.4 | 0.69 | 2.85 | <0.4 | 1.51 | 0.80 | 1.19 | 0.84 | 2.90 | 2.71 | 1.11 | <0.4 | 3.23 |
| Dibenz [a,h] anthracene | ng/g | 0.3 | 0.91 | 4.43 | <0.3 | <0.3 | <0.3 | 4.43 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | 1.41 | 1.01 | 3.05 | <0.3 | 0.91 | <0.3 |
| Sum PAHs | ng/g |  | 2.32 | 103.4 | 48.2 | 2.3 | 10.2 | 96.3 | 20.5 | 87.6 | 60.6 | 103.4 | 70.6 | 37.3 | 24.1 | 77.8 | 74.2 | 25.8 | 57.3 | 76.3 |
| Fines<50 um | % |  |  |  | 86.4 | 72.7 | 63.6 | 99.8 | 30.9 | 99.2 | 6.4 | 90.5 | 93 | 10.7 | 22 | 93.9 | 86.6 | 20.6 | 72.5 | 84.8 |
| UCM/R >4 |  |  |  |  | 2.56 | 0.20 | 0.50 | 3.97 | 1.67 | 3.29 | 2.33 | 8.12 | 7.13 | 2.83 | 4.75 | 13.00 | 17.02 | 4.81 | 9.92 | 8.79 |

Tab. 7 PAH content (continue)

## Pesticides

|  | Unit | MDL | Min | Max | AZ1 | AZ2 | AZ3 | AZ4 | AZ5 | AZ6 | AZ7 | AZ8 | AZ9 | AZ10 | AZ11 | AZ12 | AZ13 | AZ14 | AZ15 | AZ16 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| HCB | ng/g | <0.5 | 0.43 | 0.63 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | 0.63 | <0.5 | <0.5 | 0.51 | <0.5 | 0.43 | <0.5 | <0.5 | <0.5 |
| a HCH | ng/g | <0.5 | 0.63 | 2.28 | 1.85 | 1.1 | 0.64 | 2.28 | 1.21 | 1.37 | 0.63 | <0.5 | 1.04 | <0.5 | 1.28 | 0.74 | 2.23 | <0.5 | 0.95 | 0.86 |
| b HCH | ng/g | <0.5 | 0.55 | 19.3 | 0.72 | 0.63 | 0.55 | 4.3 | 0.91 | 2.8 | <0.5 | 19.3 | 3.6 | 0.78 | 0.7 | <0.5 | 1.6 | 1.7 | 2.3 | 1.17 |
| Lindane | ng/g | <0.5 | 0.68 | 1.06 | 0.93 | <0.5 | <0.5 | 1.06 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | 1.04 | <0.2 | 0.68 |
| d HCH | ng/g | <0.5 | 0.74 | 1.69 | <0.5 | <0.5 | <0.5 | 1.12 | <0.5 | <0.5 | <0.5 | <0.5 | 1.69 | <0.5 | 1.35 | 0.74 | 1.67 | 1.61 | <0.5 | <0.5 |
| pp' DDE | ng/g | <0.5 | 0.63 | 1.20 | 0.71 | <0.5 | <0.5 | 0.73 | <0.5 | 1.2 | 0.68 | 0.63 | 0.7 | <0.5 | <0.5 | 0.83 | <0.5 | <0.5 | 0.8 | 0.94 |
| pp' DDD | ng/g | <0.4 | 0.61 | 1.63 | <0.4 | <0.4 | <0.4 | 0.68 | <0.4 | 1.63 | <0.4 | 0.71 | 0.9 | <0.4 | 0.86 | 0.61 | 1.34 | 1.6 | 1.3 | 1.2 |
| pp' DDT | ng/g | <0.5 | 0.62 | 1.40 | <0.5 | <0.5 | <0.5 | 1.03 | <0.5 | 0.7 | <0.5 | <0.5 | 0.7 | <0.5 | 0.62 | 0.94 | 1.17 | <0.5 | 1.4 | 0.85 |
| DDMU | ng/g | <0.6 | 0.00 | 0.00 | <0.6 | <0.6 | <0.6 | <0.6 | <0.6 | <0.6 | <0.6 | <0.6 | <0.6 | <0.6 | <0.6 | <0.6 | <0.6 | <0.6 | <0.6 | <0.6 |
| op' DDE | ng/g | <0.5 | 0.68 | 1.26 | 0.68 | <0.5 | <0.5 | 0.94 | <0.5 | 0.75 | <0.5 | <0.5 | 0.97 | <0.5 | <0.5 | 0.77 | 0.68 | <0.5 | 0.94 | 1.26 |
| op' DDD | ng/g | <0.5 | 0.67 | 1.31 | <0.5 | <0.5 | <0.5 | 0.67 | <0.5 | 0.68 | <0.5 | 0.68 | 1.31 | <0.5 | <0.5 | 0.93 | 0.73 | <0.5 | 1.28 | 0.78 |
| op' DDT | ng/g | <0.5 | 0.71 | 1.63 | 0.73 | <0.5 | <0.5 | 0.71 | <0.5 | <0.5 | <0.5 | <0.5 | 0.83 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | 0.88 | 1.63 |
| cis Chlordane | ng/g | <0.5 | 0.00 | 0.00 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 |
| trans Chlordane | ng/g | <0.5 | 0.00 | 0.00 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 |
| trans Nonachlor | ng/g | <0.5 | 0.00 | 0.00 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 |
| Heptachlor | ng/g | <0.5 | 0.00 | 0.00 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 |
| Aldrin | ng/g | <0.5 | 1.64 | 1.64 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | 1.64 | <0.5 | <0.5 |
| Dieldrin | ng/g | <0.5 | 0.00 | 0.00 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 |
| Endrin | ng/g | <0.5 | 0.00 | 0.00 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 |
| Heptachlor epoxide | ng/g | <0.5 | 0.72 | 0.72 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | 0.72 | <0.5 | <0.5 |
| Methoxychlor | ng/g | <1.5 | 0.00 | 0.00 | <1.5 | <1.5 | <1.5 | <1.5 | <1.5 | <1.5 | <1.5 | <1.5 | <1.5 | <1.5 | <1.5 | <1.5 | <1.5 | <1.5 | <1.5 | <1.5 |
| Alpha Endosulfan | ng/g | <0.5 | 0.64 | 5.18 | 0.94 | <0.5 | 0.64 | <0.5 | <0.5 | 5.18 | <0.5 | 2.64 | 0.83 | <0.5 | 0.71 | 0.86 | 1.16 | 1.83 | 1.83 | 1.72 |
| Beta Endosulfan | ng/g | <0.5 | 0.82 | 1.77 | <0.5 | <0.5 | <0.5 | 1.77 | <0.5 | 1.49 | <0.5 | 0.82 | <0.5 | <0.5 | <0.5 | 1.18 | <0.5 | <0.5 | 0.92 | 1.68 |
| Endosulfan sulfate | ng/g | <0.5 | 0.53 | 2.19 | <0.5 | <0.5 | <0.5 | <0.5 | 0.53 | 0.55 | <0.5 | 0.64 | 1.17 | 0.62 | 0.8 | 1.94 | 1.6 | 0.8 | 2.19 | 2.17 |
| Aroclor 1254 | ng/g | <0.5 | 0.00 | 0.00 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 |
| Aroclor 1260 | ng/g | <0.5 | 0.00 | 0.00 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 |
| Sum of Pesticides | ng/g |  | 3.89 | 30.04 | 8.69 | 5.68 | 3.89 | 30.04 | 11.34 | 22.02 | 4.46 | 13.92 | 21.58 | 6.2 | 6.2 | 16.42 | 29.22 | 4.15 | 14.65 | 14.14 |
| Fines<50 um | % |  |  |  | 86.4 | 72.7 | 63.6 | 99.8 | 30.9 | 99.2 | 6.4 | 90.5 | 93 | 10.7 | 22 | 93.9 | 86.6 | 20.6 | 72.5 | 84.8 |
| Lipid content | % |  |  |  | 0.24 | 0.19 | 0.05 | 0.31 | 0.26 | 0.28 | 0.21 | 0.3 | 0.2 | 0.16 | 0.27 | 0.14 | 0.24 | 0.3 | 0.28 | 0.32 |

Tab. 8 Pesticides content

## PCBs

|  | Unit |  | Min | Max | AZ1 | AZ2 | AZ3 | AZ4 | AZ5 | AZ6 | AZ7 | AZ8 | AZ9 | AZ10 | AZ11 | AZ12 | AZ13 | AZ14 | AZ15 | AZ16 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| PCB 8 | ng/g | 0.1 | 0.30 | 0.50 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | 0.5 | 0.3 | <0.1 | <0.1 |
| PCB 18 | ng/g | 0.1 | 0.40 | 14.30 | <0.1 | <0.1 | <0.1 | 0.4 | 1.49 | <0.1 | <0.1 | 3.64 | 12.1 | <0.1 | 0.55 | <0.1 | 14.3 | <0.1 | 1.58 | <0.1 |
| PCB 28 | ng/g | 0.1 | 0.48 | 2.17 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | 0.7 | <0.1 | <0.1 | <0.1 | 0.9 | 0.48 | 2.17 | <0.1 |
| PCB 31 | ng/g | 0.1 | 0.40 | 1.17 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | 0.4 | 0.8 | 1.15 | <0.1 | <0.1 | <0.1 | <0.1 | 0.9 | 1.17 | 0.83 | <0.1 |
| PCB 44 | ng/g | 0.1 | 0.30 | 0.93 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | 0.6 | 0.7 | 0.3 | 0.9 | 0.93 | 0.58 | <0.1 |
| PCB 49 | ng/g | 0.1 | 0.20 | 1.73 | <0.1 | <0.1 | <0.1 | 0.8 | <0.1 | 0.6 | <0.1 | <0.1 | <0.1 | 0.27 | 0.48 | 1.73 | 0.2 | 0.3 | <0.1 | <0.1 |
| PCB 52 | ng/g | 0.1 | 0.40 | 8.55 | <0.1 | <0.1 | <0.1 | 2.99 | 0.6 | 2.33 | 1.27 | 0.5 | 1.3 | 0.54 | 0.89 | 8.55 | 0.4 | <0.1 | <0.1 | 4.3 |
| PCB 66/95 | ng/g | 0.1 | 0.30 | 0.80 | <0.1 | <0.1 | <0.1 | 0.41 | <0.1 | 0.5 | <0.1 | <0.1 | <0.1 | 0.7 | 0.4 | 0.8 | 0.3 | <0.1 | 0.47 | <0.1 |
| PCB 87 | ng/g | 0.1 | 0.30 | 1.33 | <0.1 | <0.1 | <0.1 | 0.7 | 0.3 | 0.92 | 0.3 | <0.1 | <0.1 | 0.6 | 0.58 | 0.6 | 1.33 | <0.1 | 0.72 | 0.6 |
| PCB 97 | ng/g | 0.1 | 0.60 | 2.69 | <0.1 | <0.1 | <0.1 | 2.69 | 0.8 | 0.7 | <0.1 | <0.1 | 1.94 | <0.1 | 0.6 | <0.1 | 0.86 | <0.1 | 1.15 | <0.1 |
| PCB 101 | ng/g | 0.1 | 0.20 | 6.41 | <0.1 | <0.1 | 1.17 | 5.86 | 1.15 | 6.41 | 0.8 | 2.16 | 3.57 | 0.54 | 0.44 | 1.02 | 6.17 | 0.67 | 0.2 | 1.77 |
| PCB 105 | ng/g | 0.1 | 0.24 | 0.84 | <0.1 | <0.1 | <0.1 | 0.82 | 0.24 | 0.37 | <0.1 | 0.84 | <0.1 | 0.3 | 0.7 | <0.1 | 0.6 | <0.1 | <0.1 | <0.1 |
| PCB 110/77 | ng/g | 0.1 | 0.30 | 0.95 | <0.1 | <0.1 | 0.4 | 0.46 | 0.81 | 0.6 | <0.1 | <0.1 | <0.1 | 0.43 | 0.5 | <0.1 | 0.4 | 0.3 | 0.95 | <0.1 |
| PCB 118 | ng/g | 0.1 | 0.30 | 2.17 | <0.1 | <0.1 | <0.1 | 0.6 | 0.7 | <0.1 | <0.1 | <0.1 | <0.1 | 0.3 | <0.1 | 0.86 | <0.1 | <0.1 | 2.17 | <0.1 |
| PCB 126 | ng/g | 0.1 | 0.70 | 1.54 | <0.1 | <0.1 | <0.1 | 1.54 | 0.72 | 0.94 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | 0.7 | <0.1 | <0.1 | 1.13 | <0.1 |
| PCB 128 | ng/g | 0.1 | 0.30 | 0.70 | 0.7 | 0.6 | 0.42 | 0.53 | 0.62 | 0.3 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | 0.4 | <0.1 | <0.1 | 0.7 | <0.1 |
| PCB 138 | ng/g | 0.1 | 0.29 | 5.91 | 1.07 | 1.28 | 1.9 | 5.91 | 0.89 | 4.67 | 0.29 | <0.1 | <0.1 | 0.37 | <0.1 | 0.98 | <0.1 | <0.1 | 0.68 | 1.68 |
| PCB 149 | ng/g | 0.1 | 0.23 | 3.34 | <0.1 | <0.1 | <0.1 | 3.34 | 0.72 | 0.4 | 0.23 | <0.1 | <0.1 | 0.29 | <0.1 | 0.28 | <0.1 | <0.1 | 0.49 | 0.59 |
| PCB 153 | ng/g | 0.1 | 0.20 | 1.68 | <0.1 | 0.56 | <0.1 | 1.16 | 0.55 | 1.68 | 0.47 | <0.1 | <0.1 | 0.53 | <0.1 | 0.2 | <0.1 | <0.1 | <0.1 | 1.23 |
| PCB 156 | ng/g | 0.1 | 0.26 | 0.80 | <0.1 | <0.1 | <0.1 | 0.73 | 0.35 | 0.8 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | 0.26 |
| PCB 169 | ng/g | 0.1 | 0.30 | 0.67 | <0.1 | 0.3 | <0.1 | 0.3 | <0.1 | 0.4 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | 0.67 |
| PCB 170 | ng/g | 0.1 | 0.30 | 0.53 | 0.5 | <0.1 | <0.1 | 0.3 | 0.4 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | 0.3 | <0.1 | <0.1 | 0.53 |
| PCB 174 | ng/g | 0.1 | 0.37 | 0.60 | 0.4 | <0.1 | <0.1 | 0.5 | 0.6 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | 0.37 |
| PCB 177 | ng/g | 0.1 | 0.30 | 1.10 | 1.1 | 0.5 | <0.1 | <0.1 | 0.4 | <0.1 | <0.1 | 0.52 | 0.48 | 0.3 | <0.1 | <0.1 | 0.5 | <0.1 | <0.1 | 0.74 |

Tab. 9 PCB content

|  | Unit |  | Min | Max | AZ1 | AZ2 | AZ3 | AZ4 | AZ5 | AZ6 | AZ7 | AZ8 | AZ9 | AZ10 | AZ11 | AZ12 | AZ13 | AZ14 | AZ15 | AZ16 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| PCB 180 | ng/g | 0.1 | 0.30 | 0.83 | 0.4 | 0.3 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | 0.71 | 0.65 | 0.43 | 0.36 | <0.1 | 0.36 | <0.1 | 0.83 | 0.76 |
| PCB 183 | ng/g | 0.1 | 0.30 | 0.87 | 0.58 | 0.47 | <0.1 | <0.1 | <0.1 | <0.1 | 0.3 | 0.87 | <0.1 | <0.1 | <0.1 | <0.1 | 0.3 | <0.1 | <0.1 | 0.44 |
| PCB 187 | ng/g | 0.1 | 0.47 | 0.68 | 0.5 | 0.47 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | 0.68 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 |
| PCB 189 | ng/g | 0.1 | 0.72 | 0.72 | 0.72 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 |
| PCB 194 | ng/g | 0.1 | 0.20 | 0.92 | 0.92 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | 0.2 |
| PCB 195 | ng/g | 0.1 | 0.40 | 0.84 | 0.4 | 0.7 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | 0.73 | 0.84 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 |
| PCB 201 | ng/g | 0.1 | 0.20 | 0.67 | 0.3 | 0.2 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | 0.67 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 |
| PCB 206 | ng/g | 0.1 | 0.30 | 0.94 | 0.7 | 0.3 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | 0.94 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 |
| PCB 209 | ng/g | 0.1 | 0.40 | 0.51 | 0.4 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | 0.51 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 | <0.1 |
| Sum of PCBs | ng/g |  | 3.89 | 30.04 | 8.69 | 5.68 | 3.89 | 30.04 | 11.34 | 22.02 | 4.46 | 13.92 | 21.58 | 6.2 | 6.2 | 16.42 | 29.22 | 4.15 | 14.65 | 14.14 |
| Fines<50 um | % |  |  |  | 86.4 | 72.7 | 63.6 | 99.8 | 30.9 | 99.2 | 6.4 | 90.5 | 93 | 10.7 | 22 | 93.9 | 86.6 | 20.6 | 72.5 | 84.8 |
| Lipid content | % |  |  |  | 0.24 | 0.19 | 0.05 | 0.31 | 0.26 | 0.28 | 0.21 | 0.3 | 0.2 | 0.16 | 0.27 | 0.14 | 0.24 | 0.3 | 0.28 | 0.32 |

Tab. 10 PCB content (continue)

# Text boxes

|  | A Z E C O L A B |
| --- | --- |
|  | av.H.Javid 31a, Institute of Radiation Problems, Baku, Azerbaijan Tel: +99412 383592; Fax: +99412 479616; E-mail: ael@azecolab.com www.azecolab.com |