P.P.Shirshov Institute of Oceanology. Russian Academy of Sciences.

Results of the Analyses of the Sediment Samples Collected in the Northern Caspian

during the Scientific Sea Cruise of R/V Tantal in November 2005 (Leg 3 of SSG-2005)

in frames of Caspian Environmental Program (CEP-SAP Project)

Report on the Small Contract for Services

(Ref. 00034997/2006/002 Amendment 1)

Analyses were fulfilled by the Geochemical Laboratory of the P.P. Shirshov Institute of Oceanology of Russian Academy of Sciences (SIO RAS) in cooperation with Laboratories of ROSHYDROMET in Obninsk (Typhoon) and Moscow (SOI) in period from 15 May 2006 to 31 July 2006 according to the Small Contract for Services (United Nations Office for Project Services. Ref. 00034997/2006/002. Amendment 1).

L.I.Lobkovsky (Director SIO RAS)

A.G.Rozanov (responsible for the Contract)

Moscow

July 2006

Results of the Analyses of the Sediment Samples Collected in the Northern Caspian

during the Scientific Sea Cruise of R/V Tantal in November 2005 (Leg 3 of SSG-2005) in frames of Caspian Environmental Program (CEP-SAP Project)

Report on the Small Contract for Services

(Ref. 00034997/2006/002 Amendment 1)

Report contains tables of the results of sample analyses (Part I – V), accompanied by the description of methodology/sample preparation, laboratory procedures and QA/QC procedures. Sometimes description of routine technique is omitted.

Page

Content                                                                                                                          2

Part I.        List of sampling points (station numbers and coordinates), table 1            3

Part II        Sediment characterization:                                                                          4

Grain size of sediment, table 2                                               4

Organic Carbon of the sediment, table 3                                7

Carbonate of the sediment, table 3                                         7

Part III     Trace metals                                                                                                  8

Sample preparation and acid dissolution for TM                   8

Methods                                                                                  8

Results, table 4                                                                        9

Part IV     Oil and oil products and Extracted Organic matter (EOM)                          12

Extraction of alkane - naphthene hydrocarbons (HC)             12

HC gas chromatographic analysis                                           12

Results, table 5                                                                         13

Part V      Petroleum and organic antropogenic compouns                                           18

1. Introduction                                                                           18

2. Analytical methods                                                               18

2.1 PCBs                                                                                    18

2.2 Chlorinated Pesticides                                                           21

2.3 PAHs                                                                                     23

2.4 Dioxins/Furans                                                                      26

2.5 Dioxin-like Complanar Congeneres                                     29

2.6 Aroclor 1254, Aroclor 1260                                                32

3. Results                                                                                    35

4. Quality control                                                                        62

Part 1. Points of sampling (station numbers, coordinates)

| File | Region | Sample | X | Y | Date | Parameters |
| --- | --- | --- | --- | --- | --- | --- |
| CEP-2006 | North Caspean Sea | RU-1 | 42° 55.9’ | 47°41.1’ | 08 – 15/11/ 2005 | Grane Size of sediment, Organic Carbon and Carbonate, Tracemetals, Oil and oil products, Extracted organic matter, PAHs, Chlorinated Pestisides, PCBs, Dioxin-like Complanar Congeneres, Dioxin/Furans |
|  |  | RU-2 | 42° 27.9’ | 48° 03.1’ |  |  |
|  |  | RU-3 | 42° 02.0’ | 48° 23.4’ |  |  |
|  |  | RU-4 | 41° 55.2’ | 48° 30.1’ |  |  |
|  |  | RU-5 | 43° 13.1’ | 47° 31.7’ |  |  |
|  |  | RU-6 | 43° 14.4’ | 47о 33.6’ |  |  |
|  |  | RU-7 | 43° 13.4’ | 47° 36.0’ |  |  |
|  |  | RU-8 | 43° 31.0’ | 47° 32.0’ |  |  |
|  |  | RU-9 | 43° 33.0’ | 47° 32.9’ |  |  |
|  |  | RU-10 | 43° 33.0’ | 47° 38.3’ |  |  |
|  |  | RU-11 | 43° 59.3’ | 48° 05.9’ |  |  |
|  |  | RU-12 | 44° 18.0’ | 48° 55.9’ |  |  |
|  |  | KZ-1 | 44° 23.3’ | 49° 24.5’ |  |  |
|  |  | KZ-2 | 44° 30.4’ | 49° 47.9’ |  |  |
|  |  | KZ-3 | 45° 53.0’ | 50° 43.0’ |  |  |
|  |  | KZ-4 | 46° 01.1’ | 50° 50.0’ |  |  |
|  |  | KZ-5 | 45° 10.0’ | 50° 57.9’ |  |  |
|  |  | KZ-6 | 46° 19.0’ | 51° 04.9’ |  |  |
|  |  | KZ-7 | 46° 27.0’ | 51° 11.9’ |  |  |
|  |  | KZ-8 | 46° 36.0’ | 51° 19.0’ |  |  |
|  |  | KZ-13 | 46° 36.0’ | 51° 19.0’ |  |  |
|  |  | Ст. 8, проба 7 | 46° 3.8’ | 48° 30.8’ | 30/08 –07/09/2005 |  |
|  |  | Ст.11, проба 10 | 45° 21.0’ | 48° 13.0’ |  |  |
|  |  | Ст 12, проба 14 | 45° 37.7’ | 48° 1.0’ |  |  |
|  |  | Ст. 16, проба 11 | 45° 41.4’ | 48° 16.6’ |  |  |
|  |  | Ст. 19, проба 18 | 45° 51.8’ | 47° 38.2’ |  |  |
|  |  | Ст. 23, проба 20 | 46° 42.5 | 47° 51.1 |  |  |
|  |  | Ст. 14, проба Lagan-R | 45° 17.815’ | 47° 30.021’ |  |  |

Part II. Sediment Characterization:

Grane size of sediment

Wet sediment about (20 g) is heated in solution of dispergator (Na tripolyphosfate) and washed out by distilled water into 6-l glass cylinder through 0.1 and 0.05 mm sieves where coarse grain size fractions (>0.1 and 0.1-0.05 mm) collected. Fractions are dried, the fraction >0.1 mm is run by further sieving, after that all collected fractions (0.1-0.05; 0.25-0 1; 0.5-0.25; 1-0.5; 2-1; 3-2; 5-3; 7-5; 10-7; >10 mm) are weighted.

Content of thin aleurolite and pelite fractions (<0.05 mm) in suspended matter from the cylinder is estimated on the base of Stocks low. The suspended matter after mixing is pipetting in determined intervals of time, aliquots are evaporized and dry residues are weighted. It gives the following pelite fractions: 0.01-0.005; 0.005-0.001 and <0.001 mm . Thin alevrolite fraction (0.05-0.01 mm) setteled on the bottom of the cylinder is washed out by water till no presence turbidity in washing water, dryed and weighted too. Results are given in table 2. Analyses by V.Kazakova and A.Rudakova.

Literature:

- V. P. Petelin. 1967. Graine size analysis of bottom sediments. Nauka Pbl. Moscow. 128 pg.

- T. N. Alekseeva, V. N. Svalnov. 2006. Grain size parameters of marine sediments. Oceanologia (Rus). V. 46.  №3. P. 461-470.

Table 2. Grain Size of the Sediments of the Caspian Sea (granulometric fractions, %)

|  | Station | NOV 8 RU-1 | NOV 8 RU-2 | NOV 8 RU-3 | NOV8 RU-4 | NOV10 RU-5 | NOV10 RU-6 |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | H2O content, % | 11.47 | 21.00 | 13.37 | 16.77 | 10.39 | 14.04 |
|  | Dry specimen, g | 69.45 | 37.93 | 43.64 | 32.83 | 32.43 | 35.88 |
| Granulometric fraction, mm | >10 | - | 17.29 | 7.26 |  | - |  |
|  | 10-7 | - | 7.29 | 6.36 |  | - |  |
|  | 7-5 | - | 7.67 | 4.19 |  | - |  |
|  | 5-3 | - | 9.71 | 4.26 |  | - |  |
|  | 3-2 | - | 7.67 | 8.53 |  | - |  |
|  | 2-1 | - | 14.57 | 16.68 |  | - |  |
|  | 1-0,5 | - | 5.14 | 0.67 |  | - |  |
|  | 0,5-0,25 | - | 3.38 | 33.06 | 0.08 | - | 0.21 |
|  | 0,25 – 0,1 | 0.09 | 2.57 | 10.02 | 0.16 | 7.41 | 1.07 |
|  | 0,1-0,05 | 0.09 | 1.00 | 1.20 | 0.30 | 37.64 | 1.21 |
|  | 0.05-0.01 | 0.35 | 0.76 | 0.67 | 0.06 | 6.35 | 0.36 |
|  | 0.01-0.005 | 8.89 | 3.81 | 7.10 | 6.25 | 9.53 | 8.58 |
|  | 0.005-0.001 | 18.48 | 4.86 |  | 27.34 | 14.45 | 20.11 |
|  | <0.001 | 72.10 | 14.28 |  | 65.81 | 24.62 | 68.46 |

|  | Station | NOV11 RU-7 | NOV 11 RU-8 | NOV 11 RU-9 | NOV 11 RU-10 | NOV11 RU-11 | NOV11 RU-12 |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | H2O content, % | 743 | 7.38 | 10.31 | 10.53 | 16.66 | 19.68 |
|  | Dry specimen, g | 56.80 | 53.37 | 45.88 | 58.62 | 20.96 | 21.66 |
| Granulometric fraction, mm | >10 | - |  |  |  |  | 6.25 |
|  | 10-7 | - |  |  |  |  | 0.30 |
|  | 7-5 | - |  |  |  | 2.34 |  |
|  | 5-3 | - |  |  |  | 1.26 | 0.66 |
|  | 3-2 | - |  |  | 0.38 | 0.66 | 0.30 |
|  | 2-1 | - |  |  | 1.04 | 1.56 | 0.15 |
|  | 1-0,5 | - |  | 0.29 | 0.47 | 0.78 | 0.05 |
|  | 0,5-0,25 | - |  | 0.39 | 0.47 | 1.50 | 0.20 |
|  | 0,25 – 0,1 | 0.54 | 0.55 | 0.19 | 1.14 | 69.21 | 61.18 |
|  | 0,1-0,05 | 0.40 | 0.41 | 0.62 | 1.90 | 8.16 | 17.48 |
|  | 0.05-0.01 | 4.17 | 3.66 | 0.39 | 0.57 | 0.42 | 0.25 |
|  | 0.01-0.005 | 8.07 | 8.13 | 11.41 | 9.66 |  |  |
|  | <0.01 |  |  |  |  | 14.15 | 13.18 |
|  | 0.005-0.001 | 18.05 | 19.82 | 24.62 | 19.53 |  |  |
|  | <0.001 | 68.72 | 67.43 | 60.09 | 64.84 |  |  |

|  | Station | NOV 12 KZ-1 | NOV 12 KZ-2 | NOV 13 KZ-3 | NOV13 KZ-4 | NOV 13 KZ-5 (basic) | NOV 13 KZ-5 (control) |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | H2O content, % | 21.81 | 22.79 | 19.56 | 35.07 | 36.28 | 37.50 |
|  | Dry specimen, g | 21.30 | 38.86 | 34.88 | 23.71 | 25.84 | 25.91 |
| Granulometric fraction, mm | >10 |  | 0.57 | 0.92 | 1.60 | 1.27 | 1.33 |
|  | 10-7 | 0.58 | 4.96 | 2.25 | 1.17 | 2.15 | 2.16 |
|  | 7-5 | 3.14 | 7.72 | 1.79 | 1.91 | 3.72 | 3.79 |
|  | 5-3 | 2.40 | 6.54 | 4.75 | 9.52 | 11.11 | 10.64 |
|  | 3-2 | 2.09 | 3.73 | 5.16 | 13.80 | 14.03 | 13.63 |
|  | 2-1 | 2.44 | 9.08 | 16.36 | 31.42 | 32.00 | 32.08 |
|  | 1-0,5 | 0.81 | 4.26 | 6.75 | 16.77 | 15.24 | 15.01 |
|  | 0,5-0,25 | 1.54 | 7.77 | 8.95 | 15.76 | 14.86 | 14.51 |
|  | 0,25 – 0,1 | 66.37 | 16.67 | 10.43 | 3.16 | 2.32 | 2.40 |
|  | 0,1-0,05 | 17.94 | 7.59 | 19.63 | 0.17 | 0.25 | 0.27 |
|  | 0.05-0.01 | 0.23 | 2.68 | 3.83 | 0.09 | 0.08 | 0.11 |
|  | <0.01 | 2.46 |  | 19.18 | 4.63 | 2.97 | 4.07 |
|  | 0.01-0.005 |  | 3.29 |  |  |  |  |
|  | 0.005-0.001 |  | 9.00 |  |  |  |  |
|  | <0.001 |  | 16.14 |  |  |  |  |

|  | Station | NOV 13 KZ-6 | NOV13 KZ-7 | NOV13 KZ-8 | NOV15 RU-13 | 7 | 10 |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | H2O content, % | 25.08 | 23.29 | 24.58 | 10.62 | 21.73 | 21.04 |
|  | Dry specimen, g | 20.96 | 29.16 | 24.73 | 56.43 | 26.14 | 28.61 |
| Granulometric fraction, mm | >10 |  |  |  |  |  |  |
|  | 10-7 | 0.64 | 1.81 | 0.65 |  |  |  |
|  | 7-5 | 1.20 | 2.62 |  |  |  |  |
|  | 5-3 | 4.78 | 14.73 |  |  |  |  |
|  | 3-2 | 10.05 | 19.84 | 5.95 |  | 0.27 | 0.21 |
|  | 2-1 | 29.78 | 33.88 | 13.75 |  | 0.23 | 0.45 |
|  | 1-0,5 | 12.80 | 10.87 | 4.19 | 1.22 | 0.15 | 0.31 |
|  | 0,5-0,25 | 24.24 | 7.65 | 8.95 | 1.97 | 0.31 | 0.49 |
|  | 0,25 – 0,1 | 10.93 | 1.72 | 18.51 | 2.18 | 15.38 | 12.55 |
|  | 0,1-0,05 | 0.96 | 0.07 | 28.56 | 17.70 | 45.64 | 42.65 |
|  | 0.05-0.01 | 0.96 | 0.26 | 0.41 | 0.38 | 14.19 | 17.72 |
|  | <0.01 | 3.66 | 6.54 | 19.03 | 12.67 | 23.93 | 25.62 |
|  | 0.01-0.005 |  |  |  |  |  |  |
|  | 0.005-0.001 |  |  |  | 21.59 |  |  |
|  | <0.001 |  |  |  | 42.29 |  |  |

|  | Station | 11 | 14 | Logan P | 18 | 20 |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | H2O content, % | 22.85 | 24.11 | 23.91 | 42.74 | 19.33 |  |
|  | Dry specimen, g | 24.93 | 25.48 | 21.08 | 15.44 | 25.09 |  |
| Granulometric fraction, mm | >10 |  |  | 5.69 |  |  |  |
|  | 10-7 |  |  | 0.57 |  |  |  |
|  | 7-5 |  |  | 0.90 |  |  |  |
|  | 5-3 |  |  | 1.94 |  |  |  |
|  | 3-2 | 0.68 | 0.12 | 2.13 | 0.52 | 0.57 |  |
|  | 2-1 | 0.24 | 0.23 | 2.70 | 0.32 | 0.31 |  |
|  | 1-0,5 | 0.20 | 0.35 | 1.57 | 0.13 | 0.10 |  |
|  | 0,5-0,25 | 0.36 | 0.55 | 2.42 | 0.32 | 0.21 |  |
|  | 0,25 – 0,1 | 3.21 | 1.73 | 48.91 | 30.51 | 15.56 |  |
|  | 0,1-0,05 | 21.18 | 33.12 | 14.52 | 45.01 | 32.95 |  |
|  | 0.05-0.01 | 21.70 | 27.98 | 4.17 | 6.93 | 5.93 |  |
|  | <0.01 |  | 35.92 | 14.48 | 16.26 |  |  |
|  | 0.01-0.005 | 10.83 |  |  |  | 15.37 |  |
|  | 0.005-0.001 | 15.60 |  |  |  | 11.28 |  |
|  | <0.001 | 26.00 |  |  |  | 17.72 |  |

Note: KZ-5 – repeating analyses

Organic Carbon and Carbonate of the Sediment

otal Organic Carbon (Corg, % dry) and carbonate (CO2, % dry) of sediments were determined by AN-7529 analyzer (Russia) with guaranty of Limit of Detection not worse than 100 mg/Kg (0.01%) TOC and reproducibility of 0.05% for Corg 1.5-4.0% and 0.005% for Corg less 1.5%. Russian marine sediment standards were used for testing and calibration (CDO-2).

Total Organic carbon (Corg) and CO2 from carbonate totally were determined by burning of dry sediment specimen (0.25g) in oxygen flow in tube furnace at 800 C. In the analyzer AN-7529 the method of automatic titration with fixation of pH was used. Determination of Corg was performed by the same method from separate specimen after previous treatment of the sediment by hydrochloric acid (1:1) for the carbonate removal. Carbonate content was calculated as a difference between these two determinations. Results for Corg and CO2 in sediments are given in Table 3. Analyses by N. Tolmachova.

Table 3. Carbonate (CO2, %) and Total Organic Carbon (TOC, %) in sediments of the Caspian Sea.

(TOC Limit of Detection: 100 mg /kg dry = 0.01%)

| Element | Unit | MDL | RU1 | RU2 | RU3 | RU4 | RU5 | RU6 | RU7 | RU8 | RU9 | RU10 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| CO2 | % | 0.01 | 13.91 | 35.06 | 33.74 | 2.34 | 7.06 | 6.81 | 10.58 | 8.82 | 7.35 | 9.26 |
| TOC | % | 0.1 | 2.45 | 1.22 | 0.98 | 0.94 | 0.65 | 0.89 | 2.10 | 1.94 | 0.96 | 2.15 |

| Element | RU11 | RU12 | RU13 | KZ1 | KZ2 | KZ3 | KZ4 | KZ5 | KZ6 | KZ7 | KZ8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| CO2 | 9.66 | 0.80 | 7.21 | 6.95 | 35.28 | 25.43 | 44.54 | 43.04 | 42.60 | 42.52 | 25.72 |
| TOC | 0.41 | 0.13 | 2.20 | 0.25 | 1.44 | 2.10 | 0.12 | 0.69 | 0.73 | 0.66 | 0.60 |

| Element | 7 | 10 | 11 | 14 | 18 | 20 | Lagan | CDO-2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  |  | passport |
| CO2 | 0.73 | 1.13 | 2.38 | 1.83 | 1.72 | 1.61 | 7.94 | 2.39 | 2.38 |
| TOC | 0.18 | 0.19 | 0.50 | 0.48 | 0.48 | 0.52 | 0.38 | 0.29 | 0.29 |

Part III. Trace metals.

Sample preparation and acid dissolution for TM

Samples of Caspian sediments stored in polyethylene parcels in the freezing camera during 8 months and before the analyses were unfrozen and divided in parts for different investigations. Average specimen for the analyses of trace metals, carbonate and organic carbon of sediments was sampled from 8 fragments of sediment sample, that were brought together, homogenized, dried at air (105º) and pulverized in the agate mortal to 200 mesh. So prepared samples were quartered and stored in desiceator above CaCl2. Specimens of determined weights were used for various determinations.

Samples for TM analyses (0.5g) were dissolved in mixture of hydrofluoric acid and chloric acid, heated, then almost dry residue was dissolved in 10 ml of nitric acid. (1:8),  Q-water was added to 50 ml and solutions were used for AAS analyses. Samples for Hg determination were treated by the mixture of hydrofluoric and nitric acid . Preparations by S.Pachomova.

Methods

Al, Fe, Cu, Zn, Ni, Co, Cr, Pb, Mn

As, Aq, Se, Sb, Cd, Hg

Ba, Ca, Li, Sn

To measure the content of heavy metals, Al and As the atomic absorption spectrometry was used. Concentrations of Al, Fe, Cu, Zn, Ni, Co, Cr, Pb, and Mn were determined with “QUANT-2A” (flame version) AAS spectrometer, while the content of As, Ag, Se, Sb, Cd and Hg and “QUANT-Z.ETA” equipments (non flame version using a Zeeman correction), the Hg content was detected by cold vapour with hydride generation.

The quality of the method used was checked and confirmed  with  Quasimeme  QTM072MS and QTM073MS standard reference material (the Netherlands). The mean recoveries were from 70 % (Hg) to 98 %. Reproducibility of parallel measurements of Fe, Mn, Zn, Cu, Ni, Co, Cr, Pb, As  was from 1 to 5 %, Сd – 8%,  and Hg – 14%. The results of reference samples determinations were laying in the limits between 85% and 115% for all the elements.

QC elements: Method blanks was performed with  frequency  one per extraction batch to 10.

Four samples (order number 2-3, 5-6, 8-9, 18-19 were analyzwd repeatedly)

Results are given in Table 1.

(Analysеs by L. Diomona and V. Gordeev. Li, Ca, Sn, Ba by А.Syroezhkin)

Results

Table 4. Trace elements in the sediments of the Caspian Sea

| Order namber | Sediment sample | Fe % | Al % | Cu µg/g | Zn µg/g | Ni µg/g | Co µg/g | Cr µg/g | Pb µg/g | Mn µg/g | As µg/g | Ag µg/g | Se µg/g | Sb µg/g | Cd µg/g | Hg µg/g |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Control Sample |  |  |
|  | Limit of detection, µg/g | 0.2 | 0.5 | 0.1 | 0.05 | 0.2 | 0.1 | 0.2 | 0.2 | 0.1 | 0.07 | 0.01 | 0.05 | 0.1 | 0.03 | 0.005 |
|  | QTM 072MS |  |
|  | Passport data | 2.45 | 4.36 | 17.84 | 133.18 | 26.24 |  | 75.33 | 54.72 | 412.57 | 16.98 |  |  |  | 0.629 | 0.326 |
|  | This work | 2.39 | 4.41 | 16.0 | 132 | 25.9 |  | 70.5 | 55.4 | 410 | 15.54 |  |  |  | 0.65 | 0.543 |
|  |  | 2.60 | 4.42 | 18.7 | 133 | 28.2 |  | 74.8 | 54.1 | 407 | 12.75 |  |  |  | 0.87 | 0.500 |
|  |  | 2.50 | 4.34 | 18.7 | 130 | 26.6 |  | 73.5 | 56.3 | 411 | 13.73 |  |  |  | 0.89 | 0.438 |
|  | QTM 073MS |  |
|  | Passport data | 4.68 | 6.55 | 184.76 | 632.66 | 51.8 |  | 313.37 | 225.83 | 702.6 | 17.42 |  |  |  | 1.958 | 0.668 |
|  | This work | 4.65 | 6.38 | 175 | 624 | 47.2 |  | 293 | 220.0 | 676 | 19.58 |  |  |  | 1.68 | 0.807 |
|  |  | 4.40 | 6.48 | 174 | 635 | 50.8 |  | 310 | 224.5 | 702 | 17.90 |  |  |  | 1.91 | 0.765 |
|  |  | 4.52 | 6.62 | 164 | 620 | 48.6 |  | 302 | 226.3 | 685 | 20.35 |  |  |  | 1.53 | 0.732 |
| 1 | RU 1 | 3.82 | 6.13 | 30.0 | 75 | 45.8 | 14.3 | 74.0 | 18.2 | 790 | 15.17 | 0.090 | 0.05 | 1.76 | 0.39 | 0.039 |
| 2 | RU 2 | 1.42 | 2.12 | 10.1 | 27 | 15.6 | 5.3 | 37.8 | 6.6 | 335 | 8.80 | 0.072 | 0.85 | 1.85 | 0.21 | 0.034 |
| 3 | RU2 | 1.35 | 2.01 | 9.6 | 26 | 14.5 | 5.2 | 37.3 | 6.3 | 333 | 13.91 | 0.037 | 0.76 | 1.40 | 0.11 | 0.036 |
| 4 | RU 3 | 1.45 | 1.93 | 7.7 | 25 | 12.5 | 5.0 | 32.3 | 7.8 | 365 | 9.56 | 0.063 | 0.87 | 1.63 | 0.24 | 0.038 |
| 5 | RU 4 | 5.16 | 10.20 | 29.2 | 104 | 42.2 | 19.0 | 77.0 | 21.8 | 874 | 12.49 | 0.035 | 0.08 | 0.49 | 0.11 | 0.056 |
| 6 | RU 4 | 5.03 | 9.94 | 29.0 | 103 | 41.8 | 18.5 | 79.7 | 21.6 | 858 | 10.72 | 0.034 | 0.05 | 0.52 | 0.08 | 0.044 |
| 7 | RU 5 | 3.48 | 6.62 | 20.2 | 69 | 31.6 | 14.0 | 48.5 | 13.6 | 563 | 8.35 | 0.051 | 0.06 | 0.74 | 0.35 | 0.035 |
| 8 | RU 6 | 4.24 | 8.07 | 25.8 | 87 | 40.8 | 16.2 | 72.7 | 16.6 | 654 | 12.21 | 0.042 | 0.14 | 0.94 | 0.51 | 0.043 |
| 9 | RU 6 | 4.18 | 7.93 | 25.6 | 86 | 42.3 | 16.3 | 74.3 | 16.8 | 651 | 15.13 | 0.037 | 0.13 | 0.99 | 0.48 | 0.045 |
| 10 | RU 7 | 4.39 | 7.21 | 31.9 | 93 | 44.9 | 16.1 | 76.0 | 21.3 | 890 | 13.01 | 0.037 | 0.11 | 0.87 | 0.59 | 0.043 |
| 11 | RU 8 | 4.01 | 7.21 | 28.3 | 89 | 40.4 | 15.0 | 71.2 | 21.8 | 855 | 13.87 | 0.016 | 0.30 | 0.60 | 0.87 | 0.042 |
| 12 | RU 9 | 3.54 | 6.96 | 21.9 | 82 | 33.0 | 13.6 | 66.6 | 19.3 | 700 | 8.34 | 0.022 | 0.18 | 0.61 | 0.79 | 0.038 |
| 13 | RU 9 | 3.47 | 6.82 | 21.8 | 82 | 34.4 | 13.5 | 63.3 | 19.2 | 700 | 7.42 | 0.018 | 0.12 | 0.70 | 0.83 | 0.030 |
| 14 | RU 10 | 3.52 | 5.87 | 24.5 | 64 | 39.1 | 13.5 | 68.0 | 16.0 | 720 | 21.83 | 0.024 | 0.05 | 0.79 | 0.43 | 0.073 |
| 15 | RU 11 | 0.71 | 1.92 | 4.1 | 9.7 | 8.1 | 3.6 | 43.5 | 5.6 | 270 | 4.06 | 0.033 | 0.06 | 0.63 | 0.03 | 0.043 |
| 16 | RU 12 | 1.00 | 2.40 | 3.7 | 11.0 | 8.5 | 3.7 | 60.0 | 6.2 | 310 | 1.42 | 0.013 | 0.05 | 0.37 | 0.05 | 0.037 |
| 17 | KZ 1 | 0.53 | 1.77 | 3.0 | 6.6 | 6.0 | 2.4 | 36.5 | 5.1 | 175 | 4.21 | 0.014 | 0.07 | 0.64 | 0.01 | 0.029 |
| 18 | KZ 2 | 0.67 | 1.07 | 8.0 | 14.6 | 11.6 | 3.3 | 30.3 | 5.7 | 135 | 16.66 | 0.022 | 0.87 | 0.97 | 0.08 | 0.030 |
| 19 | KZ 2 | 0.64 | 1.01 | 7.6 | 14.2 | 11.3 | 3.2 | 29.0 | 5.6 | 134 | 11.14 | 0.028 | 0.84 | 1.37 | 0.05 | 0.034 |
| 20 | KZ 3 | 0.65 | 1.50 | 6.5 | 15.4 | 10.5 | 4.0 | 37.4 | 4.5 | 150 | 14.29 | 0.031 | 0.72 | 1.23 | 0.07 | 0.027 |
| 21 | KZ 4 | 0.35 | 0.015 | 1.8 | 4.4 | 2.6 | 1.6 | 15.9 | 1.7 | 31.2 | 9.55 | 0.016 | 1.32 | 1.03 | <0.01 | 0.024 |
| 22 | KZ 5 | 0.58 | 0.016 | 2.0 | 2.6 | 3.1 | 1.8 | 14.4 | 2.9 | 35.0 | 17.85 | 0.010 | 1.31 | 0.32 | 0.05 | 0.024 |
| 23 | KZ 6 | 0.66 | 0.010 | 1.7 | 2.8 | 2.6 | 1.6 | 15.6 | 3.1 | 33.5 | 13.62 | 0.016 | 0.72 | 1.25 | 0.13 | 0.025 |
| 24 | KZ 7 | 0.29 | 0.12 | 2.2 | 8.5 | 3.5 | 1.8 | 19.0 | 4.0 | 45.5 | 6.19 | 0.023 | 1.00 | 1.66 | 0.14 | 0.029 |
| 25 | KZ 8 | 0.45 | 1.32 | 3.2 | 8.4 | 6.2 | 3.1 | 33.8 | 4.4 | 120 | 2.89 | 0.019 | 0.51 | 1.76 | 0.01 | 0.033 |
| 26 | KZ 13 | 1.86 | 4.08 | 13.3 | 32 | 25.5 | 8.8 | 52.7 | 8.2 | 450 | 31.52 | 0.024 | 0.06 | 0.69 | 0.06 | 0.037 |
| Additional 7 Samples |
| 1 | 7 | 2.09 | 3.48 | 14.3 | 30 | 29.8 | 9.1 | 55.5 | 5.1 | 340 | 3.61 | 0.015 | 1.09 | 8.86 | 0.33 | 0.015 |
| 2 | 10 | 2.16 | 4.01 | 14.3 | 33 | 31.5 | 9.2 | 52.0 | 6.5 | 408 | 4.10 | 0.018 | 0.72 | 5.87 | 0.28 | 0.024 |
| 3 | 11 | 2.28 | 3.29 | 18.4 | 37 | 36.0 | 10.5 | 58.8 | 6.7 | 540 | 4.91 | 0.019 | 0.91 | 6.11 | 0.62 | 0.021 |
| 4 | 14 | 2.47 | 4.47 | 17.8 | 39 | 35.4 | 10.0 | 55.4 | 6.3 | 440 | 3.43 | 0.024 | 0.74 | 3.70 | 0.35 | 0.024 |
| 5 | (14) | 0.50 | 1.44 | 4.8 | 10 | 8.3 | 2.7 | 16.8 | 3.5 | 158 | 3.22 | 0.017 | 0.37 | 4.34 | 0.10 | 0.012 |
| 6 | 18 | 1.79 | 3.38 | 15.0 | 36 | 26.1 | 7.3 | 47.0 | 7.5 | 290 | 3.18 | 0.018 | 0.38 | 6.11 | 0.13 | 0.012 |
| 7 | 20 | 2.25 | 3.92 | 17.3 | 36 | 33.1 | 9.4 | 55.3 | 7.0 | 475 | 3.64 | 0.020 | 0.90 | 3.71 | 0.21 | 0.012 |

| Sample | Li, mkg/g | Ca, mg/g | Sn, mkg/g | Ba, mkg/g |
| --- | --- | --- | --- | --- |
| RU1 | 27.8 | 63.2 | 7.0 | 223 |
| RU2 | 13.5 | 48.2 | 5.2 | 88.4 |
| RU2* | 12.4 | 40.6 | 5.6 | 93.1 |
| RU3 | 13.0 | 43.7 | 2.1 | 75.7 |
| RU4 | 62.4 | 59.6 | 3.5 | 287 |
| RU4* | 25.0 | 68.5 | 3.9 | 209.7 |
| RU5 | 59.6 | 51.8 | 4.8 | 205 |
| RU6 | 49.3 | 64.0 | 2.0 | 252 |
| RU6* | 28.2 | 59.8 | 2.8 | 159.8 |
| RU7 | 42.8 | 61.8 | 2.8 | 211 |
| RU8 | 43.1 | 60.6 | 7.7 | 212 |
| RU9 | 27.5 | 49.1 | 1.2 | 239.8 |
| RU9* | 42.7 | 60.4 | 1.5 | 174.8 |
| RU10 | 35.6 | 53.7 | 3.4 | 182 |
| RU11 | 2.5 | 44.1 | 0.2 | 65.9 |
| RU12 | 12.1 | 44.7 | 0.3 | 71.6 |
| KZ1 | 10.4 | 41.1 | <0,1 | 49.9 |
| KZ2 | 6.2 | 44.2 | 1.1 | 56.6 |
| KZ2* | 5.6 | 44.8 | 1.0 | 55.4 |
| KZ3 | 12.1 | 44.8 | 1.0 | 73.3 |
| KZ4 | 1.2 | 40.3 | 0.6 | 46.7 |
| KZ5 | 1.6 | 50.0 | 1.8 | 30.6 |
| KZ6 | 1.2 | 40.2 | 6.0 | 31.2 |
| KZ7 | 13.2 | 47.1 | 3.0 | 59.9 |
| KZ8 | 0.5 | 47.7 | 0.4 | 71.6 |
| KZ13 | 26.3 | 53.7 | 0.3 | 93.2 |
| 7 | 51.4 | 10.7 | 1.0 | 464 |
| 10 | 96.5 | 12.9 | 1.6 | 538 |
| 11 | 30.2 | 10.4 | 2.0 | 431 |
| 14 | 123.0 | 14.1 | 1.7 | 591 |
| 14* | 37.1 | 5.6 | 1.7 | 200 |
| 18 | 51.8 | 25.2 | 1.7 | 232 |
| 20 | 58.7 | 25.5 | 1.9 | 269 |

Part IV.   Oil , Oil products and Extracted Organic Matter (EOM) in the sediments of the Caspian Sea.

Extraction of alkane - naphthene hydrocarbons (HC).

Extraction of HC from sediments was carried out by the method of hexane or methylene chloride (50:50) extraction using the «Branson Ultrasonic B.V.» ultrasonic bath model «Branson - 1210». The sample was dried at a temperature of 50 - 60°C and weighed with an analytical balance, and then was placed in the bath for extraction at 25°C for 20 minutes. Then the extract was filtered through GF/F fiberglass filters, and the solvent was evaporated to dryness in the «Yamato RE-52» vacuum rotary evaporator at 35°C. Dry HC extract was dissolved in a small amount of hexane and was passed through a column with activated metallic copper (chips) to remove dissolved sulphide. Then the extract was evaporated to dryness in nitrogen flow and weighed with an analytical balance accurate to 0.01 mg. The mass of the dry extract (g) expresses the EOM value. The extract was kept in a refrigerator in a desiccator above CaCl2 until chromatographic analysis was performed.

HC gas chromatographic analysis.

HC patterns were analyzed with the use of the «Yanako G-180» GC (Japan) equipped with a split/splitless injector, an FID-detector and the SE-30 fused silica capillary column (35 m ( 0.25 mm; 0.2 (m film thickness) was used. Helium was used as the carrier gas at ca. 1.5 ml/min. Thermostatic oven temperature was programmed to change from initial t =100°C to 320°C at the rate of 4°C/min; detector and evaporator temperature was 320°C. HC identification and concentration computations were performed using the «Chromatopac C-R3A» data processing system with the FDD-1A disk and display. Quantitative calculations were carried out with the use of the internal standard method (squalane is a standard – 3mg/ml). Limit of detection < 1mg/Kg dry. Results are given in Table 2. Analyses by V.Peresypkin

Literature:

- Peresypkin V.I., Lein A.Y., Bogdanov Yu. A., Bortnikov N.S. On the nature of lipids in hydrothermal formations at the Broken Spur and vent field of the Mid-Atlantic Ridge // Explor. Mining Geol. 1999. V. 8. No. 3. P. 365-377.

- Simoneit B.R.T., Lein A.Yu., Peresypkin V.I., Osipov G.A. Composition and origin of hydrothermal petroleum and associated lipids in the sulfide deposits of the Rainbow Field (Mid-Atlantic Ridge at 36(N) // Geochim. Cosmochim. Acta. 2004. V. 68. №. 10. P. 2275-2294.

Table 5. Oil and oil products and exracted organic matter (EOM) in the sediments of the Cacpian sea (mg/g)

| Element | Unit | concentration |
| --- | --- | --- |
|  |  | NOV 8 RU-1 | NOV 8 RU-2 | NOV 8 RU-3 | NOV8 RU-4 | NOV10 RU-5 | NOV10 RU-6 |
| n-C12 | µg/g | 0.0411 | 0.0369 | 0.0002 | 0.0179 | 0.0034 | 0.0403 |
| n-C13 | µg/g | 0.0094 | 0.0123 | 0.0004 | 0.0125 | 0.0079 | 0.0343 |
| n-C14 | µg/g | 0.0366 | 0.065 | 0.0032 | 0.0344 | 0.0437 | 0.0871 |
| n-C15 | µg/g | 0.0287 | 0.0606 | 0.011 | 0.2567 | 0.0486 | 0.104 |
| n-C16 | µg/g | 0.046 | 0.1103 | 0.0533 | 0.0748 | 0.1507 | 0.1995 |
| n-C17 | µg/g | 0.0584 | 0.0783 | 0.0148 | 0.0174 | 0.0746 | 0.1383 |
| n-C18 | µg/g | 0.0218 | 0.0389 | 0.0196 | 0.0179 | 0.0496 | 0.0871 |
| n-C19 | µg/g | 0.0183 | 0.0296 | 0.0092 | 0.0314 | 0.0501 | 0.1179 |
| n-C20 | µg/g | 0.0158 | 0.0207 | 0.0156 | 0.0135 | 0.0437 | 0.0841 |
| n-C21 | µg/g | 0.0851 | 0.4773 | 0.0118 | 0.008 | 0.0628 | 0.098 |
| n-C22 | µg/g | 0.0183 | 0.0241 | 0.0106 | 0.0105 | 0.0417 | 0.0821 |
| n-C23 | µg/g | 0.0416 | 0.0473 | 0.0058 | 0.007 | 0.0501 | 0.0876 |
| n-C24 | µg/g | 0.0188 | 0.0266 | 0.0048 | 0.0085 | 0.0393 | 0.0716 |
| n-C25 | µg/g | 0.0406 | 0.068 | 0.0076 | 0.0169 | 0.056 | 0.0836 |
| n-C26 | µg/g | 0.0153 | 0.0414 | 0.0042 | 0.0075 | 0.0457 | 0.0751 |
| n-C27 | µg/g | 0.0748 | 0.1606 | 0.0106 | 0.006 | 0.0746 | 0.0871 |
| n-C28 | µg/g | 0.0312 | 0.0305 | 0.0054 | 0.0075 | 0.025 | 0.0413 |
| n-C29 | µg/g | 0.0941 | 0.1207 | 0.0154 | 0.0095 | 0.0781 | 0.1065 |
| n-C30 | µg/g | 0.0149 | 0.0182 | 0.0032 | 0.012 | 0.0191 | 0.0378 |
| n-C31 | µg/g | 0.0644 | 0.0877 | 0.0132 | 0.0035 | 0.0643 | 0.0905 |
| n-C32 | µg/g | 0.0292 | 0.0493 | 0.0068 | 0.0169 | 0.0275 | 0.0294 |
| n-C33 | µg/g | 0.0252 | 0.0355 | 0.0054 | 0.002 | 0.029 | 0.0463 |
| n-C34 | µg/g | 0.0059 | 0.0089 | 0.0016 | 0.009 | 0.0118 | 0.0209 |
| n-C35 | µg/g | 0.0094 | 0.0123 | 0.0054 | 0.003 | 0.0201 | 0.0274 |
| n-C36 | µg/g | 0.0025 | 0.003 | 0.0006 | 0.0055 | 0.0039 | 0.0055 |
| n-C37 | µg/g | 0.0045 | 0.0059 | 0.0008 | 0.001 | 0.0069 | 0.0129 |
| n-C38 | µg/g | 0.0025 | 0.0044 | 0.0008 | 0.001 | 0.0069 | 0.0119 |
| n-C39 | µg/g | 0.002 | 0.003 | 0.0004 | 0.0002 | 0.0025 | 0.0065 |
| n-C40 | µg/g | 0.0015 | 0.002 | 0.0002 | 0.001 | 0.002 | 0.003 |
| Pristane | µg/g | 0.026 | 0.041 | 0.019 | 0.015 | 0.095 | 0.267 |
| Phytane | µg/g | 0.016 | 0.034 | 0.012 | 0.101 | 0.063 | 0.15 |
| Squalane | µg/g | 0.022 | 0.042 | 0.047 | 0.054 | 0.109 | 0.102 |
| ∑n-C14-C34 | µg/g | 0.785 | 1.6 | 0.233 | 0.571 | 1.086 | 1.776 |
| Resolved Aliphatics | µg/g | 0.923 | 1.797 | 0.319 | 0.783 | 1.406 | 2.437 |
| Total Aliphatics | µg/g | 48.515 | 48.768 | 11.384 | 22.931 | 42.71 | 95.025 |
| EOM | µg/g | 163.366 | 133.005 | 27.961 | 54.835 | 58.91 | 109.453 |

| Еlement | Unit | concentration |
| --- | --- | --- |
|  |  | NOV 11 RU-7 | NOV 11 RU-8 | NOV 11 RU-9 | NOV11 RU-10 | NOV11 RU-11 | NOV12 RU-12 |
| n-C12 | µg/g | - | 0.0126 | 0.017 | 0.0114 | 0.0018 | 0.002 |
| n-C13 | µg/g | - | 0.0083 | 0.013 | 0.007 | 0.0002 | 0.001 |
| n-C14 | µg/g | - | 0.0451 | 0.0559 | 0.0382 | 0.0018 | 0.0104 |
| n-C15 | µg/g | - | 0.065 | 0.0539 | 0.0636 | 0.0027 | 0.1217 |
| n-C16 | µg/g | 0.0029 | 0.1981 | 0.1618 | 0.1807 | 0.0123 | 0.051 |
| n-C17 | µg/g | 0.0141 | 0.1709 | 0.0669 | 0.1435 | 0.0092 | 0.0078 |
| n-C18 | µg/g | 0.0102 | 0.0495 | 0.0369 | 0.0427 | 0.007 | 0.006 |
| n-C19 | µg/g | 0.0068 | 0.0534 | 0.033 | 0.0353 | 0.0076 | 0.0028 |
| n-C20 | µg/g | 0.0063 | 0.0345 | 0.0315 | 0.0218 | 0.0043 | 0.0032 |
| n-C21 | µg/g | 0.0126 | 0.1053 | 0.0414 | 0.074 | 0.0059 | 0.0102 |
| n-C22 | µg/g | 0.0053 | 0.033 | 0.029 | 0.0194 | 0.0114 | 0.0024 |
| n-C23 | µg/g | 0.0097 | 0.0529 | 0.0344 | 0.0437 | 0.0051 | 0.0018 |
| n-C24 | µg/g | 0.0053 | 0.032 | 0.031 | 0.0204 | 0.0057 | 0.0026 |
| n-C25 | µg/g | 0.0078 | 0.0718 | 0.0474 | 0.066 | 0.0037 | 0.0076 |
| n-C26 | µg/g | 0.0068 | 0.0461 | 0.0424 | 0.0278 | 0.0086 | 0.0028 |
| n-C27 | µg/g | 0.0087 | 0.1364 | 0.0794 | 0.1336 | 0.0037 | 0.0024 |
| n-C28 | µg/g | 0.0068 | 0.0282 | 0.0245 | 0.0367 | 0.0127 | 0.0044 |
| n-C29 | µg/g | 0.0087 | 0.1218 | 0.1038 | 0.1048 | 0.0061 | 0.0042 |
| n-C30 | µg/g | 0.0015 | 0.0189 | 0.0195 | 0.0139 | 0.0143 | 0.0078 |
| n-C31 | µg/g | 0.0044 | 0.0883 | 0.0819 | 0.0655 | 0.0023 | 0.0026 |
| n-C32 | µg/g | 0.0078 | 0.0398 | 0.026 | 0.0357 | 0.0102 | 0.0014 |
| n-C33 | µg/g | 0.0029 | 0.0379 | 0.0379 | 0.0243 | 0.0057 | 0.0018 |
| n-C34 | µg/g | 0.001 | 0.0092 | 0.0095 | 0.0055 | 0.0037 | 0.0012 |
| n-C35 | µg/g | 0.0015 | 0.0199 | 0.02 | 0.0109 | 0.0012 | 0.0048 |
| n-C36 | µg/g | 0.0005 | 0.0029 | 0.0025 | 0.0015 | 0.0022 | 0.0008 |
| n-C37 | µg/g | 0.0005 | 0.0058 | 0.005 | 0.003 | 0.0004 | 0.0004 |
| n-C38 | µg/g | - | 0.0039 | 0.004 | 0.002 | 0.0006 | 0.0004 |
| n-C39 | µg/g | - | 0.0029 | 0.002 | 0.002 | 0.0004 | 0.001 |
| n-C40 | µg/g | - | 0.0024 | 0.0015 | 0.001 | 0.0001 | 0.0002 |
| Pristane | µg/g | 0.011 | 0.109 | 0.06 | 0.088 | 0.008 | 0.007 |
| Phytane | µg/g | 0.013 | 0.067 | 0.043 | 0.05 | 0.008 | 0.05 |
| Squalane | µg/g | 0.029 | 0.102 | 0.107 | 0.067 | 0.019 | 0.043 |
| ∑n-C14-C34 | µg/g | 0.13 | 1.438 | 1.048 | 1.197 | 0.144 | 0.256 |
| Resolved Aliphatics | µg/g | 0.184 | 1.774 | 1.324 | 1.441 | 0.186 | 0.365 |
| Total Aliphatics | µg/g | 4.951 | 53.398 | 32.951 | 56.107 | 5.286 | 6.773 |
| EOM | µg/g | 92.233 | 150.485 | 79.88 | 168.818 | 15.662 | 17.928 |

| Element | Unit | concentration |
| --- | --- | --- |
|  |  | NOV 12 KZ-1 | NOV 12 KZ-2 | NOV 13 KZ-3 | NOV 13 KZ-4 | NOV 13 KZ-5 | NOV 13 KZ-6 |
| n-C12 | µg/g | - | 0.0066 | 0.0002 | 0.0002 | 0.0002 | 0.0002 |
| n-C13 | µg/g | 0.0002 | 0.0037 | 0.0004 | 0.0004 | 0.0004 | 0.0004 |
| n-C14 | µg/g | 0.0022 | 0.0225 | 0.0058 | 0.0028 | 0.0084 | 0.0022 |
| n-C15 | µg/g | 0.0032 | 0.0225 | 0.0082 | 0.0084 | 0.0336 | 0.0091 |
| n-C16 | µg/g | 0.0294 | 0.09 | 0.0392 | 0.0487 | 0.0874 | 0.0523 |
| n-C17 | µg/g | 0.0038 | 0.0267 | 0.0247 | 0.023 | 0.0991 | 0.0314 |
| n-C18 | µg/g | 0.0052 | 0.0135 | 0.0111 | 0.0136 | 0.05 | 0.0195 |
| n-C19 | µg/g | 0.0028 | 0.0066 | 0.0046 | 0.0058 | 0.0259 | 0.0117 |
| n-C20 | µg/g | 0.0052 | 0.0081 | 0.0085 | 0.009 | 0.0146 | 0.0087 |
| n-C21 | µg/g | 0.0098 | 0.3105 | 0.0181 | 0.0152 | 0.0166 | 0.0097 |
| n-C22 | µg/g | 0.0042 | 0.0069 | 0.007 | 0.0056 | 0.0071 | 0.0056 |
| n-C23 | µg/g | 0.0032 | 0.012 | 0.0103 | 0.0062 | 0.0069 | 0.0046 |
| n-C24 | µg/g | 0.0016 | 0.0049 | 0.0044 | 0.0034 | 0.0035 | 0.0022 |
| n-C25 | µg/g | 0.0032 | 0.0186 | 0.0153 | 0.0072 | 0.008 | 0.0062 |
| n-C26 | µg/g | 0.0022 | 0.0118 | 0.0038 | 0.0074 | 0.0029 | 0.0028 |
| n-C27 | µg/g | 0.0058 | 0.0225 | 0.0249 | 0.0194 | 0.0215 | 0.0107 |
| n-C28 | µg/g | 0.0048 | 0.0096 | 0.0123 | 0.0092 | 0.0055 | 0.0066 |
| n-C29 | µg/g | 0.0076 | 0.0355 | 0.028 | 0.0251 | 0.027 | 0.0111 |
| n-C30 | µg/g | 0.0018 | 0.0056 | 0.0034 | 0.0048 | 0.0027 | 0.0024 |
| n-C31 | µg/g | 0.0064 | 0.0282 | 0.0201 | 0.0138 | 0.0153 | 0.0083 |
| n-C32 | µg/g | 0.0026 | 0.0115 | 0.0135 | 0.0072 | 0.0053 | 0.0048 |
| n-C33 | µg/g | 0.0024 | 0.0083 | 0.0087 | 0.0048 | 0.0124 | 0.0034 |
| n-C34 | µg/g | 0.0012 | 0.0022 | 0.0014 | 0.0018 | 0.0009 | 0.001 |
| n-C35 | µg/g | 0.0062 | 0.0069 | 0.0058 | 0.0054 | 0.0027 | 0.0048 |
| n-C36 | µg/g | 0.0006 | 0.0012 | 0.0004 | 0.0018 | 0.0004 | 0.0006 |
| n-C37 | µg/g | 0.0004 | 0.0012 | 0.0008 | 0.0006 | 0.0004 | 0.0004 |
| n-C38 | µg/g | 0.0002 | 0.0029 | 0.0004 | 0.0006 | 0.0002 | 0.0002 |
| n-C39 | µg/g | 0.0001 | 0.0007 | 0.0004 | 0.0004 | 0.0002 | 0.0004 |
| n-C40 | µg/g | 0.0002 | 0.0005 | 0.0002 | 0.0002 | - | - |
| Pristane | µg/g | 0.007 | 0.035 | 0.009 | 0.025 | 0.057 | 0.027 |
| Phytane | µg/g | 0.005 | 0.014 | 0.007 | 0.018 | 0.042 | 0.021 |
| Squalane | µg/g | 0.059 | 0.053 | 0.047 | 0.054 | 0.094 | 0.055 |
| ∑n-C14-C34 | µg/g | 0.109 | 0.678 | 0.273 | 0.242 | 0.454 | 0.214 |
| Resolved Aliphatics | µg/g | 0.188 | 0.804 | 0.345 | 0.348 | 0.652 | 0.324 |
| Total Aliphatics | µg/g | 4.599 | 15.441 | 10.537 | 8.184 | 21.681 | 11.531 |
| EOM | µg/g | 13.997 | 63.725 | 51.69 | 23.752 | 65.044 | 27.038 |

| Element | concentration |
| --- | --- |
|  | NOV 13 KZ-7 | NOV 13 KZ-8 | NOV 15 RU-13 | №7 | №10 | №14 |
| n-C12 | 0.0002 | 0.0002 | 0.0069 | 0.0012 | 0.0004 | 0.0097 |
| n-C13 | 0.0004 | 0.0004 | 0.0054 | 0.0014 | 0.0006 | 0.005 |
| n-C14 | 0.0042 | 0.0026 | 0.0431 | 0.0106 | 0.0028 | 0.0268 |
| n-C15 | 0.0184 | 0.0088 | 0.0376 | 0.0236 | 0.0226 | 0.0196 |
| n-C16 | 0.0734 | 0.0503 | 0.0762 | 0.0598 | 0.087 | 0.0633 |
| n-C17 | 0.0278 | 0.0226 | 0.2257 | 0.064 | 0.057 | 0.0411 |
| n-C18 | 0.0166 | 0.0158 | 0.0332 | 0.0308 | 0.0224 | 0.0185 |
| n-C19 | 0.0138 | 0.0102 | 0.0307 | 0.0118 | 0.0164 | 0.0147 |
| n-C20 | 0.0118 | 0.0098 | 0.0129 | 0.0076 | 0.0104 | 0.0083 |
| n-C21 | 0.0134 | 0.0112 | 0.0292 | 0.0034 | 0.0042 | 0.0036 |
| n-C22 | 0.0072 | 0.0064 | 0.0114 | 0.0046 | 0.0052 | 0.005 |
| n-C23 | 0.0048 | 0.0058 | 0.0292 | 0.0058 | 0.0084 | 0.0062 |
| n-C24 | 0.0032 | 0.0036 | 0.0079 | 0.0026 | 0.0068 | 0.004 |
| n-C25 | 0.0066 | 0.0068 | 0.0441 | 0.013 | 0.0172 | 0.0127 |
| n-C26 | 0.003 | 0.0026 | 0.0233 | 0.0038 | 0.0124 | 0.0036 |
| n-C27 | 0.0082 | 0.0146 | 0.0658 | 0.0348 | 0.0564 | 0.0389 |
| n-C28 | 0.008 | 0.0056 | 0.0158 | 0.0064 | 0.0176 | 0.0093 |
| n-C29 | 0.0112 | 0.0168 | 0.0634 | 0.027 | 0.1132 | 0.0423 |
| n-C30 | 0.0022 | 0.0026 | 0.0074 | 0.0028 | 0.0054 | 0.0032 |
| n-C31 | 0.0082 | 0.0154 | 0.0436 | 0.0166 | 0.046 | 0.0315 |
| n-C32 | 0.0048 | 0.0044 | 0.0371 | 0.0032 | 0.0048 | 0.0038 |
| n-C33 | 0.0028 | 0.0058 | 0.0144 | 0.0054 | 0.0146 | 0.0107 |
| n-C34 | 0.0012 | 0.0014 | 0.0025 | 0.001 | 0.0018 | 0.0018 |
| n-C35 | 0.0046 | 0.0058 | 0.005 | 0.002 | 0.0042 | 0.0026 |
| n-C36 | 0.0004 | 0.0006 | 0.0005 | 0.0002 | 0.0006 | 0.0002 |
| n-C37 | 0.0004 | 0.0006 | 0.0015 | 0.0004 | 0.0008 | 0.001 |
| n-C38 | 0.0002 | 0.0004 | 0.0005 | 0.0002 | 0.0004 | 0.0002 |
| n-C39 | 0.0002 | 0.0004 | - | - | 0.0004 | 0.0002 |
| n-C40 | 0.0002 | 0.0002 | - | - | 0.0002 | 0.0004 |
| Pristane | 0.043 | 0.015 | 0.042 | 0.033 | 0.055 | 0.031 |
| Phytane | 0.029 | 0.013 | 0.028 | 0.019 | 0.034 | 0.027 |
| Squalane | 0.059 | 0.058 | 0.026 | 0.01 | 0.021 | 0.007 |
| ∑n-C14-C34 | 0.251 | 0.223 | 0.854 | 0.339 | 0.532 | 0.369 |
| Resolved Aliphatics | 0.388 | 0.318 | 0.97 | 0.407 | 0.651 | 0.453 |
| Total Aliphatics | 11.998 | 6.793 | 16.139 | 7.78 | 14.994 | 32.143 |
| EOM | 30.794 | 24.775 | 27.723 | 18.6 | 33.986 | 89.286 |

| Element | concentration |
| --- | --- |
|  | №11 | №18 | №20 | Lagan-R |
| n-C12 | 0.0016 | 0.0014 | 0.0002 | 0.0002 |
| n-C13 | 0.0022 | 0.0016 | 0.0002 | 0.0002 |
| n-C14 | 0.0144 | 0.0115 | 0.0022 | 0.0042 |
| n-C15 | 0.0188 | 0.0381 | 0.0162 | 0.025 |
| n-C16 | 0.0266 | 0.103 | 0.0617 | 0.0572 |
| n-C17 | 0.0294 | 0.096 | 0.0619 | 0.0268 |
| n-C18 | 0.0162 | 0.0332 | 0.0221 | 0.0196 |
| n-C19 | 0.005 | 0.0233 | 0.0132 | 0.0082 |
| n-C20 | 0.0068 | 0.0134 | 0.0087 | 0.0098 |
| n-C21 | 0.0026 | 0.0057 | 0.0312 | 0.0032 |
| n-C22 | 0.0042 | 0.0065 | 0.0047 | 0.0052 |
| n-C23 | 0.0054 | 0.0077 | 0.0097 | 0.0108 |
| n-C24 | 0.0028 | 0.0042 | 0.0067 | 0.0024 |
| n-C25 | 0.0094 | 0.0146 | 0.0273 | 0.0222 |
| n-C26 | 0.003 | 0.0043 | 0.0097 | 0.0042 |
| n-C27 | 0.0292 | 0.0391 | 0.0903 | 0.0288 |
| n-C28 | 0.0098 | 0.0089 | 0.0162 | 0.007 |
| n-C29 | 0.0304 | 0.0488 | 0.0852 | 0.0276 |
| n-C30 | 0.0046 | 0.0045 | 0.0043 | 0.0038 |
| n-C31 | 0.0246 | 0.0407 | 0.046 | 0.0148 |
| n-C32 | 0.0068 | 0.0043 | 0.0049 | 0.0102 |
| n-C33 | 0.0084 | 0.016 | 0.0134 | 0.0046 |
| n-C34 | 0.0016 | 0.0024 | 0.0018 | 0.001 |
| n-C35 | 0.0018 | 0.0047 | 0.004 | 0.0028 |
| n-C36 | 0.0002 | 0.0004 | 0.0004 | 0.0004 |
| n-C37 | 0.0008 | 0.0014 | 0.0008 | 0.0006 |
| n-C38 | 0.0006 | 0.0008 | 0.0002 | 0.0004 |
| n-C39 | 0.0002 | 0.0002 | 0.0002 | 0.0004 |
| n-C40 | 0.0002 | 0.0006 | - | 0.0002 |
| Pristane | 0.011 | 0.054 | 0.036 | 0.018 |
| Phytane | 0.008 | 0.033 | 0.025 | 0.01 |
| Squalane | 0.005 | 0.014 | 0.016 | 0.022 |
| ∑n-C14-C34 | 0.26 | 0.526 | 0.538 | 0.296 |
| Resolved Aliphatics | 0.291 | 0.638 | 0.62 | 0.351 |
| Total Aliphatics | 23.177 | 25.494 | 23.518 | 10.394 |
| EOM | 63.936 | 29.644 | 55.336 | 33.98 |

# Part V. Petroleum and organic antropogenic compouns.

1. INTRODUCTION

In compliance with Requirements Specifications of the agreement No. 293/06-16 from 03.06.2006, 29 samples of marine bottom sediments collected on the Caspian shelf were delivered to the laboratory of the Typhoon’s Center for Environmental Chemistry. The samples were collected and transported by the Customer.

According to Requirements Specifications, the aim of this work is to quantify content of polychlorinated biphenyls, organochlorine pesticides, and polycyclic aromatic hydrocarbons in the samples.  The content of polychlorinated dibenzo-p-dioxins and dibenzofurans, and planar (non-ortho and mono-ortho substituted) polychlorinated biphenyls was additionally quantitatively determined in the part of the samples at Customer’s option.

TYPHOON’s Center for Environmental Chemistry has been accredited by Gosstandart of the Russian Federation to compliance with the requirements of the Analytical Laboratories Accreditation System and to technical competence according to the requirements of GOST ISO/IEC 17025.

Accreditation Certificate No. РОСС-Ru. 0001.512808 from 20.08.2004

2. BRIEF DESCRIPTION OF ANALYTICAL METHODS

2.1. Polychlorinated biphenyls

2.1.1 General

The method used for determination of polychlorinated biphenyls (PCBs) is based on extraction of analyzed compounds with dichloromethane in a Soxhlet apparatus. Extracts were cleaned-up using activated copper and column chromatography with florisil. Identification of substances was performed by chromatography-mass spectrometry method. Determination intervals range from 0.02 to 500 (g/kg. To control quality of analysis a system of surrogate isotope-labeled standards added at different stages is used.

2.1.2. Sample extraction

A pre-weighed part of a wet bottom sediment sample was mixed with the equal amount of dehydrated sodium sulfate in an Erlenmeyer flask. A surrogate standard (mixture of isotope-labeled PCB congeners) was introduced into the sample; then it was extracted in a Soxhlet apparatus for 16 hours. The extract was dried by sodium sulfate. 3 ml of hexane was added to the extract; then it was reduced using a rotary evaporator to 1-1.5 ml and cleaned from sulfur by activated copper. After that, the extract was transferred into a column with florisil (2.1% Н2О). The column was eluted with hexane. The fraction containing PCBs was concentrated to 100 (l and transferred to a microvial. To determine surrogate standard yield an internal standard – 4 ng of PCB#166 – was introduced just before instrumental analysis.

    - Instrumental analysis

The analysis was carried out with a Varian Saturn 2100 MS/MS chromatography-mass spectrometer.

Injector type                                                split/splitless

Column type                                               VF-5MS 30 m х 0.25 х 0.25 (m

Initial column temperature                         80 0С

Holdup time                                                1 min.

Heating speed                                             20 0С/min to 200  0С;10 С/min to 290  0С

Detector temperature                                 290  0С

Injector temperature                                   290  0С

Injected volume                                         1 (l

Helium flow                                               1.2 ml/min

Mass scanning area                                    180-520 AMU

The instrument was calibrated using the standard mixture of polychlorinated biphenyls, BP-MS from Wellington Laboratories. The instrument linearity was verified by calibration by 5 points in the concentration range from 1 to 200 ng/ml. After the analysis of the analytical batch, the calibration was verified by analysis of a medium concentration standard solution.

Results of analyses were processed with Varian 5.2 software.

2.1.4. Identification of individual PCB congeners

Identification was performed by characteristic mass-spectra and retention times of individual PCB congeners.

2.1.5. Calculation of results

The content of individual PCB congeners, Cn ((g/kg), was calculated on the basis of the signals obtained for each specific congener from the following formula:

Сn = (Sn) mr /(Sr) (RRF)n(REC)s M,

where: Sn is the peak area of a PCB congener;

Sr is the peak area of internal standard (recovery);

M is a sample weight, kg;

mr is the amount of injected internal standard, μg;

(RRF)n is a relative response factor for an individual PCB congener;

(REC)s is a recovery coefficient for a corresponding surrogate standard.

(RRF)n is determined by analysis of PCB calibration solutions as:

(RRF)n = (Sns ) mrs /(Srs ) mns,

where:  Sns is the peak area of a PCB congener in calibration solution;

Srs is the peak area of an internal standard (recovery) in calibration solution;

mns is the amount of a PCB congener in calibration solution, ng;

mrs is the amount of internal standard in calibration solution, ng.

The recovery coefficient for surrogate standard (REC)s is determined from the formula:

(REC)s = (Ssur) mr /(Srs)ms(RRFsr),

where:  Ssur is the area of surrogate standard in an analyzed sample;

Srs is the area of internal standard in an analyzed sample;

ms  is the amount of the surrogate standard introduced into the analyzed sample, ng;

mr is the amount of added internal standard (recovery), ng;

(RRF)sr is the relative response factor for surrogate standard:

RRFsr = (Ssurs) mrs /(Srs) msur

where Ssur and msur are the peak area and amount of surrogate standard in PCB calibration solution  respectively.

The PCB content was calculated using the recovery coefficients of appropriate surrogate isotope-labeled PCB congeners for each group depending on degree of chlorination.

    - Method detection limit

The detection limit determined statistically with the probability of 99% using a series of duplicate analyses of blank samples for individual PCB congeners is 0.02 – 0.1 μg/kg for soil and bottom sediments. The mentioned detection limits were verified in the analysis of analytical batches of check samples.

2.1.7.  Quality control

The analysis of samples was carried out in batches. Each batch included 11 field samples and a duplicate (one of the samples was analyzed twice), certified EC-5 bottom sediment material produced by National Water Research Institute of Canada, and a blank sample.

The EC4058 mixture produced by Cambridge Isotope Lab was used as surrogate standard. It contains 13С isotope-labeled #28, #52, #101, #138, #153, #180, #209 PCB congeners.

PCB #166 was used as internal standard.

### Allowable criteria of analysis quality:

### The content of individual PCB congeners in a blank sample is less than 1 ng.

The determined content of PCB congeners in the EC-5 bottom sediment material certified by NWRI of Canada complied with the Analysis Certificate for 90% of analyzed compounds.

The deviation of duplicate sample analysis results is no more than ( 25% of an average value plus a method detection limit value for 90% of analyzed compounds.

The values of surrogate standard recovery range between 40% and 120%.

##### Quality of instrumental data

Instrument sensitivity was determined once a day (or after adjustment of the instrument) by analysis of standard PCB calibration solution.

Acceptable quality criterion: signal-noise ratio is more than 3:1 for 0.01 ng of 13C-PCB #180 in injected volume.

Chromatographic resolution was verified by the analysis of calibration standards performed prior to and after the analysis of an analytical batch.

Acceptable value: complete separation of PCB#74 and PCB#70 peaks.

Mass-spectral resolution determined during automatic adjustment of the instrument for ions m/z=264 and 265 as R=l/2b, where l is a distance between peak centers, b is a peak half-width, was not less than 0.95.

Linearity of instrument calibration was determined by analysis of 5 standard PCB solutions with concentrations from 1 to 200 ng/ml.

Quality criterion: permissible standard deviation of calculated relative response factor RRF should be less than 20%.

Instrument stability was verified prior and after the analysis of a sample batch by the analysis of PCB calibration solution with medium concentration.

Quality criterion is the differences in the values of the relative response factor RRF calculated prior to and after sample batch analysis, should not be more than (15%.

Examination of instrument contamination with respect to the analyte content was performed after each analysis of calibration standard solution by injection of hexane.  It makes possible to assure that the signal of analytes in the sample is not due to a previous sample.

Acceptable criterion is the value of the error introduced due to instrument background; it should not be more than 1% of the mean value of determined concentrations.

2.2.  Organochlorine pesticides (OCPs)

2.2.1. General

The method used for determination of organochlorine pesticides (OCPs) is based on extraction of these compounds from a sample with the mixture of dichloromethane and acetone, clean-up of extracts from sulfur and co-extractive compounds using activated copper and a chromatographic column with florisil, and subsequent chromatography-mass spectrometric identification and quantitative determination of individual pesticides. Determination intervals range from 0.02 to 500 μg/kg. To control quality of performed analysis the system of the surrogate internal standards added to samples at different stages of analysis was used.

The list of the OCPs determined in this study is given below:

| - hexachlorobenzene; | - 4,4`-DDE; | - trans-nonachlor; |
| --- | --- | --- |
| - α-HCH; | -2,4`-DDE; | - cis-nonachlor; |
| - β-HCH; | - 4,4`-DDD; | - dieldrin |
| - γ-HCH; | -2,4`-DDD; | - trans-chlordane; |
| - δ-HCH; | - 4,4`-DDT; | - cis-chlordane; |
| - heptachlor; | -2,4`-DDT; | - aldrin; |
| - heptachlor epoxide; | - oxychlordane | - mirex; |

2.2.2.   Sample extraction

A pre-weighed part of a bottom sediment or soil sample was placed within an extraction beaker into a Soxhlet apparatus. The mixture of isotope-labeled surrogate standards was introduced into the sample; then it was extracted for 16 hours. The extract was rinsed with two portions of distilled water and dried by dehydrated sodium sulfate. 3 ml of hexane was added to the extract; then it was reduced using a rotary evaporator to 1-1.5 ml and cleaned from sulfur by activated copper.  After that, the extract was transferred into a column with florisil (2.1% Н2О). The column was eluted consecutively with hexane, hexane:dichloromethane = 85:15 mixture, and hexane:dichloromethane = 1:2 mixture. Then the first and second fractions containing non-polar and low-polar pesticides were combined. The purified extracts were concentrated to 100 μl and transferred into microvials. To determine surrogate standard yield an internal standard – 100 ng of 1-bromadamantane – was introduced just before instrumental analysis

2.2.3.   Instrumental analysis

The analysis was carried out with a Varian SATURN 2100 MS/MS chromatography-mass spectrometer.

Injector type                                                split/splitless

Column type                                               VF-5MS 30 m х 0.25 х 0.25 μm

Initial column temperature                         60 0С

Holdup time                                                1 min.

Heating speed                                             20 0С/min to 200  0С;10 С/min to 290  0С

Detector temperature                                 290  0С

Injector temperature                                   290  0С

Injected volume                                         1 μl

Helium flow                                               1.2 ml/min

Mass scanning area                                     60-350 AMU

The instrument was calibrated using standard solutions of organochlorine pesticides – SRM-1492 NIST. The instrument linearity was verified by calibration by 5 points in the concentration range from 100 to 5000 ng/ml. After the analysis of the analytical batch, the calibration was verified by analysis of medium concentration standard solution.

Results of analyses were processed with Chemstation software.

2.2.4. Identification of organochlorine pesticides

Identification was performed by characteristic mass-spectra and retention times of organochlorine pesticides.

2.4.5.  Calculation of results

The content of organochlorine pesticides, Cn (μg/kg), was calculated on the basis of the signals obtained for each specific compound from the equation:

Сn = (Sn) mr /(Sr) (RRF)n(REC)s M

where:   Sn is an OCP peak area,

Sr is the peak area of internal standard (recovery),

M is a sample weight, kg,

mr is the amount of injected internal standard, μg,

(RRF)n is a relative response factor for an individual OCP.

(REC)s is a recovery coefficient for surrogate standard.

(RRF)n is determined by analysis of OCP calibration solutions as:

(RRF)n = (Sns ) mrs /(Srs ) mns

where: Sns is the peak area of an individual OCP in the standard,

Srs is the peak area of internal standard (recovery) in the standard,

mns  is the amount of an individual OCP, μg,  in calibration solution,

mrs is the amount of internal standard in calibration solution, μg.

The recovery coefficient for surrogate standard (REC)s is determined from the formula:

(REC)s = (Ssur) mr /(Srs)ms(RRFsr)

where:   Ssur is the area of surrogate standard in an analyzed sample,

ms  is the amount of the surrogate standard introduced into an analyzed sample, μg.

(RRF)sr is a relative response factor for surrogate standard:

RRFsr = (Ssurs) mrs /(Sr) mns

where: Ssurs and mns are the peak area and amount of surrogate standard in OCP calibration solution respectively.

The organochlorine pesticide content was calculated using the recovery coefficients of surrogate standards.

2.2.6.  Method detection limit

The detection limit determined statistically with the probability of 99% using a series of duplicate analyses of blank samples for different OCPs is 0.02-0.5 μg/kg for soil and bottom sediments. The mentioned detection limit was verified in the analysis of the batch of prepared check samples.

2.2.7. Quality control

The analysis of samples was carried out in batches. Each batch included no more than 11 field samples and a duplicate (one of the samples was analyzed twice), a check sample prepared in CEC, and a blank sample (procedural blank).

The mixture containing isotope-labeled standards produced by CIL (USA) was used as surrogate standard.

13С12   p,p- DDE

13С12   p,p- DDT

13С6    Hexachlorobenzene

13С6    γ-HCH;

PCB #166 was used as internal standard.

Allowable criteria of analysis quality:

The content of OCPs in a blank sample is less than 0.005 μg.

The recovery of the analyzed OCPs from a CEC check sample ranged between 70% and 120% for 90% of the compounds introduced into the sample.

The deviation of duplicate sample analysis results is no more than (25% of an average value plus a method detection limit value for 90% of analyzed compounds.

The values of surrogate standard recovery ranged from 40% to 120%.

### Quality of instrumental data

Instrument sensitivity was determined once a day (or after adjustment of the instrument) by the analysis of standard OCP solution.

Acceptable quality criterion: signal:noise ratio is more than 3:1 for 0.005 ng of hexachlorobenzene in injected volume.

Chromatographic resolution was verified by the analysis of calibration standards performed prior to and after the analysis of an analytical batch. Acceptable quality: separation of 4,4’-DDD and 2,4’-DDT peaks by no less than 50% of peak height.

Mass-spectral resolution determined during automatic adjustment of the instrument for ions m/z=502 and 503 as R=l/2b, where l is a distance between peak centers, b is a peak half-width, was not less than 0.95.

Linearity of instrument calibration was determined by analysis of 5 standard OCP solutions with concentrations from 100 to 5000 ng/ml.

Quality criterion: permissible standard deviation of calculated relative response factor RRF should be less than 20%.

Instrument stability was verified prior and after the analysis of a sample batch by the analysis of OCP calibration solution with medium concentration.

Quality criterion is the differences in the values of the relative response factor RRF calculated prior to and after sample batch analysis; it should not be more than (15%.

Examination of instrument contamination with respect to the analyte content was performed after each analysis of calibration standard solution by injection of hexane.  It makes possible to assure that the signal of analytes in the sample is not due to a previous sample.

Acceptable criterion is the value of the error introduced due to instrument background; it should not be more than 1% of the mean value of determined concentrations.

2.3. Polycyclic aromatic hydrocarbons (PAHs)

2.3.1. General

The method used for determination of polycyclic aromatic hydrocarbons (PAHs) is based on extraction of these compounds from a sample with dichloromethane, consecutive clean-up of extracts from organic sulfur compounds using activated copper, clean-up from interfering impurities by means of columns with silica gel, and subsequent chromatography-mass spectrometric identification and quantitative determination of individual PAHs. Determination intervals range from 0.3 to 1000 μg/kg. To control quality of performed analysis the system of the isotope-labeled surrogate and internal standards added to samples at different stages of analysis was used.

2.3.2. Sample extraction

A pre-weighed part of a wet ground sample was mixed with equal amount of dehydrated sodium sulfate in an Erlenmeyer flask. Surrogate standard (mixture of deuterated PAHs) was introduced into the sample; then it was extracted by two 50 ml portions of dichloromethane on ultrasonic bath for 15 minutes. The combined extract was dried with sodium sulfate. 3 ml of n-hexane was added to the extract; then it was reduced using a rotary evaporator to 1-1.5 ml and cleaned from sulfur by activated copper. After that, the extract was transferred into a column with deactivated (3% Н2О) silica gel. 40 ml of n-hexane was passed. A hexane fraction was discarded; PAHs were eluted with 2:8 hexane-dichloromethane mixture. The purified extract was concentrated to 100 μl and transferred into a microvial. To determine surrogate standard yield an internal standard – 50 ng of 1-bromadamantane – was introduced just before instrumental analysis.

2.3.3.   Instrumental analysis

The analysis was carried out with a HP 5890/5972A chromatography-mass spectrometer under the following conditions:

Injector type                                                 split/splitless

Column type                                               VF-5MS 30 m х 0.25 х 0.25 μm

Initial column temperature                         60 0С

Holdup time                                                1 min.

Heating speed                                             20 0С/min to 200  0С;10 С/min to 290  0С

Detector temperature                                 290  0С

Injector temperature                                   290  0С

Injected volume                                         1 μl

Helium flow                                               1.2 ml/min

Mass scanning area                                     60-300 AMU

The instrument was calibrated using standard PAH solutions, #CLPS-B, produced by PROTOCOL Analytical Supplies, inc.  The instrument linearity was verified by calibration by 5 points in the concentration range from 50 to 5000 ng/ml.

After analysis of the analytical batch, the calibration was verified by analysis of medium concentration standard solution.

Results of analyses were processed with Chemstation software.

2.5.4. Identification of individual polycyclic aromatic hydrocarbons

Identification was performed by characteristic mass-spectra and chromatographic retention times of individual PAHs.

2.3.5.  Calculation of results

The content of individual PAHs, Cn (μg/kg), was calculated on the basis of the signals obtained for each specific compound from the equation:

Сn = (Sn) mr /(Sr) (RRF)n(REC)s M

where:   Sn is the peak area of an individual PAH,

Sr is the peak area of internal standard (recovery),

M is a sample weight, kg,

mr is the amount of injected internal standard, μg,

(RRF)n is a relative response factor for an individual PAH.

(REC)s is a recovery coefficient for surrogate standard.

(RRF)n is determined by analysis of PAH calibration solutions as:

(RRF)n = (Sns ) mrs /(Srs ) mns

where: Sns is the peak area of an individual PAH in the standard,

Srs is the peak area of internal standard (recovery) in the standard,

mns  is the amount of an individual PAH, μg,  in calibration solution,

mrs is the amount of internal standard in calibration solution, μg.

The recovery coefficient for surrogate standard (REC)s is determined from the formula:

(REC)s = (Ssur) mr /(Srs)ms(RRFsr)

where:   Ssur is the area of surrogate standard in an analyzed sample,

ms  is the amount of the surrogate standard introduced into an analyzed sample, μg.

(RRF)sr is a relative response factor for surrogate standard:

RRFsr = (Ssurs) mrs /(Sr) mns

where:  Ssurs and mns are the peak area and amount of surrogate standard in PAH calibration solution respectively.

The content of groups of individual PAHs was calculated using the recovery coefficients obtained for corresponding isotope-labeled standards. PAH groups and appropriate isotope-labeled standards are given below:

Naphthalene, methylnaphthalenes                          (REC)1   Naphthalene-D8,

Acenaphthylene, acenaphthene, fluorene               (REC)2   Acenaphthene-D10,

Phenanthrene, anthracene, fluoranthene                 (REC)3   Phenanthrene-D10,

Benzo[a]anthracene, chrysene, pyrene                   (REC)4   Chrysene-D10

The other PAHs                                                      (REC)5  Perylene-D12.

2.3.6.  Method detection limit

The detection limit determined statistically with the probability of 99% using a series of duplicate analyses of blank samples for different PAHs is 0.3-3.0 μg/kg for soil and bottom sediments. The mentioned detection limit was verified in the analysis of the batch of prepared check samples.

    - Quality control

The analysis of samples was carried out in batches. Each batch included 11 field samples and a duplicate (one of the samples was analyzed twice), a check sample, and a blank sample (procedural blank).

The #PP-HC8 mixture containing deuterated PAHs produced by Сhem.Service, US, was used as surrogate standard. These PAHs comprised naphthalene-D8, acenaphthene-D10,  phenanthrene-D10, chrysene-D10 and  perylene-D12..

1-bromadamantane was used as internal (recovery) standard.

Allowable criteria of analysis quality:

The content of individual PAHs in a blank sample is less than 0.005 μg.

The PAH content which was determined in EC-5 Certified Reference Material produced by  National Water Research Institute complied with the Analysis Certificate for 90% of analyzed compounds.

The deviation of duplicate sample analysis results is no more than (25% of an average value plus a method detection limit value for 90% of analyzed compounds.

The values of surrogate standard recovery ranged between 20% and 120%.

### Quality of instrumental data:

Instrument sensitivity was determined once a day (or after adjustment of the instrument) by the analysis of standard PAH solution.

Acceptable quality criterion: signal:noise ratio is more than 3:1 for 0.02 ng of anthracene in injected volume.

Chromatographic resolution was verified by the analysis of calibration standards performed prior to and after the analysis of an analytical batch.

Acceptable value: complete separation of phenanthrene and anthracene peaks.

Mass-spectral resolution determined during automatic adjustment of the instrument for ions m/z=502 and 503 as R=l/2b, where l is a distance between peak centers, b is a peak half-width, was not less than 0.95.

Linearity of instrument calibration was determined by analysis of 5 standard PAH solutions with concentrations from 50 to 5000 ng/ml.

Quality criterion: permissible standard deviation of calculated relative response factor RRF should be less than 20%.

Instrument stability was verified prior and after the analysis of a sample batch by the analysis of PAH calibration solution with medium concentration.

Quality criterion is the differences in the values of the relative response factor RRF calculated prior to and after sample batch analysis; it should not be more than (15%.

Examination of instrument contamination with respect to the analyte content was performed after each analysis of calibration standard solution by injection of n-hexane. It makes possible to assure that the signal of analytes in the sample is not due to a previous sample.

Acceptable criterion is the value of the error introduced due to instrument background; it should not be more than 1% of the mean value of determined concentrations.

2.4. Determination of polychlorinated dibenzo-p-dioxins/dibenzofurans (PCDD/Fs)

2.4.1 General

The method used for determination of polychlorinated dibenzo-p-dioxins and dibenzofurans is based on extraction of these compounds from bottom sediment samples with azeotropic benzene-ethanol mixture, consecutive clean-up of extracts by means of columns with modified silica gel, activated alumina, АХ-21 carbon sorbent, and subsequent chromatography-mass spectrometric identification and quantitative determination of individual PCDD/F congeners.

Determination intervals range from 0.5 to 5000 ng/kg of bottom sediments. To control quality of performed analysis the system of the isotope-labeled surrogate and internal standards added to samples at different stages of analysis was used.

The analysis was performed in accordance with PND F (Russian federal environmental norms) 16.1.7-97, PND F 14.1:2:4.124-97, OSW 8280 EPA US, STP (Russian standards of enterprises and organizations) 18.40.2000 [1-4].

2.4.2.   Extraction of PCDD/Fs and extract clean-up

Soil and bottom sediment samples were dried at room temperature to air-dry condition, extracted in a Soxhlet apparatus with azeotropic benzene-ethanol mixture. A surrogate standard (mixture of 13С isotope-labeled PCDD/F analogs) was introduced into the treated sample; then it was extracted with azeotropic benzene-ethanol mixture in a Soxhlet apparatus for 12 hours. The combined extract was dried with sodium sulfate, evaporated and the solvent was replaced with nonane. The concentrated extract was quantitatively transferred into a column filled consecutively with silica gel, silica gel modified by potassium hydroxide and sulphuric acid; 200 ml of hexane was passed through the column. The hexane fraction was concentrated and transferred to a column with activated (Brockman activity I) alumina. 100 ml of hexane-methylene chloride mixture (98:2) was passed through the column, and a target fraction was eluted with 100 ml of hexane-methylene chloride mixture (40:60). The target fraction was concentrated and introduced into the column containing 4.5% АХ-21 on Celit-545. 2 ml of cyclohexane-methylene chloride mixture (1:1), 2 ml of toluene-ethyl acetate mixture (1:1) were passed through the column. The column was overturned, and the target fraction was eluted with 50 ml of toluene. 25 μl of tetradecane was added into the extract, and the solution was evaporated to specified volume, internal standard was introduced, and then chromatography-mass spectrometric analysis was performed.

2.4.3.   Instrumental analysis

The analysis was carried out with a SATURN 1200 MS/MS chromatography-mass spectrometer using chemical ionization of a sample with detection of negative ions in the mode of scanning of analyte characteristic ion masses (SIM)

Injector type                                                split/splitless

Column type                                               DB-5MS

Column length                                            30 m

Column diameter                                        0.25 mm

Phase film thickness                                   0.25 μ

Temperature programming:

Initial column temperature                         160 0С

Initial holdup time                                      1 min.

Heating speed                                             10 0С/min to 200 0С; 30 С/min to 290  0С

Injector temperature                                   290  0С

Injected volume                                          1 μl

Reagent gas                                                methane

The instrument was calibrated using standard PCDD/F solutions prepared on the basis of EDF 7999 mixture from Cambrige Isotope Lab. The instrument linearity was verified by calibration by 5 points in the concentration range from 0.2 to 200 ng/ml. After the analytical batch, the calibration was verified by analysis of standard solution with medium concentration.

2.4.4. Identification of individual PCDD/F congeners

Chromatographic retention times of PCDD/F congeners, presence of characteristic ions, and the value of characteristic ion intensity ratio for a determined congener were used for the identification purpose.

2.4.5.  Method detection limit

The detection limits of individual PCDD/F congeners in bottom sediment samples determined statistically with the probability of 99% using a series of duplicate analyses of blank samples are given in protocols of each analysis, and they amount to 0.08 pg/g for tetrachlorinated PCDD congeners and 0.02 pg/g for the other congeners.

2.4.6.   Quality control

The analysis of samples is carried out in batches. Each batch includes not more than 15 samples and a duplicate (one of the samples is analyzed twice), a check sample, and a blank sample (procedural blank).

Certified EC-05 samples with known PCDD/F content produced by PROMOCHEM were used as check samples of bottom sediments.

ЕРА 23ISS mixture produced by Wellington Lab. was used as surrogate standard. It contains:

13С12-2378-TCDD                                13С12-2378-TCDF

13С12-12378-PnCDD                             13С12-12378-PnCDF

13С12-123678-HcCDD                           13С12-123678-HcCDF

13С12-1234678-HpCDD                         13С12-1234678-HpCDF

13С12-OCDD

NK-IS-A mixture, Lot № NKISA1199, was used as internal standard (recovery). It contains:

13С12-1234-TCDD

13С12-123789 –HcDD

Allowable criteria of analysis quality:

The content of PCDD/Fs in a blank sample is below detection limit.

The determined content of PCDD/Fs in a check sample lies within 70-125% of certified quantity of each congener.

The deviation of duplicate sample analysis results is no more than (25% of an average value plus a method detection limit.

The values of surrogate standard recovery ranged between 50% and 125%.

Quality of instrumental data

Instrument sensitivity was determined once a day (or after adjustment of the instrument) by the analysis of standard PCDD/F solution.

Acceptable quality criterion: signal:noise ratio is more than 3:1 for 0.2 pg of 2378-TCDD in injected volume; for OCDF this ratio is more than 3:1 at injection of 0.02 pg.

Chromatographic resolution was verified by the analysis of calibration standards performed prior to and after the analytical batch.

Acceptable value: separation of 2378-TCDD and 1234-TCDD peaks no less than by 80%.

Mass-spectral resolution determined during automatic adjustment is better than or equal to 0.8 AMU.

Linearity of instrument calibration was determined by analysis of 5 standard PCDD/F solutions with concentrations from 5 to 500 ng/ml.

Quality criterion: permissible standard deviation of calculated relative response factor RRF should be less than 20%.

Instrument stability was verified prior and after the analysis of a sample batch by the analysis of PCDD/F calibration solution with medium concentration.

Quality criterion is the differences in the values of the relative response factor RRF calculated prior to and after sample batch analysis; it should not be more than (15%.

Examination of instrument contamination with respect to the analyte content was performed after each analysis of calibration standard solution by injection of hexane.  It makes possible to assure that the signal of analytes in the sample is not due to a previous sample.

Acceptable criterion is the value of the error introduced due to instrument background; it should not be more than 1% of the mean value of determined concentrations.

If quality criteria are inconsistent with the specified values after an analytical batch has been performed, the causes of the deviations are determined and batch reanalysis is performed.

2.5 . Polychlorinated planar (non-ortho and mono-ortho substituted) biphenyls

2.5.1 General

In the course of analysis, planar non-ortho substituted and mono-ortho substituted polychlorinated biphenyls (PCBs) are determined. The IUPAC numbers of these compounds are given below:

PCB   #77, #81, #105, #114, #118, #123, #126, #156, #157, #167, #169, #170, #180, #189.

The method used for determination of PCBs is based on extraction of analyzed compounds with mixture of organic solvents (benzene:ethanol = 68:32 v/v) in a Soxhlet apparatus. Extracts are cleaned-up using activated copper and column chromatography with various sorbents. Identification of substances is performed by chromatography-mass spectrometry method.  Determination intervals range from 0.02 to 500 μg/kg. To control quality of analysis a system of surrogate isotope-labeled standards added at different stages is used. The analysis is performed on the basis of the normative document, STP 18.47–2001 “The procedure for identification of polychlorinated biphenyl congeners in environmental objects using chromatography-mass spectrometry” [5], which has been worked out according to Method 1668 [6] of US Environmental Protection Agency.

2.5.2 Sample extraction

Prior to extraction, bottom sediment samples are dried to air-dry condition. A surrogate standard (mixture of isotope-labeled PCB congeners) is introduced into the pre-weighed sample; then it is extracted in a Soxhlet apparatus for 16 hours. On completion of the extraction, the extract in concentrated on a rotary evaporator and shifted into isooctane. Then it is cleaned up from sulfur using activated copper. After cleaning, the extract is transferred into a chromatographic column with silica gel. Silica gel activated at 325°С and also silica gel impregnated with concentrated sulphuric acid and potassium hydroxide are used for a multiplayer column. The multiplayer column is eluted with hexane. Then the extract concentrated on the rotary evaporator is cleaned up using the column with 10 g of activated alumina. The first fraction is eluted with 100 ml of hexane and discarded. The fraction containing PCBs is eluted with hexane:dichloromethane mixture (95:5), concentrated to 200 μl, and transferred into a microvial. To determine surrogate standard yield an internal standard – 4 ng of PCB#166 – is introduced just before instrumental analysis.

Isotope labeled PCB standards were introduced into 5 l water samples; after that, extraction with two toluene portions was carried out.  The obtained extracts were cleaned up from interfering impurities as described above.

    - Instrumental analysis

The analysis iss carried out with a Varian Saturn 4D MS/MS chromatography-mass spectrometer in the mode of sample ionization by electron impact at mass scanning in the range of m/e = 180-450 AMU.

Injector type			                       split/splitless

Injector purging holdup			1 min

Solvent discharge time   			3 min

Column type                                      		DB-5MS

Column length                 		           30 m

Column diameter                  			0.25 mm

Phase film thickness         			0.25 (

Temperature programming:

Initial column temperature    		           80(C

Initial holdup time 			       1 min

Heating speed      			       20(C/min to 180(C; 4(C/min to 280(C

Detector temperature			       290(C

Injected volume			       1 μl

Helium flow	                        	       1.2 ml/min

The instrument is calibrated using standard mixture of polychlorinated biphenyls, BP-MS, from Wellington Laboratories. The instrument linearity is verified by calibration by 5 points in the concentration range from 1 to 200 ng/ml. After analysis of the analytical batch, the calibration is verified by analysis of a medium concentration standard solution.

The results of analyses are processed with Varian 5.2 software.

The NK-LCSP-A standard mixture produced by Wellington Laboratories is used as surrogate standard. It contains the following 13С isotope labeled compounds:  PCB #7713С12, #8113С12, #10513С12, #11413С12, #11813С12, #12313С12, #12613С12, #15613С12, #15713С12, #16713С12, #16913С12, #17013С12, #18013С12, #18913С12.

    - Identification of individual PCB congeners

Identification was performed by characteristic mass-spectra and retention times of individual PCB congeners

    - Calculation of results

The content of individual PCB congeners, Cn (μg/kg) was calculated on the basis of the signals obtained for each specific congener from the following formula:

Сn = (Sn) mr /(Sr) (RRF)n(REC)s M,

where: Sn is the peak area of a PCB congener;

Sr is the peak area of internal standard (recovery);

M is a sample weight, kg;

mr is the amount of injected internal standard, μg;

(RRF)n is a relative response factor for an individual PCB congener;

(REC)s is a recovery coefficient for a corresponding surrogate standard.

(RRF)n is determined by analysis of PCB calibration solutions as:

(RRF)n = (Sns ) mrs /(Srs ) mns,

where:  Sns is the peak area of a PCB congener in calibration solution;

Srs is the peak area of internal standard (recovery) in calibration solution;

mns is the amount of a PCB congener in calibration solution, ng;

mrs is the amount of an internal standard in calibration solution, ng.

The recovery coefficient for surrogate standard (REC)s is determined from the formula:

(REC)s = (Ssur) mr /(Srs)ms(RRFsr),

where:  Ssur is the area of surrogate standard in the analyzed sample;

Srs is the area of internal standard in the analyzed sample;

ms  is the amount of the surrogate standard introduced into the analyzed sample, ng;

mr is the amount of added internal standard (recovery), ng;

(RRF)sr is the relative response factor for surrogate standard:

RRFsr = (Ssurs) mrs /(Srs) msur

where Ssur and msur are the peak area and amount of surrogate standard in PCB calibration solution  respectively.

The PCB content was calculated using the extraction coefficients of appropriate surrogate isotope-labeled PCB congeners for each group depending on degree of chlorination.

Method detection limit

The detection limit determined statistically with the probability of 99% using a series of duplicate analyses of blank samples for individual PCB congeners is given in Table 2.5.6.1.

Table 2.5.6.1

Detection limits of non-ortho and mono-ortho substituted PCBs

| PCB congener | Soil, bottom sediments μg/kg |
| --- | --- |
| #77 | 0.005 |
| #81 | 0.005 |
| #105 | 0.01 |
| #114 | 0.01 |
| #118 | 0.01 |
| #123 | 0.01 |
| #126 | 0.01 |
| #156 | 0.01 |
| #157 | 0.01 |
| #167 | 0.02 |
| #169 | 0.02 |
| #170 | 0.02 |
| #180 | 0.02 |
| #189 | 0.03 |

The mentioned detection limits were verified in the analysis of analytical batches of check samples.

    - Quality control

The analysis of samples is carried out in batches. Each batch includes up to 15 field samples and a duplicate (one of the samples is analyzed twice) for soil and bottom sediments, and also certified DX-3 bottom sediment material produced by National Water Research Institute of Canada and a blank sample.

PCB #166 was used as internal standard.

### Allowable criteria of analysis quality

The content of individual PCB congeners in a blank sample is less than 1 ng.

The determined content of PCB congeners in the DX-3 bottom sediment material certified by NWRI of Canada complied with the Analysis Certificate for 90% of analyzed compounds.

The deviation of duplicate sample analysis results is no more than ( 25% of an average value plus a method detection limit value for 90% of analyzed compounds.

The values of surrogate standard recovery range between 40% and 120%.

##### Quality of instrumental data

Instrument sensitivity was determined once a day (or after adjustment of the instrument) by analysis of standard PCB calibration solution.

Acceptable quality criterion: signal-noise ratio is more than 3:1 for 0.01 ng of 13C-PCB #180 in injected volume.

Chromatographic resolution was verified by the analysis of calibration standards performed prior to and after the analysis of an analytical batch.

Acceptable value: complete separation of PCB#123 and PCB#118 peaks.

Mass-spectral resolution was determined during automatic adjustment of the instrument for ions m/z=264 and 265 as R=l/2b, where l is a distance between peak centers, b is a peak half-width; it was not less than 0.95.

Linearity of instrument calibration was determined by analysis of 5 standard PCB solutions with concentrations from 1 to 200 ng/ml.

Quality criterion: permissible standard deviation of calculated relative response factor RRF should be less than 20%.

Instrument stability was verified prior and after the analysis of a sample batch by the analysis of PCB calibration solution with medium concentration.

Quality criterion is the differences in the values of the relative response factor RRF calculated prior to and after sample batch analysis; it should not be more than (15%.

Examination of instrument contamination with respect to the analyte content was performed after each analysis of calibration standard solution by injection of hexane.  It makes possible to assure that the signal of analytes in the sample is not due to a previous sample.

Acceptable criterion is the value of the error introduced due to instrument background; it should not be more than 1% of the mean value of determined concentrations.

2.6. Polychlorinated biphenyls, total content as Arochlor-1256 and Arochlor-1260

2.6.1 General

The method used for total determination of polychlorinated biphenyls (PCBs) in the form of Arochlor-1256 and Arochlor-1260 technical mixtures is based on extraction of analyzed compounds with dichloromethane in a Soxhlet apparatus. Extracts were cleaned-up using activated copper and column chromatography with florisil. The analysis was performed chromatographically using an Electron Capture Detector (ECD) selective to organochlorine compounds. Determination intervals range from 0.1 to 1000 μg/kg.

2.6.2. Sample extraction

A pre-weighed part of a wet bottom sediment sample was mixed with equal amount of dehydrated sodium sulfate in an Erlenmeyer flask. The sample was extracted in a Soxhlet apparatus for 16 hours. The extract was dried with sodium sulfate. 3 ml of hexane was added to the extract; then it was reduced using a rotary evaporator to 1-1.5 ml and cleaned from sulfur by activated copper. After that, the extract was transferred into a column with florisil (2.1% Н2О). The column was eluted with hexane. The fraction containing PCBs was concentrated to 100 μl and transferred to a microvial. 4 ng of internal standard, PCB#166, was introduced just before instrumental analysis.

    - Instrumental analysis

The analysis was performed using a НР 5890 gas-liquid chromatograph with an electron capture detector.

Injector type                                               split/splitless

Column type                                               VF-5MS 30 m х 0.25 х 0.25 μm

Initial column temperature                         80 0С

Holdup time                                                1 min.

Heating speed                                             20 0С/min to 200  0С;10 С/min to 290  0С

Detector temperature                                 290  0С

Injector temperature                                   290  0С

Injected volume                                          1 μl

Helium flow                                               1.2 ml/min

The instrument was calibrated using standard Arochlor-1256 and Arochlor-1260 mixtures produced by СIL, USA. The instrument linearity was verified by calibration by 5 points in the concentration range from 5 to 1000 ng/ml. After analysis of the analytical batch, the calibration was verified by analysis of a medium concentration standard solution.

2.6.4. Identification of PCBs as Arochlor-1256 and Arochlor-1260

Identification was carried out using characteristic peaks in a chromatogram for the substances detected by a selective ECD within the time of the beginning and end of Arochlor-1256 and Arochlor-1260 retention.

2.6.5. Calculation of results

The PCB content as Arochlor-1256 and Arochlor-1260 mixtures, Cn (μg/kg), was calculated on the basis of the obtained total signal in the chromatogram determined within the retention time of each abovementioned mixture. It was gained from the following formula:

Сn = (Sn) mr /(Sr) (RRF)n M,

where: Sn is a total peak area within the retention time for Arochlor-1256 mixture;

Sr is the peak area of internal standard (recovery);

M is a sample weight, kg;

mr is the amount of injected internal standard, μg;

(RRF)n is a relative response factor for Arochlor-1256 mixture;

(RRF)n is determined by analysis of PCB calibration solutions as:

(RRF)n = (Sns ) mrs /(Srs ) mns,

where:  Sns is a total peak area within the retention time for Arochlor-1256 mixture in calibration solution;

Srs is the peak area of internal standard (recovery) in calibration solution;

mns is the amount of Arochlor-1256 mixture in calibration solution, ng;

mrs is the amount of internal standard in calibration solution, ng.

The content of Arochlor-1260 mixture is calculated in a similar way.

    - Method detection limit

The detection limit determined statistically with the probability of 99% using a series of duplicate analyses of blank samples for Arochlor-1256 and Arochlor-1260 is 0.1 μg/kg for soil and bottom sediments. The mentioned detection limits were verified in the analysis of analytical batches of check samples.

2.6.7.  Quality control

The analysis of samples was carried out in batches. Each batch included not more than 11 field samples and a duplicate (one of the samples was analyzed twice), certified EC-5 bottom sediment material produced by National Water Research Institute of Canada, and a blank sample.

PCB #166 was used as internal standard.

### Allowable criteria of analysis quality:

### The content of Arochlor-1256 and Arochlor-1260  in a blank sample is less than 10 ng.

The deviation of duplicate sample analysis results is no more than (25% of an average value plus a method detection limit.

##### Quality of instrumental data:

Instrument sensitivity was determined once a day (or after adjustment of the instrument) by analysis of PCB #166 internal standard solution with concentration of 0.01 μg/ml.        Acceptable quality criterion: signal:noise ratio is more than 10:1 for a PCB #166 peak.

Linearity of instrument calibration was determined by analysis of 5 standard Arochlor-1256 solutions with concentrations from 10 to 2000 ng/ml.

Quality criterion: permissible standard deviation of calculated relative response factor RRF should be less than 20%.

Instrument stability was verified prior to and after the analysis of a sample batch by the analysis of Arochlor-1256 calibration solution with medium concentration.

Quality criterion is the differences in the values of the relative response factor RRF calculated prior to and after sample batch analysis, should not be more than (15%.

Examination of instrument contamination with respect to the analyte content was performed after each analysis of calibration standard solution by injection of hexane.  It makes possible to assure that the signal of analytes in the sample is not due to a previous sample.

Acceptable criterion is the value of the error introduced due to instrument background; it should not be more than 1% of the mean value of determined concentrations.

ANNEX 1

Results of analyses

1.1 Polychlorinated biphenyls (PCBs)

Table 1.1.1

The content of polychlorinated biphenyls in bottom sediment samples, μg/kg

| PCB congener | Customer’s sample code: |
| --- | --- |
|  | NOV8 Sed1 RU-1 | NOV8 Sed1 RU-2 | NOV8 Sed1 RU-3 | NOV8 Sed1 RU-4 | NOV10 Sed1 RU-5 |
| 8[CL2] | 0.43 | 0.22 | 0.21 | 0.26 | 0.43 |
| 18[CL3] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 16[CL3] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 26[CL3] | <0.15 | <0.15 | <0.15 | <0.15 | <0.15 |
| 25[CL3] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| (31+28)[CL3] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 33[CL3] | <0.05 | 0.10 | 0.08 | <0.05 | <0.05 |
| 52[CL4] | 1.08 | 0.34 | <0.15 | <0.15 | <0.15 |
| 49[CL4] | <0.15 | <0.15 | <0.15 | <0.15 | <0.15 |
| 47[CL4] | 0.88 | 0.34 | 0.33 | 0.28 | 0.34 |
| 44[CL4] | 0.17 | <0.05 | <0.05 | <0.05 | <0.05 |
| 37[CL3] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 41[CL4] | 0.09 | <0.05 | 0.08 | <0.05 | 0.06 |
| 74[CL4] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 70[CL4] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 66[CL4] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 95[CL5] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 60[CL4] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 101[CL5] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 99[CL5] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 97[CL5] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 87[CL5] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 110[CL5] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 151[CL6] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 135[CL6] | 0.10 | <0.05 | <0.05 | <0.05 | <0.05 |
| 118[CL5] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 149[CL6] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 146[CL6] | 0.10 | <0.05 | <0.05 | <0.05 | <0.05 |
| 153[CL6] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 105[CL5] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 141[CL6] | 0.06 | <0.05 | <0.05 | <0.05 | <0.05 |
| 138[CL6] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 126[CL5] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 187[CL7] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 183[CL7] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| (128+167)[CL6] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 174[CL7] | <0.05 | 0.09 | <0.05 | <0.05 | <0.05 |
| 177[CL7] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 171[CL7] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 201[CL8] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 180[CL7] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 170[CL7] | 0.10 | <0.05 | 0.07 | <0.05 | <0.05 |
| 199[CL8] | 0.18 | <0.05 | <0.05 | <0.05 | <0.05 |
| (196+203)[CL8] | <0.05 | 0.13 | <0.05 | <0.05 | <0.05 |
| 189[CL7] | <0.07 | <0.07 | <0.07 | <0.07 | <0.07 |
| 195[CL8] | <0.07 | <0.07 | <0.07 | <0.07 | <0.07 |
| 194[CL8] | <0.07 | <0.07 | <0.07 | <0.07 | <0.07 |
| 206[CL9] | <0.07 | <0.07 | <0.07 | <0.07 | <0.07 |
| 209[CL10] | 0.30 | <0.07 | <0.07 | <0.07 | <0.07 |
| Sum of PCBs | 3.48 | 1.23 | 0.78 | 0.54 | 0.83 |

Table 1.1.2

The content of polychlorinated biphenyls in bottom sediment samples, μg/kg

| PCB congener ↓ | Customer’s sample code: |
| --- | --- |
|  | NOV10 Sed2 RU-6 | NOV11 Sed1 RU-7 | NOV11 Sed1 RU-8 | NOV11 Sed2 RU-9 | NOV11 Sed2 RU-10 |
| 8[CL2] | 0.25 | 0.62 | 0.13 | 0.28 | 0.26 |
| 18[CL3] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 16[CL3] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 26[CL3] | <0.15 | <0.15 | <0.15 | <0.15 | <0.15 |
| 25[CL3] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| (31+28)[CL3] | <0.10 | <0.10 | <0.10 | <0.10 | 0.27 |
| 33[CL3] | 0.06 | 0.08 | 0.08 | <0.05 | <0.05 |
| 52[CL4] | <0.15 | 0.61 | <0.15 | <0.15 | <0.15 |
| 49[CL4] | <0.15 | <0.15 | <0.15 | <0.15 | <0.15 |
| 47[CL4] | 0.10 | 0.18 | 0.18 | 0.46 | 0.22 |
| 44[CL4] | 0.14 | 0.11 | 0.19 | 0.12 | 0.11 |
| 37[CL3] | 0.13 | <0.05 | <0.05 | 0.12 | <0.05 |
| 41[CL4] | <0.05 | 0.07 | <0.05 | <0.05 | <0.05 |
| 74[CL4] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 70[CL4] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 66[CL4] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 95[CL5] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 60[CL4] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 101[CL5] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 99[CL5] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 97[CL5] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 87[CL5] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 110[CL5] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 151[CL6] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 135[CL6] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 118[CL5] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 149[CL6] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 146[CL6] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 153[CL6] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 105[CL5] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 141[CL6] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 138[CL6] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 126[CL5] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 187[CL7] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 183[CL7] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| (128+167)[CL6] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 174[CL7] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 177[CL7] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 171[CL7] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 201[CL8] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 180[CL7] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 170[CL7] | <0.05 | <0.05 | <0.05 | 0.06 | <0.05 |
| 199[CL8] | <0.05 | <0.05 | <0.05 | <0.05 | 0.07 |
| (196+203)[CL8] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 189[CL7] | <0.07 | <0.07 | <0.07 | <0.07 | <0.07 |
| 195[CL8] | <0.07 | <0.07 | <0.07 | <0.07 | <0.07 |
| 194[CL8] | <0.07 | <0.07 | <0.07 | <0.07 | <0.07 |
| 206[CL9] | <0.07 | <0.07 | <0.07 | <0.07 | <0.07 |
| 209[CL10] | <0.07 | <0.07 | <0.07 | <0.07 | <0.07 |
| Sum of PCBs | 0.68 | 1.67 | 0.58 | 1.05 | 0.92 |

Table 1.1.3

The content of polychlorinated biphenyls in bottom sediment samples, μg/kg

| PCB congener ↓ | Customer’s sample code: |
| --- | --- |
|  | NOV11 Sed2 RU-11 | NOV11 Sed2 RU-12 | NOV15 Sed1 RU-13 | NOV12 Sed2 KZ-1 | NOV12 Sed1 KZ-2 |
| 8[CL2] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 18[CL3] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 16[CL3] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 26[CL3] | <0.15 | <0.15 | <0.15 | <0.15 | <0.15 |
| 25[CL3] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| (31+28)[CL3] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 33[CL3] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 52[CL4] | <0.15 | <0.15 | <0.15 | 0.32 | <0.15 |
| 49[CL4] | <0.15 | <0.15 | <0.15 | <0.15 | <0.15 |
| 47[CL4] | 0.09 | <0.05 | <0.05 | 0.08 | <0.05 |
| 44[CL4] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 37[CL3] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 41[CL4] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 74[CL4] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 70[CL4] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 66[CL4] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 95[CL5] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 60[CL4] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 101[CL5] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 99[CL5] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 97[CL5] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 87[CL5] | <0.10 | <0.10 | <0.10 | 0.14 | <0.10 |
| 110[CL5] | <0.10 | <0.10 | 0.13 | <0.10 | 0.10 |
| 151[CL6] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 135[CL6] | <0.05 | <0.05 | 0.05 | <0.05 | <0.05 |
| 118[CL5] | <0.10 | <0.10 | <0.10 | 0.20 | <0.10 |
| 149[CL6] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 146[CL6] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 153[CL6] | <0.05 | <0.05 | 0.07 | 0.13 | 0.16 |
| 105[CL5] | 0.07 | <0.05 | 0.14 | 0.20 | 0.15 |
| 141[CL6] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 138[CL6] | <0.10 | <0.10 | <0.10 | <0.10 | 0.12 |
| 126[CL5] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 187[CL7] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 183[CL7] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| (128+167)[CL6] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 174[CL7] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 177[CL7] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 171[CL7] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 201[CL8] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 180[CL7] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 170[CL7] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 199[CL8] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| (196+203)[CL8] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 189[CL7] | <0.07 | <0.07 | <0.07 | <0.07 | <0.07 |
| 195[CL8] | <0.07 | <0.07 | <0.07 | <0.07 | <0.07 |
| 194[CL8] | <0.07 | <0.07 | <0.07 | <0.07 | <0.07 |
| 206[CL9] | <0.07 | <0.07 | <0.07 | <0.07 | <0.07 |
| 209[CL10] | <0.07 | <0.07 | <0.07 | <0.07 | <0.07 |
| Sum of PCBs | 0.16 | - | 0.38 | 1.08 | 0.53 |

Table 1.1.4.

The content of polychlorinated biphenyls in bottom sediment samples, μg/kg

| PCB congener ↓ | Customer’s sample code: |
| --- | --- |
|  | NOV13 Sed1 KZ-3 | NOV13 Sed2 KZ-4 | NOV13 Sed1 KZ-5 | NOV13 Sed2 KZ-6 | NOV13 Sed1 KZ-7 | NOV13 Sed1 KZ-8 |
| 8[CL2] | <0.05 | <0.05 | 0.10 | 0.05 | <0.05 | <0.05 |
| 18[CL3] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 16[CL3] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 26[CL3] | <0.15 | <0.15 | <0.15 | <0.15 | <0.15 | <0.15 |
| 25[CL3] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| (31+28)[CL3] | <0.10 | 0.16 | <0.10 | <0.10 | <0.10 | <0.10 |
| 33[CL3] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 52[CL4] | <0.15 | <0.15 | <0.15 | <0.15 | <0.15 | <0.15 |
| 49[CL4] | <0.15 | <0.15 | <0.15 | <0.15 | <0.15 | <0.15 |
| 47[CL4] | <0.05 | <0.05 | <0.05 | <0.05 | 0.06 | <0.05 |
| 44[CL4] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 37[CL3] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 | 0.06 |
| 41[CL4] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 74[CL4] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 70[CL4] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 66[CL4] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 95[CL5] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 60[CL4] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 101[CL5] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 99[CL5] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 97[CL5] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 87[CL5] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 110[CL5] | <0.10 | 0.15 | <0.10 | 0.13 | 0.14 | <0.10 |
| 151[CL6] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 135[CL6] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 118[CL5] | <0.10 | 0.11 | <0.10 | <0.10 | 0.15 | 0.14 |
| 149[CL6] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 | <0.10] |
| 146[CL6] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 153[CL6] | 0.08 | 0.08 | <0.05 | 0.08 | 0.11 | 0.08 |
| 105[CL5] | 0.08 | 0.14 | 0.07 | 0.05 | 0.16 | 0.09 |
| 141[CL6] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 138[CL6] | <0.10 | <0.10 | <0.10 | <0.10 | 0.18 | <0.10 |
| 126[CL5] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 187[CL7] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 183[CL7] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| (128+167)[CL6] | <0.10 | <0.10 | <0.10 | <0.10 | 0.11 | <0.10 |
| 174[CL7] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 177[CL7] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 171[CL7] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 201[CL8] | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| 180[CL7] | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 | <0.05 |
| 170[CL7] | <0.05 | 0.09 | <0.05 | <0.05 | <0.05 | <0.05 |
| 199[CL8] | <0.05 | 0.06 | <0.05 | <0.05 | <0.05 | <0.05 |
| (196+203)[CL8] | <0.05 | 0.07 | <0.05 | <0.05 | <0.05 | <0.05 |
| 189[CL7] | <0.07 | <0.07 | <0.07 | <0.07 | <0.07 | <0.07 |
| 195[CL8] | <0.07 | <0.07 | <0.07 | <0.07 | <0.07 | <0.07 |
| 194[CL8] | <0.07 | <0.07 | <0.07 | <0.07 | <0.07 | <0.07 |
| 206[CL9] | <0.07 | <0.07 | <0.07 | <0.07 | <0.07 | <0.07 |
| 209[CL10] | <0.07 | <0.07 | <0.07 | <0.07 | <0.07 | <0.07 |
| Sum of PCBs | 0.16 | 0.85 | 0.17 | 0.31 | 0.91 | 0.37 |

Table 1.1.5

The content of polychlorinated biphenyls in bottom sediment samples, μg/kg

| PCB congener ↓ | Customer’s sample code: |
| --- | --- |
|  | 7 | 10 | 11 | 14 |
| 8[CL2] | <0.05 | <0.05 | 0.08 | <0.05 |
| 18[CL3] | <0.10 | <0.10 | <0.10 | <0.10 |
| 16[CL3] | <0.05 | <0.05 | <0.05 | <0.05 |
| 26[CL3] | <0.15 | <0.15 | <0.15 | <0.15 |
| 25[CL3] | <0.05 | <0.05 | <0.05 | <0.05 |
| (31+28)[CL3] | <0.10 | <0.10 | <0.10 | <0.10 |
| 33[CL3] | <0.05 | <0.05 | <0.05 | <0.05 |
| 52[CL4] | <0.15 | <0.15 | <0.15 | <0.15 |
| 49[CL4] | <0.15 | <0.15 | <0.15 | <0.15 |
| 47[CL4] | <0.05 | <0.05 | <0.05 | <0.05 |
| 44[CL4] | <0.05 | <0.05 | <0.05 | <0.05 |
| 37[CL3] | <0.05 | <0.05 | <0.05 | <0.05 |
| 41[CL4] | <0.05 | <0.05 | <0.05 | <0.05 |
| 74[CL4] | <0.10 | <0.10 | <0.10 | <0.10 |
| 70[CL4] | <0.10 | <0.10 | <0.10 | <0.10 |
| 66[CL4] | <0.10 | <0.10 | <0.10 | <0.10 |
| 95[CL5] | <0.10 | <0.10 | <0.10 | <0.10 |
| 60[CL4] | <0.10 | <0.10 | <0.10 | <0.10 |
| 101[CL5] | <0.10 | <0.10 | <0.10 | <0.10 |
| 99[CL5] | <0.10 | <0.10 | <0.10 | <0.10 |
| 97[CL5] | <0.10 | <0.10 | <0.10 | <0.10 |
| 87[CL5] | <0.10 | <0.10 | <0.10 | <0.10 |
| 110[CL5] | <0.10 | <0.10 | <0.10 | <0.10 |
| 151[CL6] | <0.05 | <0.05 | <0.05 | <0.05 |
| 135[CL6] | <0.05 | <0.05 | <0.05 | <0.05 |
| 118[CL5] | <0.10 | <0.10 | 0.14 | 0.11 |
| 149[CL6] | <0.05 | <0.05 | <0.05 | <0.05 |
| 146[CL6] | <0.05 | <0.05 | <0.05 | 0.06 |
| 153[CL6] | <0.05 | <0.05 | 0.07 | 0.09 |
| 105[CL5] | <0.05 | <0.05 | <0.05 | <0.05 |
| 141[CL6] | <0.10 | <0.10 | <0.10 | <0.10 |
| 138[CL6] | <0.10 | <0.10 | <0.10 | <0.10 |
| 126[CL5] | <0.05 | <0.05 | <0.05 | <0.05 |
| 187[CL7] | <0.05 | <0.05 | <0.05 | <0.05 |
| 183[CL7] | <0.10 | <0.10 | <0.10 | <0.10 |
| (128+167)[CL6] | <0.05 | <0.05 | <0.05 | <0.05 |
| 174[CL7] | <0.05 | <0.05 | <0.05 | <0.05 |
| 177[CL7] | <0.10 | <0.10 | <0.10 | <0.10 |
| 171[CL7] | <0.10 | <0.10 | <0.10 | <0.10 |
| 201[CL8] | <0.05 | <0.05 | <0.05 | <0.05 |
| 180[CL7] | <0.05 | <0.05 | <0.05 | <0.05 |
| 170[CL7] | <0.05 | <0.05 | <0.05 | <0.05 |
| 199[CL8] | <0.05 | <0.05 | <0.05 | <0.05 |
| (196+203)[CL8] | <0.07 | <0.07 | <0.07 | <0.07 |
| 189[CL7] | <0.07 | <0.07 | <0.07 | <0.07 |
| 195[CL8] | <0.07 | <0.07 | <0.07 | <0.07 |
| 194[CL8] | <0.07 | <0.07 | <0.07 | <0.07 |
| 206[CL9] | <0.07 | <0.07 | <0.07 | <0.07 |
| 209[CL10] | <0.07 | <0.07 | <0.07 | <0.07 |
| Sum of PCBs | - | - | 0.29 | 0.26 |

Table 1.1.6.

The content of polychlorinated biphenyls in bottom sediment samples, μg/kg

| PCB congener ↓ | Customer’s sample code: |
| --- | --- |
|  | 18 | 20 | Lagan-R |
| 8[CL2] | <0.05 | 0.06 | 0.07 |
| 18[CL3] | <0.10 | <0.10 | <0.10 |
| 16[CL3] | <0.05 | <0.05 | <0.05 |
| 26[CL3] | <0.15 | <0.15 | <0.15 |
| 25[CL3] | <0.05 | <0.05 | <0.05 |
| (31+28)[CL3] | <0.10 | <0.10 | <0.10 |
| 33[CL3] | <0.05 | <0.05 | <0.05 |
| 52[CL4] | <0.15 | <0.15 | 0.50 |
| 49[CL4] | <0.15 | <0.15 | <0.15 |
| 47[CL4] | <0.05 | <0.05 | 0.11 |
| 44[CL4] | <0.05 | <0.05 | 0.20 |
| 37[CL3] | <0.05 | <0.05 | 0.08 |
| 41[CL4] | <0.05 | <0.05 | 0.13 |
| 74[CL4] | <0.10 | <0.10 | 0.17 |
| 70[CL4] | <0.10 | <0.10 | 0.42 |
| 66[CL4] | <0.10 | <0.10 | 0.25 |
| 95[CL5] | <0.10 | <0.10 | 0.45 |
| 60[CL4] | <0.10 | <0.10 | 0.19 |
| 101[CL5] | <0.10 | <0.10 | 0.94 |
| 99[CL5] | <0.10 | <0.10 | 0.44 |
| 97[CL5] | <0.10 | <0.10 | 0.31 |
| 87[CL5] | <0.10 | <0.10 | 0.72 |
| 110[CL5] | <0.10 | <0.10 | 0.86 |
| 151[CL6] | <0.05 | <0.05 | 0.17 |
| 135[CL6] | <0.05 | <0.05 | 0.13 |
| 118[CL5] | <0.10 | 0.10 | 1.47 |
| 149[CL6] | <0.05 | <0.05 | 0.05 |
| 146[CL6] | 0.06 | <0.05 | 0.44 |
| 153[CL6] | 0.06 | 0.05 | 0.65 |
| 105[CL5] | <0.05 | <0.05 | 0.09 |
| 141[CL6] | 0.11 | <0.10 | 0.75 |
| 138[CL6] | <0.10 | <0.10 | 0.10 |
| 126[CL5] | <0.05 | <0.05 | <0.05 |
| 187[CL7] | <0.05 | <0.05 | <0.05 |
| 183[CL7] | <0.10 | <0.10 | 0.30 |
| (128+167)[CL6] | <0.05 | <0.05 | <0.05 |
| 174[CL7] | <0.05 | <0.05 | <0.05 |
| 177[CL7] | <0.10 | <0.10 | 0.18 |
| 171[CL7] | <0.10 | <0.10 | <0.10 |
| 201[CL8] | 0.07 | <0.05 | 0.09 |
| 180[CL7] | <0.05 | <0.05 | 0.07 |
| 170[CL7] | <0.05 | <0.05 | <0.05 |
| 199[CL8] | <0.05 | <0.05 | <0.05 |
| (196+203)[CL8] | <0.07 | <0.07 | <0.07 |
| 189[CL7] | <0.07 | <0.07 | <0.07 |
| 195[CL8] | <0.07 | <0.07 | <0.07 |
| 194[CL8] | <0.07 | <0.07 | <0.07 |
| 206[CL9] | <0.07 | <0.07 | <0.07 |
| 209[CL10] | <0.07 | <0.07 | <0.07 |
| Sum of PCBs | 0.30 | 0.21 | 10.34 |

1.2. Organochlorine pesticides (OCPs)

Table 1.2.1

The content of organochlorine pesticides in bottom sediment samples, μg/kg of dry weight

| Analyte | Sample code: |
| --- | --- |
|  | NOV8 Sed1 RU-1 | NOV8 Sed1 RU-2 | NOV8 Sed1 RU-3 | NOV8 Sed1 RU-4 | NOV10 Sed1 RU-5 |
| Hexachlorobenzene | 0.13 | 0.09 | 0.13 | 0.10 | 0.32 |
| α-HCH | 0.13 | 0.07 | 0.12 | 0.67 | 0.33 |
| β-HCH | 0.15 | 0.08 | 0.16 | 0.26 | 0.08 |
| γ-HCH | 0.04 | 0.03 | 0.02 | 0.12 | 0.02 |
| δ-HCH | na | na | na | na | na |
| Heptachlor | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| Heptachlor epoxide | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| Aldrin | <0.02 | <0.02 | <0.02 | <0.02 | <0.02 |
| Dieldrin | <0.02 | <0.02 | <0.02 | <0.02 | <0.02 |
| Endrin | <0.03 | <0.03 | <0.03 | <0.03 | <0.03 |
| Oxychlordane | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| trans-Chlordane | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| cis-Chlordane | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| α - Endosulfan | <0.03 | <0.03 | <0.03 | <0.03 | <0.03 |
| β - Endosulfan | <0.04 | <0.04 | <0.04 | <0.04 | <0.04 |
| Endosulfan Sulfate | <0.03 | <0.03 | <0.03 | <0.03 | <0.03 |
| 2, 4΄-DDE | 0.04 | 0.01 | 0.05 | 0.02 | <0.01 |
| 4, 4΄-DDE | 0.91 | 0.73 | 0.53 | 1.04 | 1.41 |
| DDMU | 0.13 | 0.04 | <0.01 | 0.18 | 0.29 |
| 2, 4΄-DDD | <0.01 | 0.07 | 0.05 | 0.05 | 0.24 |
| 4, 4΄-DDD | 0.16 | 0.13 | 0.12 | 0.14 | 0.62 |
| 2, 4΄-DDT | 0.09 | <0.01 | <0.01 | 0.16 | 0.05 |
| 4, 4΄-DDT | 0.17 | 0.07 | 0.05 | 0.63 | 0.47 |
| trans-Nonachlor | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| cis-Nonachlor | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| Methoxychlor | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| Mirex | <0.02 | <0.02 | <0.02 | <0.02 | <0.02 |

Table 1.2.2.

The content of organochlorine pesticides in bottom sediment samples, μg/kg of dry weight

| Analyte | Sample code: |
| --- | --- |
|  | NOV10 Sed2 RU-6 | NOV11 Sed1 RU-7 | NOV11 Sed1 RU-8 | NOV11 Sed2 RU-9 | NOV11 Sed2 RU-10 |
| Hexachlorobenzene | 0.18 | 0.28 | 0.33 | 0.09 | 0.05 |
| α-HCH | 0.35 | 0.18 | 0.11 | 0.20 | 0.06 |
| β-HCH | 0.40 | 0.12 | 0.23 | 0.31 | 0.09 |
| γ-HCH | 0.07 | 0.12 | 0.01 | 0.03 | 0.05 |
| δ-HCH | na | na | na | na | na |
| Heptachlor | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| Heptachlor epoxide | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| Aldrin | <0.02 | <0.02 | <0.02 | <0.02 | <0.02 |
| Dieldrin | <0.02 | <0.02 | <0.02 | <0.02 | <0.02 |
| Endrin | <0.03 | <0.03 | <0.03 | <0.03 | <0.03 |
| Oxychlordane | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| trans-Chlordane | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| cis-Chlordane | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| α - Endosulfan | <0.03 | <0.03 | <0.03 | <0.03 | <0.03 |
| β - Endosulfan | <0.04 | <0.04 | <0.04 | <0.04 | <0.04 |
| Endosulfan Sulfate | <0.03 | <0.03 | <0.03 | <0.03 | <0.03 |
| 2, 4΄-DDE | <0.01 | 0.09 | <0.01 | <0.01 | 0.13 |
| 4, 4΄-DDE | 1.09 | 0.96 | 0.80 | 1.11 | 0.62 |
| DDMU | 0.16 | <0.01 | <0.01 | <0.01 | 0.03 |
| 2, 4΄-DDD | 0.14 | 0.05 | 0.12 | 0.09 | 0.03 |
| 4, 4΄-DDD | 0.59 | 0.44 | 0.31 | 0.47 | 0.24 |
| 2, 4΄-DDT | <0.01 | 0.06 | <0.01 | <0.01 | <0.01 |
| 4, 4΄-DDT | 0.83 | 0.10 | 0.15 | 0.30 | 0.11 |
| trans-Nonachlor | <0.01 | <0.01 | <0.01 | <0.01 | 0.01 |
| cis-Nonachlor | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| Methoxychlor | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| Mirex | <0.02 | <0.02 | <0.02 | <0.02 | <0.02 |

Table 1.2.3.

The content of organochlorine pesticides in bottom sediment samples, μg/kg of dry weight

| Analyte | Sample code: |
| --- | --- |
|  | NOV11 Sed2 RU-11 | NOV11 Sed2 RU-12 | NOV15 Sed1 RU-13 | NOV12 Sed2 KZ-1 | NOV12 Sed1 KZ-2 |
| Hexachlorobenzene | 0.20 | 0.15 | 0.19 | 0.14 | 0.15 |
| α-HCH | <0.01 | <0.01 | 0.05 | 0.05 | 0.06 |
| β-HCH | <0.01 | <0.01 | <0.01 | 0.21 | 0.19 |
| γ-HCH | <0.01 | <0.01 | <0.01 | 0.10 | 0.05 |
| δ-HCH | na | na | na | na | na |
| Heptachlor | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| Heptachlor epoxide | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| Aldrin | <0.02 | <0.02 | <0.02 | <0.02 | <0.02 |
| Dieldrin | <0.02 | <0.02 | <0.02 | <0.02 | <0.02 |
| Endrin | <0.03 | <0.03 | <0.03 | <0.03 | <0.03 |
| Oxychlordane | <0.01 | <0.01 | 0.02 | <0.01 | <0.01 |
| trans-Chlordane | 0.10 | <0.01 | <0.01 | <0.01 | <0.01 |
| cis-Chlordane | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| α - Endosulfan | <0.03 | <0.03 | <0.03 | <0.03 | <0.03 |
| β - Endosulfan | <0.04 | <0.04 | <0.04 | <0.04 | <0.04 |
| Endosulfan Sulfate | <0.03 | <0.03 | <0.03 | <0.03 | <0.03 |
| 2, 4΄-DDE | <0.01 | <0.01 | <0.01 | <0.01 | 0.04 |
| 4, 4΄-DDE | 0.97 | 0.29 | 0.06 | 0.03 | 0.25 |
| DDMU | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| 2, 4΄-DDD | <0.01 | <0.01 | <0.01 | 0.07 | 0.07 |
| 4, 4΄-DDD | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| 2, 4΄-DDT | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| 4, 4΄-DDT | <0.01 | <0.01 | <0.01 | <0.01 | 0.05 |
| trans-Nonachlor | <0.01 | <0.01 | 0.02 | <0.01 | <0.01 |
| cis-Nonachlor | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| Methoxychlor | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| Mirex | <0.02 | <0.02 | <0.02 | <0.02 | <0.02 |

Table 1.2.4.

The content of organochlorine pesticides in bottom sediment samples, μg/kg of dry weight

| Analyte | Sample code: |
| --- | --- |
|  | NOV13 Sed1 KZ-3 | NOV13 Sed2 KZ-4 | NOV13 Sed1 KZ-5 | NOV13 Sed2 KZ-6 | NOV13 Sed1 KZ-7 | NOV13 Sed1 KZ-8 |
| Hexachlorobenzene | 0.15 | 0.09 | 0.19 | 0.16 | 0.10 | 0.21 |
| α-HCH | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| β-HCH | 0.15 | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| γ-HCH | 0.11 | 0.10 | 0.04 | 0.06 | <0.01 | <0.01 |
| δ-HCH | na | na | na | na | na | na |
| Heptachlor | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| Heptachlor epoxide | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| Aldrin | <0.02 | <0.02 | <0.02 | <0.02 | <0.02 | <0.02 |
| Dieldrin | <0.02 | <0.02 | <0.02 | <0.02 | <0.02 | <0.02 |
| Endrin | <0.03 | <0.03 | <0.03 | <0.03 | <0.03 | <0.03 |
| Oxychlordane | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| trans-Chlordane | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| cis-Chlordane | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| α - Endosulfan | <0.03 | <0.03 | <0.03 | <0.03 | <0.03 | <0.03 |
| β - Endosulfan | <0.04 | <0.04 | <0.04 | <0.04 | <0.04 | <0.04 |
| Endosulfan Sulfate | <0.03 | <0.03 | <0.03 | <0.03 | <0.03 | <0.03 |
| 2, 4΄-DDE | 0.03 | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| 4, 4΄-DDE | <0.01 | <0.01 | <0.01 | 0.02 | <0.01 | <0.01 |
| DDMU | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| 2, 4΄-DDD | 0.05 | <0.01 | <0.01 | 0.05 | <0.01 | <0.01 |
| 4, 4΄-DDD | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| 2, 4΄-DDT | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| 4, 4΄-DDT | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| trans-Nonachlor | 0.02 | 0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| cis-Nonachlor | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| Methoxychlor | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 | <0.01 |
| Mirex | <0.02 | <0.02 | <0.02 | <0.02 | <0.02 | <0.02 |

Table 1.2.5.

The content of organochlorine pesticides in bottom sediment samples, μg/kg of dry weight

| Analyte | Sample code: |
| --- | --- |
|  | 7 | 10 | 11 | 14 |
| Hexachlorobenzene | <0.01 | <0.01 | <0.01 | <0.01 |
| α-HCH | 0.01 | 0.01 | 0.05 | 0.02 |
| β-HCH | <0.01 | <0.01 | 0.01 | 0.03 |
| γ-HCH | <0.01 | <0.01 | 0.04 | <0.01 |
| δ-HCH | na | na | na | na |
| Heptachlor | <0.01 | <0.01 | <0.01 | <0.01 |
| Heptachlor epoxide | <0.01 | <0.01 | <0.01 | <0.01 |
| Aldrin | <0.02 | <0.02 | <0.02 | <0.02 |
| Dieldrin | <0.02 | <0.02 | <0.02 | <0.02 |
| Endrin | <0.03 | <0.03 | <0.03 | <0.03 |
| Oxychlordane | <0.01 | <0.01 | <0.01 | <0.01 |
| trans-Chlordane | <0.01 | <0.01 | <0.01 | 0.01 |
| cis-Chlordane | <0.01 | <0.01 | <0.01 | <0.01 |
| α - Endosulfan | <0.03 | <0.03 | <0.03 | <0.03 |
| β - Endosulfan | <0.04 | <0.04 | <0.04 | <0.04 |
| Endosulfan Sulfate | <0.03 | <0.03 | <0.03 | <0.03 |
| 2, 4΄-DDE | 0.03 | 0.01 | 0.04 | <0.01 |
| 4, 4΄-DDE | 0.02 | 0.14 | 0.07 | 0.15 |
| DDMU | <0.01 | <0.01 | <0.01 | 0.02 |
| 2, 4΄-DDD | 0.01 | 0.01 | 0.02 | 0.25 |
| 4, 4΄-DDD | 0.04 | 0.08 | 0.12 | 0.55 |
| 2, 4΄-DDT | <0.01 | <0.01 | <0.01 | 0.03 |
| 4, 4΄-DDT | 0.03 | 0.19 | 0.07 | 0.37 |
| trans-Nonachlor | <0.01 | <0.01 | <0.01 | <0.01 |
| cis-Nonachlor | <0.01 | <0.01 | <0.01 | <0.01 |
| Methoxychlor | <0.01 | <0.01 | <0.01 | <0.01 |
| Mirex | <0.02 | <0.02 | <0.02 | <0.02 |

Table 1.2.6.

The content of organochlorine pesticides in bottom sediment samples, μg/kg of dry weight

| Analyte | Sample code: |
| --- | --- |
|  | 18 | 20 | Lagan-R |
| Hexachlorobenzene | 0.01 | 0.03 | 0.04 |
| α-HCH | 0.02 | 0.02 | 0.02 |
| β-HCH | <0.01 | <0.01 | 0.03 |
| γ-HCH | <0.01 | <0.01 | <0.01 |
| δ-HCH | na | na | na |
| Heptachlor | <0.01 | <0.01 | <0.01 |
| Heptachlor epoxide | <0.01 | <0.01 | <0.01 |
| Aldrin | <0.02 | <0.02 | <0.02 |
| Dieldrin | <0.02 | <0.02 | <0.02 |
| Endrin | <0.03 | <0.03 | <0.03 |
| Oxychlordane | <0.01 | <0.01 | <0.01 |
| trans-Chlordane | <0.01 | 0.04 | 0.04 |
| cis-Chlordane | <0.01 | <0.01 | <0.01 |
| α - Endosulfan | <0.03 | <0.03 | <0.03 |
| β - Endosulfan | <0.04 | <0.04 | <0.04 |
| Endosulfan Sulfate | <0.03 | <0.03 | <0.03 |
| 2, 4΄-DDE | <0.01 | 0.03 | <0.01 |
| 4, 4΄-DDE | 0.22 | 0.09 | 0.06 |
| DDMU | <0.01 | 0.01 | <0.01 |
| 2, 4΄-DDD | 0.08 | 0.02 | <0.01 |
| 4, 4΄-DDD | 0.22 | 0.10 | 0.11 |
| 2, 4΄-DDT | <0.01 | <0.01 | <0.01 |
| 4, 4΄-DDT | 0.28 | 0.07 | 0.32 |
| trans-Nonachlor | <0.01 | <0.01 | <0.01 |
| cis-Nonachlor | <0.01 | <0.01 | <0.01 |
| Methoxychlor | <0.01 | <0.01 | <0.01 |
| Mirex | <0.02 | <0.02 | <0.02 |

1.3. Polycyclic aromatic hydrocarbons (PAHs)

Table 1.3.1.

The content of polycyclic aromatic hydrocarbons in bottom sediment samples, μg/kg

| Compound ↓ | Customer’s sample code: |
| --- | --- |
|  | NOV8 Sed1 RU-1 | NOV8 Sed1 RU-2 | NOV8 Sed1 RU-3 | NOV8 Sed1 RU-4 | NOV10 Sed1 RU-5 |
| Naphthalene | 6.43 | 4.28 | 7.44 | 46.4 | 11.7 |
| 1-Methylnaphthalene | <0.3 | <0.3 | <0.3 | 89.5 | <0.3 |
| 2-Methylnaphthalene | <0.3 | <0.3 | <0.3 | 92.8 | <0.3 |
| C2-Naphthalenes | 60.1 | 26.5 | 26.2 | 198.0 | <0.3 |
| C3-Naphthalenes | <0.3 | <0.3 | <0.3 | 188.0 | <0.3 |
| C4-Naphthalenes | <0.3 | <0.3 | <0.3 | 33.8 | <0.3 |
| Acenaphthylene | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| Acenaphthene | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| Fluorene | <0.3 | <0.3 | <0.3 | 12.2 | <0.3 |
| C1-Fluorenes | <0.3 | <0.3 | <0.3 | 41.4 | <0.3 |
| C2-Fluorenes | <0.3 | <0.3 | <0.3 | 71.7 | <0.3 |
| C3-Fluorenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| Phenanthrene | 5.68 | 5.37 | 6.71 | 72.7 | 17.4 |
| Anthracene | 0.47 | 0.36 | 0.42 | 4.11 | 0.96 |
| C1-Phenanthrenes/Anthracenes | <0.3 | <0.3 | 20.6 | 115.0 | 64.4 |
| C2-Phenanthrenes/Anthracenes | <0.3 | 16.5 | 32.6 | 91.6 | 82.5 |
| C3-Phenanthrenes/Anthracenes | <0.3 | 12.9 | 11.6 | 52.7 | 111.0 |
| C4-Phenanthrenes/Anthracenes | <0.3 | <0.3 | 11.7 | 7.28 | 37.4 |
| Dibenzothiophene | <0.3 | <0.3 | <0.3 | 4.28 | 6.09 |
| C1-Dibenzothiophenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C2-Dibenzothiophenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C3-Dibenzothiophenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C4-Dibenzothiophenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| Fluoranthene | 12.9 | 6.91 | 5.38 | 7.10 | 12.8 |
| Pyrene | 13.7 | 6.18 | 7.33 | 11.3 | 14.1 |
| Retene | <0.3 | <0.3 | <0.3 | 5.6 | <0.3 |
| C1-Fluoranthenes/Pyrenes | <0.3 | <0.3 | <0.3 | 40.8 | 36.0 |
| C2-Fluoranthenes/Pyrenes | <0.3 | <0.3 | <0.3 | 34.0 | <0.3 |
| C3-Fluoranthenes/Pyrenes | <0.3 | <0.3 | <0.3 | 20.2 | <0.3 |
| Benzo(a)anthracene | 5.64 | 2.72 | 5.14 | 12.0 | 8.80 |
| Chrysene | 9.11 | 2.88 | 4.07 | 13.1 | 5.85 |
| C1-Chrysenes | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 |
| C2-Chrysenes | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 |
| C3-Chrysenes | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 |
| Benzo(b+j)fluoranthene | 5.72 | 2.65 | 2.81 | 6.84 | <0.6 |
| Benzo(k)fluoranthene | 5.46 | 3.16 | 2.01 | 4.66 | <0.6 |
| Benzo(e)pyrene | 6.49 | 3.01 | 2.39 | 11.1 | <0.7 |
| Benzo(a)pyrene | <0.7 | <0.7 | <0.7 | <0.7 | <0.7 |
| Perylene | 24.9 | 13.0 | 47.2 | 8.47 | 130.0 |
| Indeno(1,2,3-cd)pyrene | <1.0 | <1.0 | <1.0 | <1.0 | <1.0 |
| Dibenzo(a,h)anthracene | <1.0 | <1.0 | <1.0 | <1.0 | <1.0 |
| Benzo(g,h,i)perylene | <1.0 | <1.0 | <1.0 | <1.0 | <1.0 |

Table 1.3.2.

The content of polycyclic aromatic hydrocarbons in bottom sediment samples, μg/kg

| Compound ↓ | Customer’s sample code: |
| --- | --- |
|  | NOV10 Sed2 RU-6 | NOV11 Sed1 RU-7 | NOV11 Sed1 RU-8 | NOV11 Sed2 RU-9 | NOV11 Sed2 RU-10 |
| Naphthalene | 11.3 | 13.8 | 10.0 | 7.50 | 4.60 |
| 1-Methylnaphthalene | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| 2-Methylnaphthalene | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C2-Naphthalenes | 62.9 | 39.8 | 32.1 | 30.3 | 25.1 |
| C3-Naphthalenes | 142.0 | <0.3 | 51.8 | <0.3 | <0.3 |
| C4-Naphthalenes | 115.0 | <0.3 | <0.3 | <0.30 | <0.3 |
| Acenaphthylene | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| Acenaphthene | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| Fluorene | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C1-Fluorenes | 33.0 | <0.3 | <0.3 | <0.30 | <0.3 |
| C2-Fluorenes | 17.5 | <0.3 | <0.3 | 9.40 | <0.3 |
| C3-Fluorenes | <0.30 | <0.3 | <0.3 | <0.3 | <0.3 |
| Phenanthrene | 21.7 | 9.12 | 9.50 | 10.0 | 5.50 |
| Anthracene | 1.17 | 0.88 | 0.56 | 0.42 | 0.32 |
| C1-Phenanthrenes/Anthracenes | 67.4 | 28.4 | 33.0 | 27.9 | 15.7 |
| C2-Phenanthrenes/Anthracenes | 94.6 | 31.1 | 37.1 | 37.9 | 19.8 |
| C3-Phenanthrenes/Anthracenes | 63.7 | 22.6 | 62.5 | 31.4 | 12.9 |
| C4-Phenanthrenes/Anthracenes | 26.8 | 14.4 | 14.3 | 14.2 | <0.30 |
| Dibenzothiophene | 4.96 | <0.3 | <0.3 | <0.3 | <0.3 |
| C1-Dibenzothiophenes | 4.50 | <0.3 | <0.3 | <0.3 | <0.3 |
| C2-Dibenzothiophenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C3-Dibenzothiophenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C4-Dibenzothiophenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| Fluoranthene | 9.98 | 12.8 | 9.00 | 6.80 | 4.90 |
| Pyrene | 13.3 | 12.2 | 12.5 | 7.10 | 6.30 |
| Retene | 1.6 | <0.3 | <0.3 | <0.3 | <0.3 |
| C1-Fluoranthenes/Pyrenes | 38.4 | <0.3 | <0.3 | 10.1 | <0.3 |
| C2-Fluoranthenes/Pyrenes | 38.9 | <0.3 | <0.3 | <0.3 | <0.3 |
| C3-Fluoranthenes/Pyrenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| Benzo(a)anthracene | 7.53 | 7.03 | <0.5 | 4.00 | <0.5 |
| Chrysene | 10.5 | 10.0 | <0.5 | <0.5 | <0.5 |
| C1-Chrysenes | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 |
| C2-Chrysenes | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 |
| C3-Chrysenes | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 |
| Benzo(b+j)fluoranthene | 3.01 | <0.6 | <0.6 | <0.6 | <0.6 |
| Benzo(k)fluoranthene | 2.88 | <0.6 | <0.6 | <0.6 | <0.6 |
| Benzo(e)pyrene | 5.70 | <0.7 | <0.7 | <0.7 | <0.7 |
| Benzo(a)pyrene | <0.7 | <0.7 | <0.7 | <0.7 | <0.7 |
| Perylene | 163.0 | 69.8 | 59.4 | 38.0 | <1.0 |
| Indeno(1,2,3-cd)pyrene | <1.0 | <1.0 | <1.0 | <1.0 | <1.0 |
| Dibenzo(a,h)anthracene | <1.0 | <1.0 | <1.0 | <1.0 | <1.0 |
| Benzo(g,h,i)perylene | <1.0 | <1.0 | <1.0 | <1.0 | <1.0 |

Table 1.3.3.

The content of polycyclic aromatic hydrocarbons in bottom sediment samples, μg/kg

| Compound ↓ | Customer’s sample code: |
| --- | --- |
|  | NOV11 Sed2 RU-11 | NOV11 Sed2 RU-12 | NOV15 Sed1 RU-13 | NOV12 Sed2 KZ-1 | NOV12 Sed1 KZ-2 |
| Naphthalene | <3.0 | <3.0 | <3.0 | <3.0 | <3.0 |
| 1-Methylnaphthalene | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| 2-Methylnaphthalene | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C2-Naphthalenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C3-Naphthalenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C4-Naphthalenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| Acenaphthylene | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| Acenaphthene | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| Fluorene | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C1-Fluorenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C2-Fluorenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C3-Fluorenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| Phenanthrene | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| Anthracene | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C1-Phenanthrenes/Anthracenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C2-Phenanthrenes/Anthracenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C3-Phenanthrenes/Anthracenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C4-Phenanthrenes/Anthracenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| Dibenzothiophene | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C1-Dibenzothiophenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C2-Dibenzothiophenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C3-Dibenzothiophenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C4-Dibenzothiophenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| Fluoranthene | <0.3 | <0.3 | 8.89 | <0.3 | <0.3 |
| Pyrene | <0.3 | <0.3 | 6.20 | <0.3 | <0.3 |
| Retene | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C1-Fluoranthenes/Pyrenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C2-Fluoranthenes/Pyrenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C3-Fluoranthenes/Pyrenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| Benzo(a)anthracene | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 |
| Chrysene | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 |
| C1-Chrysenes | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 |
| C2-Chrysenes | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 |
| C3-Chrysenes | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 |
| Benzo(b+j)fluoranthene | <0.6 | <0.6 | <0.6 | <0.6 | <0.6 |
| Benzo(k)fluoranthene | <0.6 | <0.6 | <0.6 | <0.6 | <0.6 |
| Benzo(e)pyrene | <0.7 | <0.7 | <0.7 | <0.7 | <0.7 |
| Benzo(a)pyrene | <0.7 | <0.7 | <0.7 | <0.7 | <0.7 |
| Perylene | <1.0 | <1.0 | <1.0 | <1.0 | <1.0 |
| Indeno(1,2,3-cd)pyrene | <1.0 | <1.0 | <1.0 | <1.0 | <1.0 |
| Dibenzo(a,h)anthracene | <1.0 | <1.0 | <1.0 | <1.0 | <1.0 |
| Benzo(g,h,i)perylene | <1.0 | <1.0 | <1.0 | <1.0 | <1.0 |

Table 1.3.4.

The content of polycyclic aromatic hydrocarbons in bottom sediment samples, μg/kg

| Compound ↓ | Customer’s sample code: |
| --- | --- |
|  | NOV13 Sed1 KZ-3 | NOV13 Sed2 KZ-4 | NOV13 Sed1 KZ-5 | NOV13 Sed2 KZ-6 | NOV13 Sed1 KZ-7 | NOV13 Sed1 KZ-8 |
| Naphthalene | <3.0 | <3.0 | <3.0 | <3.0 | <3.0 | <3.0 |
| 1-Methylnaphthalene | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| 2-Methylnaphthalene | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C2-Naphthalenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C3-Naphthalenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C4-Naphthalenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| Acenaphthylene | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| Acenaphthene | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| Fluorene | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C1-Fluorenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C2-Fluorenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C3-Fluorenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| Phenanthrene | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| Anthracene | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C1-Phenanthrenes/Anthracenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C2-Phenanthrenes/Anthracenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C3-Phenanthrenes/Anthracenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C4-Phenanthrenes/Anthracenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| Dibenzothiophene | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C1-Dibenzothiophenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C2-Dibenzothiophenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C3-Dibenzothiophenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C4-Dibenzothiophenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| Fluoranthene | 0.99 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| Pyrene | 2.29 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| Retene | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C1-Fluoranthenes/Pyrenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C2-Fluoranthenes/Pyrenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C3-Fluoranthenes/Pyrenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| Benzo(a)anthracene | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 |
| Chrysene | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 |
| C1-Chrysenes | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 |
| C2-Chrysenes | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 |
| C3-Chrysenes | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 |
| Benzo(b+j)fluoranthene | <0.6 | <0.6 | <0.6 | <0.6 | <0.6 | <0.6 |
| Benzo(k)fluoranthene | <0.6 | <0.6 | <0.6 | <0.6 | <0.6 | <0.6 |
| Benzo(e)pyrene | <0.7 | <0.7 | <0.7 | <0.7 | <0.7 | <0.7 |
| Benzo(a)pyrene | <0.7 | <0.7 | <0.7 | <0.7 | <0.7 | <0.7 |
| Perylene | <1.0 | <1.0 | <1.0 | <1.0 | <1.0 | <1.0 |
| Indeno(1,2,3-cd)pyrene | <1.0 | <1.0 | <1.0 | <1.0 | <1.0 | <1.0 |
| Dibenzo(a,h)anthracene | <1.0 | <1.0 | <1.0 | <1.0 | <1.0 | <1.0 |
| Benzo(g,h,i)perylene | <1.0 | <1.0 | <1.0 | <1.0 | <1.0 | <1.0 |

Table 1.3.5.

The content of polycyclic aromatic hydrocarbons in bottom sediment samples, μg/kg

| Compound ↓ | Customer’s sample code: |
| --- | --- |
|  | 7 | 10 | 11 | 14 | 18 | 20 | Lagan-R |
| Naphthalene | <3.0 | <3.0 | <3.0 | <3.0 | <3.0 | <3.0 | <3.0 |
| 1-Methylnaphthalene | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| 2-Methylnaphthalene | <0.3 | <0.3 | 0.80 | <0.3 | 0.55 | 0.50 | <0.3 |
| C2-Naphthalenes | 4.04 | <0.30 | 12.1 | 2.65 | 4.30 | 3.85 | 1.24 |
| C3-Naphthalenes | <0.3 | <0.3 | <0.3 | 3.7 | 2.96 | <0.3 | <0.3 |
| C4-Naphthalenes | <0.3 | <0.3 | <0.30 | 3.93 | <0.30 | <0.3 | <0.3 |
| Acenaphthylene | <0.3 | <0.3 | 0.36 | 0.44 | 0.69 | <0.3 | <0.3 |
| Acenaphthene | <0.3 | <0.3 | <0.30 | <0.30 | 0.36 | <0.3 | <0.3 |
| Fluorene | <0.3 | <0.3 | 0.31 | <0.30 | 0.43 | <0.3 | <0.3 |
| C1-Fluorenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C2-Fluorenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C3-Fluorenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| Phenanthrene | 0.39 | <0.3 | 1.22 | 0.88 | 2.46 | 0.63 | 0.53 |
| Anthracene | <0.30 | <0.3 | 0.37 | 0.35 | 0.80 | <0.30 | <0.30 |
| C1-Phenanthrenes/Anthracenes | 0.76 | <0.3 | 1.77 | 1.83 | 2.04 | 0.69 | 0.41 |
| C2-Phenanthrenes/Anthracenes | 1.06 | <0.3 | 2.53 | 4.43 | 4.05 | 2.42 | <0.3 |
| C3-Phenanthrenes/Anthracenes | <0.3 | <0.3 | <0.3 | 5.32 | 1.50 | 1.33 | <0.3 |
| C4-Phenanthrenes/Anthracenes | <0.3 | <0.3 | <0.3 | 0.40 | 0.31 | <0.3 | <0.3 |
| Dibenzothiophene | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C1-Dibenzothiophenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C2-Dibenzothiophenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C3-Dibenzothiophenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C4-Dibenzothiophenes | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| Fluoranthene | 0.53 | 3.25 | 1.53 | 2.40 | 7.27 | 0.87 | 0.79 |
| Pyrene | 0.59 | 4.02 | 1.37 | 2.11 | 6.03 | 0.73 | 0.78 |
| Retene | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 | <0.3 |
| C1-Fluoranthenes/Pyrenes | <0.3 | <0.3 | <0.3 | 1.63 | 4.91 | <0.3 | <0.3 |
| C2-Fluoranthenes/Pyrenes | <0.3 | <0.3 | <0.3 | 3.77 | <0.3 | <0.3 | <0.3 |
| C3-Fluoranthenes/Pyrenes | <0.3 | <0.3 | <0.3 | 2.98 | <0.3 | <0.3 | <0.3 |
| Benzo(a)anthracene | <0.5 | <0.5 | <0.5 | <0.5 | 0.99 | <0.5 | <0.5 |
| Chrysene | 0.96 | <0.5 | <0.5 | 2.91 | 6.61 | 1.32 | <0.5 |
| C1-Chrysenes | <0.5 | <0.5 | <0.5 | 1.87 | <0.5 | <0.5 | <0.5 |
| C2-Chrysenes | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 |
| C3-Chrysenes | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 | <0.5 |
| Benzo(b+j)fluoranthene | 0.80 | <0.6 | <0.6 | 1.34 | 3.11 | <0.6 | <0.6 |
| Benzo(k)fluoranthene | <0.6 | <0.6 | <0.6 | 1.28 | 1.49 | <0.6 | <0.6 |
| Benzo(e)pyrene | <0.7 | <0.7 | <0.7 | 1.52 | 2.36 | <0.7 | <0.7 |
| Benzo(a)pyrene | <0.7 | <0.7 | <0.7 | <0.7 | 3.18 | <0.7 | <0.7 |
| Perylene | 2.37 | <1.0 | <1.0 | 6.97 | 3.95 | 3.53 | <1.0 |
| Indeno(1,2,3-cd)pyrene | <1.0 | <1.0 | <1.0 | <1.0 | <1.0 | <1.0 | <1.0 |
| Dibenzo(a,h)anthracene | <1.0 | <1.0 | <1.0 | <1.0 | <1.0 | <1.0 | <1.0 |
| Benzo(g,h,i)perylene | <1.0 | <1.0 | <1.0 | <1.0 | <1.0 | <1.0 | <1.0 |

1.4. Polychlorinated dibenzo-p-dioxins and dibenzofurans

Table 1.4.1

The content of polychlorinated dibenzo-p-dioxins and dibenzofurans in bottom sediment samples

| Sample code: | СЕР 2005 NOV8 Sed1 RU-1 | Matrix | Bottom sediments |
| --- | --- | --- | --- |
| Analyte | Toxicity equivalency factor, TEF | Results of analyses |
|  |  | Concentration, pg/g | Toxic equivalency quantity, TEQ, pg/g |
| 2,3,7,8-TCDD | 1.0 | n.d. | - |
| 1,2,3,7,8-PnCDD | 1.0 | n.d. | - |
| 1,2,3,4,7,8-HcCDD | 0.1 | 0.47 | 0.047 |
| 1,2,3,6,7,8-HcCDD | 0.1 | 0.58 | 0.058 |
| 1,2,3,7,8,9-HcCDD | 0.1 | 0.46 | 0.046 |
| 1,2,3,4,6,7,8-HpCDD | 0.01 | 3.2 | 0.032 |
| OCDD | 0.0001 | 13.5 | 0.00135 |
| 2,3,7,8-TCDF | 0.1 | 0.17 | 0.017 |
| 1,2,3,7,8-PnCDF | 0.05 | 0.26 | 0.013 |
| 2,3,4,7,8-PnCDF | 0.5 | 0.39 | 0.195 |
| 1,2,3,4,7,8-HcCDF | 0.1 | 0.67 | 0.067 |
| 1,2,3,6,7,8-HcCDF | 0.1 | 0.42 | 0.042 |
| 2,3,4,6,7,8-HcCDF | 0.1 | 0.36 | 0.036 |
| 1,2,3,7,8,9-HcCDF | 0.1 | n.d. | - |
| 1,2,3,4,6,7,8-HpCDF | 0.01 | 1.3 | 0.013 |
| 1,2,3,4,7,8,9-HpCDF | 0.01 | n.d. | - |
| OCDF | 0.0001 | n.d. | - |
| Total toxic equivalency quantity, TEQ, pg/g | 0.58 |
| Other TCDDs |  | n.d. |  |
| Other TCDFs |  | 3.25 |  |
| Other PnCDDs |  | n.d. |  |
| Other PnCDFs |  | 3.4 |  |
| Other HcCDDs |  | 4.3 |  |
| Other HcCDFs |  | 1.71 |  |
| Other HpCDDs |  | 3.8 |  |
| Other HpCDFs |  | 0.54 |  |
| Internal standard | Detection limit, pg/g | Recovery, % |
| (13С12)2,3,7,8-TCDD | 0.08 | 86 |
| (13С12)2,3,7,8-TCDF | 0.02 | 90 |
| (13С12)1,2,3,7,8-PnCDD | 0.02 | 93 |
| (13С12)1,2,3,7,8-PnCDF | 0.02 | 100 |
| (13С12)1,2,3,6,7,8-HcCDD | 0.02 | 99 |
| (13С12)1,2,3,6,7,8-HcCDF | 0.02 | 89 |
| (13С12)1,2,3,4,6,7,8-HpCDD | 0.02 | 91 |
| (13С12)1,2,3,4,6,7,8-HpCDF | 0.02 | 96 |
| (13С12)OCDD | 0.02 | 95 |

*n.d. – not detectable (below a detection limit)

Table 1.4.2.

The content of polychlorinated dibenzo-p-dioxins and dibenzofurans in bottom sediment samples

| Sample code: | СЕР 2005 NOV11 Sed1 RU-7 | Matrix | Bottom sediments |
| --- | --- | --- | --- |
| Analyzed component | Toxicity equivalency factor, TEF | Results of analyses |
|  |  | Concentration, pg/g | Toxic equivalency quantity, TEQ, pg/g |
| 2,3,7,8-TCDD | 1.0 | n.d. | - |
| 1,2,3,7,8-PnCDD | 1.0 | n.d. | - |
| 1,2,3,4,7,8-HcCDD | 0.1 | 0.40 | 0.04 |
| 1,2,3,6,7,8-HcCDD | 0.1 | 0.49 | 0.049 |
| 1,2,3,7,8,9-HcCDD | 0.1 | 0.32 | 0.032 |
| 1,2,3,4,6,7,8-HpCDD | 0.01 | 2.2 | 0.022 |
| OCDD | 0.0001 | 9.4 | 0.00094 |
| 2,3,7,8-TCDF | 0.1 | 0.07 | 0.007 |
| 1,2,3,7,8-PnCDF | 0.05 | 0.09 | 0.0045 |
| 2,3,4,7,8-PnCDF | 0.5 | 0.13 | 0.065 |
| 1,2,3,4,7,8-HcCDF | 0.1 | 0.23 | 0.023 |
| 1,2,3,6,7,8-HcCDF | 0.1 | 0.09 | 0.009 |
| 2,3,4,6,7,8-HcCDF | 0.1 | 0.18 | 0.018 |
| 1,2,3,7,8,9-HcCDF | 0.1 | n.d. | - |
| 1,2,3,4,6,7,8-HpCDF | 0.01 | 0.33 | 0.0033 |
| 1,2,3,4,7,8,9-HpCDF | 0.01 | n.d. | - |
| OCDF | 0.0001 | n.d. | - |
| Total toxic equivalency quantity, TEQ, pg/g | 0.28 |
| Other TCDDs |  | n.d. |  |
| Other TCDFs |  | 1.44 |  |
| Other PnCDDs |  | n.d. |  |
| Other PnCDFs |  | 1.25 |  |
| Other HcCDDs |  | 2.2 |  |
| Other HcCDFs |  | 0.46 |  |
| Other HpCDDs |  | 2.34 |  |
| Other HpCDFs |  | 0.16 |  |
| Internal standard | Detection limit, pg/g | Recovery, % |
| (13С12)2,3,7,8-TCDD | 0.08 | 90 |
| (13С12)2,3,7,8-TCDF | 0.02 | 87 |
| (13С12)1,2,3,7,8-PnCDD | 0.02 | 92 |
| (13С12)1,2,3,7,8-PnCDF | 0.02 | 99 |
| (13С12)1,2,3,6,7,8-HcCDD | 0.02 | 89 |
| (13С12)1,2,3,6,7,8-HcCDF | 0.02 | 88 |
| (13С12)1,2,3,4,6,7,8-HpCDD | 0.02 | 90 |
| (13С12)1,2,3,4,6,7,8-HpCDF | 0.02 | 84 |
| (13С12)OCDD | 0.02 | 96 |

*n.d. – not detectable (below a detection limit)

Table 1.4.3.

The content of polychlorinated dibenzo-p-dioxins and dibenzofurans in bottom sediment samples

| Sample code: | СЕР 2005 NOV11 Sed1 RU-8 | Matrix | Bottom sediments |
| --- | --- | --- | --- |
| Analyzed component | Toxicity equivalency factor, TEF | Results of analyses |
|  |  | Concentration, pg/g | Toxic equivalency quantity, TEQ, pg/g |
| 2,3,7,8-TCDD | 1.0 | n.d. | - |
| 1,2,3,7,8-PnCDD | 1.0 | n.d. | - |
| 1,2,3,4,7,8-HcCDD | 0.1 | 0.24 | 0.024 |
| 1,2,3,6,7,8-HcCDD | 0.1 | 0.29 | 0.029 |
| 1,2,3,7,8,9-HcCDD | 0.1 | 0.32 | 0.032 |
| 1,2,3,4,6,7,8-HpCDD | 0.01 | 1.61 | 0.0161 |
| OCDD | 0.0001 | 6.4 | 0.00064 |
| 2,3,7,8-TCDF | 0.1 | 0.13 | 0.013 |
| 1,2,3,7,8-PnCDF | 0.05 | 0.07 | 0.0035 |
| 2,3,4,7,8-PnCDF | 0.5 | 0.17 | 0.085 |
| 1,2,3,4,7,8-HcCDF | 0.1 | 0.19 | 0.019 |
| 1,2,3,6,7,8-HcCDF | 0.1 | 0.09 | 0.009 |
| 2,3,4,6,7,8-HcCDF | 0.1 | 0.10 | 0.010 |
| 1,2,3,7,8,9-HcCDF | 0.1 | n.d. | - |
| 1,2,3,4,6,7,8-HpCDF | 0.01 | 0.30 | 0.003 |
| 1,2,3,4,7,8,9-HpCDF | 0.01 | n.d. | - |
| OCDF | 0.0001 | n.d. | - |
| Total toxic equivalency quantity, TEQ, pg/g | 0.25 |
| Other TCDDs |  | n.d. |  |
| Other TCDFs |  | 1.6 |  |
| Other PnCDDs |  | n.d. |  |
| Other PnCDFs |  | 1.2 |  |
| Other HcCDDs |  | 2.0 |  |
| Other HcCDFs |  | 0.33 |  |
| Other HpCDDs |  | 1.5 |  |
| Other HpCDFs |  | 0.14 |  |
| Internal standard | Detection limit, pg/g | Recovery, % |
| (13С12)2,3,7,8-TCDD | 0.08 | 99 |
| (13С12)2,3,7,8-TCDF | 0.02 | 90 |
| (13С12)1,2,3,7,8-PnCDD | 0.02 | 92 |
| (13С12)1,2,3,7,8-PnCDF | 0.02 | 98 |
| (13С12)1,2,3,6,7,8-HcCDD | 0.02 | 89 |
| (13С12)1,2,3,6,7,8-HcCDF | 0.02 | 90 |
| (13С12)1,2,3,4,6,7,8-HpCDD | 0.02 | 97 |
| (13С12)1,2,3,4,6,7,8-HpCDF | 0.02 | 89 |
| (13С12)OCDD | 0.02 | 93 |

*n.d. – not detectable (below a detection limit)

Table 1.4.4.

The content of polychlorinated dibenzo-p-dioxins and dibenzofurans in bottom sediment samples

| Sample code: | СЕР 2005 NOV12 Sed2 KZ-1 | Matrix | Bottom sediments |
| --- | --- | --- | --- |
| Analyzed component | Toxicity equivalency factor, TEF | Results of analyses |
|  |  | Concentration, pg/g | Toxic equivalency quantity, TEQ, pg/g |
| 2,3,7,8-TCDD | 1.0 | n.d. | - |
| 1,2,3,7,8-PnCDD | 1.0 | n.d. | - |
| 1,2,3,4,7,8-HcCDD | 0.1 | n.d. | - |
| 1,2,3,6,7,8-HcCDD | 0.1 | n.d. | - |
| 1,2,3,7,8,9-HcCDD | 0.1 | n.d. | - |
| 1,2,3,4,6,7,8-HpCDD | 0.01 | 0.11 | 0.0011 |
| OCDD | 0.0001 | 0.15 | 0.000015 |
| 2,3,7,8-TCDF | 0.1 | 0.02 | 0.002 |
| 1,2,3,7,8-PnCDF | 0.05 | n.d. | - |
| 2,3,4,7,8-PnCDF | 0.5 | 0.04 | 0.02 |
| 1,2,3,4,7,8-HcCDF | 0.1 | 0.03 | 0.003 |
| 1,2,3,6,7,8-HcCDF | 0.1 | 0.02 | 0.002 |
| 2,3,4,6,7,8-HcCDF | 0.1 | 0.03 | 0.003 |
| 1,2,3,7,8,9-HcCDF | 0.1 | n.d. | - |
| 1,2,3,4,6,7,8-HpCDF | 0.01 | n.d. | - |
| 1,2,3,4,7,8,9-HpCDF | 0.01 | n.d. | - |
| OCDF | 0.0001 | n.d. | - |
| Total toxic equivalency quantity, TEQ, pg/g | 0.031 |
| Other TCDDs |  | n.d. |  |
| Other TCDFs |  | 1.4 |  |
| Other PnCDDs |  | n.d. |  |
| Other PnCDFs |  | 0.19 |  |
| Other HcCDDs |  | n.d. |  |
| Other HcCDFs |  | 0.07 |  |
| Other HpCDDs |  | n.d. |  |
| Other HpCDFs |  | n.d. |  |
| Internal standard | Detection limit, pg/g | Recovery, % |
| (13С12)2,3,7,8-TCDD | 0.08 | 91 |
| (13С12)2,3,7,8-TCDF | 0.02 | 89 |
| (13С12)1,2,3,7,8-PnCDD | 0.02 | 99 |
| (13С12)1,2,3,7,8-PnCDF | 0.02 | 94 |
| (13С12)1,2,3,6,7,8-HcCDD | 0.02 | 88 |
| (13С12)1,2,3,6,7,8-HcCDF | 0.02 | 90 |
| (13С12)1,2,3,4,6,7,8-HpCDD | 0.02 | 98 |
| (13С12)1,2,3,4,6,7,8-HpCDF | 0.02 | 100 |
| (13С12)OCDD | 0.02 | 99 |

*n.d. – not detectable (below a detection limit)

Table 1.4.5.

The content of polychlorinated dibenzo-p-dioxins and dibenzofurans in bottom sediment samples

| Sample code: | СЕР 2005 NOV12 Sed1 KZ-3 | Matrix | Bottom sediments |
| --- | --- | --- | --- |
| Analyzed component | Toxicity equivalency factor, TEF | Results of analyses |
|  |  | Concentration, pg/g | Toxic equivalency quantity, TEQ, pg/g |
| 2,3,7,8-TCDD | 1.0 | n.d. | - |
| 1,2,3,7,8-PnCDD | 1.0 | n.d. | - |
| 1,2,3,4,7,8-HcCDD | 0.1 | n.d. | - |
| 1,2,3,6,7,8-HcCDD | 0.1 | n.d. | - |
| 1,2,3,7,8,9-HcCDD | 0.1 | n.d. | - |
| 1,2,3,4,6,7,8-HpCDD | 0.01 | 0.44 | 0.0044 |
| OCDD | 0.0001 | 1.4 | 0.00014 |
| 2,3,7,8-TCDF | 0.1 | 0.04 | 0.004 |
| 1,2,3,7,8-PnCDF | 0.05 | 0.03 | 0.0015 |
| 2,3,4,7,8-PnCDF | 0.5 | 0.08 | 0.04 |
| 1,2,3,4,7,8-HcCDF | 0.1 | 0.07 | 0.007 |
| 1,2,3,6,7,8-HcCDF | 0.1 | 0.04 | 0.004 |
| 2,3,4,6,7,8-HcCDF | 0.1 | 0.03 | 0.003 |
| 1,2,3,7,8,9-HcCDF | 0.1 | n.d. | - |
| 1,2,3,4,6,7,8-HpCDF | 0.01 | n.d. | - |
| 1,2,3,4,7,8,9-HpCDF | 0.01 | n.d. | - |
| OCDF | 0.0001 | n.d. | - |
| Total toxic equivalency quantity, TEQ, pg/g | 0.065 |
| Other TCDDs |  | n.d. |  |
| Other TCDFs |  | 0.46 |  |
| Other PnCDDs |  | n.d. |  |
| Other PnCDFs |  | 0.37 |  |
| Other HcCDDs |  | n.d. |  |
| Other HcCDFs |  | 0.11 |  |
| Other HpCDDs |  | 0.79 |  |
| Other HpCDFs |  | n.d. |  |
| Internal standard | Detection limit, pg/g | Recovery, % |
| (13С12)2,3,7,8-TCDD | 0.08 | 88 |
| (13С12)2,3,7,8-TCDF | 0.02 | 90 |
| (13С12)1,2,3,7,8-PnCDD | 0.02 | 99 |
| (13С12)1,2,3,7,8-PnCDF | 0.02 | 92 |
| (13С12)1,2,3,6,7,8-HcCDD | 0.02 | 101 |
| (13С12)1,2,3,6,7,8-HcCDF | 0.02 | 95 |
| (13С12)1,2,3,4,6,7,8-HpCDD | 0.02 | 89 |
| (13С12)1,2,3,4,6,7,8-HpCDF | 0.02 | 90 |
| (13С12)OCDD | 0.02 | 97 |

*n.d. – not detectable (below a detection limit)

1.5. Planar (non-ortho and mono-ortho substituted) PCBs

Table 1.5.1

The results of bottom sediment sample analysis for the content of planar PCB congeners, μg/kg

| IUPAC number of PCB congener | TEQ | Sample code |
| --- | --- | --- |
|  |  | NOV8 Sed1 RU-1 | NOV11 Sed1 RU-7 | NOV11 Sed1 RU-8 |
| #77 | 0.0001 | n.d. | n.d. | n.d. |
| #81 | 0.0001 | n.d. | n.d. | n.d. |
| #105 | 0.0001 | 0.06 | n.d. | 0.07 |
| #114 | 0.0005 | n.d. | n.d. | n.d. |
| #118 | 0.0001 | 0.12 | n.d. | 0.09 |
| #123 | 0.0001 | n.d. | n.d. | n.d. |
| #126 | 0.1 | n.d. | n.d. | n.d. |
| #156 | 0.0005 | 0.06 | n.d. | n.d. |
| #157 | 0.0005 | 0.05 | n.d. | n.d. |
| #167 | 0.00001 | n.d. | n.d. | n.d. |
| #169 | 0.01 | n.d. | n.d. | n.d. |
| #170 | - | n.d. | n.d. | n.d. |
| #180 | - | n.d. | n.d. | n.d. |
| #189 | 0.0001 | n.d. | n.d. | n.d. |
| Total toxic equivalency quantity, TEQ, ng/kg |  | 0.073 | n.d. | 0.016 |
| Recovery of surrogate internal standards, % |
| 13С12#77 |  | 72 | 74 | 77 |
| 13С12#81 |  | 71 | 61 | 99 |
| 13С12#105 |  | 76 | 68 | 70 |
| 13С12#114 |  | 81 | 80 | 97 |
| 13С12#118 |  | 86 | 81 | 97 |
| 13С12#123 |  | 86 | 81 | 95 |
| 13С12#126 |  | 57 | 38 | 40 |
| 13С12#156 |  | 92 | 102 | 100 |
| 13С12#157 |  | 89 | 98 | 86 |
| 13С12#167 |  | 88 | 92 | 90 |
| 13С12#169 |  | 77 | 64 | 70 |
| 13С12#170 |  | 84 | 98 | 96 |
| 13С12#180 |  | 82 | 83 | 115 |
| 13С12#189 |  | 84 | 80 | 82 |

n.d. – below a detection limit

Table 1.5.2.

The results of bottom sediment sample analysis for the content of planar PCB congeners, μg/kg

| IUPAC number of PCB congener | TEQ | Sample code |
| --- | --- | --- |
|  |  | NOV12 Sed2 KZ-1 | NOV13 Sed1 KZ-3 |  |
| #77 | 0.0001 | n.d. | n.d. |  |
| #81 | 0.0001 | n.d. | n.d. |  |
| #105 | 0.0001 | 0.18 | 0.12 |  |
| #114 | 0.0005 | n.d. | n.d. |  |
| #118 | 0.0001 | 0.26 | 0.08 |  |
| #123 | 0.0001 | n.d. | n.d. |  |
| #126 | 0.1 | n.d. | n.d. |  |
| #156 | 0.0005 | 0.04 | n.d. |  |
| #157 | 0.0005 | 0.05 | n.d. |  |
| #167 | 0.00001 | n.d. | n.d. |  |
| #169 | 0.01 | n.d. | n.d. |  |
| #170 | - | n.d. | n.d. |  |
| #180 | - | n.d. | n.d. |  |
| #189 | 0.0001 | n.d. | n.d. |  |
| Total toxic equivalency quantity, TEQ, ng/kg |  | 0.089 | 0.02 |  |
| Recovery of surrogate internal standards, % |
| 13С12#77 |  | 77 | 77 |  |
| 13С12#81 |  | 72 | 67 |  |
| 13С12#105 |  | 89 | 83 |  |
| 13С12#114 |  | 68 | 77 |  |
| 13С12#118 |  | 83 | 85 |  |
| 13С12#123 |  | 86 | 88 |  |
| 13С12#126 |  | 97 | 67 |  |
| 13С12#156 |  | 87 | 67 |  |
| 13С12#157 |  | 72 | 71 |  |
| 13С12#167 |  | 74 | 74 |  |
| 13С12#169 |  | 68 | 66 |  |
| 13С12#170 |  | 88 | 82 |  |
| 13С12#180 |  | 83 | 83 |  |
| 13С12#189 |  | 68 | 78 |  |

n.d. – below a detection limit

1.6. Aroclor 1254 and Aroclor 1260

Table 1.6.1.

The content of Aroclors in bottom sediment samples, μg/kg of dry weight

| Analyte | Sample code: |
| --- | --- |
|  | NOV8 Sed1 RU-1 | NOV8 Sed1 RU-2 | NOV8 Sed1 RU-3 | NOV8 Sed1 RU-4 | NOV8 Sed1 RU-4 D | NOV10 Sed1 RU-5 |
| Aroclor 1254 | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| Aroclor 1260 | 1.26 | 0.38 | <0.10 | <0.10 | <0.10 | <0.10 |

Table 1.6.2.

The content of Aroclors in bottom sediment samples, μg/kg of dry weight

| Analyte | Sample code: |
| --- | --- |
|  | NOV10 Sed2 RU-6 | NOV11 Sed1 RU-7 | NOV11 Sed1 RU-8 | NOV11 Sed2 RU-9 | NOV11 Sed2 RU-10 |
| Aroclor 1254 | <0.10 | <0.10 | <0.10 | <0.10 | <0.10 |
| Aroclor 1260 | <0.10 | <0.10 | <0.10 | 0.12 | 0.12 |

Table 1.6.3

The content of Aroclors in bottom sediment samples, μg/kg of dry weight

| Analyte | Sample code: |
| --- | --- |
|  | NOV11 Sed2 RU-11 | NOV11 Sed2 RU-12 | NOV15 Sed1 RU-13 | NOV12 Sed2 KZ-1 | NOV12 Sed1 KZ-2 |
| Aroclor 1254 | 0.60 | <0.10 | 1.32 | 1.28 | 1.28 |
| Aroclor 1260 | 0.15 | <0.10 | <0.10 | 0.25 | 0.14 |

Table 1.6.4.

The content of Aroclors in bottom sediment samples, μg/kg of dry weight

| Analyte | Sample code: |
| --- | --- |
|  | NOV13 Sed1 KZ-3 | NOV13 Sed2 KZ-4 | NOV13 Sed1 KZ-5 | NOV13 Sed2 KZ-6 | NOV13 Sed1 KZ-7 | NOV13 Sed1 KZ-8 |
| Aroclor 1254 | <0.10 | 1.20 | 0.58 | 1.26 | 1.48 | 0.63 |
| Aroclor 1260 | <0.10 | 1.1 | 0.1 | 0.35 | 1.3 | 0.42 |

Table 1.6.5.

The content of Aroclors in bottom sediment samples, μg/kg of dry weight

| Analyte | Sample code: |
| --- | --- |
|  | 7 | 10 | 11 | 14 | 18 | 20 |
| Aroclor 1254 | <0.10 | <0.10 | 0.18 | 0.18 | 0.15 | 0.17 |
| Aroclor 1260 | <0.10 | <0.10 | <0.10 | 0.15 | 0.35 | <0.10 |

Table 1.6.6.

The content of Aroclors in bottom sediment samples, μg/kg of dry weight

| Analyte | Sample code: |
| --- | --- |
|  | Lagan-R |
| Aroclor 1254 | 12.2 |
| Aroclor 1260 | 7.5 |

ANNEX 2

Results of quality control

2.1. Polychlorinated biphenyls

Table 2.1.1

The results of quality control for the analysis of bottom sediment samples for CAS-PCB+CLP-06S polychlorinated biphenyl content

| PCB congener ↓ | Detection limit, μg/kg | Duplicate divergence (NOV8 Sed1 RU-4), % | PBS-06 blank sample, μg/kg | ЕС-5 certified sample (A Humber River Sediment for Toxic Organics) |
| --- | --- | --- | --- | --- |
|  |  |  |  | Determined, μg/kg | Certified value, μg/kg |
| 8[CL2] | 0.05 | 18 | <0.05 | ─ | ─ |
| 18[CL3] | 0.10 | ─ | 0.12 | 2.90 | 3.0±1.1 |
| 16[CL3] | 0.05 | ─ | <0.05 | ─ | ─ |
| 26[CL3] | 0.15 | ─ | 0.16 | ─ | ─ |
| 25[CL3] | 0.05 | ─ | <0.05 | ─ | ─ |
| (31+28)[CL3] | 0.10 | ─ | <0.10 | 5.20 | 5.3±1.3 |
| 33[CL3] | 0.05 | ─ | <0.05 | ─ | ─ |
| 52[CL4] | 0.15 | ─ | <0.15 | 10.9 | 13.3±4.1 |
| 49[CL4] | 0.15 | ─ | 0.18 | ─ | ─ |
| 47[CL4] | 0.05 | 14 | <0.05 | ─ | ─ |
| 44[CL4] | 0.05 | ─ | <0.05 | 7.03 | 7.3±2.4 |
| 37[CL3] | 0.05 | ─ | <0.05 | ─ | ─ |
| 41[CL4] | 0.05 | ─ | <0.05 | ─ | ─ |
| 74[CL4] | 0.10 | ─ | <0.10 | ─ | ─ |
| 70[CL4] | 0.10 | ─ | 0.19 | ─ | ─ |
| 66[CL4] | 0.10 | ─ | 0.08 | ─ | ─ |
| 95[CL5] | 0.10 | ─ | 0.06 | ─ | ─ |
| 60[CL4] | 0.10 | ─ | 0.10 | ─ | ─ |
| 101[CL5] | 0.10 | ─ | 0.26 | 22.5 | 24.6±6.0 |
| 99[CL5] | 0.10 | ─ | 0.11 | ─ | ─ |
| 97[CL5] | 0.10 | ─ | 0.06 | ─ | ─ |
| 87[CL5] | 0.10 | ─ | 0.05 | 8.63 | 9.6±1.4 |
| 110[CL5] | 0.10 | ─ | 0.14 | 33.0 | 33.3±11.9 |
| 151[CL6] | 0.05 | ─ | 0.07 | 6.98 | 8.4±2.8 |
| 135[CL6] | 0.05 | ─ | <0.05 | ─ | ─ |
| 118[CL5] | 0.10 | ─ | 0.26 | ─ | 17.0±7.4 |
| 149[CL6] | 0.05 | ─ | <0.05 | ─ | ─ |
| 146[CL6] | 0.05 | ─ | 0.06 | 22.6 | 27.2±5.5 |
| 153[CL6] | 0.05 | ─ | 0.14 | 7.23 | 7.6±2.7 |
| 105[CL5] | 0.05 | ─ | <0.05 | 9.64 | 8.4±1.9 |
| 141[CL6] | 0.10 | ─ | 0.12 | 25.3 | 28.6±9.1 |
| 138[CL6] | 0.10 | ─ | <0.10 | ─ | ─ |
| 126[CL5] | 0.05 | ─ | <0.05 | ─ | ─ |
| 187[CL7] | 0.05 | ─ | <0.05 | 6.09 | 7.2±2.8 |
| 183[CL7] | 0.10 | ─ | 0.12 | 5.19 | 5.5±2.3 |
| (128+167)[CL6] | 0.05 | ─ | <0.05 | ─ | ─ |
| 174[CL7] | 0.05 | ─ | <0.05 | ─ | ─ |
| 177[CL7] | 0.10 | ─ | <0.10 | ─ | ─ |
| 171[CL7] | 0.10 | ─ | <0.10 | 5.22 | 5.7±2.7 |
| 201[CL8] | 0.05 | ─ | <0.05 | 20.1 | 22.3±7.6 |
| 180[CL7] | 0.05 | ─ | <0.05 | 11.0 | 10.1±1.6 |
| 170[CL7] | 0.05 | ─ | <0.05 | ─ | ─ |
| 199[CL8] | 0.05 | ─ | <0.05 | ─ | ─ |
| (196+203)[CL8] | 0.07 | ─ | <0.07 | ─ | ─ |
| 189[CL7] | 0.07 | ─ | <0.07 | ─ | ─ |
| 195[CL8] | 0.07 | ─ | <0.07 | 9.63 | 8.1±10.1 |
| 194[CL8] | 0.07 | ─ | <0.07 | 2.22 | 2.2±0.9 |
| 206[CL9] | 0.07 | ─ | <0.07 | 1.02 | 1.2±0.9 |
| 209[CL10] | 0.07 | - | <0.07 | 2.2 | 2.7 ±1.2 |

Table 2.1.2.

The results of quality control for the analysis of bottom sediment samples for CAS-PCB+CLP-27S polychlorinated biphenyl content

| PCB congener ↓ | Detection limit, μg/kg | Duplicate divergence (20), % | PBS-27 blank sample, μg/kg | ЕС-5 certified sample (A Humber River Sediment for Toxic Organics) |
| --- | --- | --- | --- | --- |
|  |  |  |  | Determined, μg/kg | Certified value, μg/kg |
| 8[CL2] | 0.05 | 10 | <0.05 | ─ | ─ |
| 18[CL3] | 0.10 | ─ | 0.07 | 2.92 | 3.0±1.1 |
| 16[CL3] | 0.05 | ─ | <0.05 | ─ | ─ |
| 26[CL3] | 0.15 | ─ | <0.15 | ─ | ─ |
| 25[CL3] | 0.05 | ─ | <0.05 | ─ | ─ |
| (31+28)[CL3] | 0.10 | ─ | <0.10 | 5.36 | 5.3±1.3 |
| 33[CL3] | 0.05 | ─ | <0.05 | ─ | ─ |
| 52[CL4] | 0.15 | ─ | <0.15 | 15.0 | 13.3±4.1 |
| 49[CL4] | 0.15 | ─ | 0.09 | ─ | ─ |
| 47[CL4] | 0.05 | ─ | 0.05 | ─ | ─ |
| 44[CL4] | 0.05 | ─ | <0.05 | 5.93 | 7.3±2.4 |
| 37[CL3] | 0.05 | ─ | <0.05 | ─ | ─ |
| 41[CL4] | 0.05 | ─ | <0.05 | ─ | ─ |
| 74[CL4] | 0.10 | ─ | <0.10 | ─ | ─ |
| 70[CL4] | 0.10 | ─ | <0.10 | ─ | ─ |
| 66[CL4] | 0.10 | ─ | <0.10 | ─ | ─ |
| 95[CL5] | 0.10 | ─ | <0.10 | ─ | ─ |
| 60[CL4] | 0.10 | ─ | <0.10 | ─ | ─ |
| 101[CL5] | 0.10 | ─ | <0.10 | 23.5 | 24.6±6.0 |
| 99[CL5] | 0.10 | ─ | <0.10 | ─ | ─ |
| 97[CL5] | 0.10 | ─ | <0.10 | ─ | ─ |
| 87[CL5] | 0.10 | ─ | <0.10 | 9.03 | 9.6±1.4 |
| 110[CL5] | 0.10 | ─ | <0.10 | 36.4 | 33.3±11.9 |
| 151[CL6] | 0.05 | ─ | <0.05 | 8.25 | 8.4±2.8 |
| 135[CL6] | 0.05 | ─ | <0.05 | ─ | ─ |
| 118[CL5] | 0.10 | 7 | 0.12 | 20.1 | 17.0±7.4 |
| 149[CL6] | 0.05 | ─ | <0.05 | ─ | ─ |
| 146[CL6] | 0.05 | ─ | <0.05 | 28.2 | 27.2±5.5 |
| 153[CL6] | 0.05 | 25 | <0.05 | 5.29 | 7.6±2.7 |
| 105[CL5] | 0.05 | ─ | <0.05 | 7.69 | 8.4±1.9 |
| 141[CL6] | 0.10 | ─ | <0.10 | 23.6 | 28.6±9.1 |
| 138[CL6] | 0.10 | ─ | <0.10 | ─ | ─ |
| 126[CL5] | 0.05 | ─ | <0.05 | ─ | ─ |
| 187[CL7] | 0.05 | ─ | <0.05 | 6.54 | 7.2±2.8 |
| 183[CL7] | 0.10 | ─ | <0.10 | 5.04 | 5.5±2.3 |
| (128+167)[CL6] | 0.05 | ─ | <0.05 | ─ | ─ |
| 174[CL7] | 0.05 | ─ | <0.05 | ─ | ─ |
| 177[CL7] | 0.10 | ─ | <0.10 | ─ | ─ |
| 171[CL7] | 0.10 | ─ | <0.10 | 3.95 | 5.7±2.7 |
| 201[CL8] | 0.05 | ─ | <0.05 | 20.9 | 22.3±7.6 |
| 180[CL7] | 0.05 | ─ | <0.05 | 9.60 | 10.1±1.6 |
| 170[CL7] | 0.05 | ─ | <0.05 | ─ | ─ |
| 199[CL8] | 0.05 | ─ | <0.05 | ─ | ─ |
| (196+203)[CL8] | 0.07 | ─ | <0.07 | ─ | ─ |
| 189[CL7] | 0.07 | ─ | <0.07 | ─ | ─ |
| 195[CL8] | 0.07 | ─ | <0.07 | 11.2 | 8.1±10.1 |
| 194[CL8] | 0.07 | ─ | <0.07 | 2.00 | 2.2±0.9 |
| 206[CL9] | 0.07 | ─ | <0.07 | 1.02 | 1.2±0.9 |
| 209[CL10] | 0.07 | - | <0.07 | 1.9 | 2.7 ±1.2 |

Table 2.1.3

Recovery of surrogate standards, %

| PCB congener | Customer’s sample code: |
| --- | --- |
|  | NOV8 Sed1 RU-1 | NOV8 Sed1 RU-2 | NOV8 Sed1 RU-3 | NOV8 Sed1 RU-4 | NOV10 Sed1 RU-5 |
| # 28- C13 | 79 | 87 | 83 | 87 | 90 |
| # 52- C13 | 96 | 90 | 91 | 79 | 80 |
| # 101- C13 | 81 | 103 | 88 | 88 | 79 |
| # 138- C13 | 87 | 85 | 89 | 92 | 84 |
| # 153- C13 | 101 | 96 | 79 | 78 | 93 |
| # 180- C13 | 72 | 74 | 68 | 78 | 82 |
| # 209- C13 | 76 | 65 | 67 | 62 | 66 |

Table 2.1.4

Recovery of surrogate standards, %

| PCB congener ↓ | Customer’s sample code: |
| --- | --- |
|  | NOV10 Sed2 RU-6 | NOV11 Sed1 RU-7 | NOV11 Sed1 RU-8 | NOV11 Sed2 RU-9 | NOV11 Sed2 RU-10 |
| # 28- C13 | 81 | 82 | 82 | 77 | 78 |
| # 52- C13 | 86 | 84 | 101 | 103 | 97 |
| # 101- C13 | 76 | 85 | 92 | 89 | 84 |
| # 138- C13 | 76 | 80 | 89 | 94 | 84 |
| # 153- C13 | 79 | 80 | 87 | 87 | 82 |
| # 180- C13 | 65 | 74 | 78 | 78 | 62 |
| # 209- C13 | 63 | 62 | 73 | 70 | 59 |

Table 2.1.5

Recovery of surrogate standards, %

| PCB congener ↓ | Customer’s sample code: |
| --- | --- |
|  | NOV11 Sed2 RU-11 | NOV11 Sed2 RU-12 | NOV15 Sed1 RU-13 | NOV12 Sed2 KZ-1 | NOV12 Sed1 KZ-2 |
| # 28- C13 | 86 | 85 | 85 | 89 | 81 |
| # 52- C13 | 84 | 80 | 78 | 94 | 80 |
| # 101- C13 | 87 | 85 | 76 | 92 | 84 |
| # 138- C13 | 80 | 86 | 75 | 81 | 81 |
| # 153- C13 | 82 | 83 | 78 | 87 | 79 |
| # 180- C13 | 69 | 70 | 62 | 64 | 67 |
| # 209- C13 | 69 | 65 | 58 | 62 | 66 |

Table 2.1.6

Recovery of surrogate standards, %

| PCB congener ↓ | Customer’s sample code: |
| --- | --- |
|  | NOV13 Sed1 KZ-3 | NOV13 Sed2 KZ-4 | NOV13 Sed1 KZ-5 | NOV13 Sed2 KZ-6 | NOV13 Sed1 KZ-7 | NOV13 Sed1 KZ-8 |
| # 28- C13 | 86 | 84 | 76 | 104 | 85 | 86 |
| # 52- C13 | 91 | 87 | 78 | 106 | 86 | 101 |
| # 101- C13 | 91 | 89 | 75 | 97 | 96 | 98 |
| # 138- C13 | 93 | 76 | 73 | 94 | 84 | 95 |
| # 153- C13 | 88 | 84 | 68 | 102 | 87 | 96 |
| # 180- C13 | 78 | 65 | 62 | 79 | 69 | 70 |
| # 209- C13 | 73 | 67 | 57 | 80 | 66 | 70 |

Table 2.1.7

Recovery of surrogate standards, %

| PCB congener ↓ | Customer’s sample code: |
| --- | --- |
|  | 7 | 10 | 11 | 14 |
| # 28- C13 | 84 | 89 | 80 | 89 |
| # 52- C13 | 87 | 103 | 81 | 89 |
| # 101- C13 | 85 | 96 | 75 | 78 |
| # 138- C13 | 90 | 83 | 79 | 83 |
| # 153- C13 | 92 | 85 | 78 | 87 |
| # 180- C13 | 66 | 80 | 70 | 67 |
| # 209- C13 | 59 | 74 | 67 | 68 |

Table 2.1.8

Recovery of surrogate standards, %

| PCB congener ↓ | Customer’s sample code: |
| --- | --- |
|  | 18 | 20 | Lagan-R |
| # 28- C13 | 89 | 85 | 104 |
| # 52- C13 | 89 | 82 | 106 |
| # 101- C13 | 94 | 85 | 98 |
| # 138- C13 | 90 | 79 | 92 |
| # 153- C13 | 98 | 81 | 96 |
| # 180- C13 | 73 | 68 | 71 |
| # 209- C13 | 58 | 59 | 75 |

2.2. Organochlorine pesticides

Table 2.2.1.

The results of quality control for the analysis of bottom sediment samples for CAS-PCB+CLP-06S organochlorine pesticide content

| Analyte | Detection limit, μg/kg | Duplicate divergence (NOV8 Sed1 RU-4), % | PBS-06 blank sample, μg/kg | Lot No.324 |
| --- | --- | --- | --- | --- |
|  |  |  |  | Determined, μg/kg | Certified value, μg/kg | Allowable range, μg/kg |
| Hexachlorobenzene | 0.01 | 22 | 0.09 | ─ | ─ | ─ |
| α-HCH | 0.01 | 18 | <0.01 | ─ | ─ | ─ |
| β-HCH | 0.01 | 14 | <0.01 | 136.0 | 145 | 25-213 |
| γ-HCH | 0.01 | 11 | <0.01 | 193.0 | 219 | 70-273 |
| Heptachlor | 0.01 | ─ | <0.01 | 206.0 | 297 | 101-330 |
| Heptachlor epoxide | 0.01 | ─ | <0.01 | ─ | ─ | ─ |
| Aldrin | 0.02 | ─ | <0.02 | 222.0 | 246 | 103-300 |
| Dieldrin | 0.02 | ─ | <0.02 | 82.9 | 101 | 36-147 |
| Oxychlordane | 0.01 | ─ | <0.01 | ─ | ─ | ─ |
| trans-Chlordane | 0.01 | ─ | 0.16 | ─ | ─ | ─ |
| cis-Chlordane | 0.01 | ─ | <0.01 | ─ | ─ | ─ |
| 2, 4΄-DDE | 0.01 | 16 | <0.01 | ─ | ─ | ─ |
| 4, 4΄-DDE | 0.01 | 19 | <0.01 | 463.0 | 455 | 137-660 |
| 2, 4΄-DDD | 0.01 | 21 | 0.06 | ─ | ─ | ─ |
| 4, 4΄-DDD | 0.01 | 10 | <0.01 | 126.0 | 334 | 104-471 |
| 2, 4΄-DDT | 0.01 | 21 | <0.01 | ─ | ─ | ─ |
| 4, 4΄-DDT | 0.01 | 18 | <0.01 | 305.0 | 297 | 72-459 |
| trans-Nonachlor | 0.01 | ─ | <0.01 | ─ | ─ | ─ |
| cis-Nonachlor | 0.01 | ─ | <0.01 | ─ | ─ | ─ |
| Mirex | 0.02 | ─ | <0.02 | ─ | ─ | ─ |

Table 2.2.2.

The results of quality control for the analysis of bottom sediment samples for CAS-PCB+CLP-12S organochlorine pesticide content

| Analyte | Detection limit, μg/kg | Duplicate divergence (NOV12 Sed1 KZ-2), % | PBS-12 blank sample, μg/kg | Lot No.324 |
| --- | --- | --- | --- | --- |
|  |  |  |  | Determined, μg/kg | Certified value, μg/kg | Allowable range, μg/kg |
| Hexachlorobenzene | 0.01 | 17 | <0.01 | ─ | ─ | ─ |
| α-HCH | 0.01 | 20 | <0.01 | ─ | ─ | ─ |
| β-HCH | 0.01 | 15 | <0.01 | 123.0 | 145 | 25-213 |
| γ-HCH | 0.01 | 1 | <0.01 | 122.0 | 219 | 70-273 |
| Heptachlor | 0.01 | ─ | <0.01 | 186.0 | 297 | 101-330 |
| Heptachlor epoxide | 0.01 | ─ | <0.01 | ─ | ─ | ─ |
| Aldrin | 0.02 | ─ | <0.02 | 220.0 | 246 | 103-300 |
| Dieldrin | 0.02 | ─ | <0.02 | 97.8 | 101 | 36-147 |
| Oxychlordane | 0.01 | ─ | <0.01 | ─ | ─ | ─ |
| trans-Chlordane | 0.01 | ─ | <0.01 | ─ | ─ | ─ |
| cis-Chlordane | 0.01 | ─ | <0.01 | ─ | ─ | ─ |
| 2, 4΄-DDE | 0.01 | 3 | <0.01 | ─ | ─ | ─ |
| 4, 4΄-DDE | 0.01 | 16 | <0.01 | 563.0 | 455 | 137-660 |
| 2, 4΄-DDD | 0.01 | 10 | <0.01 | ─ | ─ | ─ |
| 4, 4΄-DDD | 0.01 | ─ | <0.01 | 264.0 | 334 | 104-471 |
| 2, 4΄-DDT | 0.01 | ─ | <0.01 | ─ | ─ | ─ |
| 4, 4΄-DDT | 0.01 | 5 | <0.01 | 290.0 | 297 | 72-459 |
| trans-Nonachlor | 0.01 | ─ | <0.01 | ─ | ─ | ─ |
| cis-Nonachlor | 0.01 | ─ | <0.01 | ─ | ─ | ─ |
| Mirex | 0.02 | ─ | <0.02 | ─ | ─ | ─ |

Table 2.2.3.

Recovery of surrogate standards, %

| Analyte | Customer’s sample code: |
| --- | --- |
|  | NOV8 Sed1 RU-1 | NOV8 Sed1 RU-2 | NOV8 Sed1 RU-3 | NOV8 Sed1 RU-4 | NOV10 Sed1 RU-5 |
| 13С6 Hexachlorobenzene | 90 | 97 | 99 | 97 | 104 |
| 13С6 γ-HCH | 68 | 76 | 76 | 71 | 73 |
| 13С12 p,p- DDE | 96 | 102 | 105 | 100 | 95 |
| 13С12 p,p- DDT | 82 | 84 | 83 | 80 | 80 |

Table 2.2.4.

Recovery of surrogate standards, %

| Analyte | Customer’s sample code: |
| --- | --- |
|  | NOV10 Sed2 RU-6 | NOV11 Sed1 RU-7 | NOV11 Sed1 RU-8 | NOV11 Sed2 RU-9 | NOV11 Sed2 RU-10 |
| 13С6 Hexachlorobenzene | 93 | 100 | 99 | 94 | 97 |
| 13С6 γ-HCH | 65 | 72 | 75 | 63 | 68 |
| 13С12 p,p- DDE | 87 | 89 | 89 | 86 | 97 |
| 13С12 p,p- DDT | 74 | 68 | 76 | 67 | 70 |

Table 2.2.5.

Recovery of surrogate standards, %

| Analyte | Customer’s sample code: |
| --- | --- |
|  | NOV11 Sed2 RU-11 | NOV11 Sed2 RU-12 | NOV15 Sed1 RU-13 | NOV12 Sed2 KZ-1 | NOV12 Sed1 KZ-2 |
| 13С6 Hexachlorobenzene | 100 | 102 | 102 | 92 | 96 |
| 13С6 γ-HCH | 74 | 74 | 72 | 65 | 76 |
| 13С12 p,p- DDE | 97 | 95 | 90 | 89 | 98 |
| 13С12 p,p- DDT | 73 | 75 | 68 | 68 | 62 |

Table 2.2.6.

Recovery of surrogate standards, %

| Analyte | Customer’s sample code: |
| --- | --- |
|  | NOV13 Sed1 KZ-3 | NOV13 Sed2 KZ-4 | NOV13 Sed1 KZ-5 | NOV13 Sed2 KZ-6 | NOV13 Sed1 KZ-7 | NOV13 Sed1 KZ-8 |
| 13С6 Hexachlorobenzene | 93 | 104 | 96 | 95 | 99 | 96 |
| 13С6 γ-HCH | 63 | 82 | 74 | 70 | 70 | 78 |
| 13С12 p,p- DDE | 85 | 100 | 94 | 94 | 97 | 100 |
| 13С12 p,p- DDT | 62 | 73 | 68 | 70 | 64 | 63 |

Table 2.2.7.

Recovery of surrogate standards, %

| Analyte | Customer’s sample code: |
| --- | --- |
|  | 7 | 10 | 11 | 14 |
| 13С6 Hexachlorobenzene | 96 | 100 | 97 | 95 |
| 13С6 γ-HCH | 78 | 75 | 74 | 80 |
| 13С12 p,p- DDE | 101 | 98 | 94 | 103 |
| 13С12 p,p- DDT | 78 | 67 | 62 | 69 |

Table 2.2.8.

Recovery of surrogate standards, %

| Analyte | Customer’s sample code: |
| --- | --- |
|  | 18 | 20 | Lagan-R |
| 13С6 Hexachlorobenzene | 99 | 89 | 98 |
| 13С6 γ-HCH | 75 | 70 | 89 |
| 13С12 p,p- DDE | 96 | 76 | 97 |
| 13С12 p,p- DDT | 61 | 63 | 71 |

2.3. Polycyclic aromatic hydrocarbons

Table 2.3.1.

The results of quality control for the analysis of bottom sediment samples for CAS-PAH-13S polycyclic aromatic hydrocarbon content

| Compound | Detection limit, μg/kg | Duplicate divergence (NOV10 Sed1 RU-5), % | PBS-13 blank sample, μg/kg | ЕС-5 certified sample (A Humber River Sediment for Toxic Organics) |
| --- | --- | --- | --- | --- |
|  |  |  |  | Determined, μg/kg | Certified value, μg/kg |
| Naphthalene | 3.00 | 5 | <3.00 | 32.0 | 26±6 |
| 1-Methylnaphthalene | 0.30 | ─ | <0.30 | ─ | ─ |
| 2-Methylnaphthalene | 0.30 | ─ | <0.30 | ─ | ─ |
| C2-Naphthalenes | 0.30 | ─ | <0.30 | ─ | ─ |
| C3-Naphthalenes | 0.30 | ─ | <0.30 | ─ | ─ |
| C4-Naphthalenes | 0.30 | ─ | <0.30 | ─ | ─ |
| Acenaphthylene | 0.30 | ─ | <0.30 | 40.5 | 41±9 |
| Acenaphthene | 0.30 | ─ | <0.30 | 20.6 | 29±9 |
| Fluorene | 0.30 | ─ | <0.30 | 92.5 | 84±26 |
| C1-Fluorenes | 0.30 | ─ | <0.30 | ─ | ─ |
| C2-Fluorenes | 0.30 | ─ | <0.30 | ─ | ─ |
| C3-Fluorenes | 0.30 | ─ | <0.30 | ─ | ─ |
| Phenanthrene | 0.30 | 13 | <0.30 | 639.0 | 612±57 |
| Anthracene | 0.30 | ─ | <0.30 | 110.0 | 113±17 |
| C1-Phenanthrenes/Anthracenes | 0.30 | 16 | <0.30 | ─ | ─ |
| C2-Phenanthrenes/Anthracenes | 0.30 | 25 | <0.30 | ─ | ─ |
| C3-Phenanthrenes/Anthracenes | 0.30 | 16 | <0.30 | ─ | ─ |
| C4-Phenanthrenes/Anthracenes | 0.30 | 9 | <0.30 | ─ | ─ |
| Dibenzothiophene | 0.30 | 22 | <0.30 | ─ | ─ |
| C1-Dibenzothiophenes | 0.30 | ─ | <0.30 | ─ | ─ |
| C2-Dibenzothiophenes | 0.30 | ─ | <0.30 | ─ | ─ |
| C3-Dibenzothiophenes | 0.30 | ─ | <0.30 | ─ | ─ |
| Fluoranthene | 0.30 | 13 | <0.30 | 874.0 | 823±74 |
| Pyrene | 0.30 | 7 | <0.30 | 895.0 | 987±134 |
| C1-Fluoranthenes/Pyrenes | 0.30 | 17 | <0.30 | ─ | ─ |
| C2-Fluoranthenes/Pyrenes | 0.30 | ─ | <0.30 | ─ | ─ |
| C3-Fluoranthenes/Pyrenes | 0.30 | ─ | <0.30 | ─ | ─ |
| Benzo(a)anthracene | 0.50 | 4 | <0.50 | 510.0 | 503±47 |
| Chrysene | 0.50 | 7 | <0.50 | 625.0 | 619±60 |
| C1-Chrysenes | 0.50 | ─ | <0.50 | ─ | ─ |
| C2-Chrysenes | 0.50 | ─ | <0.50 | ─ | ─ |
| C3-Chrysenes | 0.50 | ─ | <0.50 | ─ | ─ |
| Benzo(b+j)fluoranthene | 0.60 | ─ | <0.60 | 403.0 | 480±88 |
| Benzo(k)fluoranthene | 0.60 | ─ | <0.60 | 456.0 | 419±49 |
| Benzo(e)pyrene | 0.70 | ─ | <0.70 | 443.0 | 440±76 |
| Benzo(a)pyrene | 0.70 | ─ | <0.70 | 496.0 | 449±61 |
| Perylene | 1.00 | 14 | <1.00 | 164.0 | 187±28 |
| Indeno(1,2,3-cd)pyrene | 1.00 | ─ | <1.00 | 329.0 | 386±66 |
| Dibenzo(a,h)anthracene | 1.00 | ─ | <1.00 | 210.0 | 195±44 |
| Benzo(g,h,i)perylene | 1.00 | ─ | <1.00 | 269.0 | 333±53 |
| Recovery of surrogate standards, % |
| Naphthalene d8 | 0.05 | ─ | 66 | 67 |
| Acenaphthene d10 | 0.05 | ─ | 93 | 101 |
| Phenanthrene d10 | 0.05 | ─ | 87 | 100 |
| Chrysene d12 | 0.05 | ─ | 73 | 94 |
| Perylene d12 | 0.05 | ─ | 70 | 65 |

Table 2.3.2.

The results of quality control for the analysis of bottom sediment samples for CAS-PAH-14S polycyclic aromatic hydrocarbon content

| Compound | Detection limit, μg/kg | Duplicate divergence (NOV12 Sed2 KZ-1), % | PBS-14 blank sample, μg/kg | ЕС-5 certified sample (A Humber River Sediment for Toxic Organics) |
| --- | --- | --- | --- | --- |
|  |  |  |  | Determined, μg/kg | Certified value, μg/kg |
| Naphthalene | 3.00 | ─ | <3.00 | 20.8 | 26±6 |
| 1-Methylnaphthalene | 0.30 | ─ | <0.30 | ─ | ─ |
| 2-Methylnaphthalene | 0.30 | ─ | <0.30 | ─ | ─ |
| C2-Naphthalenes | 0.30 | ─ | <0.30 | ─ | ─ |
| C3-Naphthalenes | 0.30 | ─ | <0.30 | ─ | ─ |
| C4-Naphthalenes | 0.30 | ─ | <0.30 | ─ | ─ |
| Acenaphthylene | 0.30 | ─ | <0.30 | 50.0 | 41±9 |
| Acenaphthene | 0.30 | ─ | <0.30 | 22.2 | 29±9 |
| Fluorene | 0.30 | ─ | <0.30 | 61.4 | 84±26 |
| C1-Fluorenes | 0.30 | ─ | <0.30 | ─ | ─ |
| C2-Fluorenes | 0.30 | ─ | <0.30 | ─ | ─ |
| C3-Fluorenes | 0.30 | ─ | <0.30 | ─ | ─ |
| Phenanthrene | 0.30 | ─ | <0.30 | 606.0 | 612±57 |
| Anthracene | 0.30 | ─ | <0.30 | 119.0 | 113±17 |
| C1-Phenanthrenes/Anthracenes | 0.30 | ─ | <0.30 | ─ | ─ |
| C2-Phenanthrenes/Anthracenes | 0.30 | ─ | <0.30 | ─ | ─ |
| C3-Phenanthrenes/Anthracenes | 0.30 | ─ | <0.30 | ─ | ─ |
| C4-Phenanthrenes/Anthracenes | 0.30 | ─ | <0.30 | ─ | ─ |
| Dibenzothiophene | 0.30 | ─ | <0.30 | ─ | ─ |
| C1-Dibenzothiophenes | 0.30 | ─ | <0.30 | ─ | ─ |
| C2-Dibenzothiophenes | 0.30 | ─ | <0.30 | ─ | ─ |
| C3-Dibenzothiophenes | 0.30 | ─ | <0.30 | ─ | ─ |
| Fluoranthene | 0.30 | ─ | <0.30 | 846.0 | 823±74 |
| Pyrene | 0.30 | ─ | <0.30 | 896.0 | 987±134 |
| C1-Fluoranthenes/Pyrenes | 0.30 | ─ | <0.30 | ─ | ─ |
| C2-Fluoranthenes/Pyrenes | 0.30 | ─ | <0.30 | ─ | ─ |
| C3-Fluoranthenes/Pyrenes | 0.30 | ─ | <0.30 | ─ | ─ |
| Benzo(a)anthracene | 0.50 | ─ | <0.50 | 540.0 | 503±47 |
| Chrysene | 0.50 | ─ | <0.50 | 627.0 | 619±60 |
| C1-Chrysenes | 0.50 | ─ | <0.50 | ─ | ─ |
| C2-Chrysenes | 0.50 | ─ | <0.50 | ─ | ─ |
| C3-Chrysenes | 0.50 | ─ | <0.50 | ─ | ─ |
| Benzo(b+j)fluoranthene | 0.60 | ─ | <0.60 | 444.0 | 480±88 |
| Benzo(k)fluoranthene | 0.60 | ─ | <0.60 | 433.0 | 419±49 |
| Benzo(e)pyrene | 0.70 | ─ | <0.70 | 409.0 | 440±76 |
| Benzo(a)pyrene | 0.70 | ─ | <0.70 | 437.0 | 449±61 |
| Perylene | 1.00 | ─ | <1.00 | 168.0 | 187±28 |
| Indeno(1,2,3-cd)pyrene | 1.00 | ─ | <1.00 | 329.0 | 386±66 |
| Dibenzo(a,h)anthracene | 1.00 | ─ | <1.00 | 169.0 | 195±44 |
| Benzo(g,h,i)perylene | 1.00 | ─ | <1.00 | 356.0 | 333±53 |
| Recovery of surrogate standards, % |
| Naphthalene d8 | 0.05 | ─ | 80 | 75 |
| Acenaphthene d10 | 0.05 | ─ | 99 | 89 |
| Phenanthrene d10 | 0.05 | ─ | 92 | 78 |
| Chrysene d12 | 0.05 | ─ | 85 | 78 |
| Perylene d12 | 0.05 | ─ | 86 | 82 |

Table 2.3.3.

Recovery of surrogate standards

| Compound | Customer’s sample code: |
| --- | --- |
|  | NOV8 Sed1 RU-1 | NOV8 Sed1 RU-2 | NOV8 Sed1 RU-3 | NOV8 Sed1 RU-4 | NOV10 Sed1 RU-5 |
| Naphthalene d8 | 66 | 70 | 68 | 67 | 77 |
| Acenaphthene d10 | 92 | 87 | 79 | 93 | 103 |
| Phenanthrene d10 | 93 | 90 | 88 | 104 | 106 |
| Chrysene d12 | 78 | 84 | 87 | 74 | 62 |
| Perylene d12 | 61 | 62 | 68 | 65 | 66 |

Table 2.3.4.

Recovery of surrogate standards

| Compound | Customer’s sample code: |
| --- | --- |
|  | NOV10 Sed2 RU-6 | NOV11 Sed1 RU-7 | NOV11 Sed1 RU-8 | NOV11 Sed2 RU-9 | NOV11 Sed2 RU-10 |
| Naphthalene d8 | 76 | 63 | 69 | 72 | 68 |
| Acenaphthene d10 | 119 | 101 | 75 | 96 | 101 |
| Phenanthrene d10 | 107 | 125 | 84 | 109 | 98 |
| Chrysene d12 | 89 | 77 | 60 | 83 | 75 |
| Perylene d12 | 69 | 70 | 69 | 63 | 70 |

Table 2.3.5.

Recovery of surrogate standards

| Compound | Customer’s sample code: |
| --- | --- |
|  | NOV11 Sed2 RU-11 | NOV11 Sed2 RU-12 | NOV15 Sed1 RU-13 | NOV12 Sed2 KZ-1 | NOV12 Sed1 KZ-2 |
| Naphthalene d8 | 75 | 71 | 69 | 78 | 66 |
| Acenaphthene d10 | 106 | 93 | 83 | 110 | 86 |
| Phenanthrene d10 | 110 | 107 | 89 | 106 | 93 |
| Chrysene d12 | 76 | 82 | 80 | 74 | 76 |
| Perylene d12 | 60 | 72 | 63 | 72 | 71 |

Table 2.3.6.

Recovery of surrogate standards

| Compound | Customer’s sample code: |
| --- | --- |
|  | NOV13 Sed1 KZ-3 | NOV13 Sed2 KZ-4 | NOV13 Sed1 KZ-5 | NOV13 Sed2 KZ-6 | NOV13 Sed1 KZ-7 | NOV13 Sed1 KZ-8 |
| Naphthalene d8 | 68 | 102 | 71 | 73 | 68 | 71 |
| Acenaphthene d10 | 91 | 113 | 100 | 94 | 100 | 111 |
| Phenanthrene d10 | 91 | 102 | 121 | 115 | 107 | 104 |
| Chrysene d12 | 77 | 73 | 80 | 77 | 75 | 79 |
| Perylene d12 | 69 | 66 | 66 | 74 | 64 | 69 |

Table 2.3.7.

Recovery of surrogate standards

| Compound | Customer’s sample code: |
| --- | --- |
|  | 7 | 10 | 11 | 14 |
| Naphthalene d8 | 97 | 75 | 81 | 91 |
| Acenaphthene d10 | 117 | 116 | 113 | 110 |
| Phenanthrene d10 | 117 | 109 | 95 | 116 |
| Chrysene d12 | 74 | 61 | 76 | 80 |
| Perylene d12 | 70 | 63 | 70 | 60 |

Table 2.3.8.

Recovery of surrogate standards

| Compound | Customer’s sample code: |
| --- | --- |
|  | 18 | 20 | Lagan-R |
| Naphthalene d8 | 96 | 78 | 87 |
| Acenaphthene d10 | 105 | 110 | 112 |
| Phenanthrene d10 | 122 | 102 | 96 |
| Chrysene d12 | 77 | 64 | 64 |
| Perylene d12 | 64 | 75 | 80 |

2.4. Polychlorinated dibenzo-p-dioxins and dibenzofurans

Table 2.4.1.

The results of quality control for the analysis of polychlorinated dibenzo-p-dioxins and dibenzofurans in bottom sediment samples

| Analyte | PBS-01 blank sample, ng/kg | Detection limit, ng/kg | SMS 01 check sample |
| --- | --- | --- | --- |
|  |  |  | Determined, ng | Added, ng | % recovery |
| 2,3,7,8-TCDD | <0.08 | 0.08 | 0.18 | 0.20 | 89 |
| 1,2,3,7,8-PnCDD | <0.02 | 0.02 | 0.17 | 0.20 | 87 |
| 1,2,3,4,7,8-HcCDD | <0.02 | 0.02 | 0.17 | 0.20 | 84 |
| 1,2,3,6,7,8-HcCDD | <0.02 | 0.02 | 0.17 | 0.20 | 85 |
| 1,2,3,7,8,9-HcCDD | <0.02 | 0.02 | 0.15 | 0.20 | 76 |
| 1,2,3,4,6,7,8-HpCDD | <0.02 | 0.02 | 0.14 | 0.20 | 72 |
| OCDD | <0.02 | 0.02 | 0.34 | 0.40 | 84 |
| 2,3,7,8-TCDF | <0.02 | 0.02 | 0.04 | 0.04 | 96 |
| 1,2,3,7,8-PnCDF | <0.02 | 0.02 | 0.16 | 0.20 | 78 |
| 2,3,4,7,8-PnCDF | <0.02 | 0.02 | 0.20 | 0.20 | 99 |
| 1,2,3,4,7,8-HcCDF | <0.02 | 0.02 | 0.15 | 0.20 | 77 |
| 1,2,3,6,7,8-HcCDF | <0.02 | 0.02 | 0.17 | 0.20 | 85 |
| 2,3,4,6,7,8-HcCDF | <0.02 | 0.02 | 0.16 | 0.20 | 80 |
| 1,2,3,7,8,9-HcCDF | <0.02 | 0.02 | 0.17 | 0.20 | 86 |
| 1,2,3,4,6,7,8-HpCDF | <0.02 | 0.02 | 0.19 | 0.20 | 96 |
| 1,2,3,4,7,8,9-HpCDF | <0.02 | 0.02 | 0.19 | 0.20 | 93 |
| OCDF | <0.02 | 0.02 | 0.32 | 0.40 | 79 |
| Recovery of surrogate standards, % |  |
| (13С12)2,3,7,8-TCDD | 93 | 0.08 | 0.95 | 1.25 | 76 |
| (13С12)2,3,7,8-TCDF | 100 | 0.02 | 1.05 | 1.25 | 84 |
| (13С12)1,2,3,7,8-PnCDD | 99 | 0.02 | 1.19 | 1.25 | 95 |
| (13С12)1,2,3,7,8-PnCDF | 90 | 0.02 | 0.94 | 1.25 | 75 |
| (13С12)1,2,3,6,7,8-HcCDD | 89 | 0.02 | 1.04 | 1.25 | 83 |
| (13С12)1,2,3,6,7,8-HcCDF | 103 | 0.02 | 1.00 | 1.25 | 80 |
| (13С12)1,2,3,4,6,7,8-HpCDD | 100 | 0.02 | 1.18 | 1.25 | 94 |
| (13С12)1,2,3,4,6,7,8-HpCDF | 95 | 0.02 | 1.24 | 1.25 | 99 |
| (13С12)OCDD | 90 | 0.02 | 2.23 | 2.50 | 89 |

2.5. Planar (non-ortho and mono-ortho substituted) PCBs

The results of quality control for the analysis of planar PCBs in bottom sediment samples

| IUPAC number of PCB congener |  | SMS 03 check sample |
| --- | --- | --- |
|  | Blank sample PBS-03, ng/kg | Detection limit, ng/kg | Determined, ng | Added, ng | % recovery |
| #77 | <0.005 | 0.005 | 0.19 | 0.2 | 95 |
| #81 | <0.005 | 0.005 | 0.16 | 0.2 | 80 |
| #105 | 0.02 | 0.01 | 0.24 | 0.2 | 120 |
| #114 | <0.01 | 0.01 | 0.17 | 0.2 | 85 |
| #118 | 0.11 | 0.01 | 0.28 | 0.2 | 140 |
| #123 | <0.01 | 0.01 | 0.20 | 0.2 | 100 |
| #126 | <0.01 | 0.01 | 0.16 | 0.2 | 80 |
| #156 | <0.01 | 0.01 | 0.18 | 0.2 | 90 |
| #157 | <0.01 | 0.01 | 0.18 | 0.2 | 90 |
| #167 | <0.02 | 0.02 | 0.17 | 0.2 | 85 |
| #169 | <0.02 | 0.02 | 0.14 | 0.2 | 70 |
| #170 | <0.02 | 0.02 | 0.22 | 0.2 | 110 |
| #180 | <0.02 | 0.02 | 0.24 | 0.2 | 120 |
| #189 | <0.03 | 0.03 | 0.17 | 0.2 | 85 |
| Recovery of surrogate standards, % |  |
| 13С12#77 | 72 | 0.005 | 1.76 | 2.0 | 88 |
| 13С12#81 | 71 | 0.005 | 1.86 | 2.0 | 93 |
| 13С12#105 | 76 | 0.01 | 1.97 | 2.0 | 98.5 |
| 13С12#114 | 81 | 0.01 | 1.83 | 2.0 | 91.5 |
| 13С12#118 | 86 | 0.01 | 1.77 | 2.0 | 88.5 |
| 13С12#123 | 86 | 0.01 | 2.0 | 2.0 | 100 |
| 13С12#126 | 57 | 0.01 | 1.80 | 2.0 | 90 |
| 13С12#156 | 92 | 0.01 | 1.85 | 2.0 | 92 |
| 13С12#157 | 89 | 0.01 | 1.69 | 2.0 | 84.5 |
| 13С12#167 | 88 | 0.02 | 2.11 | 2.0 | 105.5 |
| 13С12#169 | 77 | 0.02 | 2.05 | 2.0 | 102.5 |
| 13С12#170 | 84 | 0.02 | 2.13 | 2.0 | 106.5 |
| 13С12#180 | 82 | 0.02 | 2.0 | 2.0 | 100 |
| 13С12#189 | 84 | 0.03 | 2.17 | 2.0 | 108.5 |

. 2.6. Aroclor 1254 and Aroclor 1260

The results of quality control for the analysis of Aroclor 1254 and Aroclor 1260 in bottom sediment samples

| Analyte | Blank sample PBS-11, ng/kg | Detection limit, ng/kg | Duplicate divergence, % (NOV13 Sed2 KZ) | SMS11 check sample |
| --- | --- | --- | --- | --- |
|  |  |  |  | Determined, ng | Added, ng | % recovery |
| Aroclor 1254 | <0.10 | <0.10 | 17 | 58 | 50 | 104 |
| Aroclor 1260 | <0.10 | <0.10 | 22 | 53 | 50 | 101.5 |