International Atomic Energy Agency

Marine Environmental Laboratory

CASPIAN SEA 2005

CONTAMINANT SCREENING SURVEY

Monaco, May 2006

4, Quai Antoine 1er

MC 98000 Monaco

Tel. :  (377) 97.97.72.72    Fax :  (377) 97.97.72.73

E-mail :  mel@iaea.org

Contents :

Page

Project reference			  3

- Sample sites and sampling of sediments	  4

II.  Analytical protocol			  5

II.1	Hydrocarbons and organochlorine compounds	  6

II.1.1	Sample pre-treatment and extraction	  6

II.1.2	Clean-up and fractionation	  6

II.1.3	Quantification and quality control	  7

II.2	Trace elements			  9

II.2.1	Sample pre-treatment	  9

II.2.2	Microwave digestion	  9

II.2.3	Quantification by ICP-MS and quality control	  9

II.3	Mercury					10

II.3.1	Digestion			10

II.3.2	Quantification and quality control	10

II.4	Arsenic						10

II.4.1	Digestion			10

II.4.2	Determination of Arsenic	10

II.5	Calcium					10

II.5.1	Digestion			10

II.5.2	Determination of Calcium			10

II.6	Grain size				11

III. Results						12

III.1			Dry/Wet ratio, TOC, Lipid content and Carbonate	12

III.2		Hydrocarbons			14

III.3		Organochlorines		28

III.4		Trace elements		42

III.5		Grain size			44

List of tables

Table 1	Site description of sediment samples.	    4

Table 2	Dry/Wet ratio, TOC, Lipid content and Carbonate in sediment samples.	  12

Table 3	Petroleum hydrocarbon in sediment samples.	  14

Table 4	Chlorinated pesticides in sediment samples.	  28

Table 5	PCBs in sediment samples	  35

Table 6	Trace metals in sediment samples	  42

project reference

PROJECT:	CASPIAN SEA 2005:

Contaminant screening survey

Samples collected from Iran and Turkmenistan (Automn 2005).

Sampling Team:

C. GUITART FERRARONS

MESL staff:	Responsible officer:

S. de MORA (Head MESL)

Analyses done by:

S. AZEMARD

J. BARTOCCI

M. CAMBELL

R. CASSI

C. CATTINI

Report prepared by:

J.-P. VILLENEUVE

Cleared by:

S. de MORA (Head MESL)

- Sample sites and sampling of sediment

Nineteen sediment samples (Iran) and heighteen sediment samples (Turkmenistan) were collected for analyses of chlorinated compounds, petroleum hydrocarbons and trace metals. Samples were collected by MESL’s staff on board of the Iranian R/V Guilan.

Table 1: Site description of sediment samples. Stations are listed according to code order of the countries. The same order is used for all data tables and grain size distribution (see Figure below for the position of stations).

| COUNTRY | ST # | NAME | Latitude | Longitude |
| --- | --- | --- | --- | --- |
| IRAN | IR-1 | Astara-chai | 38° 23’ 53” | 48° 55’ 59” |
|  | IR-2 | Gorgan-roud | 37° 49’ 17” | 49° 01’ 54” |
|  | IR-3 | Shafa-roud | 37° 37’ 13” | 49° 09’ 54” |
|  | IR-4 | Anzali wetland | 37° 30’ 09” | 49° 28’ 58” |
|  | IR-5 | Sefid-roud | 37° 29’ 14” | 49° 57’ 20” |
|  | IR-6 | Shalman-roud | 37° 12’ 40” | 50° 19’ 11” |
|  | IR-7 | Pol-roud | 37° 07’ 03” | 50° 26’ 34” |
|  | IR-8 | She-hezar (Tonekabon) | 36° 51’ 07” | 50° 53’ 20” |
|  | IR-9 | Nashta-roud | 36° 46’ 38” | 51° 05’ 07” |
|  | IR-10 | Chalous | 36° 41’ 37” | 51° 28’ 13” |
|  | IR-11 | Noor-Rouyan | 36° 36’ 44” | 52° 01’ 33” |
|  | IR-12 | Mahmoudabad | 36° 39’ 40” | 52° 13’ 15” |
|  | IR-13 | Haraz | 36° 42’ 48” | 52° 27’ 39” |
|  | IR-14 | Babol-roud | 36° 45’ 42” | 52° 42’ 05” |
|  | IR-15 | Tajan | 36° 52’ 45” | 53° 08’ 42” |
|  | IR-16 | Neka | 36° 54’ 02” | 53° 15’ 45” |
|  | IR-16A | Neka | 36° 53’ 25” | 53° 23’ 43” |
|  | IR-17 | Gorgan | 36° 58’ 08” | 53° 49’ 09” |
|  | IR-18 | Atrak | 37° 15’ 11” | 53° 39’ 60” |
| TURKMENISTAN | TK-2 | Mys Suye (off-shore) | 41° 44’ 32” | 52° 12’ 37” |
|  | TK-4 | Carabogaz (off-shore) | 40° 58’ 16” | 52° 52’ 16” |
|  | TK-5 | Carabogaz | 40° 45’ 56” | 52° 16’ 28” |
|  | TK-6 | Carshi | 40° 37’ 01” | 52° 06’ 07” |
|  | TK-7 | Ciyanli | 40° 10’ 38” | 52° 39’ 50” |
|  | TK-9 | Carababa | 39° 53’ 55” | 52° 48’ 48” |
|  | TK-10 | Osyshnoi island | 39° 39’ 13” | 53° 10’ 00” |

| COUNTRY | ST # | NAME | Latitude | Longitude |
| --- | --- | --- | --- | --- |
| TURKMENISTAN | TK-11 | Cheleken city (North) | 39° 26’ 36” | 52° 35’ 54” |
|  | TK-12 | Cheleken city (South) | 39° 26’ 01” | 53° 01’ 06” |
|  | TK-13 | Ogurchinskiy island (North) | 39° 01’ 42” | 53° 07’ 24” |
|  | TK-14 | Turkmen bay (East) | 38° 57’ 40” | 53° 34’ 05” |
|  | TK-15 | Ogurchinskiy island (South) | 38° 44’ 55” | 53° 09’ 03” |
|  | TK-16 | Turkmen bay (off-shore) | 38° 44’ 16” | 52° 42’ 32” |
|  | TK-17 | Turkmen bay (South) | 38° 24’ 35” | 53° 34’ 16” |
|  | TK-18 | Okarem port | 37° 56’ 06” | 53° 35’ 19” |
|  | TK-19 | Okarem port (off-shore) | 37° 55’ 15” | 53° 12’ 13” |
|  | TK-20 | Chekshlyar | 37° 32’ 42” | 53° 33’ 36” |
|  | TK-21 | Chekshlyar (off-shore) | 37° 30’ 02” | 53° 05’ 21” |

Map of cruise stations:

II.	Analytical protocols

The following section provides details of the protocols, which were used to quantify the contaminants.

II.1 	Hydrocarbons and organochlorine compounds

II.1.1	Sample pre-treatment and extraction

Following freeze-drying, the samples were sieved through stainless steel sieves with mesh sizes of 250 µm.  Sediments were then homogenized prior to extraction.

The extraction was realised with a microwave oven.15 grams of freeze-dried sediment sample were put in the glass tube of the reactor with 40 ml of a mixture of hexane/dichloromethane (50:50). Internal standards were added, these standards are used for quantifying the overall recovery of the analytical procedures:

(	n-C24-d50 for the aliphatic hydrocarbon fraction;

(	Hexamethylbenzene, Naphthalene-d8, Anthracene-d10, Pyrene-d10 and Perylene-d12 for the aromatic hydrocarbon fraction; Chrysene-d12 as GC internal standard.

(	PCB29, PCB198, HCH and Endosulfan 1-d4 for the organochlorine fractions.

The operating conditions of the microwave oven were as follows:

Power of the microwaves: 1200 Watts

Temperature increase to 115 °C in 10 minutes

Extraction maintained at 115 °C for 30 minutes

Cooling to ambient temperature within one hour.

After cooling down to room temperature, the solvent mixture was recovered in a 100 ml glass flask. The sediment was rinced three times with 10 ml of hexane.

A sulphur removal procedure was performed using activated elemental copper in order to avoid sulphur interference when using gas chromatography.  Sulphur compounds are specially detected and can cause interference in the analysis of chlorinated hydrocarbons.

Extractable Organic Matter (EOM) was determined by evaporating a measured small volume of this extract on the pan of an electro-balance.

The extracts were then separated into two aliquots: 1/3 for hydrocarbons and 2/3 for chlorinated hydrocarbons analyses.

II.1.2	Clean-up and fractionation

Hydrocarbons:

The extract was passed through a silica/alumina column (silica and alumina were activated first at 200°C for 4 hours and partially deactivated with 5% water). The chromatography column was prepared by slurry packing 5 g of silica, then 10 g of alumina and finally 1 g of sodium sulphate was added to the surface to avoid disturbance of the top layer when pouring the solvent. Elution was performed using 20 mL of hexane to yield the first fraction (which contains the aliphatic hydrocarbons), then, 30 mL of hexane/methylene chloride (90:10) to recover the second fraction, which contains the aromatic hydrocarbons (PAH).

Chlorinated compounds:

The extract was passed through a Florisil (17 g) column, which had been activated for 12 hours at 130°C and partially deactivated with 0.5% water. From this column, three fractions were collected. A first fraction with 70 mL of hexane (containing PCBs, pp' and op DDE and some other pesticides such as HCB, aldrin, heptachlor, DDMU). A second fraction with 45 mL of hexane/methylene chloride (70:30) (containing the DDTs, DDDs, most of the toxaphene and some pesticides such as HCH isomers and chlordane components) and then a third fraction with 70 mL of methylene chloride (containing mainly dieldrin, endrin and endosulfan components).

II.1.3	Quantification and quality control

Hydrocarbons :

UVF procedure

Emission scans and synchronous excitation/emission scans were recorded to evaluate the relative fluorescence and to characterise the aromatic hydrocarbons in the samples.  Standard response curves of fluorescence intensity versus concentration were generated for Kuwait crude (ROPME) oil and for the standard aromatic hydrocarbon: Chrysene.  Samples were diluted in order to give a reading within the linear calibration range of the fluorometer.  Conditions of the fluorometer were adjusted as follows:

1st procedure :

Excitation wavelength fixed: 310 nm

a) Single calibrated measurement: Emission wavelength at 360 nm

b) Scan: Emission wavelength from 320 nm to 550 nm

2nd procedure : Qualitative characterisation

Excitation wavelength from 237 nm to 527 nm

Emission wavelength from 260 nm to 550 nm

l = 23 nm.

cGC-FID conditions used were as follows:

Both aliphatic and aromatic hydrocarbon fractions were analysed using cGC-FID.

Gas Chromatograph	: Hewlett Packard HP5890 series II

Detector	: Flame Ionization Detector (FID)

Injection mode	: Splitless

Carrier gas	: Helium 1.4 mL.min-1

Column	: HP-5 (crosslinked 5% Ph Me Silicone)

30m x 0.25mm i.d. x 0.25µm film thickness

Injector temperature	: 270 °C

Detector temperature	: 320°C

Oven temperature program	: 60°C initial for 0.5 min.,	 60°C to 300°C at 6°C.min-1, 300°C for 30 min

cGC-MS conditions used were as follows:

The aromatic hydrocarbons were analysed using selective ion monitoring (SIM) to enhance sensitivity.

Gas Chromatograph	: Hewlett Packard HP5890 series II

Detector	: 5989B MS "Engine"

Injection mode	: Splitless

Carrier gas	: Helium 1.5 mL.min-1

Column	: HP-5 MS (crosslinked 5% Ph Me Silicone)

30 m x 0.25 mm i.d. x 0.25 µm film thickness

Injection specifications	: inj. press. : 13 psi, Constant flow on 13 psi at 60°C, t° injector 270°C

Transfert line	: 280°C

Ion source	: 240°C

Analyser	: 100°C

Oven temperature program	: 60°C initial,	 60°C to 100°C at 10°C.min-1,

100°C to 285°C at 4°C.min-1, 285°C for 20 min

Chlorinated compounds :

Fraction 1 and 3:

Conditions used were as follows:

Gas Chromatograph	: Hewlett Packard HP6890

Detector	: Electron Capture Detector 63Ni (ECD)

Injection mode	: Splitless

Carrier gas	: Helium 1.2 mL.min-1

Column	: HP-5 (crosslinked 5% Ph Me Silicone)

30 m x 0.25 mm i.d. x 0.25 µm film thickness

Injection temperature	: 250°C

Detector temperature	: 300°C

Oven temperature program	: 70°C for 2 min, 70°C to 260°C at 3°C.min-1,  260°C for 20 min

Fraction 2 and 3:

Conditions used were as follows:

Gas Chromatograph	: Hewlett Packard HP6890

Detector	: Electron Capture Detector 63Ni (ECD)

Injection mode	: Splitless

Carrier gas	: Helium 0.5 mL.min-1

Column	: DB-5 (crosslinked 5% Ph Me Silicone)

20 m x 0.10 mm i.d. x 0.40 µm film thickness

Injection temperature	: 250°C

Detector temperature	: 310°C

Oven temperature program	: 100°C for 0.5 min, 100°C to 140°C at 9°C.min-1,

140°C for 0.5 min, 140°C to 250°C at 2°C.min-1,

250°C for 0.5 min, 250°C to 300°C at 12°C.min-1,  300°C for 15 min

Appropriate blanks were analysed with each set of analyses and in addition, reference material IAEA-408 (IAEA, sediment) was analysed simultaneously. This sediment has certified concentrations of chlorinated compounds and hydrocarbons.

II.2 	Trace elements

II.2.1 	Sample pre-treatment

Sediment samples were first freeze-dried then sieved through an acid washed plastic sieve 1 mm. They were then transferred to clean plastic containers and shaken to obtain a homogeneous powder. These samples were used for TM and Hg analyses.

II.2.2	Microwave Digestion

All samples were digested using a CEM MARS5 high pressure microwave digestion system. The system is able to maintain a pre-set pressure and temperature via a special monitoring vessel (which also contains the sample being digested).

Aliquots of between 200 and 300 mg of dried sediment material were weighed for digestion. Samples were digested in acid-cleaned Teflon microwave vessels with 5 mL of ultrapure nitric acid and 2 mL ultrapure concentrated hydrofluoric acid. Samples were prepared in batches of 12, which included both samples and quality control (QC) samples (IAEA-433) and appropriate reagent blanks. In addition, each batch also contained a sample replicate.

The digestion procedure involved gradually ramping the temperature to 200°C over a 30 minute interval, then holding at that temperature for an additional 12 minutes. After allowing at least 1 hour for the vessel to cool to room temperature, the vessels were opened and the digests quantitatively transferred to a graduated 50 ml plastic test tube containing 0.8 g boric acid to neutralise excess HF and dissolve the fluoride precipitates. The digested sample was then brought up to the 50 ml mark with Milli-Q water, capped, and placed in an ultrasonic bath for ~1 hour to assist in dissolving residual solid material. For some samples an extra 2 ml of HF was added in order to dissolve the remaining precipitate.

II.2.3	Quantification by ICP-MS and quality control

Samples were analyzed for trace metals (except for arsenic and mercury) using a Finnigan Element inductively-coupled plasma mass spectrometer (ICPMS). The Element is a magnetic sector device and the mass spectrometer can operate in high resolution mode which allows the separation of certain polyatomic interferences from analyte peaks, thus providing results that are virtually free from interferences that have traditionally been problematic for quadrupole ICPMS. For example, 56Fe can be easily separated from 40Ar16O in ‘medium’ resolution mode, while ‘high’ resolution is required to separate 75As from 40Ar35Cl.

A microconcentric nebulizer (MCN) with a standard double-pass spray chamber was used as the method of sample introduction. The nebulizer can be run in a self-aspirating mode and operated without the need for a peristaltic pum; this has the advantage that the noise component induced by the peristaltic pump on the analyte signal is avoided. Sample delivery rate to the plasma ranged between 60 and 100 microliters per minute during this suite of analyses.

Sample digests were typically diluted 1 + 24 in 2% nitric acid prior to analysis. In was added to all blanks, standards and samples to correct for matrix effects and instrument drift. Larger dilutions, a further 1 + 99, were necessary for the analysis of analytes present at relatively high concentrations (e.g., Fe, Mg, Ca and Al).

Results were quantified via an external calibration, normalised against In. Appropriate standards were prepared by serial dilutions from a stock solution containing all analytes of interest. The stock solution was prepared by combining appropriate amounts of mono elemental standard solutions (1000 µg/ml).

II.3 	Mercury

II.3.1 	Digestion

Mercury was determined using a solid AAS analyser (AMA 254, Altech) so no digestion was needed. A portion of about 100 mg of sediment was measured.

II.3.2 	Quantification and quality control

The internal calibration of the instrument is checked every day by an external standard solution (of the appropriate concentration) and 2 different reference materials at different weight, IAEA-433 and MESS-2 (NRCC), in order to check the calibration from 5 to 50 ng of mercury. The instrument is recalibrated if one of the checks failed.

Replicate blanks and reference material were analysed for quality control purposes through out the run as well as replicate samples.

II.4	Arsenic

II.4.1	Digestion (see II.2.2)

II.4.2.	Determination of Arsenic

Arsenic was determined by graphite furnace atomic absorption (Varian 220z zeeman), using platform graphite furnace. The instrument was calibrated from 50 to 200 ppb, volume of injection was 23 µl including 3 µl of sample and 3 µl of a Pd/Mg matrix modifier.

Replicate blanks and reference material were analyzed for quality control purposes through out the run as well as replicate samples.

II.5	Calcium

II.5.1	Digestion (see II.2.2)

II.5.2	Determination of Calcium

Calcium was determined by Flame AAS (Varian 220FS), using an air acetylene flame by flame emission. Sample solutions were diluted 1000 times, and a solution of La-Cs was added to a final concentration of 1 % as matrix modifying agent (ionisation suppression). The instrument was calibrated from 0.1 to 2 ppm.

Reference materials were analysed for quality control purpose through out the run as well as replicate samples. The batch reagent blanks were also analysed to verify that their calcium content was negligible (in the event that significant contamination were to be found, digestion of the entire batch would have been repeated). As IAEA-433 has no reference values for Ca, MESS-3 was also incorporated in the analytical run for a QC check.

II.6.	Grain size

Preparation of samples

Samples were freeze-dried and sieved at 250(m. 52 aliquots of about 1gramme were set aside for particle size analysis.

Preparation prior particle size analysis:

Approximately an aliquot of 1g of sediment was put in a 10mL tube. 5mL of MilliQ water is added and tube is shaken in order to separate the silt particles properly. An equilibration period of about half an hour is taken to assure that the sample was uniformly wet before analysis.

Particle Size Analysis

The particle size distribution was determined using a Malvern Instrument Mastersizer device. The principle of this device is that small particles cause incident light to be diffracted through a large angle whereas large particles will diffract incident light through a small angle. Particle size information is derived by deconvolution of the diffraction data obtained by the instrument.

Apparatus used

The MALVERN Mastersizer Micro v2.12 is designed to analyze particle size of silty sediments (<300µm), particles need to stay in suspension during the measurement process (this device is not suited to the analysis of coarse, sandy material).

Protocol used

The analysis of particles is achieved by slurrying a sediment sample into a beaker containing 500mL of water. The mixture is pumped through a cell which is interrogasted by the instrument’s laser beam. The particle size distribution is determined from the resulting diffraction pattern.

III.	Results

Results are listed in the following tables:

Table n°	Table title		Page

Table  3	Dry/Wet ratio, Total Organic Carbon and Lipids content for sediment samples	  12

Table  4	Petroleum Hydrocarbons in sediment samples				  14

Table  5	Chlorinated Pesticides in sediment samples		  28

Table  6	PCB Congeners in sediment samples		  35

Table  7	Trace metals in sediment samples		  42

Please note legend for all result tables:

“ < ”: detection limit

“ - ”: not analysed

“n.q.”: not quantified owing to an interfering peak

“ * “: information value only

III.1	Dry/Wet ratio, Total Organic Carbon, Lipid content and Carbonate of sediment samples

Table 3: Dry/Wet ratio, Total Organic Carbon, lipid content and carbonate in sediment samples.

| Sample: | IR-1 | IR-2 | IR-3 | IR-4 | IR-5 | IR-6 | IR-7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Dry/Wet Weight | 0.73 | 0.59 | 0.62 | 0.62 | 0.54 | 0.69 | 0.70 |
| TOC ( % ) | 0.3 | 0.4 | 0.3 | 0.3 | 0.4 | 0.2 | 0.2 |
| Lipid (mg/g) | 0.057 | 0.074 | 0.037 | 0.067 | 0.035 | 0.023 | 0.062 |
| Carbonates (%) | 2.4 | 1.7 | 1.5 | 2.1 | 1.7 | 1.6 | 1.6 |

| Sample: | IR-8 | IR-9 | IR-10 | IR-11 | IR-12 | IR-13 | IR-14 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Dry/Wet Weight | 0.64 | 0.55 | 0.55 | 0.59 | 0.64 | 0.69 | 0.59 |
| TOC ( % ) | 0.5 | 0.8 | 1.0 | 0.7 | 0.8 | 0.4 | 0.8 |
| Lipid (mg/g) | 0.056 | 0.068 | 0.089 | 0.091 | 0.067 | 0.034 | 0.053 |
| Carbonates (%) | 1.8 | 1.8 | 2.0 | 2.5 | 3.7 | 3.5 | 3.1 |

| Sample: | IR-15 | IR-16 | IR-16A | IR-17 | IR-18 | TK-2 | TK-4 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Dry/Wet Weight | 0.52 | 0.54 | 0.74 | 0.67 | 0.45 | 0.49 | 0.72 |
| TOC ( % ) | 1.0 | 1.0 | 0.2 | 0.5 | 0.9 | 4.0 | 0.8 |
| Lipid (mg/g) | 0.063 | 0.080 | 0.040 | 0.048 | 0.075 | 0.31 | 0.056 |
| Carbonates (%) | 3.4 | 3.5 | 2.8 | 3.5 | 5.6 | 5.3 | 6.5 |

| Sample: | TK-5 | TK-6 | TK-7 | TK-9 | TK-10 | TK-11 | TK-12 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Dry/Wet Weight | 0.69 | 0.82 | 0.64 | 0.52 | 0.59 | 0.52 | 0.78 |
| TOC ( % ) | 0.4 | 2.0 | 0.7 | 2.6 | 1.1 | 0.9 | 0.2 |
| Lipid (mg/g) | 0.056 | 0.040 | 0.080 | 0.27 | 0.087 | 0.30 | 0.047 |
| Carbonates (%) | 3.8 | 7.8 | 7.1 | 2.6 | 7.8 | 3.7 | 1.3 |

| Sample: | TK-13 | TK-14 | TK-15 | TK-16 | TK-17 | TK-18 | TK-19 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Dry/Wet Weight | 0.42 | 0.60 | 0.44 | 0.58 | 0.70 | 0.49 | 0.42 |
| TOC ( % ) | 1.2 | 0.9 | 1.4 | 1.7 | 0.4 | 0.9 | 1.2 |
| Lipid (mg/g) | 0.17 | 0.095 | 0.16 | 0.25 | 0.047 | 0.075 | 0.097 |
| Carbonates (%) | 4.1 | 5.5 | 4.3 | 8.4 | 3.1 | 7.4 | 7.6 |

| Sample: | TK-20 | TK-21 |
| --- | --- | --- |
| Dry/Wet Weight | 0.41 | 0.38 |
| TOC ( % ) | 1.1 | 1.3 |
| Lipid (mg/g) | 0.081 | 0.099 |
| Carbonates (%) | 7.5 | 7.1 |

III.2		Hydrocarbons

Table 4 Petroleum Hydrocarbon concentrations in sediment samples. Results expressed on dry

weight basis.

| Compounds | IR-1 | IR-2 | IR-3 | IR-4 | IR-5 | IR-6 |
| --- | --- | --- | --- | --- | --- | --- |
| UVF Chrysene equivalent µg/g | 1.8 | 4.9 | 1.6 | 2.1 | 1.5 | 0.5 |
| UVF ROPME oil equivalent µg/g | 12 | 35 | 11 | 15 | 11 | 3.1 |
| Resolved aliphatics µg/g | 0.944 | 2.39 | 1.889 | 2.33 | 2.821 | 0.822 |
| Unresolved aliphatics µg/g | 4.801 | 13 | 4.768 | 8.43 | 5.653 | 2.046 |
| Total aliphatics µg/g | 5.745 | 15 | 6.658 | 10.76 | 8.474 | 2.868 |
|  n-Alk.C12-C36 µg/g | 0.731 | 1.272 | 1.361 | 1.334 | 2.452 | 0.706 |
| n-C12 ng/g | 4.2 | 10 | 16 | 11 | 16 | 6.1 |
| n-C13 ng/g | 6.0 | 15 | 19 | 13 | 19 | 6.7 |
| n-C14 ng/g | 9.4 | 25 | 23 | 13 | 20 | 5.1 |
| n-C15 ng/g | 34 | 60 | 50 | 32 | 47 | 19 |
| n-C16 ng/g | 27 | 51 | 51 | 33 | 52 | 21 |
| n-C17 ng/g | 33 | 61 | 65 | 41 | 57 | 18 |
| n-C18 ng/g | 20 | 36 | 49 | 34 | 44 | 11 |
| n-C19 ng/g | 14 | 31 | 20 | 4.3 | 20 | 7.8 |
| n-C20 ng/g | 17 | 27 | 44 | 36 | 38 | 10 |
| n-C21 ng/g | 16 | 33 | 44 | 43 | 38 | 10 |
| n-C22 ng/g | 18 | 29 | 42 | 42 | 31 | 11 |
| n-C23 ng/g | 22 | 38 | 50 | 55 | 44 | 15 |
| n-C24 ng/g | 18 | 30 | 44 | 56 | 29 | 12 |
| n-C25 ng/g | 28 | 52 | 48 | 73 | 82 | 18 |
| n-C26 ng/g | 18 | 34 | 46 | 69 | 47 | 14 |
| n-C27 ng/g | 65 | 104 | 113 | 131 | 265 | 68 |
| n-C28 ng/g | 25 | 47 | 57 | 77 | 58 | 22 |
| n-C29 ng/g | 102 | 196 | 189 | 192 | 607 | 147 |
| n-C30 ng/g | 18 | 33 | 42 | 54 | 48 | 15 |
| n-C31 ng/g | 112 | 195 | 184 | 150 | 593 | 156 |
| n-C32 ng/g | 12 | 19 | 28 | 36 | 31 | 13 |
| n-C33 ng/g | 39 | 72 | 72 | 60 | 198 | 51 |
| n-C34 ng/g | 13 | 16 | 27 | 31 | 21 | 13 |
| n-C35 ng/g | 48 | 46 | 22 | 28 | 34 | 16 |
| n-C36 ng/g | 12 | 10 | 16 | 22 | 11 | 19 |
| Pristane ng/g | 22 | 47 | 56 | 28 | 37 | 6.7 |
| Phytane ng/g | 12 | 24 | 25 | 21 | 28 | 5.7 |
| Squalane ng/g | < 1.2 | < 1.2 | 5.6 | < 1.8 | 5.9 | < 1.8 |

Table 4 continued

| Compounds | IR-1 | IR-2 | IR-3 | IR-4 | IR-5 | IR-6 |
| --- | --- | --- | --- | --- | --- | --- |
| Resolved aromatics µg/g | 0.21 | 0.45 | 0.496 | 0.518 | 0.406 | 0.085 |
| Unresolved aromatics µg/g | 4.34 | 4.656 | 4.795 | 4.047 | 2.171 | 3.528 |
| Total aromatics µg/g | 4.55 | 5.11 | 5.291 | 4.565 | 2.577 | 3.613 |
| Naphthalene ng/g | 1.0 | 3.0 | 2.4 | 1.7 | 9.5 | 0.9 |
| C1-naphthalenes ng/g | 2.2 | 7.6 | 5.1 | 3.4 | 25 | 2.2 |
| C2-naphthalenes ng/g | 13 | 30 | 12 | 3.4 | 43 | < 0.2 |
| C3-naphthalenes ng/g | 3.6 | 7.3 | 8.8 | 5.2 | 12 | 2.0 |
| C4-naphthalenes ng/g | < 0.2 | 1.1 | 2.7 | 1.9 | 0.6 | 0.3 |
| Biphenyl ng/g | 1.0 | 2.1 | 1.8 | 1.3 | 7.0 | 0.8 |
| Acenaphthylene ng/g | < 0.2 | < 0.2 | < 0.1 | < 0.1 | 0.2 | < 0.1 |
| Acenaphthene ng/g | 0.7 | < 0.2 | < 0.1 | < 0.1 | < 0.1 | < 0.1 |
| Fluorene ng/g | 1.1 | 1.5 | 1.2 | 0.8 | 1.6 | 0.3 |
| C1-fluorenes ng/g | < 0.4 | 2.9 | 4.0 | 2.2 | 3.9 | 0.3 |
| C2-fluorenes ng/g | < 0.4 | 2.3 | 4.1 | 4.4 | 3.2 | < 0.1 |
| C3-fluorenes ng/g | < 0.4 | < 0.4 | 1.6 | < 0.1 | 2.4 | < 0.1 |
| Dibenzothiophene ng/g | < 0.3 | < 0.3 | 0.6 | 0.7 | 1.1 | 0.2 |
| C1-dibenzothiophenes ng/g | 1.7 | 2.0 | 1.2 | 2.6 | 5.2 | 0.6 |
| C2-dibenzothiophenes ng/g | < 0.3 | < 0.3 | 14 | 3.5 | 9.3 | < 0.1 |
| C3-dibenzothiophenes ng/g | < 0.4 | < 0.4 | 2.1 | 9.4 | 7.0 | < 0.1 |
| C4-dibenzothiophenes ng/g | < 0.4 | < 0.4 | < 0.1 | 4.3 | 2.6 | < 0.1 |
| Phenanthrene ng/g | 3.6 | 8.0 | 5.4 | 3.5 | 17 | 1.5 |
| Anthracene ng/g | 0.4 | 0.5 | 0.3 | < 0.1 | 0.6 | < 0.1 |
| C1-phenanthrenes ng/g | 10 | 26 | 22 | 13 | 36 | 4.3 |
| C2-phenanthrenes ng/g | 12 | 26 | 23 | 20 | 27 | 1.5 |
| C3-phenanthrenes ng/g | 2.5 | 6.5 | 6.4 | 5.9 | 6.0 | < 0.1 |
| C4-phenanthrenes ng/g | 1.2 | 1.7 | 2.0 | 2.7 | 1.7 | < 0.1 |
| Retene ng/g | < 0.4 | < 0.4 | 0.7 | 0.6 | 0.6 | < 0.1 |
| Fluoranthene ng/g | 1.0 | 3.6 | 4.7 | 2.4 | 2.8 | 0.6 |
| Pyrene ng/g | 1.1 | 2.3 | 3.0 | 2.3 | 2.7 | 0.9 |
| C1-pyrenes ng/g | 3.4 | 13 | 9.4 | 8.7 | 14 | 3.5 |
| Benz[a]anthracene ng/g | < 0.8 | 3.3 | 1.9 | 1.4 | 2.5 | 1.0 |
| Chrysene ng/g | 4.8 | 11 | 7.1 | 5.2 | 14 | 1.7 |
| C1-chrysenes ng/g | 5.7 | 11 | 6.5 | 5.2 | 11 | < 0.2 |
| C2-chrysenes ng/g | < 1.2 | 14 | 5.9 | 3.9 | 7.1 | < 0.1 |
| C3-chrysenes ng/g | < 1.2 | < 1.2 | < 0.2 | < 0.2 | < 0.2 | < 0.2 |
| Benzo[b+j]fluoranthene ng/g | < 1.2 | 4.6 | 3.2 | 1.9 | 7.2 | 1.8 |
| Benzo[k]fluoranthene ng/g | < 0.9 | 3.2 | 2.1 | 0.9 | 2.2 | 0.7 |
| Benzo[a]fluoranthene ng/g | < 1.2 | < 1.2 | < 0.3 | < 0.3 | < 0.3 | < 0.3 |
| Benzo[e]pyrene ng/g | 2.9 | 6.4 | 4.0 | 2.3 | 8.2 | 1.4 |
| Benzo[a]pyrene ng/g | < 1.1 | 1.4 | 1.6 | 1.2 | 2.0 | 1.3 |
| Perylene ng/g | 19 | 40 | 18 | 10 | 3.5 | 7.9 |
| Indeno[1,2,3-cd]pyrene ng/g | < 1.5 | 1.9 | 0.9 | 0.8 | 1.5 | < 0.6 |
| Benzo[g,h,i]perylene ng/g | < 1.2 | 3.4 | 1.4 | 1.5 | 3.4 | < 0.4 |
| Dibenz[a,h]anthracene ng/g | < 1.5 | < 1.5 | < 0.6 | < 0.6 | < 0.6 | < 0.6 |

Table 4 continued

| Compounds | IR-7 | IR-8 | IR-9 | IR-10 | IR-11 | IR-12 |
| --- | --- | --- | --- | --- | --- | --- |
| UVF Chrysene equivalent µg/g | 1.0 | 1.8 | 2.8 | 3.7 | 3.5 | 3.4 |
| UVF ROPME oil equivalent µg/g | 6.7 | 13 | 19 | 26 | 24 | 23 |
| Resolved aliphatics µg/g | 1.546 | 1.763 | 3.786 | 6.546 | 4.077 | 2.833 |
| Unresolved aliphatics µg/g | 3.986 | 4.069 | 5.452 | 14.589 | 10.769 | 2.970 |
| Total aliphatics µg/g | 5.531 | 5.832 | 9.238 | 21.135 | 14.847 | 5.803 |
|  n-Alk.C12-C36 µg/g | 1.21 | 1.213 | 2.078 | 5.533 | 2.265 | 1.729 |
| n-C12 ng/g | 8.3 | 13 | 20 | 31 | 25 | 26 |
| n-C13 ng/g | 11 | 13 | 24 | 37 | 27 | 28 |
| n-C14 ng/g | 11 | 13 | 20 | 41 | 27 | 29 |
| n-C15 ng/g | 25 | 31 | 60 | 90 | 58 | 60 |
| n-C16 ng/g | 23 | 29 | 42 | 82 | 43 | 48 |
| n-C17 ng/g | 25 | 41 | 129 | 100 | 70 | 91 |
| n-C18 ng/g | 16 | 20 | 28 | 73 | 38 | 57 |
| n-C19 ng/g | 35 | 14 | 59 | 65 | 118 | 10 |
| n-C20 ng/g | 14 | 18 | 26 | 65 | 34 | 50 |
| n-C21 ng/g | 16 | 40 | 56 | 86 | 47 | 69 |
| n-C22 ng/g | 18 | 18 | 26 | 71 | 42 | 56 |
| n-C23 ng/g | 23 | 30 | 46 | 96 | 57 | 75 |
| n-C24 ng/g | 18 | 20 | 29 | 76 | 44 | 53 |
| n-C25 ng/g | 29 | 41 | 77 | 162 | 71 | 91 |
| n-C26 ng/g | 22 | 24 | 38 | 93 | 50 | 49 |
| n-C27 ng/g | 113 | 122 | 200 | 425 | 189 | 157 |
| n-C28 ng/g | 34 | 38 | 62 | 146 | 69 | 54 |
| n-C29 ng/g | 265 | 253 | 419 | 1137 | 379 | 268 |
| n-C30 ng/g | 33 | 38 | 41 | 127 | 110 | 40 |
| n-C31 ng/g | 277 | 240 | 426 | 1642 | 359 | 250 |
| n-C32 ng/g | 14 | 16 | 24 | 83 | 23 | 17 |
| n-C33 ng/g | 114 | 88 | 133 | 616 | 256 | 89 |
| n-C34 ng/g | 20 | 16 | 40 | 46 | 39 | 26 |
| n-C35 ng/g | 31 | 25 | 42 | 89 | 75 | 26 |
| n-C36 ng/g | 15 | 12 | 11 | 20 | 15 | 8.3 |
| Pristane ng/g | 17 | 15 | 19 | 56 | 41 | 47 |
| Phytane ng/g | 10 | 11 | 17 | 48 | 23 | 15 |
| Squalane ng/g | < 1.8 | < 1.8 | < 1.8 | < 1.8 | < 1.8 | 15 |

Table 4 continued

| Compounds | IR-7 | IR-8 | IR-9 | IR-10 | IR-11 | IR-12 |
| --- | --- | --- | --- | --- | --- | --- |
| Resolved aromatics µg/g | 0.16 | 0.183 | 0.233 | 0.503 | 0.612 | 0.41 |
| Unresolved aromatics µg/g | 2.843 | 1.741 | 1.625 | 3.314 | 3.801 | 2.072 |
| Total aromatics µg/g | 3.003 | 1.923 | 1.858 | 3.816 | 4.413 | 2.482 |
| Naphthalene ng/g | 4.2 | 5.9 | 11 | 26 | 27 | 28 |
| C1-naphthalenes ng/g | 11 | 16 | 31 | 67 | 86 | 83 |
| C2-naphthalenes ng/g | 16 | 25 | 62 | 174 | 217 | 207 |
| C3-naphthalenes ng/g | 6.2 | 7.1 | 14 | 38 | 46 | 40 |
| C4-naphthalenes ng/g | 1.3 | 1.2 | 1.7 | 7.6 | 10 | 8.6 |
| Biphenyl ng/g | 3.1 | 4.2 | 8.7 | 19 | 13 | 10 |
| Acenaphthylene ng/g | < 0.1 | < 0.1 | 0.2 | 0.8 | 0.9 | 0.6 |
| Acenaphthene ng/g | < 0.1 | < 0.1 | < 0.1 | 0.6 | < 0.1 | < 0.1 |
| Fluorene ng/g | 0.6 | 1.0 | 2.1 | 4.6 | 3.9 | 2.7 |
| C1-fluorenes ng/g | 1.9 | 2.6 | 2.6 | 11 | 7.9 | 6.3 |
| C2-fluorenes ng/g | 1.3 | 1.7 | 2.5 | 10 | 7.5 | 4.7 |
| C3-fluorenes ng/g | < 0.1 | 0.5 | 2.3 | 6.3 | 5.3 | 2.4 |
| Dibenzothiophene ng/g | 0.9 | 1.0 | 2.2 | 6.8 | 3.6 | 2.0 |
| C1-dibenzothiophenes ng/g | 1.1 | 1.3 | 2.4 | 12 | 6.9 | 4.3 |
| C2-dibenzothiophenes ng/g | 4.8 | 11 | < 0.1 | 10 | < 0.1 | < 0.1 |
| C3-dibenzothiophenes ng/g | 0.9 | 0.7 | 1.8 | 12 | 4.7 | 3.0 |
| C4-dibenzothiophenes ng/g | < 0.1 | < 0.1 | 1.0 | 5.1 | < 0.1 | < 0.1 |
| Phenanthrene ng/g | 6.5 | 7.3 | 17 | 42 | 35 | 26 |
| Anthracene ng/g | 0.2 | 0.3 | 0.2 | 0.4 | 1.6 | 1.6 |
| C1-phenanthrenes ng/g | 14 | 16 | 31 | 86 | 85 | 59 |
| C2-phenanthrenes ng/g | 11 | 14 | 22 | 71 | 67 | 43 |
| C3-phenanthrenes ng/g | 3.5 | 3.3 | 4.1 | 13 | 14 | 9.6 |
| C4-phenanthrenes ng/g | 0.9 | 1.3 | 2.0 | 3.3 | 4.3 | 4.4 |
| Retene ng/g | 0.2 | 0.3 | 0.5 | 0.9 | 2.6 | 2.7 |
| Fluoranthene ng/g | 1.8 | 2.1 | 3.0 | 6.5 | 8.8 | 7.3 |
| Pyrene ng/g | 1.6 | 2.1 | 2.6 | 5.5 | 5.4 | 4.5 |
| C1-pyrenes ng/g | 5.7 | 7.4 | 13 | 29 | 33 | 25 |
| Benz[a]anthracene ng/g | 1.9 | 2.5 | 2.3 | 5.5 | 6.9 | 5.3 |
| Chrysene ng/g | 5.7 | 6.5 | 8.6 | 31 | 19 | 11 |
| C1-chrysenes ng/g | 3.8 | 3.4 | 7.1 | 17 | 13 | 8.7 |
| C2-chrysenes ng/g | < 0.1 | 3.4 | 5.9 | 17 | 11 | 7.4 |
| C3-chrysenes ng/g | < 0.2 | < 0.2 | 5.2 | < 0.2 | < 0.2 | < 0.2 |
| Benzo[b+j]fluoranthene ng/g | 4.3 | 3.3 | 5.3 | 15 | 8.0 | 4.9 |
| Benzo[k]fluoranthene ng/g | 1.8 | 2.3 | 2.4 | 5.2 | 4.6 | 3.4 |
| Benzo[a]fluoranthene ng/g | < 0.3 | < 0.3 | < 0.3 | < 0.3 | < 0.3 | < 0.3 |
| Benzo[e]pyrene ng/g | 3.5 | 3.5 | 5.1 | 12 | 8.4 | 4.8 |
| Benzo[a]pyrene ng/g | 1.7 | 1.8 | 2.6 | 3.7 | 5.8 | 2.9 |
| Perylene ng/g | 9.7 | 6.0 | 9.9 | 8.7 | 13 | 9.2 |
| Indeno[1,2,3-cd]pyrene ng/g | 1.8 | 1.5 | 1.8 | 2.2 | 2.1 | 1.8 |
| Benzo[g,h,i]perylene ng/g | 2.2 | 2.1 | 2.5 | 4.5 | 4.3 | 2.9 |
| Dibenz[a,h]anthracene ng/g | < 0.6 | < 0.6 | < 0.6 | < 0.6 | < 0.6 | < 0.6 |

Table 4 continued

| Compounds | IR-13 | IR-14 | IR-15 | IR-16 | IR-16A | IR-17 |
| --- | --- | --- | --- | --- | --- | --- |
| UVF Chrysene equivalent µg/g | 1.2 | 0.5 | 4.2 | 4.0 | 0.7 | 1.7 |
| UVF ROPME oil equivalent µg/g | 8.6 | 3.0 | 29 | 27 | 5.2 | 12 |
| Resolved aliphatics µg/g | 1.134 | 1.981 | 3.232 | 4.727 | 0.606 | 1.457 |
| Unresolved aliphatics µg/g | 3.434 | 5.22 | 8.054 | 11.621 | 3.55 | 4.226 |
| Total aliphatics µg/g | 4.568 | 7.201 | 11.287 | 16.348 | 4.156 | 5.682 |
|  n-Alk.C12-C36 µg/g | 0.829 | 1.322 | 2.145 | 2.476 | 0.41 | 0.903 |
| n-C12 ng/g | 12 | 5.7 | 33 | 38 | 6.6 | 15 |
| n-C13 ng/g | 12 | 8.9 | 35 | 39 | 7.9 | 18 |
| n-C14 ng/g | 15 | 17 | 36 | 41 | 12 | 22 |
| n-C15 ng/g | 42 | 50 | 102 | 101 | 27 | 50 |
| n-C16 ng/g | 22 | 49 | 52 | 61 | 18 | 28 |
| n-C17 ng/g | 44 | 72 | 80 | 83 | 21 | 35 |
| n-C18 ng/g | 25 | 53 | 50 | 58 | 16 | 26 |
| n-C19 ng/g | 21 | 14 | 14 | 149 | 10 | 11 |
| n-C20 ng/g | 20 | 40 | 42 | 50 | 13 | 24 |
| n-C21 ng/g | 26 | 46 | 63 | 72 | 14 | 27 |
| n-C22 ng/g | 21 | 39 | 43 | 50 | 14 | 23 |
| n-C23 ng/g | 28 | 49 | 61 | 67 | 15 | 29 |
| n-C24 ng/g | 20 | 36 | 44 | 49 | 12 | 23 |
| n-C25 ng/g | 33 | 57 | 77 | 82 | 13 | 31 |
| n-C26 ng/g | 21 | 37 | 48 | 53 | 12 | 24 |
| n-C27 ng/g | 78 | 132 | 201 | 218 | 42 | 84 |
| n-C28 ng/g | 27 | 44 | 68 | 71 | 14 | 29 |
| n-C29 ng/g | 136 | 214 | 385 | 457 | 53 | 144 |
| n-C30 ng/g | 21 | 29 | 46 | 78 | 10 | 20 |
| n-C31 ng/g | 133 | 192 | 387 | 376 | 48 | 137 |
| n-C32 ng/g | 11 | 16 | 26 | 20 | 9.3 | 11 |
| n-C33 ng/g | 48 | 73 | 170 | 149 | 21 | 53 |
| n-C34 ng/g | < 1.8 | 26 | 30 | 37 | < 1.8 | 21 |
| n-C35 ng/g | 16 | 22 | 42 | 64 | < 1.7 | 19 |
| n-C36 ng/g | < 1.7 | < 1.7 | 11 | 13 | < 1.7 | < 1.7 |
| Pristane ng/g | 17 | 31 | 22 | 41 | 9.0 | 17 |
| Phytane ng/g | 7.0 | 17 | 15 | 32 | 5.0 | 11 |
| Squalane ng/g | < 1.1 | < 1.1 | < 1.1 | < 1.1 | < 1.1 | < 1.1 |

Table 4 continued

| Compounds | IR-13 | IR-14 | IR-15 | IR-16 | IR-16A | IR17 |
| --- | --- | --- | --- | --- | --- | --- |
| Resolved aromatics µg/g | 0.078 | 0.565 | 0.639 | 1.395 | 0.090 | 0.273 |
| Unresolved aromatics µg/g | 2.923 | 5.733 | 1.799 | 4.122 | 1.845 | 2.457 |
| Total aromatics µg/g | 3.001 | 6.297 | 2.438 | 5.517 | 1.935 | 2.729 |
| Naphthalene ng/g | 8.5 | 29 | 26 | 40 | 3.9 | 12 |
| C1-naphthalenes ng/g | 24 | 118 | 102 | 162 | 12 | 44 |
| C2-naphthalenes ng/g | 49 | 491 | 249 | 362 | 34 | 122 |
| C3-naphthalenes ng/g | 9.9 | 172 | 51 | 77 | 7.3 | 24 |
| C4-naphthalenes ng/g | 1.7 | 39 | 8.1 | 15 | 1.4 | 4.9 |
| Biphenyl ng/g | 4.6 | 29 | 17 | 22 | 3.8 | 8.5 |
| Acenaphthylene ng/g | 0.3 | 1.9 | 0.7 | 1.0 | < 0.1 | 0.4 |
| Acenaphthene ng/g | < 0.1 | < 0.1 | < 0.1 | < 0.1 | < 0.1 | < 0.1 |
| Fluorene ng/g | 1.4 | 19 | 5.3 | 8.8 | 1.3 | 3.0 |
| C1-fluorenes ng/g | 2.8 | 52 | 13 | 21 | 3.4 | 7.7 |
| C2-fluorenes ng/g | 2.0 | 47 | 13 | 18 | 2.9 | 5.7 |
| C3-fluorenes ng/g | < 0.1 | 24 | 6.8 | 11 | 0.9 | 2.4 |
| Dibenzothiophene ng/g | 1.2 | 2.9 | 3.8 | 6.3 | 1.0 | 2.0 |
| C1-dibenzothiophenes ng/g | 1.8 | 6.2 | 8.2 | 14 | 1.7 | 3.8 |
| C2-dibenzothiophenes ng/g | < 0.1 | 17 | 17 | 38 | < 0.1 | 1.6 |
| C3-dibenzothiophenes ng/g | 0.8 | 6.0 | 8.8 | 16 | 1.4 | 3.4 |
| C4-dibenzothiophenes ng/g | < 0.1 | 2.0 | 3.5 | 5.6 | < 0.1 | < 0.1 |
| Phenanthrene ng/g | 12 | 27 | 33 | 55 | 8.1 | 18 |
| Anthracene ng/g | 0.5 | 1.2 | 1.3 | 1.2 | 0.5 | 1.0 |
| C1-phenanthrenes ng/g | 23 | 71 | 87 | 155 | 15 | 44 |
| C2-phenanthrenes ng/g | 18 | 62 | 70 | 132 | 12 | 32 |
| C3-phenanthrenes ng/g | 4.1 | 12 | 16 | 27 | 2.0 | 6.3 |
| C4-phenanthrenes ng/g | 1.8 | 2.7 | 3.0 | 7.8 | 0.4 | 1.5 |
| Retene ng/g | 0.6 | 2.1 | 2.2 | 4.2 | 0.2 | 0.9 |
| Fluoranthene ng/g | 2.5 | 6.6 | 7.0 | 9.9 | 3.0 | 5.3 |
| Pyrene ng/g | 2.0 | 4.5 | 5.3 | 6.8 | 1.8 | 3.5 |
| C1-pyrenes ng/g | 11 | 33 | 43 | 84 | 7.7 | 18 |
| Benz[a]anthracene ng/g | 3.6 | 3.8 | 3.3 | 12 | 1.5 | 2.3 |
| Chrysene ng/g | 8.8 | 16 | 15 | 51 | 7.3 | 9.9 |
| C1-chrysenes ng/g | 7.4 | 11 | 11 | 40 | 4.2 | 6.5 |
| C2-chrysenes ng/g | < 0.2 | 8.7 | 10 | 41 | 2.2 | 5.5 |
| C3-chrysenes ng/g | < 0.2 | < 0.2 | < 0.2 | < 0.2 | < 0.2 | < 0.2 |
| Benzo[b+j]fluoranthene ng/g | 5.5 | 5.7 | 5.1 | 15 | 4.0 | 4.7 |
| Benzo[k]fluoranthene ng/g | 2.8 | 3.5 | 4.0 | 11 | 1.5 | 2.1 |
| Benzo[a]fluoranthene ng/g | < 0.3 | < 0.3 | < 0.3 | < 0.3 | < 0.3 | < 0.3 |
| Benzo[e]pyrene ng/g | 3.9 | 6.3 | 7.1 | 20 | 2.7 | 4.5 |
| Benzo[a]pyrene ng/g | 1.7 | 3.5 | 3.6 | 14 | 0.6 | 1.8 |
| Perylene ng/g | 5.5 | 7.4 | 8.8 | 22 | 3.6 | 5.4 |
| Indeno[1,2,3-cd]pyrene ng/g | 0.8 | 1.7 | 1.8 | 2.7 | < 0.5 | 1.0 |
| Benzo[g,h,i]perylene ng/g | 1.8 | 2.4 | 3.9 | 5.7 | 0.8 | 1.6 |
| Dibenz[a,h]anthracene ng/g | < 0.5 | < 0.5 | < 0.5 | < 0.5 | < 0.5 | < 0.5 |

Table 4 continued

| Compounds | IR-18 | TK-2 | TK-4 | TK-5 | TK-6 | TK-7 |
| --- | --- | --- | --- | --- | --- | --- |
| UVF Chrysene equivalent µg/g | 2.1 | 4.6 | 0.18 | 0.5 | 0.13 | 0.25 |
| UVF ROPME oil equivalent µg/g | 14 | 32 | 1.0 | 3.7 | 0.7 | 1.6 |
| Resolved aliphatics µg/g | 3.348 | 16.281 | 0.739 | 1.649 | 0.446 | 1.829 |
| Unresolved aliphatics µg/g | 10.507 | 10.650 | 5.532 | 3.608 | 2.765 | 4.74 |
| Total aliphatics µg/g | 13.855 | 26.931 | 6.271 | 5.257 | 3.211 | 6.569 |
|  n-Alk.C12-C36 µg/g | 1.783 | 2.43 | 0.308 | 0.405 | 0.216 | 0.690 |
| n-C12 ng/g | 17 | 10 | 4.3 | 4.7 | 5.9 | 5.6 |
| n-C13 ng/g | 23 | 10 | 3.1 | 4.3 | 3.8 | 5.1 |
| n-C14 ng/g | 29 | 16 | 5.2 | 6.3 | 7.7 | 7.6 |
| n-C15 ng/g | 95 | 42 | 16 | 13 | 24 | 24 |
| n-C16 ng/g | 73 | 51 | 19 | 12 | 42 | 34 |
| n-C17 ng/g | 126 | 60 | 55 | 16 | 46 | 225 |
| n-C18 ng/g | 51 | 32 | 5.2 | 11 | 7.2 | 20 |
| n-C19 ng/g | 17 | 14 | 3.4 | 4.8 | 2.7 | 1.0 |
| n-C20 ng/g | 33 | 25 | 3.0 | 5.0 | 2.5 | 6.1 |
| n-C21 ng/g | 40 | 24 | 2.2 | 5.3 | 1.3 | 3.8 |
| n-C22 ng/g | 29 | 29 | 3.7 | 6.4 | 2.1 | 4.8 |
| n-C23 ng/g | 39 | 26 | 5.9 | 3.7 | 1.4 | 6.4 |
| n-C24 ng/g | 31 | 30 | 4.4 | 6.3 | 2.6 | 6.5 |
| n-C25 ng/g | 45 | 59 | 2.9 | 8.0 | 1.1 | 3.0 |
| n-C26 ng/g | 38 | 53 | 3.7 | 10 | 1.5 | 7.0 |
| n-C27 ng/g | 157 | 215 | 24 | 31 | 11 | 43 |
| n-C28 ng/g | 56 | 83 | 5.1 | 13 | 1.8 | 16 |
| n-C29 ng/g | 314 | 598 | 35 | 80 | 8.7 | 92 |
| n-C30 ng/g | 37 | 65 | 7.6 | 8.8 | 1.9 | 9.4 |
| n-C31 ng/g | 313 | 611 | 45 | 79 | 15 | 91 |
| n-C32 ng/g | 18 | 40 | 8.4 | 9.4 | 3.2 | 5.7 |
| n-C33 ng/g | 103 | 147 | 13 | 24 | 4.9 | 25 |
| n-C34 ng/g | 34 | 52 | 9.3 | 15 | 4.7 | 16 |
| n-C35 ng/g | 68 | 93 | 12 | 16 | 5.0 | 20 |
| n-C36 ng/g | < 1.7 | 46 | 11 | 11 | 7.6 | 14 |
| Pristane ng/g | 35 | 59 | 7.6 | 10 | 9.7 | 16 |
| Phytane ng/g | 28 | 15 | 4.4 | 6.0 | 4.9 | 12 |
| Squalane ng/g | < 1.1 | 15 | < 1.3 | < 1.3 | < 1.3 | 3.7 |

Table 4 continued

| Compounds | IR-18 | TK-2 | TK-4 | TK-5 | TK-6 | TK-7 |
| --- | --- | --- | --- | --- | --- | --- |
| Resolved aromatics µg/g | 0.713 | 8.055 | 0.115 | 0.202 | 0.023 | 0.173 |
| Unresolved aromatics µg/g | 3.664 | 15.626 | 1.301 | 1.048 | 2.004 | 0.598 |
| Total aromatics µg/g | 4.376 | 23.681 | 1.416 | 1.25 | 2.027 | 0.771 |
| Naphthalene ng/g | 13 | 13 | 0.9 | 1.6 | 1.2 | 1.3 |
| C1-naphthalenes ng/g | 45 | 23 | 1.6 | 3.1 | 2.5 | 2.1 |
| C2-naphthalenes ng/g | 108 | 125 | 4.3 | 8.0 | 9.2 | 9.2 |
| C3-naphthalenes ng/g | 22 | 17 | 1.7 | 2.1 | 2.1 | 2.7 |
| C4-naphthalenes ng/g | 3.8 | 3.0 | < 0.1 | < 0.1 | < 0.1 | < 0.1 |
| Biphenyl ng/g | 7.9 | 7.9 | < 0.2 | 0.7 | < 0.2 | 0.6 |
| Acenaphthylene ng/g | 0.4 | 3.2 | < 0.2 | < 0.2 | < 0.2 | < 0.2 |
| Acenaphthene ng/g | < 0.1 | 2.9 | < 0.3 | < 0.3 | < 0.3 | < 0.3 |
| Fluorene ng/g | 3.2 | 10 | < 0.3 | < 0.3 | < 0.3 | < 0.3 |
| C1-fluorenes ng/g | 7.8 | 12 | < 0.4 | < 0.4 | < 0.4 | < 0.4 |
| C2-fluorenes ng/g | 5.5 | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 |
| C3-fluorenes ng/g | 2.8 | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 |
| Dibenzothiophene ng/g | 2.3 | 7.0 | 5.4 | 5.7 | 6.0 | 5.7 |
| C1-dibenzothiophenes ng/g | 5.1 | 3.4 | < 0.3 | < 0.3 | < 0.3 | < 0.3 |
| C2-dibenzothiophenes ng/g | < 0.1 | 0.9 | < 0.3 | < 0.3 | < 0.3 | < 0.3 |
| C3-dibenzothiophenes ng/g | 2.8 | 11 | < 0.3 | < 0.3 | < 0.3 | < 0.3 |
| C4-dibenzothiophenes ng/g | < 0.1 | < 0.3 | < 0.3 | < 0.3 | < 0.3 | < 0.3 |
| Phenanthrene ng/g | 18 | 12 | < 0.2 | 1.4 | < 0.2 | 0.9 |
| Anthracene ng/g | 0.8 | < 0.2 | < 0.2 | < 0.2 | < 0.2 | < 0.2 |
| C1-phenanthrenes ng/g | 49 | 24 | < 0.5 | 3.1 | < 0.5 | < 0.5 |
| C2-phenanthrenes ng/g | 36 | 25 | < 0.8 | 1.7 | < 0.8 | < 0.8 |
| C3-phenanthrenes ng/g | 6.3 | 10 | < 0.3 | < 0.3 | < 0.3 | < 0.3 |
| C4-phenanthrenes ng/g | 1.1 | 0.9 | < 0.3 | < 0.3 | < 0.3 | < 0.3 |
| Retene ng/g | 0.7 | 0.9 | < 0.3 | < 0.3 | < 0.3 | < 0.3 |
| Fluoranthene ng/g | 5.1 | 4.9 | < 0.3 | < 0.3 | < 0.3 | < 0.3 |
| Pyrene ng/g | 3.4 | 4.5 | < 0.2 | 0.6 | < 0.2 | < 0.2 |
| C1-pyrenes ng/g | 20 | 14 | < 0.7 | < 0.7 | < 0.7 | < 0.7 |
| Benz[a]anthracene ng/g | 2.2 | 4.8 | < 0.9 | 0.5 | < 0.9 | < 0.9 |
| Chrysene ng/g | 9.9 | 12 | < 0.7 | 1.4 | < 0.7 | < 0.7 |
| C1-chrysenes ng/g | 7.0 | 12 | < 0.8 | 1.2 | < 0.8 | < 0.8 |
| C2-chrysenes ng/g | < 0.2 | 14 | < 1.1 | < 1.1 | < 1.1 | < 1.1 |
| C3-chrysenes ng/g | < 0.2 | < 1.1 | < 1.1 | < 1.1 | < 1.1 | < 1.1 |
| Benzo[b+j]fluoranthene ng/g | 6.3 | 20 | < 1.1 | 2.4 | < 1.1 | < 1.1 |
| Benzo[k]fluoranthene ng/g | 2.3 | 12 | < 0.9 | 1.3 | < 0.9 | < 0.9 |
| Benzo[a]fluoranthene ng/g | < 0.3 | 1.8 | < 1.2 | < 1.2 | < 1.2 | < 1.2 |
| Benzo[e]pyrene ng/g | 6.3 | 14 | < 1 | 1.7 | < 1 | < 1 |
| Benzo[a]pyrene ng/g | 3.7 | 8.2 | < 1.1 | < 1.1 | < 1.1 | < 1.1 |
| Perylene ng/g | 5.7 | 3.6 | < 1 | < 1 | < 1 | < 1 |
| Indeno[1,2,3-cd]pyrene ng/g | 1.7 | 11 | < 1.4 | 2.1 | < 1.4 | < 1.4 |
| Benzo[g,h,i]perylene ng/g | 2.8 | 15 | < 1.2 | 2.2 | < 1.2 | < 1.2 |
| Dibenz[a,h]anthracene ng/g | < 0.5 | < 1.4 | < 1.4 | < 1.4 | < 1.4 | < 1.4 |

Table 4 continued

| Compounds | TK-9 | TK-10 | TK-11 | TK-12 | TK-13 | TK-14 |
| --- | --- | --- | --- | --- | --- | --- |
| UVF Chrysene equivalent µg/g | 2.3 | 0.71 | 29 | 0.23 | 2.8 | 1.8 |
| UVF ROPME oil equivalent µg/g | 16 | 4.8 | 205 | 1.4 | 19 | 13 |
| Resolved aliphatics µg/g | 7.590 | 2.102 | 8.591 | 0.913 | 6.551 | 2.124 |
| Unresolved aliphatics µg/g | 26.763 | 9.390 | 80.953 | 4.966 | 32.062 | 12 |
| Total aliphatics µg/g | 34.353 | 11.492 | 89.544 | 5.879 | 38.613 | 14 |
|  n-Alk.C12-C36 µg/g | 3.049 | 0.934 | 1.85 | 0.384 | 2.611 | 0.934 |
| n-C12 ng/g | 8.4 | 6.1 | 9.3 | 6.3 | 10 | 3.0 |
| n-C13 ng/g | 8.4 | 5.7 | 14 | 5.8 | 12 | 2.9 |
| n-C14 ng/g | 11 | 7.8 | 10 | 7.8 | 18 | 6.3 |
| n-C15 ng/g | 61 | 36 | 40 | 23 | 120 | 59 |
| n-C16 ng/g | 68 | 37 | 25 | 44 | 79 | 38 |
| n-C17 ng/g | 618 | 153 | 70 | 59 | 233 | 104 |
| n-C18 ng/g | 39 | 19 | 56 | 19 | 42 | 22 |
| n-C19 ng/g | 2.3 | 1.7 | 19 | 12 | 15 | 14 |
| n-C20 ng/g | 25 | 14 | 28 | 7.4 | 32 | 7.9 |
| n-C21 ng/g | 24 | 26 | 75 | 7.4 | 102 | 21 |
| n-C22 ng/g | 27 | 14 | 39 | 5.9 | 28 | 7.8 |
| n-C23 ng/g | 38 | 21 | 40 | 8.9 | 83 | 22 |
| n-C24 ng/g | 36 | 15 | 40 | 6.0 | 54 | 13 |
| n-C25 ng/g | 32 | 39 | 51 | 4.2 | 102 | 27 |
| n-C26 ng/g | 50 | 12 | 48 | 4.3 | 63 | 30 |
| n-C27 ng/g | 168 | 66 | 10 | 21 | 185 | 54 |
| n-C28 ng/g | 80 | 33 | 69 | 8.7 | 104 | 27 |
| n-C29 ng/g | 627 | 145 | 264 | 28 | 347 | 137 |
| n-C30 ng/g | 67 | 17 | 59 | 4.9 | 76 | 28 |
| n-C31 ng/g | 605 | 132 | 279 | 47 | 292 | 120 |
| n-C32 ng/g | 49 | 19 | 67 | 11 | 85 | 22 |
| n-C33 ng/g | 157 | 36 | 125 | 11 | 124 | 52 |
| n-C34 ng/g | 69 | 22 | 127 | 13 | 103 | 36 |
| n-C35 ng/g | 125 | 36 | 152 | 11 | 207 | 48 |
| n-C36 ng/g | 54 | 21 | 134 | 6.6 | 96 | 32 |
| Pristane ng/g | 25 | 30 | 45 | 33 | 22 | 25 |
| Phytane ng/g | 33 | 17 | 61 | 13 | 34 | 13 |
| Squalane ng/g | < 1.3 | 5.5 | 24 | < 1.3 | < 1.3 | < 1.2 |

Table 4 continued

| Compounds | TK-9 | TK-10 | TK-11 | TK-12 | TK-13 | TK-14 |
| --- | --- | --- | --- | --- | --- | --- |
| Resolved aromatics µg/g | 0.787 | 0.269 | 0.869 | 0.104 | 1.560 | 0.205 |
| Unresolved aromatics µg/g | 2.716 | 1.385 | 23.129 | 2.437 | 11.623 | 2.583 |
| Total aromatics µg/g | 3.503 | 1.654 | 23.998 | 2.541 | 13.183 | 2.79 |
| Naphthalene ng/g | 2.9 | 1.5 | 2.7 | 0.8 | 4.8 | 1.2 |
| C1-naphthalenes ng/g | 4.6 | 1.5 | 5.1 | 1.8 | 6.6 | 1.6 |
| C2-naphthalenes ng/g | 29.1 | 7.4 | 23 | 3.2 | 25 | 5.7 |
| C3-naphthalenes ng/g | 3.9 | 2.0 | 7.3 | 1.1 | 6.4 | 1.4 |
| C4-naphthalenes ng/g | < 0.1 | < 0.1 | < 0.1 | < 0.1 | 1.9 | < 0.2 |
| Biphenyl ng/g | 1.4 | 0.5 | < 0.2 | < 0.2 | 1.3 | 0.5 |
| Acenaphthylene ng/g | 0.9 | < 0.2 | < 0.2 | < 0.2 | < 0.2 | < 0.2 |
| Acenaphthene ng/g | < 0.3 | < 0.3 | < 0.3 | < 0.3 | 0.6 | < 0.2 |
| Fluorene ng/g | 1.0 | < 0.3 | < 0.3 | < 0.3 | 0.9 | < 0.4 |
| C1-fluorenes ng/g | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 |
| C2-fluorenes ng/g | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 |
| C3-fluorenes ng/g | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 |
| Dibenzothiophene ng/g | 6.0 | 5.7 | 5.9 | 6.0 | 5.9 | < 0.3 |
| C1-dibenzothiophenes ng/g | < 0.3 | < 0.3 | < 0.3 | < 0.3 | 2.2 | 0.6 |
| C2-dibenzothiophenes ng/g | < 0.3 | < 0.3 | < 0.3 | < 0.3 | < 0.3 | < 0.3 |
| C3-dibenzothiophenes ng/g | < 0.3 | < 0.3 | < 0.3 | < 0.3 | < 0.3 | < 0.4 |
| C4-dibenzothiophenes ng/g | < 0.3 | < 0.3 | < 0.3 | < 0.3 | < 0.3 | < 0.4 |
| Phenanthrene ng/g | 4.4 | 1.5 | 3.3 | 0.7 | 3.5 | 1.6 |
| Anthracene ng/g | 0.7 | < 0.2 | < 0.2 | < 0.2 | < 0.2 | < 0.3 |
| C1-phenanthrenes ng/g | 10 | 3.0 | 17 | < 0.5 | 14 | 3.5 |
| C2-phenanthrenes ng/g | 10 | 3.1 | 28 | < 0.8 | 6.8 | < 0.8 |
| C3-phenanthrenes ng/g | 2.0 | < 0.3 | 8.0 | < 0.3 | 1.7 | < 0.4 |
| C4-phenanthrenes ng/g | < 0.3 | < 0.3 | 6.0 | < 0.3 | < 0.3 | < 0.4 |
| Retene ng/g | < 0.3 | < 0.3 | < 0.3 | < 0.3 | < 0.3 | < 0.4 |
| Fluoranthene ng/g | 2.4 | 1.0 | 1.4 | < 0.3 | 2.7 | 0.7 |
| Pyrene ng/g | 2.7 | 0.8 | 1.4 | < 0.2 | 2.1 | 0.6 |
| C1-pyrenes ng/g | 2.7 | < 0.7 | 8.9 | < 0.7 | 8.0 | < 0.8 |
| Benz[a]anthracene ng/g | 2.7 | 0.8 | 1.7 | < 0.9 | 3.3 | 1.0 |
| Chrysene ng/g | 6.4 | 1.8 | 4.9 | < 0.7 | 7.3 | 2.5 |
| C1-chrysenes ng/g | 5.2 | 2.6 | 13 | < 0.8 | 8.7 | < 0.8 |
| C2-chrysenes ng/g | < 1.1 | < 1.1 | 24 | < 1.1 | 10 | < 1.2 |
| C3-chrysenes ng/g | < 1.1 | < 1.1 | 27 | < 1.1 | < 1.1 | < 1.2 |
| Benzo[b+j]fluoranthene ng/g | 6.8 | 2.1 | 4.2 | < 1.1 | 2.9 | 1.8 |
| Benzo[k]fluoranthene ng/g | 4.9 | 1.4 | < 0.9 | < 0.9 | 2.0 | 1.4 |
| Benzo[a]fluoranthene ng/g | < 1.2 | < 1.2 | < 1.2 | < 1.2 | < 1.2 | < 1.2 |
| Benzo[e]pyrene ng/g | 5.2 | 2.6 | 6.9 | < 1 | 5.0 | 1.3 |
| Benzo[a]pyrene ng/g | 2.9 | 2.2 | 3.1 | < 1.1 | 2.4 | 1.4 |
| Perylene ng/g | 3.0 | < 1 | 1.8 | < 1 | 3.3 | 1.7 |
| Indeno[1,2,3-cd]pyrene ng/g | 6.0 | 1.7 | 3.2 | < 1.4 | 2.2 | 1.6 |
| Benzo[g,h,i]perylene ng/g | 6.5 | 2.3 | 4.4 | < 1.2 | 3.8 | 1.4 |
| Dibenz[a,h]anthracene ng/g | < 1.4 | < 1.4 | < 1.4 | < 1.4 | < 1.4 | < 1.5 |

Table 4 continued

| Compounds | TK-15 | TK-16 | TK-17 | TK-18 | TK-19 | TK-20 | TK-21 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| UVF Chrysene equivalent µg/g | 3.2 | 7.0 | 0.2 | 0.5 | 2.9 | 1.4 | 6.2 |
| UVF ROPME oil equivalent µg/g | 23 | 48 | 1.0 | 3.7 | 21 | 10 | 45 |
| Resolved aliphatics µg/g | 4.053 | 4.698 | 0.695 | 3.345 | 3.671 | 1.818 | 3.204 |
| Unresolved aliphatics µg/g | 29 | 28 | 5.513 | 7.371 | 10 | 7.266 | 7.553 |
| Total aliphatics µg/g | 33 | 32 | 6.208 | 11 | 14 | 9.084 | 11 |
|  n-Alk.C12-C36 µg/g | 1.906 | 1.862 | 0.391 | 1.198 | 1.382 | 1.109 | 1.442 |
| n-C12 ng/g | 5.5 | 7.1 | 0.6 | 4.2 | 5.0 | 8.4 | 17 |
| n-C13 ng/g | 6.1 | 6.1 | 0.7 | 5.1 | 8.3 | 10 | 16 |
| n-C14 ng/g | 11 | 17 | 1.9 | 8.2 | 8.3 | 15 | 19 |
| n-C15 ng/g | 66 | 44 | 30 | 63 | 87 | 75 | 73 |
| n-C16 ng/g | 43 | 52 | 18 | 64 | 42 | 47 | 48 |
| n-C17 ng/g | 154 | 86 | 51 | 96 | 74 | 143 | 125 |
| n-C18 ng/g | 24 | 29 | 8.5 | 43 | 20 | 67 | 31 |
| n-C19 ng/g | 23 | 23 | 5.6 | 34 | 24 | 32 | 18 |
| n-C20 ng/g | 17 | 16 | 4.3 | 33 | 24 | 28 | 23 |
| n-C21 ng/g | 65 | 150 | 8.0 | 39 | 35 | 24 | 73 |
| n-C22 ng/g | 34 | 23 | 3.3 | 31 | 25 | 17 | 21 |
| n-C23 ng/g | 61 | 17 | 9.0 | 47 | 34 | 25 | 31 |
| n-C24 ng/g | 30 | 18 | 3.0 | 50 | 41 | 15 | 23 |
| n-C25 ng/g | 72 | 29 | 11 | 56 | 57 | 38 | 51 |
| n-C26 ng/g | 51 | 40 | 4.0 | 31 | 33 | 18 | 23 |
| n-C27 ng/g | 151 | 106 | 14 | 83 | 100 | 70 | 106 |
| n-C28 ng/g | 98 | 121 | 5.7 | 71 | 84 | 25 | 47 |
| n-C29 ng/g | 312 | 312 | 38 | 144 | 182 | 141 | 221 |
| n-C30 ng/g | 43 | 91 | 4.8 | 32 | 63 | 21 | 39 |
| n-C31 ng/g | 259 | 263 | 35 | 116 | 177 | 145 | 225 |
| n-C32 ng/g | 50 | 59 | 13 | 28 | 54 | 10 | 15 |
| n-C33 ng/g | 101 | 109 | 13 | 46 | 75 | 57 | 67 |
| n-C34 ng/g | 68 | 77 | 13 | 21 | 47 | 28 | 45 |
| n-C35 ng/g | 96 | 99 | 47 | 30 | 42 | 36 | 64 |
| n-C36 ng/g | 64 | 69 | 50 | 26 | 39 | 12 | 20 |
| Pristane ng/g | 13 | 36 | 7.3 | 65 | 15 | 46 | 16 |
| Phytane ng/g | 16 | 13 | 6.7 | 22 | 10 | 32 | 11 |
| Squalane ng/g | < 1.2 | < 1.2 | 1.6 | 14 | < 1.2 | < 1.2 | < 1.2 |

Table 4 continued

| Compounds | TK-15 | TK-16 | TK-17 | TK-18 | TK-19 | TK-20 | TK-21 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Resolved aromatics µg/g | 0.625 | 0.487 | 0.11 | 0.387 | 0.493 | 0.224 | 0.625 |
| Unresolved aromatics µg/g | 5.664 | 4.67 | 2.805 | 4.332 | 6.151 | 4.269 | 8.875 |
| Total aromatics µg/g | 6.29 | 5.16 | 2.92 | 4.72 | 6.64 | 4.49 | 9.5 |
| Naphthalene ng/g | 2.2 | 30.4 | 0.4 | 1.7 | 2.4 | 3.7 | 6.7 |
| C1-naphthalenes ng/g | 2.6 | 5.1 | 0.5 | 3.2 | 4.7 | 9.5 | 19 |
| C2-naphthalenes ng/g | 10 | 18 | 5.6 | 11 | 19 | 25 | 48 |
| C3-naphthalenes ng/g | 2.1 | 3.7 | 0.9 | 1.4 | 2.6 | 4.2 | 6.7 |
| C4-naphthalenes ng/g | < 0.2 | 0.6 | < 0.2 | < 0.2 | < 0.2 | < 0.2 | 2.1 |
| Biphenyl ng/g | 0.9 | 1.4 | 0.3 | 1.1 | 1.3 | < 0.2 | 4.2 |
| Acenaphthylene ng/g | < 0.2 | < 0.2 | < 0.2 | < 0.2 | < 0.2 | 2.3 | 0.5 |
| Acenaphthene ng/g | < 0.2 | < 0.2 | < 0.2 | < 0.2 | < 0.2 | < 0.2 | 0.3 |
| Fluorene ng/g | 0.3 | 0.5 | < 0.4 | 0.4 | 0.7 | 0.7 | 1.3 |
| C1-fluorenes ng/g | < 0.4 | 0.6 | < 0.4 | 2.9 | < 0.4 | 2.5 | 4.7 |
| C2-fluorenes ng/g | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 | 3.0 |
| C3-fluorenes ng/g | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 |
| Dibenzothiophene ng/g | 0.5 | < 0.3 | < 0.3 | < 0.3 | < 0.3 | < 0.3 | 0.3 |
| C1-dibenzothiophenes ng/g | 0.8 | 1.5 | < 0.3 | 1.2 | < 0.3 | < 0.3 | 3.4 |
| C2-dibenzothiophenes ng/g | < 0.3 | < 0.3 | < 0.3 | < 0.3 | < 0.3 | < 0.3 | 9.8 |
| C3-dibenzothiophenes ng/g | < 0.4 | 1.5 | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 |
| C4-dibenzothiophenes ng/g | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 |
| Phenanthrene ng/g | 2.4 | 3.7 | 0.6 | 3.0 | 2.8 | 7.4 | 15 |
| Anthracene ng/g | 0.6 | < 0.3 | < 0.3 | < 0.3 | < 0.3 | < 0.3 | 0.8 |
| C1-phenanthrenes ng/g | 6.7 | 9.4 | 1.2 | 7.2 | 7.3 | 18 | 44 |
| C2-phenanthrenes ng/g | 6.0 | 8.7 | < 0.8 | 3.5 | 5.3 | 14 | 33 |
| C3-phenanthrenes ng/g | 1.3 | 2.5 | < 0.4 | < 0.4 | < 0.4 | < 0.4 | 4.2 |
| C4-phenanthrenes ng/g | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 |
| Retene ng/g | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 |
| Fluoranthene ng/g | 1.7 | 2.2 | 0.3 | 1.1 | 1.0 | 1.4 | 2.7 |
| Pyrene ng/g | 1.7 | 1.8 | < 0.2 | 0.9 | 0.8 | 1.3 | 2.0 |
| C1-pyrenes ng/g | 3.2 | 5.6 | < 0.8 | < 0.8 | < 0.8 | < 0.8 | 14 |
| Benz[a]anthracene ng/g | 1.3 | 1.3 | < 1 | 1.0 | < 0.8 | 3.8 | 4.0 |
| Chrysene ng/g | 4.1 | 3.3 | < 0.7 | 1.9 | 2.6 | 5.5 | 12 |
| C1-chrysenes ng/g | 3.9 | 5.0 | < 0.8 | < 0.8 | < 0.8 | < 0.8 | 1.0 |
| C2-chrysenes ng/g | < 1.2 | < 1.2 | < 1.2 | < 1.2 | < 1.2 | < 1.2 | < 1.2 |
| C3-chrysenes ng/g | < 1.2 | < 1.2 | < 1.2 | < 1.2 | < 1.2 | < 1.2 | < 1.2 |
| Benzo[b+j]fluoranthene ng/g | 3.7 | 2.3 | < 1.2 | 1.5 | 2.0 | 4.6 | 8.1 |
| Benzo[k]fluoranthene ng/g | 2.6 | 2.1 | < 0.9 | < 0.9 | 1.5 | 1.9 | 3.7 |
| Benzo[a]fluoranthene ng/g | < 1.2 | < 1.2 | < 1.2 | < 1.2 | < 1.2 | < 1.2 | < 1.2 |
| Benzo[e]pyrene ng/g | 3.5 | 2.8 | < 1 | 1.6 | 2.7 | 3.9 | 6.6 |
| Benzo[a]pyrene ng/g | 2.3 | 2.2 | < 1.1 | 1.6 | < 1.1 | 1.6 | 2.8 |
| Perylene ng/g | 2.2 | 1.2 | < 1 | 2.1 | 1.2 | 1.9 | 4.4 |
| Indeno[1,2,3-cd]pyrene ng/g | 2.5 | 2.8 | < 1.5 | 1.3 | 2.8 | 2.4 | 4.7 |
| Benzo[g,h,i]perylene ng/g | 3.1 | 3.1 | < 1.2 | 1.4 | 1.6 | 2.9 | 5.5 |
| Dibenz[a,h]anthracene ng/g | < 1.5 | < 1.5 | < 1.5 | < 1.5 | < 1.5 | < 1.5 | < 1.5 |

Table 4 Continued

| Compounds | IAEA-408 QA/QC value | IAEA-408 QA/QC value | IAEA-408 QA/QC value | IAEA-408 QA/QC value | IAEA-408 Reference value |
| --- | --- | --- | --- | --- | --- |
| UVF Chrysene equiv. µg/g | 5.6 | 6.4 | 7.4 | 7.6 | 9.9  |
| UVF ROPME oil equiv. µg/g | 39 | 45 | 51 | 53 | 79  |
| Resolved aliphatics µg/g | 12.170 | 12 | 11.971 | 10.125 | 12  |
| Unresolved aliphatics µg/g | 97.748 | 95 | 88.633 | 75.196 | 110  |
| Total aliphatics µg/g | 109.918 | 108 | 100.604 | 85.322 | 120  |
|  n-Alkanes C14-C34 µg/g | 6.829 | 6.668 | 6.741 | 6.115 | 8.6  |
| n-C12 ng/g | 29 | 19 | 32 | 18 | - |
| n-C13 ng/g | 34 | 26 | 43 | 31 | - |
| n-C14 ng/g | 61 | 57 | 64 | 56 | - |
| n-C15 ng/g | 102 | 277 | 308 | 211 | - |
| n-C16 ng/g | 104 | 101 | 110 | 95 | - |
| n-C17 ng/g | 146 | 192 | 195 | 144 | 98  |
| n-C18 ng/g | 81 | 68 | 81 | 79 | 81  |
| n-C19 ng/g | 69 | 67 | 139 | 122 | - |
| n-C20 ng/g | 55 | 18 | 61 | 45 | - |
| n-C21 ng/g | 103 | 81 | 96 | 88 | - |
| n-C22 ng/g | 87 | 71 | 76 | 81 | - |
| n-C23 ng/g | 165 | 158 | 190 | 160 | - |
| n-C24 ng/g | 111 | 98 | 116 | 104 | - |
| n-C25 ng/g | 295 | 254 | 255 | 277 | - |
| n-C26 ng/g | 160 | 176 | 110 | 104 | - |
| n-C27 ng/g | 630 | 619 | 628 | 552 | - |
| n-C28 ng/g | 182 | 231 | 198 | 189 | - |
| n-C29 ng/g | 1475 | 1393 | 1445 | 1325 | - |
| n-C30 ng/g | 185 | 167 | 163 | 163 | - |
| n-C31 ng/g | 1374 | 1293 | 1214 | 1153 | - |
| n-C32 ng/g | 180 | 201 | 190 | 170 | - |
| n-C33 ng/g | 633 | 622 | 582 | 552 | - |
| n-C34 ng/g | 162 | 175 | 154 | 147 | - |
| n-C35 ng/g | 278 | 209 | 204 | 168 | - |
| n-C36 ng/g | 126 | 99 | 88 | 79 | - |
| Pristane ng/g | 71 | 70 | 93 | 64 | 98  |
| Phytane ng/g | 117 | 110 | 125 | 101 | 100  |
| Squalane ng/g | 78 | 81 | 49 | 40 | - |

Table 4 Continued

| Compounds | IAEA-408 QA/QC value | IAEA-408 QA/QC value | IAEA-408 QA/QC value | IAEA-408 QA/QC value | IAEA-408 Reference value |
| --- | --- | --- | --- | --- | --- |
| Resolved aromatics µg/g | 0.812 | 0.763 | 1.495 | 2.251 | 3.5  |
| Unresolved aromatics µg/g | 12.642 | 5.768 | 16.535 | 19.208 | - |
| Total aromatics µg/g | 13.454 | 6.53 | 18.029 | 21.459 | 6.3  |
| Naphthalene ng/g | 26 | 26 | 27 | 29 | 34  |
| C1-naphthalenes ng/g | 24 | 32 | 33 | 43 | - |
| C2-naphthalenes ng/g | 80 | 82 | 73 | 138 | - |
| C3-naphthalenes ng/g | 14 | 14 | 20 | 36 | - |
| C4-naphthalenes ng/g | 1.8 | 2.6 | 6.2 | 12 | - |
| Biphenyl ng/g | 8.3 | 9.0 | 8.2 | 12 | - |
| Acenaphthylene ng/g | 3.2 | 3.7 | 4.2 | 5.7 | 3.4  |
| Acenaphthene ng/g | 2.2 | 2.5 | 2.6 | 4.8 | 9.7  |
| Fluorene ng/g | 4.4 | 5.0 | 5.6 | 8.7 | 13  |
| C1-fluorenes ng/g | 5.9 | 7.8 | 8.9 | 14 | - |
| C2-fluorenes ng/g | 5.3 | 11 | 8.5 | 20 | - |
| C3-fluorenes ng/g | 6.9 | 7.9 | 10 | 12 | - |
| Dibenzothiophene ng/g | 7.3 | < 0.3 | 7.1 | 7.3 | - |
| C1-dibenzothiophenes ng/g | 15 | 18 | 17 | 20 | - |
| C2-dibenzothiophenes ng/g | 34 | 53 | 60 | 49 | - |
| C3-dibenzothiophenes ng/g | 46 | 58 | 58 | 63 | - |
| C4-dibenzothiophenes ng/g | 21 | 29 | 30 | 322 | - |
| Phenanthrene ng/g | 42 | 50 | 43 | 42 | 35  |
| Anthracene ng/g | 8.3 | 8.5 | 10 | 10 | 11  |
| C1-phenanthrenes ng/g | 78 | 79 | 79 | 77 | - |
| C2-phenanthrenes ng/g | 126 | 117 | 112 | 113 | - |
| C3-phenanthrenes ng/g | 36 | 41 | 48 | 48 | - |
| C4-phenanthrenes ng/g | 6.4 | 9.5 | 18 | 22 | - |
| Retene ng/g | 9.3 | 9.5 | 9.2 | 8.9 | - |
| Fluoranthene ng/g | 100 | 121 | 177 | 112 | 85  |
| Pyrene ng/g | 54 | 65 | 103 | 67 | 76  |
| C1-pyrenes ng/g | 91 | 118 | 170 | 112 | - |
| Benz[a]anthracene ng/g | 90 | 98 | 98 | 95 | 50  |
| Chrysene ng/g | 90 | 113 | 75 | 95 | 38  |
| C1-chrysenes ng/g | 54 | 79 | 58 | 50 | - |
| C2-chrysenes ng/g | 63 | 74 | 56 | 61 | - |
| C3-chrysenes ng/g | 33 | 62 | 36 | 44 | - |
| Benzo[b+j]fluoranthene ng/g | 51 | 89 | 48 | 65 | - |
| Benzo[k]fluoranthene ng/g | 114 | 146 | 84 | 136 |  |
| Benzo[a]fluoranthene ng/g | 17 | 15 | 7.5 | 9.1 |  |
| Benzo[e]pyrene ng/g | 61 | 97 | 63 | 95 | 66  |
| Benzo[a]pyrene ng/g | 42 | 69 | 61 | 82 | 49  |
| Perylene ng/g | 132 | 336 | 163 | 220 | 270  |
| Indeno[1,2,3-cd]pyrene ng/g | 25 | 51 | 24 | 53 | 49  |
| Benzo[g,h,i]perylene ng/g | 28 | 49 | 23 | 60 | 36  |
| Dibenz[a,h]anthracene ng/g | 2.0 | 8.2 | 1.6 | 2.3 | 11  |

## III.3		Chlorinated Pesticides and PCBs

Table 5: Results of Chlorinated Pesticides in sediment samples. Results are expressed in pg/g

dry weight.

| Compounds | IR-1 | IR-2 | IR-3 | IR-4 | IR-5 | IR-6 |
| --- | --- | --- | --- | --- | --- | --- |
| HCB | 5.0 | 16 | 16 | 13 | 25 | 2.5 |
|  HCH | 5.0 | 9.0 | 14 | 7.0 | 12 | 3.0 |
|  HCH | 48 | 81 | 81 | 48 | 27 | 18 |
| Lindane | 2.0 | 4.0 | 2.5 | 2.0 | 12 | < 0.9 |
| -HCH | < 1 | < 1 | < 1 | < 1 | < 1 | < 1 |
| pp’ DDE | 40 | 130 | 185 | 655 | 820 | 85 |
| pp’ DDD | 36 | 160 | 290 | 64 | 635 | 78 |
| pp’ DDT | 4.0 | 45 | 47 | 4400 | 280 | 14 |
| DDMU | 20 | 94 | 165 | 105 | 86 | 35 |
| op DDE | 3.0 | 9.0 | 11 | 53 | 36 | 3.0 |
| op DDD | 24 | 97 | 125 | 235 | 320 | 32 |
| op DDT | 8.0 | 11 | 15 | 1310 | 74 | 6.0 |
| cis chlordane | < 1 | 3.0 | < 1 | 3.0 | 7.0 | < 1 |
| trans chlordane | < 1 | 3.0 | < 1 | 5.0 | 15 | < 1 |
| trans nonachlor | 1.0 | 1.5 | < 0.4 | < 0.4 | 1.0 | < 0.4 |
| Heptachlor | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 |
| Aldrin | 2.0 | < 0.3 | < 0.3 | < 0.3 | < 0.3 | < 0.4 |
| Dieldrin | 15 | 23 | 3.0 | 4.0 | 8.0 | 1.0 |
| Endrin | 6.0 | 7.0 | < 1.5 | < 1.5 | 5.0 | < 1.5 |
| Heptachlor epoxide | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 |
| Methoxychlor | 4.0 | 32 | 1.5 | 2.0 | 2.0 | < 1 |
|  Endosulfan | < 0.3 | < 0.3 | < 0.3 | < 0.3 | < 0.3 | < 0.3 |
|  Endosulfan | 2.0 | 3.0 | < 0.4 | < 0.4 | 2.0 | < 0.4 |
| Endosulfan sulfate | 4.0 | 7.0 | 1.5 | 1.0 | 2.5 | < 0.4 |

Table 5: continued

| Compounds | IR-7 | IR-8 | IR-9 | IR-10 | IR-11 | IR-12 |
| --- | --- | --- | --- | --- | --- | --- |
| HCB | 9.0 | 13 | 20 | 58 | 22 | 19 |
|  HCH | 6.0 | 6.0 | 7.0 | 27 | 10 | 9.0 |
|  HCH | 35 | 36 | 69 | 95 | 86 | 135 |
| Lindane | 2.0 | 2.0 | 2.0 | 13 | 1.5 | 4.0 |
| -HCH | 2.5 | < 1 | < 1 | < 1 | < 1 | < 1 |
| pp’ DDE | 170 | 240 | 330 | 1630 | 475 | 355 |
| pp’ DDD | 160 | 160 | 205 | 990 | 325 | 350 |
| pp’ DDT | 36 | 65 | 190 | 2070 | 390 | 640 |
| DDMU | 88 | 80 | 64 | 120 | 150 | 115 |
| op DDE | 14 | 12 | 8.0 | 120 | 20 | 21 |
| op DDD | 64 | 66 | 84 | 465 | 105 | 120 |
| op DDT | 11 | 18 | 27 | 615 | 36 | 30 |
| cis chlordane | < 1 | 2.0 | 6.0 | 12 | 4.0 | 5.0 |
| trans chlordane | < 1 | 3.0 | 4.0 | 15 | 5.0 | 1.5 |
| trans nonachlor | < 0.4 | < 0.4 | 1.0 | 7.0 | 1.0 | < 0.4 |
| Heptachlor | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 |
| Aldrin | < 0.3 | < 0.3 | < 0.3 | < 0.3 | < 0.3 | < 0.3 |
| Dieldrin | 4.0 | 4.0 | 8.0 | 19 | 13 | 11 |
| Endrin | < 1.5 | < 1.5 | 4.0 | 5.0 | < 1.5 | 12 |
| Heptachlor epoxide | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 | 2.0 |
| Methoxychlor | < 1 | < 1 | < 1 | 1.5 | 8.0 | 17 |
|  Endosulfan | < 0.3 | < 0.3 | < 0.3 | 7.0 | < 0.3 | < 0.3 |
|  Endosulfan | 1.5 | < 0.4 | < 0.4 | 5.0 | 3.0 | < 0.4 |
| Endosulfan sulfate | < 0.4 | 1 | 2.5 | 2.0 | < 0.4 | 1.5 |

Table 5: continued

| Compounds | IR-13 | IR-14 | IR-15 | IR-16 | IR-16A | IR-17 |
| --- | --- | --- | --- | --- | --- | --- |
| HCB | 7.0 | 19 | 18 | 29 | 8.0 | 15 |
|  HCH | 4.0 | 7.0 | 9.0 | 9.0 | 4.0 | 7.0 |
|  HCH | 35 | 79 | 92 | 125 | 36 | 66 |
| Lindane | 1.5 | 6.0 | 6.0 | 6.0 | 1.0 | 3.0 |
| -HCH | < 1 | < 1 | < 1 | < 1 | < 1 | 2.0 |
| pp’ DDE | 150 | 405 | 520 | 760 | 175 | 345 |
| pp’ DDD | 130 | 295 | 310 | 330 | 210 | 265 |
| pp’ DDT | 91 | 155 | 155 | 155 | 30 | 140 |
| DDMU | 41 | 165 | 130 | 160 | 115 | 165 |
| op DDE | 6.0 | 23 | 21 | 34 | 8.0 | 13 |
| op DDD | 2.0 | 110 | 130 | 145 | 69 | 93 |
| op DDT | 31 | 25 | 37 | 56 | 9.0 | 16 |
| cis chlordane | 1.5 | 2.5 | 3.0 | 4.0 | < 1 | < 1 |
| trans chlordane | 1.5 | 5.0 | 8.0 | 2.5 | < 1 | < 1 |
| trans nonachlor | < 0.4 | < 0.4 | 3.0 | 0.9 | < 0.4 | 0.8 |
| Heptachlor | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 |
| Aldrin | < 0.3 | < 0.3 | < 0.3 | < 0.3 | < 0.3 | < 0.3 |
| Dieldrin | 4.0 | 7.0 | 17 | 16 | 2.5 | 6.0 |
| Endrin | 3.0 | 15 | < 1.5 | 7.0 | < 1.5 | 3.0 |
| Heptachlor epoxide | 0.9 | 1.5 | 1.7 | 1.7 | < 0.4 | < 0.4 |
| Methoxychlor | 5.0 | 80 | 4.0 | 75 | 5.0 | 11 |
|  Endosulfan | < 0.3 | < 0.3 | < 0.3 | < 0.3 | < 0.3 | < 0.3 |
|  Endosulfan | < 0.4 | 1.5 | 0.9 | 9.0 | < 0.4 | < 0.4 |
| Endosulfan sulfate | 0.8 | 1.0 | 2.0 | 2.5 | 1.0 | 1.5 |

Table 5: continued

| Compounds | IR-18 | TK-2 | TK-4 | TK-5 | TK-6 | TK-7 |
| --- | --- | --- | --- | --- | --- | --- |
| HCB | 22 | 70 | 9.0 | 52 | 1.0 | 3.0 |
|  HCH | 5.0 | 29 | < 1 | 6.0 | 2.0 | 4.0 |
|  HCH | 69 | 330 | 26 | 47 | < 3 | 53 |
| Lindane | 1.5 | 19 | 2.0 | 4.0 | 2.5 | 6.0 |
| -HCH | 1.5 | 72 | < 1 | < 1 | < 1 | < 1 |
| pp’ DDE | 465 | 730 | 14 | 75 | 4.0 | 55 |
| pp’ DDD | 185 | 165 | 2.5 | 25 | 2.0 | 15 |
| pp’ DDT | 51 | 135 | 5.0 | 22 | 2.0 | 9.0 |
| DDMU | 165 | 46 | 3.0 | 25 | < 1 | 8.0 |
| op DDE | 14 | 32 | 4.0 | 11 | < 1 | 9.0 |
| op DDD | 71 | 115 | 12 | 27 | 13 | 27 |
| op DDT | 17 | 58 | 2.0 | 12 | < 2.5 | 5.0 |
| cis chlordane | 2.0 | 18 | < 1 | 4.0 | < 1 | 2.0 |
| trans chlordane | 2.0 | 11 | < 1 | < 1 | < 1 | 3.0 |
| trans nonachlor | < 0.4 | 18 | < 0.5 | < 0.5 | < 0.5 | < 0.5 |
| Heptachlor | < 0.4 | < 0.5 | < 0.5 | < 0.5 | < 0.5 | < 0.5 |
| Aldrin | < 0.3 | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 |
| Dieldrin | 8.0 | 53 | 2.0 | 6.0 | 1.5 | 6.0 |
| Endrin | 5.0 | 21 | < 2 | < 2 | < 2 | < 2 |
| Heptachlor epoxide | < 0.4 | 7.0 | < 0.5 | < 0.5 | < 0.5 | 2.0 |
| Methoxychlor | 12 | 5.0 | < 1.5 | < 1.5 | 4.0 | < 1.5 |
|  Endosulfan | 5.0 | 12 | < 0.3 | < 0.3 | < 0.3 | < 0.3 |
|  Endosulfan | 1.5 | 3.0 | < 0.4 | 1.5 | 1.5 | 1.5 |
| Endosulfan sulfate | 2.0 | 8.0 | < 0.5 | < 0.5 | 2.5 | 1.0 |

Table 5: continued

| Compounds | TK-9 | TK-10 | TK-11 | TK-12 | TK-13 | TK-14 |
| --- | --- | --- | --- | --- | --- | --- |
| HCB | 20 | 15 | 14 | 8.0 | 20 | 7.0 |
|  HCH | 13 | 5.0 | 6.0 | 2.0 | 7.0 | 4.0 |
|  HCH | 220 | 36 | 110 | 19 | 72 | 62 |
| Lindane | 8.0 | 5.0 | 5.0 | 4.0 | 5.0 | 7.0 |
| -HCH | 29 | < 1 | 7.0 | < 1 | < 1 | < 1 |
| pp’ DDE | 205 | 41 | 175 | 8.0 | 50 | 24 |
| pp’ DDD | 45 | 16 | 80 | 4.0 | 40 | 4.0 |
| pp’ DDT | 45 | 11 | 35 | 3.0 | 16 | 2.5 |
| DDMU | 21 | 4.0 | 30 | < 1 | 12 | < 1 |
| op DDE | 19 | 8.0 | 7.0 | 3.0 | 9.0 | 3.0 |
| op DDD | 53 | 24 | 47 | 9.0 | 31 | 6.0 |
| op DDT | 20 | 5.0 | 11 | < 2.5 | 5.0 | 2.5 |
| cis chlordane | 9.0 | 4.0 | 5.0 | < 1 | 2.0 | 1.5 |
| trans chlordane | 5.0 | < 1 | 8.0 | < 1 | 3.0 | < 1 |
| trans nonachlor | 4.0 | < 0.5 | 4.0 | 1.0 | < 0.5 | < 0.5 |
| Heptachlor | < 0.5 | < 0.5 | < 0.5 | < 0.5 | < 0.5 | < 0.5 |
| Aldrin | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 | 12 |
| Dieldrin | 26 | 3.5 | 11 | 1.5 | 6.0 | 4.0 |
| Endrin | 7.0 | < 2 | 6.0 | < 2 | 2.0 | < 2 |
| Heptachlor epoxide | 3.0 | < 0.5 | 3.0 | < 0.5 | < 0.5 | < 0.5 |
| Methoxychlor | 8.0 | < 1.5 | 4.0 | < 1.5 | < 1.5 | < 1.5 |
|  Endosulfan | 6.0 | < 0.3 | < 0.3 | < 0.3 | 4.0 | < 0.3 |
|  Endosulfan | 4.0 | < 0.4 | 3.0 | < 0.4 | < 0.4 | 1.0 |
| Endosulfan sulfate | 7.0 | 1.0 | 2.0 | < 0.5 | < 0.5 | < 0.5 |

Table 5: continued

| Compounds | TK-15 | TK-16 | TK-17 | TK-18 | TK-19 | TK-20 | TK-21 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| HCB | 15 | 32 | 2.5 | 9.0 | 15 | 12 | 26 |
|  HCH | 15 | 5.0 | < 1 | 3.0 | 6.0 | 6.0 | 9.0 |
|  HCH | 145 | 175 | 15 | 51 | 95 | 91 | 168 |
| Lindane | 12 | 5.0 | < 0.6 | 13 | 6.0 | 10 | 4.0 |
| -HCH | 3.0 | < 1 | < 1 | < 1 | < 1 | < 1 | < 1 |
| pp’ DDE | 54 | 142 | 5.0 | 29 | 42 | 108 | 205 |
| pp’ DDD | 36 | 31 | < 1.5 | 9.0 | 15 | 48 | 118 |
| pp’ DDT | 16 | 19 | < 1.5 | 5.0 | 4.0 | 9.0 | 31 |
| DDMU | 13 | 17 | < 1 | 24 | 14 | 76 | 67 |
| op DDE | 4.0 | 9.0 | 2.5 | 4.0 | 4.0 | 4.0 | 9.0 |
| op DDD | 29 | 24 | 6.0 | 9.0 | 12 | 21 | 58 |
| op DDT | 8.0 | 11 | < 2.5 | 16 | < 2.5 | < 2.5 | 11 |
| cis chlordane | 2.5 | 2.5 | < 1 | < 1 | < 1 | < 1 | 2.5 |
| trans chlordane | 3.0 | 2.0 | < 1 | < 1 | < 1 | < 1 | 4.0 |
| trans nonachlor | < 0.5 | < 0.5 | < 0.5 | < 0.5 | < 0.5 | < 0.5 | < 0.5 |
| Heptachlor | < 0.5 | < 0.5 | < 0.5 | < 0.5 | < 0.5 | < 0.5 | < 0.5 |
| Aldrin | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 | < 0.4 |
| Dieldrin | 10 | 9.0 | 9.0 | 11 | 6.0 | 28 | 19 |
| Endrin | < 2 | 7.0 | 8.0 | < 2 | 2.5 | 11 | 17 |
| Heptachlor epoxide | 1.5 | 7.0 | 3.0 | 8.0 | 8.0 | 6.0 | 6.0 |
| Methoxychlor | < 1.5 | < 1.5 | < 1.5 | 7.0 | < 1.5 | 9.0 | 2.5 |
|  Endosulfan | < 0.3 | < 0.3 | < 0.3 | 5.0 | < 0.3 | < 0.3 | < 0.3 |
|  Endosulfan | 4.0 | 0.5 | 1.5 | 1.0 | < 0.4 | 1.5 | < 0.4 |
| Endosulfan sulfate | 1.0 | 5.0 | < 0.5 | < 0.5 | < 0.5 | < 0.5 | < 0.5 |

Table 5 continued

| Compounds | IAEA-408 QA/QC Value | IAEA-408 QA/QC Value | IAEA-408 QA/QC Value | IAEA-408 QA/QC Value | IAEA-408 Reference Value |
| --- | --- | --- | --- | --- | --- |
| HCB | 370 | 370 | 420 | 530 | 450 ± 190 |
|  HCH | 17 | 39 | 35 | 20 | 870 ± 910* |
|  HCH | 79 | 250 | 220 | 150 | 920 ± 850* |
| Lindane | 83 | 200 | 160 | 130 | 170 ± 70 |
| pp’ DDE | 1100 | 1100 | 1100 | 1200 | 1400 ± 630 |
| pp’ DDD | 690 | 850 | 650 | 820 | 1100 ± 740* |
| pp’ DDT | 710 | 790 | 790 | 620 | 740 ± 350 |
| op DDD | 540 | 670 | 330 | 400 | 250 ± 130* |
| op DDT | 210 | 250 | 270 | 180 | 1400 ± 2100* |
| cis chlordane | 59 | 74 | 67 | 67 | 250 ± 250* |
| trans chlordane | 110 | 110 | 69 | 100 | 360 ± 370* |
| Heptachlor Epoxide | 10 | 9.0 | 10 | 12 | 1000 ± 820* |
| Heptachlor | 9.0 | 2.0 | 4.0 | 2.0 | 440 ± 270* |
| Aldrin | - | 8.0 | 11 | 7.0 | 1200 ± 1400* |
| Dieldrin | 350 | 350 | 370 | 340 | 360 ± 190 |
| Endrin | 29 | 44 | 39 | 49 | 650 ± 470* |
|  Endosulfan | 15 | 9.0 | 8.0 | 15 | 2700 ± 3100* |
| Endosulfan sulfate | 12 | 7.0 | 5.0 | 12 | 3400 ± 4200* |

“*”: information value only

“-“ : not analyzed

Table 6 Results of PCBs in sediment samples. Results in pg/g dry weight.

| Compounds | IR-1 | IR-2 | IR-3 | IR-4 | IR-5 | IR-6 |
| --- | --- | --- | --- | --- | --- | --- |
| Aroclor 1254 | 76 | 585 | 190 | 275 | 225 | 49 |
| Aroclor 1260 | < 10 | 485 | 14 | 37 | 15 | 25 |
| PCB 8 | 9.0 | 20 | 15 | 21 | 26 | 13 |
| PCB 18 | 4.0 | 17 | 11 | 10 | 14 | 3.0 |
| PCB 28 | 4.0 | 12 | 7.0 | 12 | 12 | 1.0 |
| PCB 31 | < 0.8 | < 0.8 | 7.0 | 11 | 12 | 1.0 |
| PCB 44 | < 0.8 | 9.0 | < 0.8 | 4.0 | < 0.8 | 1.0 |
| PCB 49 | < 1 | 9.0 | 11 | 9.0 | 6.0 | < 1 |
| PCB 52 | 11 | 26 | 12 | 15 | 18 | 3.0 |
| PCB 66/95 | 2.5 | 46 | 8.0 | 25 | 28 | 1.5 |
| PCB 87 | 1.5 | 17 | 6.0 | 6.0 | 7.0 | 2.0 |
| PCB 97 | 5.0 | 18 | 12 | 12 | 8.0 | 3.0 |
| PCB 101 | 6.0 | 59 | 10 | 15 | 11 | 2.5 |
| PCB 105 | 2.0 | 12 | 4.0 | 4.0 | 1.5 | < 0.5 |
| PCB 110/77 | 7.0 | 61 | 15 | 28 | 11 | 5.0 |
| PCB 118 | 6.0 | 34 | 11 | 13 | 7.0 | 4.0 |
| PCB 126 | < 0.7 | 7.0 | 1.5 | < 0.7 | < 0.7 | < 0.7 |
| PCB 128 | < 0.5 | 12 | 2.0 | 3.0 | 0.8 | 1.5 |
| PCB 138 | 1.0 | 82 | 9.0 | 18 | 8.0 | 6.0 |
| PCB 149 | 5.0 | 68 | 7.0 | 10 | 7.0 | 2.0 |
| PCB 153 | 3.0 | 73 | 7.0 | 10 | 7.0 | 7.0 |
| PCB 156 | < 0.7 | < 0.7 | < 0.7 | < 0.7 | < 0.7 | < 0.7 |
| PCB 169 | < 0.8 | < 0.8 | < 0.8 | < 0.8 | < 0.8 | < 0.8 |
| PCB 170 | 1.0 | 23 | 1.0 | < 0.6 | 0.8 | < 0.6 |
| PCB 174 | < 0.5 | 26 | < 0.5 | 2.5 | < 0.5 | 2.0 |
| PCB 177 | < 0.5 | 12 | < 0.5 | 1.0 | < 0.5 | < 0.5 |
| PCB 180 | 1.5 | 48 | 1.5 | 5.0 | 2.5 | < 0.6 |
| PCB 183 | < 0.5 | 11 | < 0.5 | < 0.5 | < 0.5 | 1.5 |
| PCB 187 | < 0.6 | 42 | 2.0 | 5.0 | 1.5 | 9.0 |
| PCB 189 | < 0.6 | < 0.6 | < 0.6 | < 0.6 | < 0.6 | < 0.6 |
| PCB 194 | < 0.5 | 9.0 | 2.5 | 1.0 | < 0.5 | < 0.5 |
| PCB 195 | < 0.5 | 6.0 | < 0.6 | < 0.6 | < 0.6 | < 0.6 |
| PCB 201 | < 0.6 | 4.0 | 1.0 | < 0.7 | < 0.7 | < 0.7 |
| PCB 206 | < 0.5 | 3.0 | < 0.8 | < 0.8 | < 0.8 | < 0.8 |
| PCB 209 | < 0.5 | < 0.5 | < 1 | < 1 | < 1 | < 1 |

Table 6 continued

| Compounds | IR-7 | IR-8 | IR-9 | IR-10 | IR-11 | IR-12 |
| --- | --- | --- | --- | --- | --- | --- |
| Aroclor 1254 | 125 | 435 | 210 | 350 | 190 | 280 |
| Aroclor 1260 | 12 | 325 | 49 | 110 | 83 | 64 |
| PCB 8 | 23 | 25 | 31 | 30 | 29 | 23 |
| PCB 18 | 7.0 | 13 | 21 | 8.0 | 14 | 8.0 |
| PCB 28 | 6.0 | 9.0 | 27 | 14 | 13 | 12 |
| PCB 31 | 7.0 | 11 | 20 | 16 | 7.0 | 8.0 |
| PCB 44 | < 0.8 | 6.0 | 8.0 | 6.0 | 3.0 | 14 |
| PCB 49 | 6.0 | 12 | 6.0 | 3.0 | 3.0 | 9.0 |
| PCB 52 | 8.0 | 19 | 19 | 21 | 13 | 18 |
| PCB 66/95 | 11 | 29 | 14 | 31 | 9.0 | 12 |
| PCB 87 | 3.0 | 11 | 5.0 | 9.0 | 5.0 | 16 |
| PCB 97 | 6.0 | 16 | 8.0 | 11 | 10 | 10 |
| PCB 101 | 8.0 | 43 | 16 | 21 | 12 | 24 |
| PCB 105 | 7.0 | 14 | 3.0 | 3.0 | 4.0 | 9.0 |
| PCB 110/77 | 9.0 | 51 | 11 | 44 | 24 | 35 |
| PCB 118 | 7.0 | 27 | 13 | 14 | 11 | 17 |
| PCB 126 | < 0.7 | 8.0 | < 0.7 | < 0.7 | < 0.7 | < 0.7 |
| PCB 128 | 1.0 | 6.0 | 0.7 | 4.0 | 2.0 | 4.0 |
| PCB 138 | 7.0 | 54 | 17 | 21 | 11 | 24 |
| PCB 149 | 9.0 | 44 | 14 | 21 | 6.0 | 11 |
| PCB 153 | 12 | 52 | 8.0 | 20 | 9.0 | 23 |
| PCB 156 | < 0.7 | 2.5 | < 0.7 | < 0.7 | < 0.7 | < 0.7 |
| PCB 169 | < 0.8 | < 0.8 | < 0.8 | < 0.8 | < 0.8 | < 0.8 |
| PCB 170 | < 0.6 | 16 | 2.5 | 6.0 | 3.0 | 3.0 |
| PCB 174 | 1.0 | 17 | 2.5 | 5.0 | 3.0 | 4.0 |
| PCB 177 | < 0.5 | 19 | 1.0 | 1.0 | < 0.5 | 2.5 |
| PCB 180 | 1.0 | 31 | 6.0 | 12 | 3.0 | 3.0 |
| PCB 183 | < 0.5 | 7.0 | 1.5 | 1.5 | 0.7 | 1.0 |
| PCB 187 | 2.5 | 40 | 2.5 | 5.0 | 6.0 | 5.0 |
| PCB 189 | < 0.6 | < 0.6 | < 0.6 | < 0.6 | < 0.6 | < 0.6 |
| PCB 194 | < 0.5 | 7.0 | 1.0 | 5.0 | 2.5 | 5.0 |
| PCB 195 | < 0.6 | 3.0 | < 0.6 | < 0.6 | < 0.6 | < 0.6 |
| PCB 201 | < 0.7 | 2.5 | < 0.7 | 0.9 | < 0.7 | 1.0 |
| PCB 206 | < 0.8 | < 0.8 | < 0.8 | < 0.8 | < 0.8 | < 0.8 |
| PCB 209 | < 1 | < 1 | < 1 | < 1 | < 1 | < 1 |

Table 6 continued

| Compounds | IR-13 | IR-14 | IR-15 | IR-16 | IR-16A | IR-17 |
| --- | --- | --- | --- | --- | --- | --- |
| Aroclor 1254 | 96 | 320 | 215 | 380 | 87 | 135 |
| Aroclor 1260 | 22 | 34 | 37 | 35 | 20 | 19 |
| PCB 8 | 14 | 34 | 11 | 18 | 8.0 | 12 |
| PCB 18 | 6.0 | 13 | 4.0 | 14 | 4.0 | 6.0 |
| PCB 28 | 5.0 | 6.0 | 10 | 20 | 2.0 | 9.0 |
| PCB 31 | 5.0 | 15 | 7.0 | 15 | 1.0 | 8.0 |
| PCB 44 | 7.0 | 20 | 9.0 | 17 | 7.0 | 10 |
| PCB 49 | 3.0 | 13 | 11 | 8.0 | 5.0 | 1.0 |
| PCB 52 | 6.0 | 20 | 11 | 24 | 6.0 | 10 |
| PCB 66/95 | 3.0 | 20 | 12 | 22 | 7.0 | 4.0 |
| PCB 87 | 4.0 | 13 | 9.0 | 14 | 4.0 | 6.0 |
| PCB 97 | 3.0 | 9.0 | 9.0 | 8.0 | 3.0 | 5.0 |
| PCB 101 | 6.0 | 26 | 14 | 26 | 6.0 | 12 |
| PCB 105 | 5.0 | 6.0 | 7.0 | 8.0 | 5.0 | 5.0 |
| PCB 110/77 | 14 | 32 | 26 | 36 | 12 | 18 |
| PCB 118 | 6.0 | 15 | 15 | 21 | 5.0 | 10 |
| PCB 126 | < 0.7 | < 0.7 | < 0.7 | < 0.7 | < 0.7 | < 0.7 |
| PCB 128 | 1.0 | 2.0 | 4.0 | 4.0 | 2.5 | 1.5 |
| PCB 138 | 8.0 | 19 | 18 | 29 | 7.0 | 12 |
| PCB 149 | 3.0 | 10 | 9.0 | 16 | 2.0 | 7.0 |
| PCB 153 | 9.0 | 20 | 18 | 21 | 10 | 11 |
| PCB 156 | < 0.7 | < 0.7 | < 0.7 | < 0.7 | < 0.7 | < 0.7 |
| PCB 169 | < 0.8 | < 0.8 | < 0.8 | < 0.8 | < 0.8 | < 0.8 |
| PCB 170 | 1.0 | 2.5 | 4.0 | 4.0 | < 0.6 | 1.0 |
| PCB 174 | < 0.7 | 3.0 | < 0.7 | 3.0 | < 0.7 | < 0.7 |
| PCB 177 | < 0.5 | < 0.5 | < 0.5 | < 0.5 | < 0.5 | < 0.5 |
| PCB 180 | 2.0 | 5.0 | 5.0 | 5.0 | 0.7 | 1.5 |
| PCB 183 | 0.7 | 1.5 | < 0.6 | 0.7 | 2.0 | 1.5 |
| PCB 187 | 5.0 | < 0.7 | < 0.7 | 1.4 | 5.0 | 4.0 |
| PCB 189 | < 0.6 | < 0.6 | < 0.6 | < 0.6 | < 0.6 | < 0.6 |
| PCB 194 | 1.0 | 3.0 | 5.0 | 1.0 | < 0.7 | 0.8 |
| PCB 195 | < 0.6 | < 0.6 | < 0.6 | < 0.6 | < 0.6 | < 0.6 |
| PCB 201 | < 0.7 | < 0.7 | < 0.7 | < 0.7 | < 0.7 | < 0.7 |
| PCB 206 | < 0.8 | < 0.8 | < 0.8 | < 0.8 | < 0.8 | < 0.8 |
| PCB 209 | < 1 | < 1 | < 1 | < 1 | < 1 | < 1 |

Table 6 continued

| Compounds | IR-18 | TK-2 | TK-4 | TK-5 | TK-6 | TK-7 |
| --- | --- | --- | --- | --- | --- | --- |
| Aroclor 1254 | 265 | 1120 | 140 | 325 | 33 | 170 |
| Aroclor 1260 | 70 | 690 | 35 | 78 | < 11 | 95 |
| PCB 8 | 15 | 35 | 4.0 | 19 | 9.0 | 6.0 |
| PCB 18 | 16 | 25 | 19 | 49 | 8.0 | 13 |
| PCB 28 | 16 | 32 | 11 | 15 | 2.5 | 11 |
| PCB 31 | 12 | 35 | < 1 | 19 | < 1 | < 1 |
| PCB 44 | 21 | 24 | 2.5 | 16 | < 0.8 | < 0.8 |
| PCB 49 | 8.0 | 30 | 7.0 | 15 | < 1 | 15 |
| PCB 52 | 16 | 35 | 15 | 47 | < 1 | 8.0 |
| PCB 66/95 | 19 | 78 | 5.0 | 13 | < 0.7 | < 0.7 |
| PCB 87 | 13 | 24 | 5.0 | 9.0 | 1.0 | 6.0 |
| PCB 97 | 9.0 | 25 | 6.0 | 12 | 2.5 | 6.0 |
| PCB 101 | 19 | 125 | 14 | 32 | 4.0 | 27 |
| PCB 105 | 11 | 38 | 4.0 | 12 | < 0.5 | 9.0 |
| PCB 110/77 | 20 | 105 | 9.0 | 20 | 2.5 | 17 |
| PCB 118 | 16 | 125 | 7.0 | 19 | 3.0 | 19 |
| PCB 126 | < 0.7 | < 1 | < 1 | < 1 | < 1 | < 1 |
| PCB 128 | 2.5 | 18 | < 0.5 | 3.0 | < 0.5 | 1.5 |
| PCB 138 | 19 | 145 | 8.0 | 22 | 2.0 | 27 |
| PCB 149 | 12 | 89 | 8.0 | 23 | 5.0 | 18 |
| PCB 153 | 23 | 98 | 5.0 | 16 | 1.0 | 21 |
| PCB 156 | 2.0 | < 0.6 | < 0.6 | < 0.6 | < 0.6 | < 0.6 |
| PCB 169 | < 0.8 | < 0.8 | < 0.8 | < 0.8 | < 0.8 | 7.0 |
| PCB 170 | 1.5 | 22 | < 0.6 | < 0.6 | < 0.6 | 5.0 |
| PCB 174 | 2.5 | 18 | < 0.7 | < 0.7 | < 0.7 | 2.5 |
| PCB 177 | 2.0 | < 0.7 | < 0.7 | < 0.7 | < 0.7 | 2.5 |
| PCB 180 | 4.0 | 39 | 2.0 | 4.0 | < 0.6 | 8.0 |
| PCB 183 | 5.0 | 12 | 1.5 | 2.0 | < 0.6 | 3.0 |
| PCB 187 | 8.0 | 37 | 13 | 13 | 2.0 | 17 |
| PCB 189 | < 0.6 | < 0.6 | < 0.6 | < 0.6 | < 0.6 | < 0.6 |
| PCB 194 | 2.5 | 60 | < 0.7 | 9.0 | < 0.7 | < 0.7 |
| PCB 195 | < 0.6 | < 0.6 | < 0.6 | < 0.6 | < 0.6 | < 0.6 |
| PCB 201 | < 0.7 | 7.0 | < 0.7 | < 0.7 | < 0.7 | < 0.7 |
| PCB 206 | < 0.8 | 16 | < 0.8 | < 0.8 | < 0.8 | < 0.8 |
| PCB 209 | < 1 | 10 | < 0.9 | < 0.9 | < 0.9 | < 0.9 |

Table 6 continued

| Compounds | TK-9 | TK-10 | TK-11 | TK-12 | TK-13 | TK-14 |
| --- | --- | --- | --- | --- | --- | --- |
| Aroclor 1254 | 415 | 210 | 210 | 91 | 415 | 130 |
| Aroclor 1260 | 165 | 105 | 83 | 21 | 100 | 21 |
| PCB 8 | 14 | 7.0 | 8.0 | 7.0 | 22 | 7.0 |
| PCB 18 | 25 | 19 | 11 | 15 | 48 | 10 |
| PCB 28 | 21 | 8.0 | 6.0 | 6.0 | 18 | 11 |
| PCB 31 | 19 | < 1 | 17 | 3.0 | 20 | 12 |
| PCB 44 | < 0.8 | 2.5 | < 0.8 | < 0.8 | < 0.8 | < 0.8 |
| PCB 49 | 21 | 13 | 3.0 | 7.0 | 14 | 10 |
| PCB 52 | 21 | 16 | 12 | 7.0 | 21 | 18 |
| PCB 66/95 | 13 | 1.5 | 9.0 | < 0.7 | 19 | 4.0 |
| PCB 87 | 10 | 6.0 | 7.0 | 4.0 | 11 | 2.5 |
| PCB 97 | 11 | 5.0 | 9.0 | 3.0 | 17 | 3.0 |
| PCB 101 | 57 | 26 | 17 | 14 | 33 | 19 |
| PCB 105 | 20 | 15 | 6.0 | < 0.5 | 12 | 1.5 |
| PCB 110/77 | 43 | 15 | 23 | 7.0 | 34 | 8.0 |
| PCB 118 | 61 | 14 | 26 | 5.0 | 23 | 6.0 |
| PCB 126 | < 1 | < 1 | < 1 | < 1 | < 1 | < 1 |
| PCB 128 | 7.0 | 2.0 | 5.0 | < 0.5 | 2.5 | < 0.5 |
| PCB 138 | 76 | 33 | 31 | 7.0 | 34 | 7.0 |
| PCB 149 | 55 | 20 | 27 | 6.0 | 16 | 6.0 |
| PCB 153 | 44 | 23 | 19 | 4.0 | 19 | 9.0 |
| PCB 156 | < 0.6 | < 0.6 | < 0.6 | < 0.6 | 5.0 | < 0.6 |
| PCB 169 | 25 | < 0.8 | < 0.8 | < 0.8 | < 0.8 | 1.0 |
| PCB 170 | 6.0 | 8.0 | 4.0 | < 0.6 | 6.0 | 1.0 |
| PCB 174 | < 0.7 | < 0.7 | < 0.7 | 1.5 | < 0.7 | < 0.7 |
| PCB 177 | 5.0 | 2.7 | < 0.7 | < 0.7 | < 0.7 | 1.5 |
| PCB 180 | 17 | 13 | 8.0 | 1.0 | 9.0 | 2.5 |
| PCB 183 | 5.0 | 5.0 | 2.0 | 1.5 | 6.0 | 1.0 |
| PCB 187 | 29 | 11 | 12 | 6.0 | 14 | 2.0 |
| PCB 189 | < 0.6 | < 0.6 | < 0.6 | < 0.6 | 1.5 | < 0.6 |
| PCB 194 | 10 | 3.0 | 4.0 | < 0.7 | 4.0 | < 0.7 |
| PCB 195 | < 0.6 | 3.0 | < 0.6 | < 0.6 | < 0.6 | < 0.6 |
| PCB 201 | < 0.7 | < 0.7 | < 0.7 | < 0.7 | < 0.7 | < 0.7 |
| PCB 206 | < 0.8 | < 0.8 | < 0.8 | < 0.8 | 3.0 | < 0.8 |
| PCB 209 | < 0.9 | < 0.9 | < 0.9 | < 0.9 | < 0.9 | < 0.9 |

Table 6 continued

| Compounds | TK-15 | TK-16 | TK-17 | TK-18 | TK-19 | TK-20 | TK-21 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Aroclor 1254 | 230 | 505 | 87 | 330 | 185 | 210 | 295 |
| Aroclor 1260 | 84 | 103 | < 11 | 17 | 46 | 25 | 85 |
| PCB 8 | < 2 | 18 | 6.0 | 6.0 | 20 | 18 | 8.0 |
| PCB 18 | 13 | 32 | 11 | < 1.5 | 13 | 7.0 | 20 |
| PCB 28 | 14 | 31 | 4.0 | 20 | 12 | 15 | 14 |
| PCB 31 | 16 | 32 | < 1 | < 1 | < 1 | < 1 | 23 |
| PCB 44 | 15 | 16 | < 0.8 | < 0.8 | 8.0 | < 0.8 | 12 |
| PCB 49 | 8.0 | 22 | < 1 | 30 | 6.0 | 17 | 6.0 |
| PCB 52 | 21 | 50 | 4.0 | 32 | 19 | 20 | 24 |
| PCB 66/95 | 8.0 | 18 | 2.0 | 12 | 2.5 | 6.0 | 8.0 |
| PCB 87 | 10 | 13 | 7.0 | 7.0 | 6.0 | 5.0 | 9.0 |
| PCB 97 | 8.0 | 11 | 4.0 | 5.0 | 7.0 | 9.0 | 10 |
| PCB 101 | 26 | 60 | 9.0 | 50 | 24 | 20 | 36 |
| PCB 105 | 5.0 | 8.0 | 3.0 | 2.5 | 2.0 | 3.0 | 9.0 |
| PCB 110/77 | 19 | 32 | 6.0 | 16 | 14 | 16 | 20 |
| PCB 118 | 14 | 30 | 5.0 | 18 | 11 | 10 | 15 |
| PCB 126 | 1.5 | 1.5 | 2.0 | < 1 | < 1 | < 1 | < 1 |
| PCB 128 | 2.0 | < 0.5 | < 0.5 | < 0.5 | 1.5 | < 0.5 | < 0.5 |
| PCB 138 | 21 | 34 | < 0.5 | 6.0 | 9.0 | 4.0 | 15 |
| PCB 149 | 13 | 31 | 4.0 | 32 | 10 | 9.0 | 9.0 |
| PCB 153 | 18 | 26 | 3.0 | 9.0 | 10 | 8.0 | 14 |
| PCB 156 | 2.0 | 6.0 | < 0.6 | < 0.6 | < 0.6 | < 0.6 | < 0.6 |
| PCB 169 | < 0.8 | < 0.8 | < 0.8 | < 0.8 | < 0.8 | < 0.8 | < 0.8 |
| PCB 170 | 2.5 | 2.5 | < 0.6 | < 0.6 | 5.0 | < 0.6 | 1.0 |
| PCB 174 | 4.0 | < 0.7 | < 0.7 | < 0.7 | 1.0 | 2.0 | 4.0 |
| PCB 177 | 3.0 | < 0.7 | < 0.7 | < 0.7 | 1.5 | 2.0 | 3.0 |
| PCB 180 | 6.0 | 8.0 | < 0.6 | 2.5 | 2.0 | 1.5 | 2.0 |
| PCB 183 | 2.5 | 2.5 | < 0.6 | < 0.6 | 1.5 | 1.5 | 2.0 |
| PCB 187 | 11 | 8.0 | < 0.6 | 6.0 | 5.0 | 5.0 | 12 |
| PCB 189 | < 0.6 | 4.0 | < 0.6 | < 0.6 | < 0.6 | < 0.6 | < 0.6 |
| PCB 194 | < 0.7 | 7.0 | < 0.7 | < 0.7 | < 0.7 | < 0.7 | < 0.7 |
| PCB 195 | < 0.6 | < 0.6 | < 0.6 | < 0.6 | < 0.6 | < 0.6 | < 0.6 |
| PCB 201 | < 0.7 | < 0.7 | < 0.7 | < 0.7 | < 0.7 | < 0.7 | 2.0 |
| PCB 206 | < 0.8 | < 0.8 | < 0.8 | < 0.8 | < 0.8 | < 0.8 | < 0.8 |
| PCB 209 | < 0.9 | < 0.9 | < 0.9 | < 0.9 | < 0.9 | < 0.9 | < 0.9 |

Table 6: continued

| Compounds | IAEA-408 QA/QC Value | IAEA-408 QA/QC Value | IAEA-408 QA/QC Value | IAEA-408 QA/QC Value | IAEA-408 Reference Value |
| --- | --- | --- | --- | --- | --- |
| Aroclor 1254 | 16000 | 19000 | 19000 | 16000 | 25000  |
| Aroclor 1260 | 10000 | 9200 | 8300 | 8400 | 14000  |
| PCB 8 | 69 | 150 | 180 | 150 | 1700  |
| PCB 18 | 170 | 290 | 290 | 230 |  |
| PCB 28 | 540 | 580 | 570 | 530 |  |
| PCB 31 | 600 | 430 | 410 | 440 |  |
| PCB 44 | 350 | 680 | 640 | 460 | 1300  |
| PCB 49 | - | 590 | 570 | 480 | 300  |
| PCB 52 | 820 | 1400 | 1300 | 920 | 600  |
| PCB 87 | 510 | 680 | 690 | 570 | 740  |
| PCB 101 | 1300 | 1700 | 1500 | 1400 | 1300  |
| PCB 105 | 330 | 320 | 470 | 500 | 560  |
| PCB 110/77 | 1300 | 1400 | 1400 | 1200 | 780  310 |
| PCB 118 | 1300 | 1100 | 1100 | 1100 | 1200  |
| PCB 128 | 150 | 200 | 250 | 290 | 380  |
| PCB 138 | 2100 | 1800 | 1900 | 2000 | 1600  |
| PCB 149 | 1700 | 1300 | 1200 | 1400 | 1400  |
| PCB 153 | 1800 | 1600 | 1700 | 1800 | 1600  |
| PCB 156 | 430 | 300 | 200 | 190 | 350  50* |
| PCB 170 | 710 | 580 | 640 | 600 | 490  |
| PCB 174 | 540 | 420 | 430 | 450 | 320  150* |
| PCB 177 | 340 | 250 | 270 | 300 | 330  120* |
| PCB 180 | 730 | 980 | 1000 | 1100 | 1000  |
| PCB 183 | 330 | 250 | 260 | 280 | 300  40* |
| PCB 187 | 700 | 640 | 660 | 690 | 690  |
| PCB 194 | 270 | 210 | 230 | 220 | 210  20 |
| PCB 195 | 110 | 95 | 110 | 100 | 110  |

“*”: information value only

“-“ : not analysed

## III.4	Trace metals

Table 7: Trace metals in sediment samples. Results are expressed in µg/g (except Al, Ca, Fe and Mg in mg/g) on dry weight basis.

| Code Site | Ag | Al | As | Ba | Ca | Cd | Co | Cr | Cu | Fe | Hg | Li | Mg | Mn | Ni | Pb | Sb | Sn | Sr | U | V | Zn | TOC | Inorganic Carbon |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| IR-1 | 0.087 | 74.4 | 15.5 | 363 | 68.1 | 0.162 | 17.2 | 118 | 43.9 | 37.6 | 0.029 | 42.2 | 20.6 | 978 | 65.9 | 15.7 | 0.61 | 1.11 | 464 | 2.13 | 134 | 84.5 | 0.300 | 2.40 |
| IR-2 | 0.268 | 65.8 | 11.9 | 381 | 71.2 | 0.119 | 15.2 | 117 | 30.7 | 37.1 | 0.028 | 34.5 | 18.5 | 884 | 58.7 | 13.6 | 0.423 | 1.32 | 545 | 1.91 | 113 | 51.0 | 0.400 | 1.70 |
| IR-3 | 0.244 | 74.4 | 10.0 | 381 | 61.6 | 0.135 | 18.1 | 128 | 34.4 | 40.9 | 0.018 | 33.5 | 19.1 | 851 | 57.6 | 14.2 | 0.421 | 1.31 | 486 | 1.98 | 128 | 81.2 | 0.300 | 1.50 |
| IR-4 | 0.200 | 67.8 | 10.9 | 434 | 80.5 | 0.144 | 14.0 | 79.5 | 35.1 | 30.4 | 0.017 | 30.5 | 17.2 | 834 | 47.8 | 16.2 | 0.536 | 1.34 | 740 | 1.92 | 98.5 | 67.2 | 0.300 | 2.10 |
| IR-5 | 0.294 | 71.5 | 18.9 | 483 | 63.3 | 0.25 | 17.5 | 76.8 | 39.1 | 39.4 | 0.033 | 31.4 | 19.5 | 896 | 40.1 | 21.7 | 1.35 | 1.83 | 358 | 2.66 | 126 | 87.9 | 0.400 | 1.70 |
| IR-6 | 0.287 | 69.9 | 14.9 | 494 | 82.7 | 0.221 | 15.3 | 89.1 | 32.9 | 37.6 | 0.022 | 28.6 | 17.0 | 797 | 38.1 | 20.9 | 1.24 | 1.71 | 460 | 2.59 | 132 | 81.4 | 0.200 | 1.60 |
| IR-7 | 0.284 | 69.4 | 13.0 | 586 | 65.6 | 0.175 | 12.9 | 59.1 | 30.0 | 34.0 | 0.017 | 23.6 | 15.5 | 787 | 28.8 | 18.1 | 1.77 | 1.63 | 500 | 2.37 | 113 | 40.8 | 0.200 | 1.60 |
| IR-8 | 0.216 | 66.6 | 17.5 | 520 | 78.4 | 0.161 | 16.9 | 98.1 | 25.6 | 39.3 | 0.025 | 28.8 | 19.6 | 760 | 38.6 | 18.9 | 1.01 | 1.7 | 571 | 2.37 | 130 | 77.4 | 0.500 | 1.80 |
| IR-9 | 0.207 | 65.9 | 13.7 | 447 | 77.0 | 0.211 | 17.3 | 108 | 29.6 | 39.6 | 0.029 | 34.5 | 20.4 | 750 | 47.0 | 20.6 | 1.01 | 1.74 | 528 | 2.66 | 125 | 83.3 | 0.800 | 1.80 |
| IR-10 | 0.349 | 75.6 | 15.7 | 560 | 69.6 | 0.224 | 18.8 | 76.5 | 44.1 | 38.2 | 0.038 | 38.2 | 28.5 | 884 | 51.3 | 28.6 | 1.28 | 2.05 | 505 | 2.98 | 120 | 79.8 | 1.00 | 2.00 |
| IR-11 | 0.225 | 59.2 | 12.2 | 410 | 87.4 | 0.165 | 15.6 | 105 | 23.4 | 38.4 | 0.028 | 34.8 | 20.5 | 652 | 41.5 | 19.9 | 0.721 | 1.82 | 530 | 2.59 | 113 | 78.8 | 0.700 | 2.50 |
| IR-12 | 0.242 | 46.6 | 13.6 | 356 | 166 | 0.153 | 11.3 | 71.9 | 17.9 | 27.6 | 0.029 | 26.8 | 16.8 | 514 | 31.6 | 14.7 | 0.648 | 1.38 | 1190 | 2.02 | 84.4 | 59.0 | 0.800 | 3.70 |
| IR-13 | 0.276 | 50.2 | 13.1 | 331 | 130 | 0.174 | 13.7 | 87.1 | 16.7 | 33.2 | 0.017 | 28.5 | 21.8 | 639 | 34.3 | 17.1 | 0.633 | 1.54 | 885 | 2.31 | 106 | 68.1 | 0.400 | 3.50 |
| IR-14 | 0.146 | 58.2 | 10.9 | 460 | 92.1 | 0.183 | 13.7 | 84.8 | 20.8 | 33.7 | 0.034 | 34.2 | 20.7 | 580 | 38.7 | 18.9 | 0.62 | 1.37 | 606 | 2.51 | 107 | 76.6 | 0.800 | 3.10 |
| IR-15 | 0.262 | 60.7 | 10.9 | 310 | 105 | 0.228 | 12.0 | 84.9 | 22.1 | 35.5 | 0.024 | 39.7 | 18.6 | 627 | 46.1 | 18.6 | 0.625 | 1.95 | 558 | 2.52 | 96 | 81.9 | 1.00 | 3.40 |
| IR-16 | 0.161 | 62.9 | 11.6 | 317 | 108 | 0.211 | 13.7 | 91.2 | 25.5 | 34.0 | 0.033 | 41.9 | 19.3 | 587 | 46.4 | 19.6 | 0.628 | 1.56 | 607 | 2.36 | 110 | 82.5 | 1.00 | 3.50 |
| IR-16A | 0.170 | 39.6 | 10.8 | 269 | 95.4 | 0.101 | 10.0 | 78.1 | 8.18 | 25.8 | 0.009 | 23.6 | 14.2 | 548 | 27.5 | 9.56 | 0.334 | 1.18 | 442 | 1.87 | 69.8 | 48.8 | 0.200 | 2.80 |
| IR-17 | 0.191 | 43.0 | 10.5 | 296 | 118 | 0.139 | 10.2 | 71.8 | 11.6 | 24.5 | 0.016 | 27.1 | 15.8 | 481 | 29.8 | 12.4 | 0.439 | 1.19 | 711 | 2.22 | 77.1 | 54.6 | 0.500 | 3.50 |
| IR-18 | 0.131 | 44.7 | 8.77 | 282 | 174 | 0.172 | 9.19 | 72.1 | 17.1 | 22.8 | 0.024 | 34.2 | 21.0 | 517 | 36.3 | 14.8 | 0.451 | 1.07 | 1380 | 1.99 | 77.5 | 64.4 | 0.900 | 5.60 |

Table 7: continuing

| Code Site | Ag | Al | As | Ba | Ca | Cd | Co | Cr | Cu | Fe | Hg | Li | Mg | Mn | Ni | Pb | Sb | Sn | Sr | U | V | Zn | TOC | Inorganic Carbon |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| TK-2 | 0.198 | 25.8 | 5.54 | 1320 | 176 | 0.132 | 5.39 | 30.9 | 33.5 | 10.7 | 0.035 | 16.5 | 15.4 | 222 | 27.2 | 13.0 | 0.583 | 0.915 | 2000 | 2.49 | 38.3 | 40.4 | 4.00 | 5.30 |
| TK-4 | 0.019 | 9.27 | 3.93 | 415 | 248 | 0.104 | 1.03 | 9.39 | 3.16 | 2.63 | 0.004 | 1.48 | 11.4 | 164 | 3.51 | 5.58 | 0.232 | 0.183 | 2230 | 2.62 | 10.1 | 5.83 | 0.800 | 6.50 |
| TK-5 | 0.219 | 21.0 | 4.31 | 888 | 219 | 0.204 | 2.96 | 13.8 | 6.28 | 6.78 | 0.006 | 5.70 | 7.57 | 250 | 6.39 | 10.2 | 0.571 | 0.463 | 1710 | 3.31 | 17.4 | 15.6 | 0.400 | 3.80 |
| TK-6 | 0.373 | 0.766 | 8.76 | 529 | 346 | 0.311 | 0.375 | 3.87 | 3.07 | 2.26 | 0.002 | 2.89 | 11.4 | 120 | 2.37 | 5.00 | 0.224 | 1.46 | 2430 | 2.13 | 7.54 | 18.8 | 2.00 | 7.80 |
| TK-7 | 0.358 | 14.4 | 3.08 | 562 | 256 | 0.133 | 2.02 | 14.4 | 12.7 | 4.97 | 0.011 | 5.90 | 9.23 | 133 | 8.66 | 6.89 | 0.302 | 0.407 | 2600 | 3.98 | 15.6 | 11.7 | 0.700 | 7.10 |
| TK-9 | 0.266 | 15.8 | 4.36 | 662 | 244 | 0.125 | 2.81 | 19.7 | 17.3 | 5.70 | 0.014 | 9.04 | 11.2 | 138 | 13.5 | 8.54 | 0.542 | 0.486 | 2590 | 2.85 | 25.1 | 18.8 | 2.60 | 2.60 |
| TK-10 | 0.031 | 30.2 | 3.96 | 478 | 172 | 0.082 | 2.31 | 21.6 | 8.73 | 5.88 | 0.009 | 5.90 | 9.84 | 225 | 8.25 | 8.29 | 0.347 | 0.662 | 1410 | 2.48 | 21.9 | 15.0 | 1.10 | 7.80 |
| TK-11 | 0.373 | 43.3 | 7.73 | 1980 | 145 | 0.247 | 9.22 | 56.1 | 43.0 | 19.4 | 0.042 | 21.3 | 20.4 | 377 | 37.3 | 22.9 | 0.844 | 1.46 | 1320 | 3.20 | 67.5 | 63.2 | 0.900 | 3.70 |
| TK-12 | <QL | 43.4 | 9.02 | 679 | 90.9 | 0.116 | 5.03 | 36.6 | 14.4 | 14.5 | 0.010 | 17.0 | 11.4 | 357 | 18.1 | 12.2 | 0.577 | 3.57 | 784 | 1.58 | 47.9 | 37.1 | 0.200 | 1.30 |
| TK-13 | 0.113 | 45.9 | 11.0 | 647 | 143 | 0.162 | 7.23 | 53.1 | 24.3 | 19.7 | 0.019 | 25.8 | 18.0 | 410 | 26.3 | 13.0 | 0.494 | 0.937 | 1490 | 3.21 | 72.2 | 49.4 | 1.20 | 4.10 |
| TK-14 | 0.158 | 24.9 | 4.12 | 299 | 207 | 0.09 | 3.48 | 19.9 | 9.84 | 8.15 | 0.015 | 11.9 | 12.0 | 209 | 10.4 | 8.92 | 0.331 | 0.878 | 1820 | 2.06 | 31.4 | 25.3 | 0.900 | 5.50 |
| TK-15 | 0.083 | 41.9 | 7.62 | 653 | 139 | 0.171 | 6.53 | 50.8 | 20.5 | 18.2 | 0.022 | 25.1 | 18.6 | 377 | 25.5 | 13.2 | 0.509 | 0.943 | 1350 | 2.71 | 65.7 | 45.6 | 1.40 | 4.30 |
| TK-16 | 0.069 | 12.4 | 4.43 | 940 | 251 | 0.154 | 2.78 | 14.2 | 12.4 | 5.40 | 0.015 | 6.77 | 11.9 | 155 | 13.0 | 6.32 | 0.271 | 0.457 | 2470 | 1.75 | 22.5 | 19.0 | 1.70 | 8.40 |
| TK-17 | 0.195 | 27.0 | 13.6 | 394 | 211 | 0.075 | 2.48 | 19.9 | 4.64 | 8.68 | 0.008 | 7.90 | 11.7 | 214 | 6.76 | 7.25 | 0.402 | 0.729 | 1680 | 1.88 | 30.6 | 18.9 | 0.400 | 3.10 |
| TK-18 | 0.062 | 22.0 | 4.96 | 300 | 234 | 0.141 | 3.87 | 29.2 | 12.2 | 11.2 | 0.015 | 12.6 | 20.9 | 229 | 16.2 | 7.11 | 0.298 | 0.886 | 2020 | 2.01 | 39.1 | 28.1 | 0.900 | 7.40 |
| TK-19 | 0.309 | 25.3 | 3.47 | 389 | 239 | 0.143 | 4.16 | 31.7 | 13.5 | 11.2 | 0.017 | 15.4 | 22.4 | 244 | 16.1 | 7.86 | 0.283 | 0.978 | 2070 | 2.01 | 37.2 | 28.0 | 1.20 | 7.60 |
| TK-20 | 0.086 | 27.4 | 4.96 | 238 | 243 | 0.154 | 5.46 | 36.3 | 13.8 | 14.3 | 0.015 | 16.6 | 23.0 | 282 | 21.4 | 9.05 | 0.274 | 1.04 | 1960 | 1.91 | 50.8 | 38.0 | 1.10 | 7.50 |
| TK-21 | 0.426 | 34.4 | 7.22 | 301 | 225 | 0.208 | 6.41 | 41.1 | 15.0 | 17.6 | 0.020 | 18.0 | 22.7 | 371 | 23.7 | 13.2 | 0.411 | 1.10 | 1880 | 2.10 | 54.9 | 48.4 | 1.30 | 7.10 |

QA/QC: Sediment Reference Material

IAEA 433 (all results in µg g-1) except for Ca MESS-3 (estuarine sediment from NRCC)

|  | Ag | Al | As | Ba | Ca | Cd | Co | Cr | Cu | Fe | Hg | Li | Mg | Mn | Ni | Pb | Sb | Sn | Sr | U | V | Zn |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Mean | 0.23 | 80099 | 20.9 | 262 | 15706 | 0.142 | 12.3 | 132 | 27.3 | 38445 | 0.158 | 55.6 | 12035 | 307 | 37.5 | 27.2 | 2.03 | 2.37 | 311 | 2.67 | 154 | 95.4 |
| Std | 0.07 | 3398 | 1.60 | 18 | 744 | 0.014 | 0.6 | 5 | 0.8 | 1868 | 0.017 | 6.5 | 768 | 9 | 1.9 | 0.6 | 0.05 | 0.34 | 8 | 0.06 | 6 | 16.2 |
| Recovery | 172.1 | 102.4 | 110.8 | 97.9 | 106.84 | 92.9 | 95.2 | 97.0 | 88.7 | 96.1 | 93.8 | 83.0 | 104.7 | 97.0 | 95.1 | 104.5 | 103.4 | 102.0 | 103.1 | 109.0 | 96.3 | 94.5 |
| Ref value | 0.133 | 78200 | 18.9 | 268 | 14700 | 0.153 | 12.9 | 136 | 30.8 | 40000 | 0.168 | 67 | 11500 | 316 | 39.4 | 26.0 | 1.96 | 2.32 | 302 | 2.45 | 160 | 101 |
| n | 9 | 3 | 9 | 9 | 5 | 9 | 9 | 9 | 9 | 9 | 8 | 9 | 3 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 |

## III.5	Grain size analysis

Iran

| Sample (Record Number): | IR-1 (40) | IR-2 (43) | IR-3 (45) | IR-4 (46) | IR-5 (48) |
| --- | --- | --- | --- | --- | --- |
| Measured beam Obscuration: (%) | 14.1 | 29.2 | 21.8 | 14.1 | 29.7 |
| Residual: (%) | 0.529 | 0.626 | 0.766 | 1.765 | 0.326 |
| Size (µm) | Volume under (%) |
| 0.364 | 0.12 | 0.12 | 0.08 | 0.00 | 0.31 |
| 0.424 | 0.36 | 0.35 | 0.24 | 0.00 | 0.90 |
| 0.494 | 0.68 | 0.67 | 0.45 | 0.00 | 1.72 |
| 0.576 | 1.06 | 1.04 | 0.71 | 0.00 | 2.70 |
| 0.671 | 1.48 | 1.44 | 0.98 | 0.00 | 3.77 |
| 0.781 | 1.90 | 1.84 | 1.25 | 0.00 | 4.86 |
| 0.910 | 2.30 | 2.21 | 1.49 | 0.14 | 5.94 |
| 1.060 | 2.67 | 2.53 | 1.72 | 0.36 | 6.96 |
| 1.235 | 3.03 | 2.83 | 1.91 | 0.58 | 7.97 |
| 1.439 | 3.38 | 3.11 | 2.09 | 0.77 | 9.00 |
| 1.677 | 3.75 | 3.41 | 2.26 | 0.93 | 10.11 |
| 1.953 | 4.17 | 3.74 | 2.43 | 1.09 | 11.37 |
| 2.276 | 4.66 | 4.11 | 2.60 | 1.27 | 12.78 |
| 2.651 | 5.20 | 4.54 | 2.71 | 1.46 | 14.35 |
| 3.089 | 5.80 | 5.01 | 2.84 | 1.67 | 16.05 |
| 3.598 | 6.45 | 5.52 | 2.98 | 1.91 | 17.85 |
| 4.192 | 7.13 | 6.07 | 3.17 | 2.18 | 19.77 |
| 4.884 | 7.85 | 6.67 | 3.43 | 2.47 | 21.79 |
| 5.690 | 8.61 | 7.33 | 3.78 | 2.77 | 23.95 |
| 6.628 | 9.45 | 8.07 | 4.24 | 3.09 | 26.31 |
| 7.722 | 10.38 | 8.91 | 4.82 | 3.41 | 28.92 |
| 8.996 | 11.44 | 9.88 | 5.47 | 3.75 | 31.84 |
| 10.480 | 12.69 | 10.98 | 6.12 | 4.15 | 35.13 |
| 12.210 | 14.15 | 12.25 | 6.67 | 4.63 | 38.82 |
| 14.224 | 15.89 | 13.68 | 7.06 | 5.25 | 42.91 |
| 16.571 | 17.90 | 15.30 | 7.27 | 6.04 | 47.35 |
| 19.306 | 20.24 | 17.15 | 7.52 | 7.02 | 52.11 |
| 22.491 | 22.90 | 19.33 | 8.19 | 8.15 | 57.11 |
| 26.202 | 25.91 | 21.98 | 9.73 | 9.36 | 62.29 |
| 30.525 | 29.32 | 25.30 | 12.69 | 10.53 | 67.56 |
| 35.562 | 33.14 | 29.50 | 17.65 | 11.53 | 72.84 |
| 41.430 | 37.41 | 34.75 | 25.00 | 12.24 | 77.97 |
| 48.265 | 42.14 | 41.14 | 34.80 | 12.62 | 82.81 |
| 56.229 | 47.31 | 48.61 | 46.56 | 13.06 | 87.18 |
| 65.507 | 52.91 | 56.90 | 59.25 | 13.99 | 90.96 |
| 76.316 | 58.87 | 65.60 | 71.54 | 15.97 | 94.05 |
| 88.908 | 65.09 | 74.15 | 82.20 | 19.61 | 96.42 |
| 103.578 | 71.41 | 81.94 | 90.39 | 25.51 | 98.10 |
| 120.668 | 77.63 | 88.47 | 95.86 | 34.20 | 99.17 |
| 140.578 | 83.49 | 93.45 | 98.86 | 45.87 | 99.75 |
| 163.773 | 88.75 | 96.81 | 99.99 | 59.85 | 99.99 |
| 190.796 | 93.17 | 98.76 | 100.00 | 74.47 | 100.00 |
| 222.277 | 96.57 | 99.67 | 100.00 | 87.15 | 100.00 |
| 258.953 | 98.86 | 99.96 | 100.00 | 95.95 | 100.00 |
| 301.680 | 100.00 | 100.00 | 100.00 | 100.00 | 100.00 |

| Sample (Record Number): | IR-6 (51) | IR-7 (53) | IR-8 (54) | IR-9 (57) | IR-10 (60) |
| --- | --- | --- | --- | --- | --- |
| Measured beam Obscuration: (%) | 26.0 | 20.9 | 16.4 | 28.5 | 22.1 |
| Residual: (%) | 0.874 | 0.780 | 0.857 | 0.645 | 0.411 |
| Size (µm) | Volume under (%) |
| 0.364 | 0.08 | 0.11 | 0.10 | 0.12 | 0.21 |
| 0.424 | 0.23 | 0.32 | 0.29 | 0.35 | 0.60 |
| 0.494 | 0.44 | 0.60 | 0.54 | 0.66 | 1.13 |
| 0.576 | 0.69 | 0.94 | 0.85 | 1.03 | 1.77 |
| 0.671 | 0.95 | 1.30 | 1.17 | 1.42 | 2.45 |
| 0.781 | 1.21 | 1.66 | 1.49 | 1.80 | 3.13 |
| 0.910 | 1.45 | 1.99 | 1.78 | 2.16 | 3.76 |
| 1.060 | 1.66 | 2.29 | 2.05 | 2.47 | 4.34 |
| 1.235 | 1.85 | 2.56 | 2.29 | 2.76 | 4.88 |
| 1.439 | 2.01 | 2.82 | 2.53 | 3.03 | 5.42 |
| 1.677 | 2.18 | 3.09 | 2.80 | 3.33 | 5.99 |
| 1.953 | 2.35 | 3.39 | 3.10 | 3.66 | 6.64 |
| 2.276 | 2.52 | 3.74 | 3.46 | 4.05 | 7.37 |
| 2.651 | 2.69 | 4.12 | 3.88 | 4.50 | 8.18 |
| 3.089 | 2.87 | 4.54 | 4.36 | 4.99 | 9.03 |
| 3.598 | 3.05 | 4.99 | 4.88 | 5.53 | 9.91 |
| 4.192 | 3.26 | 5.47 | 5.44 | 6.13 | 10.81 |
| 4.884 | 3.53 | 6.00 | 6.05 | 6.79 | 11.78 |
| 5.690 | 3.88 | 6.60 | 6.71 | 7.54 | 12.90 |
| 6.628 | 4.33 | 7.32 | 7.45 | 8.41 | 14.33 |
| 7.722 | 4.89 | 8.19 | 8.29 | 9.44 | 16.21 |
| 8.996 | 5.51 | 9.24 | 9.26 | 10.63 | 18.74 |
| 10.480 | 6.14 | 10.47 | 10.38 | 11.99 | 22.05 |
| 12.210 | 6.69 | 11.86 | 11.66 | 13.51 | 26.19 |
| 14.224 | 7.07 | 13.37 | 13.09 | 15.15 | 31.11 |
| 16.571 | 7.29 | 14.96 | 14.61 | 16.86 | 36.65 |
| 19.306 | 7.40 | 16.63 | 16.20 | 18.65 | 42.53 |
| 22.491 | 7.69 | 18.45 | 17.83 | 20.56 | 48.44 |
| 26.202 | 8.56 | 20.62 | 19.54 | 22.74 | 54.12 |
| 30.525 | 10.59 | 23.44 | 21.43 | 25.41 | 59.38 |
| 35.562 | 14.40 | 27.28 | 23.71 | 28.86 | 64.16 |
| 41.430 | 20.53 | 32.47 | 26.64 | 33.37 | 68.49 |
| 48.265 | 29.20 | 39.24 | 30.50 | 39.12 | 72.45 |
| 56.229 | 40.14 | 47.55 | 35.54 | 46.12 | 76.17 |
| 65.507 | 52.58 | 57.04 | 41.88 | 54.18 | 79.74 |
| 76.316 | 65.31 | 67.06 | 49.45 | 62.88 | 83.23 |
| 88.908 | 77.02 | 76.73 | 57.93 | 71.61 | 86.59 |
| 103.578 | 86.62 | 85.22 | 66.79 | 79.71 | 89.74 |
| 120.668 | 93.53 | 91.88 | 75.37 | 86.64 | 92.57 |
| 140.578 | 97.71 | 96.45 | 83.04 | 92.03 | 94.98 |
| 163.773 | 99.62 | 99.02 | 89.33 | 95.81 | 96.88 |
| 190.796 | 100.00 | 100.00 | 94.05 | 98.14 | 98.27 |
| 222.277 | 100.00 | 100.00 | 97.24 | 99.35 | 99.21 |
| 258.953 | 100.00 | 100.00 | 99.14 | 99.85 | 99.75 |
| 301.680 | 100.00 | 100.00 | 100.00 | 100.00 | 100.00 |

| Sample (Record Number): | IR-11 (61) | IR-12 (64) | IR-13 (66) | IR-14 (67) | IR-15 (69) |
| --- | --- | --- | --- | --- | --- |
| Measured beam Obscuration: (%) | 13.8 | 23.7 | 21.5 | 16.7 | 19.4 |
| Residual: (%) | 0.491 | 0.521 | 0.605 | 0.292 | 0.253 |
| Size (µm) | Volume under (%) |
| 0.364 | 0.13 | 0.13 | 0.11 | 0.12 | 0.18 |
| 0.424 | 0.38 | 0.37 | 0.30 | 0.34 | 0.51 |
| 0.494 | 0.72 | 0.71 | 0.58 | 0.64 | 0.97 |
| 0.576 | 1.12 | 1.11 | 0.89 | 0.98 | 1.52 |
| 0.671 | 1.55 | 1.53 | 1.22 | 1.34 | 2.10 |
| 0.781 | 1.96 | 1.94 | 1.54 | 1.69 | 2.67 |
| 0.910 | 2.35 | 2.33 | 1.82 | 1.99 | 3.20 |
| 1.060 | 2.68 | 2.67 | 2.07 | 2.26 | 3.67 |
| 1.235 | 2.98 | 2.97 | 2.29 | 2.48 | 4.11 |
| 1.439 | 3.26 | 3.27 | 2.49 | 2.69 | 4.52 |
| 1.677 | 3.55 | 3.58 | 2.71 | 2.92 | 4.96 |
| 1.953 | 3.87 | 3.94 | 2.98 | 3.20 | 5.47 |
| 2.276 | 4.24 | 4.38 | 3.31 | 3.54 | 6.06 |
| 2.651 | 4.67 | 4.88 | 3.69 | 3.93 | 6.75 |
| 3.089 | 5.17 | 5.47 | 4.14 | 4.36 | 7.51 |
| 3.598 | 5.73 | 6.14 | 4.64 | 4.85 | 8.37 |
| 4.192 | 6.38 | 6.88 | 5.18 | 5.38 | 9.31 |
| 4.884 | 7.12 | 7.73 | 5.78 | 5.97 | 10.36 |
| 5.690 | 7.99 | 8.68 | 6.43 | 6.62 | 11.54 |
| 6.628 | 9.00 | 9.76 | 7.16 | 7.37 | 12.90 |
| 7.722 | 10.18 | 11.00 | 7.99 | 8.24 | 14.49 |
| 8.996 | 11.54 | 12.43 | 8.94 | 9.26 | 16.35 |
| 10.480 | 13.08 | 14.07 | 10.05 | 10.45 | 18.53 |
| 12.210 | 14.83 | 15.95 | 11.34 | 11.84 | 21.05 |
| 14.224 | 16.79 | 18.08 | 12.81 | 13.41 | 23.91 |
| 16.571 | 19.00 | 20.47 | 14.43 | 15.16 | 27.08 |
| 19.306 | 21.53 | 23.12 | 16.15 | 17.06 | 30.54 |
| 22.491 | 24.51 | 26.06 | 17.90 | 19.11 | 34.26 |
| 26.202 | 28.11 | 29.31 | 19.60 | 21.37 | 38.26 |
| 30.525 | 32.51 | 32.92 | 21.26 | 24.00 | 42.55 |
| 35.562 | 37.86 | 36.90 | 22.93 | 27.19 | 47.18 |
| 41.430 | 44.22 | 41.26 | 24.77 | 31.16 | 52.17 |
| 48.265 | 51.49 | 45.99 | 27.02 | 36.10 | 57.52 |
| 56.229 | 59.42 | 51.02 | 29.99 | 42.17 | 63.16 |
| 65.507 | 67.62 | 56.32 | 33.98 | 49.40 | 68.96 |
| 76.316 | 75.59 | 61.81 | 39.29 | 57.59 | 74.74 |
| 88.908 | 82.82 | 67.41 | 46.14 | 66.30 | 80.26 |
| 103.578 | 88.90 | 73.05 | 54.52 | 74.75 | 85.29 |
| 120.668 | 93.60 | 78.59 | 64.05 | 82.27 | 89.63 |
| 140.578 | 96.85 | 83.91 | 73.91 | 88.42 | 93.16 |
| 163.773 | 98.80 | 88.79 | 82.94 | 93.03 | 95.84 |
| 190.796 | 99.74 | 93.04 | 90.26 | 96.24 | 97.74 |
| 222.277 | 100.00 | 96.43 | 95.40 | 98.27 | 98.97 |
| 258.953 | 100.00 | 98.79 | 98.53 | 99.46 | 99.68 |
| 301.680 | 100.00 | 100.00 | 100.00 | 100.00 | 100.00 |

| Sample (Record Number): | IR-16 (72) | IR-16A (73) | IR-17 (76) | IR-18 (78) |
| --- | --- | --- | --- | --- |
| Measured beam Obscuration: (%) | 24.0 | 14.0 | 23.0 | 24.8 |
| Residual: (%) | 0.280 | 0.696 | 0.406 | 0.277 |
| Size (µm) | Volume under (%) |
| 0.364 | 0.19 | 0.07 | 0.17 | 0.29 |
| 0.424 | 0.54 | 0.21 | 0.50 | 0.84 |
| 0.494 | 1.02 | 0.39 | 0.95 | 1.60 |
| 0.576 | 1.59 | 0.59 | 1.47 | 2.49 |
| 0.671 | 2.19 | 0.80 | 2.01 | 3.43 |
| 0.781 | 2.79 | 0.98 | 2.53 | 4.35 |
| 0.910 | 3.34 | 1.14 | 3.00 | 5.19 |
| 1.060 | 3.83 | 1.27 | 3.39 | 5.94 |
| 1.235 | 4.28 | 1.37 | 3.72 | 6.60 |
| 1.439 | 4.71 | 1.45 | 4.02 | 7.24 |
| 1.677 | 5.16 | 1.55 | 4.32 | 7.92 |
| 1.953 | 5.68 | 1.67 | 4.66 | 8.73 |
| 2.276 | 6.29 | 1.82 | 5.06 | 9.70 |
| 2.651 | 6.98 | 1.98 | 5.52 | 10.87 |
| 3.089 | 7.77 | 2.14 | 6.05 | 12.24 |
| 3.598 | 8.65 | 2.28 | 6.66 | 13.79 |
| 4.192 | 9.63 | 2.39 | 7.36 | 15.53 |
| 4.884 | 10.71 | 2.50 | 8.17 | 17.46 |
| 5.690 | 11.94 | 2.64 | 9.11 | 19.58 |
| 6.628 | 13.35 | 2.85 | 10.19 | 21.91 |
| 7.722 | 14.99 | 3.15 | 11.41 | 24.46 |
| 8.996 | 16.90 | 3.57 | 12.73 | 27.24 |
| 10.480 | 19.14 | 4.11 | 14.14 | 30.23 |
| 12.210 | 21.72 | 4.81 | 15.59 | 33.38 |
| 14.224 | 24.64 | 5.58 | 17.09 | 36.63 |
| 16.571 | 27.88 | 6.17 | 18.74 | 39.88 |
| 19.306 | 31.43 | 6.17 | 20.70 | 43.03 |
| 22.491 | 35.24 | 6.17 | 23.23 | 46.02 |
| 26.202 | 39.32 | 6.17 | 26.64 | 48.82 |
| 30.525 | 43.68 | 6.17 | 31.26 | 51.47 |
| 35.562 | 48.31 | 6.48 | 37.44 | 54.04 |
| 41.430 | 53.23 | 7.83 | 45.33 | 56.66 |
| 48.265 | 58.41 | 10.61 | 54.72 | 59.48 |
| 56.229 | 63.77 | 15.85 | 64.93 | 62.62 |
| 65.507 | 69.22 | 25.42 | 74.92 | 66.17 |
| 76.316 | 74.63 | 40.63 | 83.64 | 70.16 |
| 88.908 | 79.82 | 59.31 | 90.48 | 74.54 |
| 103.578 | 84.62 | 76.14 | 95.24 | 79.14 |
| 120.668 | 88.86 | 88.02 | 98.14 | 83.75 |
| 140.578 | 92.43 | 95.00 | 99.58 | 88.11 |
| 163.773 | 95.25 | 98.39 | 100.00 | 91.98 |
| 190.796 | 97.34 | 99.70 | 100.00 | 95.18 |
| 222.277 | 98.76 | 100.00 | 100.00 | 97.60 |
| 258.953 | 99.61 | 100.00 | 100.00 | 99.21 |
| 301.680 | 100.00 | 100.00 | 100.00 | 100.00 |

IR-1

IR-2

IR-3

IR-4

IR-5

IR-6

IR-7

IR-8

IR-9

IR-10

IR-11

IR-12

IR-13

IR-14

IR-15

IR-16

IR-16A

IR-17

IR-18

Turkmenistan

| Sample (Record Number): | TK-2 (4) | TK-4 (8) | TK-5 (7) | TK-6 (10) | TK-7 (12) |
| --- | --- | --- | --- | --- | --- |
| Measured beam Obscuration: (%) | 22.0 | 12.0 | 19.0 | 6.3 | 10.1 |
| Residual: (%) | 0.508 | 1.031 | 0.868 | 1.736 | 0.641 |
| Size (µm) | Volume under (%) |
| 0.364 | 0.00 | 0.02 | 0.00 | 0.00 | 0.00 |
| 0.424 | 0.00 | 0.06 | 0.00 | 0.00 | 0.00 |
| 0.494 | 0.00 | 0.12 | 0.00 | 0.00 | 0.00 |
| 0.576 | 0.00 | 0.21 | 0.03 | 0.00 | 0.00 |
| 0.671 | 0.00 | 0.30 | 0.09 | 0.02 | 0.00 |
| 0.781 | 0.00 | 0.40 | 0.18 | 0.08 | 0.02 |
| 0.910 | 0.24 | 0.48 | 0.29 | 0.14 | 0.14 |
| 1.060 | 0.50 | 0.54 | 0.39 | 0.20 | 0.30 |
| 1.235 | 0.68 | 0.59 | 0.46 | 0.23 | 0.48 |
| 1.439 | 0.79 | 0.61 | 0.51 | 0.24 | 0.63 |
| 1.677 | 0.87 | 0.64 | 0.56 | 0.25 | 0.77 |
| 1.953 | 0.97 | 0.67 | 0.63 | 0.26 | 0.90 |
| 2.276 | 1.09 | 0.71 | 0.74 | 0.27 | 1.03 |
| 2.651 | 1.22 | 0.77 | 0.89 | 0.28 | 1.16 |
| 3.089 | 1.36 | 0.84 | 1.07 | 0.30 | 1.29 |
| 3.598 | 1.52 | 0.93 | 1.26 | 0.33 | 1.42 |
| 4.192 | 1.70 | 0.99 | 1.38 | 0.38 | 1.54 |
| 4.884 | 1.89 | 0.99 | 1.39 | 0.44 | 1.67 |
| 5.690 | 2.10 | 0.99 | 1.39 | 0.49 | 1.81 |
| 6.628 | 2.32 | 0.99 | 1.39 | 0.53 | 1.97 |
| 7.722 | 2.58 | 0.99 | 1.43 | 0.53 | 2.18 |
| 8.996 | 2.89 | 0.99 | 1.56 | 0.53 | 2.44 |
| 10.480 | 3.26 | 1.09 | 1.78 | 0.53 | 2.79 |
| 12.210 | 3.73 | 1.26 | 2.09 | 0.53 | 3.22 |
| 14.224 | 4.32 | 1.51 | 2.51 | 0.54 | 3.73 |
| 16.571 | 5.04 | 1.84 | 3.05 | 0.62 | 4.29 |
| 19.306 | 5.89 | 2.26 | 3.59 | 0.78 | 4.88 |
| 22.491 | 6.88 | 2.61 | 3.80 | 1.01 | 5.47 |
| 26.202 | 8.00 | 2.61 | 3.80 | 1.32 | 6.11 |
| 30.525 | 9.25 | 2.61 | 3.80 | 1.68 | 6.89 |
| 35.562 | 10.66 | 2.61 | 3.80 | 2.00 | 8.02 |
| 41.430 | 12.30 | 2.61 | 3.80 | 2.00 | 9.77 |
| 48.265 | 14.27 | 2.61 | 4.70 | 2.00 | 12.45 |
| 56.229 | 16.78 | 3.48 | 6.71 | 2.00 | 16.38 |
| 65.507 | 20.06 | 5.51 | 10.32 | 2.00 | 21.84 |
| 76.316 | 24.37 | 9.24 | 16.81 | 2.21 | 28.95 |
| 88.908 | 29.96 | 16.09 | 28.13 | 4.05 | 37.62 |
| 103.578 | 36.94 | 27.81 | 44.37 | 7.35 | 47.53 |
| 120.668 | 45.36 | 44.45 | 62.23 | 12.16 | 58.10 |
| 140.578 | 55.11 | 62.60 | 77.49 | 19.17 | 68.62 |
| 163.773 | 65.85 | 77.76 | 88.01 | 29.75 | 78.36 |
| 190.796 | 77.06 | 88.44 | 94.39 | 45.72 | 86.74 |
| 222.277 | 87.50 | 94.84 | 97.71 | 67.07 | 93.29 |
| 258.953 | 95.74 | 98.40 | 99.34 | 88.98 | 97.75 |
| 301.680 | 100.00 | 100.00 | 100.00 | 100.00 | 100.00 |

| Sample (Record Number): | TK-9 (14) | TK-10 (16) | TK-11 (18) | TK-12 (21) | TK-13 (23) |
| --- | --- | --- | --- | --- | --- |
| Measured beam Obscuration: (%) | 11.7 | 11.9 | 14.1 | 15.0 | 20.4 |
| Residual: (%) | 0.376 | 0.422 | 0.931 | 1.283 | 0.319 |
| Size (µm) | Volume under (%) |
| 0.364 | 0.08 | 0.09 | 0.00 | 0.00 | 0.16 |
| 0.424 | 0.23 | 0.25 | 0.00 | 0.00 | 0.47 |
| 0.494 | 0.44 | 0.48 | 0.00 | 0.00 | 0.88 |
| 0.576 | 0.69 | 0.74 | 0.00 | 0.02 | 1.38 |
| 0.671 | 0.94 | 1.02 | 0.00 | 0.07 | 1.90 |
| 0.781 | 1.19 | 1.29 | 0.05 | 0.17 | 2.40 |
| 0.910 | 1.42 | 1.53 | 0.15 | 0.28 | 2.87 |
| 1.060 | 1.61 | 1.74 | 0.28 | 0.38 | 3.29 |
| 1.235 | 1.78 | 1.92 | 0.39 | 0.46 | 3.66 |
| 1.439 | 1.93 | 2.08 | 0.48 | 0.51 | 4.02 |
| 1.677 | 2.09 | 2.24 | 0.56 | 0.56 | 4.40 |
| 1.953 | 2.28 | 2.41 | 0.63 | 0.60 | 4.85 |
| 2.276 | 2.50 | 2.61 | 0.70 | 0.64 | 5.39 |
| 2.651 | 2.76 | 2.84 | 0.79 | 0.69 | 6.01 |
| 3.089 | 3.05 | 3.09 | 0.87 | 0.76 | 6.74 |
| 3.598 | 3.37 | 3.37 | 0.95 | 0.85 | 7.55 |
| 4.192 | 3.72 | 3.68 | 1.03 | 0.95 | 8.46 |
| 4.884 | 4.11 | 4.03 | 1.10 | 1.05 | 9.47 |
| 5.690 | 4.54 | 4.41 | 1.16 | 1.13 | 10.61 |
| 6.628 | 5.03 | 4.84 | 1.21 | 1.18 | 11.89 |
| 7.722 | 5.60 | 5.34 | 1.26 | 1.19 | 13.35 |
| 8.996 | 6.27 | 5.92 | 1.35 | 1.19 | 15.01 |
| 10.480 | 7.05 | 6.60 | 1.49 | 1.21 | 16.88 |
| 12.210 | 7.98 | 7.41 | 1.71 | 1.31 | 18.94 |
| 14.224 | 9.09 | 8.38 | 2.03 | 1.50 | 21.21 |
| 16.571 | 10.40 | 9.59 | 2.44 | 1.80 | 23.66 |
| 19.306 | 11.99 | 11.11 | 2.91 | 2.21 | 26.32 |
| 22.491 | 13.96 | 13.09 | 3.41 | 2.71 | 29.26 |
| 26.202 | 16.44 | 15.68 | 3.87 | 3.21 | 32.60 |
| 30.525 | 19.59 | 19.06 | 4.28 | 3.56 | 36.50 |
| 35.562 | 23.58 | 23.41 | 4.71 | 3.58 | 41.09 |
| 41.430 | 28.52 | 28.83 | 5.33 | 3.58 | 46.49 |
| 48.265 | 34.45 | 35.34 | 6.44 | 3.58 | 52.68 |
| 56.229 | 41.33 | 42.84 | 8.43 | 3.58 | 59.53 |
| 65.507 | 48.98 | 51.08 | 11.72 | 3.81 | 66.76 |
| 76.316 | 57.09 | 59.70 | 16.71 | 5.31 | 73.99 |
| 88.908 | 65.29 | 68.24 | 23.73 | 8.54 | 80.79 |
| 103.578 | 73.15 | 76.23 | 32.92 | 14.13 | 86.76 |
| 120.668 | 80.29 | 83.24 | 44.04 | 22.99 | 91.62 |
| 140.578 | 86.41 | 89.00 | 56.43 | 35.82 | 95.23 |
| 163.773 | 91.35 | 93.39 | 68.99 | 51.96 | 97.65 |
| 190.796 | 95.07 | 96.47 | 80.57 | 69.18 | 99.05 |
| 222.277 | 97.65 | 98.42 | 90.02 | 84.22 | 99.72 |
| 258.953 | 99.25 | 99.52 | 96.65 | 94.86 | 99.95 |
| 301.680 | 100.00 | 100.00 | 100.00 | 100.00 | 100.00 |

| Sample (Record Number): | TK-14 (24) | TK-15 (26) | TK-16 (28) | TK-17 (30) | TK-18 (32) |
| --- | --- | --- | --- | --- | --- |
| Measured beam Obscuration: (%) | 10.4 | 18.2 | 16.4 | 19.0 | 25.5 |
| Residual: (%) | 0.283 | 0.443 | 0.692 | 1.267 | 0.326 |
| Size (µm) | Volume under (%) |
| 0.364 | 0.28 | 0.11 | 0.12 | 0.10 | 0.37 |
| 0.424 | 0.81 | 0.32 | 0.33 | 0.30 | 1.06 |
| 0.494 | 1.54 | 0.60 | 0.63 | 0.56 | 2.01 |
| 0.576 | 2.40 | 0.93 | 0.97 | 0.86 | 3.12 |
| 0.671 | 3.31 | 1.28 | 1.31 | 1.18 | 4.29 |
| 0.781 | 4.20 | 1.63 | 1.64 | 1.49 | 5.42 |
| 0.910 | 5.02 | 1.93 | 1.93 | 1.75 | 6.43 |
| 1.060 | 5.75 | 2.20 | 2.17 | 1.97 | 7.29 |
| 1.235 | 6.40 | 2.44 | 2.38 | 2.16 | 8.02 |
| 1.439 | 7.03 | 2.66 | 2.58 | 2.32 | 8.69 |
| 1.677 | 7.72 | 2.90 | 2.81 | 2.50 | 9.40 |
| 1.953 | 8.54 | 3.17 | 3.11 | 2.72 | 10.25 |
| 2.276 | 9.55 | 3.51 | 3.51 | 2.99 | 11.30 |
| 2.651 | 10.77 | 3.90 | 4.00 | 3.33 | 12.60 |
| 3.089 | 12.21 | 4.36 | 4.59 | 3.73 | 14.14 |
| 3.598 | 13.86 | 4.88 | 5.27 | 4.18 | 15.93 |
| 4.192 | 15.71 | 5.45 | 6.02 | 4.67 | 17.92 |
| 4.884 | 17.74 | 6.06 | 6.83 | 5.18 | 20.10 |
| 5.690 | 19.96 | 6.73 | 7.69 | 5.69 | 22.43 |
| 6.628 | 22.39 | 7.46 | 8.59 | 6.20 | 24.89 |
| 7.722 | 25.03 | 8.27 | 9.55 | 6.72 | 27.44 |
| 8.996 | 27.90 | 9.19 | 10.58 | 7.28 | 30.07 |
| 10.480 | 31.02 | 10.26 | 11.73 | 7.90 | 32.75 |
| 12.210 | 34.41 | 11.49 | 13.02 | 8.64 | 35.48 |
| 14.224 | 38.05 | 12.94 | 14.50 | 9.50 | 38.24 |
| 16.571 | 41.94 | 14.64 | 16.19 | 10.48 | 41.01 |
| 19.306 | 46.07 | 16.60 | 18.11 | 11.55 | 43.81 |
| 22.491 | 50.45 | 18.86 | 20.23 | 12.62 | 46.66 |
| 26.202 | 55.11 | 21.44 | 22.54 | 13.59 | 49.59 |
| 30.525 | 60.05 | 24.36 | 25.00 | 14.36 | 52.66 |
| 35.562 | 65.28 | 27.65 | 27.59 | 14.92 | 55.89 |
| 41.430 | 70.72 | 31.35 | 30.25 | 15.27 | 59.30 |
| 48.265 | 76.23 | 35.49 | 32.91 | 15.75 | 62.87 |
| 56.229 | 81.62 | 40.10 | 35.58 | 16.78 | 66.56 |
| 65.507 | 86.62 | 45.23 | 38.38 | 18.85 | 70.36 |
| 76.316 | 91.01 | 50.90 | 41.50 | 22.55 | 74.22 |
| 88.908 | 94.58 | 57.07 | 45.21 | 28.37 | 78.11 |
| 103.578 | 97.22 | 63.68 | 49.74 | 36.61 | 81.98 |
| 120.668 | 98.91 | 70.56 | 55.29 | 47.14 | 85.77 |
| 140.578 | 99.77 | 77.45 | 62.02 | 59.22 | 89.36 |
| 163.773 | 100.00 | 84.04 | 69.91 | 71.55 | 92.64 |
| 190.796 | 100.00 | 89.95 | 78.87 | 82.70 | 95.46 |
| 222.277 | 100.00 | 94.79 | 88.02 | 91.47 | 97.69 |
| 258.953 | 100.00 | 98.23 | 95.87 | 97.28 | 99.22 |
| 301.680 | 100.00 | 100.00 | 100.00 | 100.00 | 100.00 |

| Sample (Record Number): | TK-19 (35) | TK-20 (36) | TK-21 (38) |
| --- | --- | --- | --- |
| Measured beam Obscuration: (%) | 29.4 | 22.5 | 17.6 |
| Residual: (%) | 0.364 | 0.306 | 0.342 |
| Size (µm) | Volume under (%) |
| 0.364 | 0.38 | 0.46 | 0.39 |
| 0.424 | 1.10 | 1.34 | 1.12 |
| 0.494 | 2.08 | 2.54 | 2.13 |
| 0.576 | 3.22 | 3.95 | 3.31 |
| 0.671 | 4.42 | 5.43 | 4.55 |
| 0.781 | 5.56 | 6.87 | 5.75 |
| 0.910 | 6.58 | 8.17 | 6.83 |
| 1.060 | 7.44 | 9.30 | 7.77 |
| 1.235 | 8.17 | 10.28 | 8.58 |
| 1.439 | 8.83 | 11.20 | 9.34 |
| 1.677 | 9.53 | 12.20 | 10.16 |
| 1.953 | 10.38 | 13.39 | 11.15 |
| 2.276 | 11.46 | 14.89 | 12.40 |
| 2.651 | 12.80 | 16.74 | 13.96 |
| 3.089 | 14.40 | 18.96 | 15.86 |
| 3.598 | 16.25 | 21.53 | 18.09 |
| 4.192 | 18.32 | 24.42 | 20.64 |
| 4.884 | 20.56 | 27.58 | 23.47 |
| 5.690 | 22.93 | 30.96 | 26.55 |
| 6.628 | 25.42 | 34.51 | 29.81 |
| 7.722 | 28.00 | 38.16 | 33.22 |
| 8.996 | 30.68 | 41.87 | 36.72 |
| 10.480 | 33.44 | 45.57 | 40.25 |
| 12.210 | 36.30 | 49.21 | 43.76 |
| 14.224 | 39.25 | 52.70 | 47.19 |
| 16.571 | 42.26 | 55.99 | 50.49 |
| 19.306 | 45.32 | 59.01 | 53.61 |
| 22.491 | 48.37 | 61.74 | 56.52 |
| 26.202 | 51.42 | 64.19 | 59.23 |
| 30.525 | 54.42 | 66.43 | 61.77 |
| 35.562 | 57.39 | 68.53 | 64.17 |
| 41.430 | 60.31 | 70.60 | 66.49 |
| 48.265 | 63.20 | 72.72 | 68.76 |
| 56.229 | 66.09 | 74.98 | 71.07 |
| 65.507 | 69.07 | 77.45 | 73.48 |
| 76.316 | 72.21 | 80.14 | 76.07 |
| 88.908 | 75.57 | 83.04 | 78.91 |
| 103.578 | 79.18 | 86.07 | 81.99 |
| 120.668 | 83.01 | 89.11 | 85.29 |
| 140.578 | 86.92 | 92.00 | 88.68 |
| 163.773 | 90.71 | 94.59 | 91.97 |
| 190.796 | 94.15 | 96.75 | 94.95 |
| 222.277 | 96.97 | 98.39 | 97.40 |
| 258.953 | 98.97 | 99.47 | 99.12 |
| 301.680 | 100.00 | 100.00 | 100.00 |

TK-2

TK-4

TK-5

TK-6

TK-7

TK-9

TK-10

TK-11

TK-12

TK-13

TK-14

TK-15

TK-16

TK-17

TK-18

TK-19

TK-20

TK-21