Action Plan on implementation of NCAP during 2008-2017

| Measures | Form of completion | Deadline, Agencies | Required means, mln. tenge/ $ USА | Possible financial sources |
| --- | --- | --- | --- | --- |
|  | Output |  |  |  |
| 1 | 2 | 3 | 4 | 5 |
| I. - Control and regulation of pollution level The purpose: Reduction of pollution risk and creation of the basis for improvement of the Caspian Sea ecosystem status |
| Task 1. To create the basis for minimization of negative impact of industrial activities on the environment and ensuring the ecological security in the region |
| 1.1. Improvement of the natural use legal base: - Study of possibility of special rules establishment for the Caspian Sea - Development of Rules for Protection and Use of the Caspian Sea - Identification of requirements and ecological limitations on sewage discharges (from vessels, inhabited barges, artificial islands, drilling rigs, and etc.) - Identification of the list of objects - potential sources of oil spills in the Kazakhstan sector of the Caspian Sea - Development of ecological requirements to applied technologies, techniques and the equipments during producing and transportation of oil and gas in the Caspian Sea - Development of special rules of carrying out the industrial ecological control on the marine oil-field objects - Identification of requirements and ecological limitations to construction of ports, terminals of pipelines - Establishment of share of financial and technical participation of natural users in fish – rehabilitation, in scientific researches connected to sturgeons and etc. - Approval of the Instruction about the procedure of the control over the designing and construction of compensatory fish – rehabilitation objects and their operation - Development and approval of the rule on damage assessment from the activities on offshore of the Caspian Sea - Development of procedure of the solid waste treatment, including wastes from drilling operation | Information to the Government Order of the MEP Order of the MEP Order of MEP Order of MEMR Order of the MEP Order of MTC Alteration in Low “About Bowels” Order MoA Order MEP Order of MEP | 2009 MEP, MoA, MEMR, MoJ 2009 MEP, MoA, MEMR 2008-2009гг. MEP, MEMR, MTC, Akimats of Pre- Caspian regions, oil companies 2009 MEP, MoA, MEMR 2009 MEMR, MEP 2009 MEMR, MEP, MoA 2009 MEP, MEMR, MoA 2009-2010гг. MoA, MEP, MEMR, oil companies 2009 MIT, MoA, MEP 2009 MoA, MIT, MEP, Akimats of Pre- Caspian oblasts 2009 MEP, MoA, MEMR, oil companies | No need No need No need No need No need No need No need No need No need No need No need |  |
| 1.2. Establishment of the mechanism of control and responsibility for the pollution of the sea from the flooded oil wells | Order of MEP | 2008 MEP, MEMR, MoA, oil companies | No need |  |
| 1.3. Introduction of changes in National Action Plan on Oil Spills Responses in the Sea and Internal Reservoirs of the Republic of Kazakhstan taking into account the international norms | Governmental Statement | 2008г. MEMR, MES, MEP, MTC, Akimats of Pre – Caspian oblasts | No need |  |
| 1.4. Establishment of Specialized Marine Emergency and Rescue Division under the Ministry of Emergency Situations for liquidation of possible fires and damages on the ships, and also for liquidation of oil spills, rescue of people suffering disasters on the Sea | Governmental Statement | 2009 MES, MEMR, MEP, MTC | 5 755 623 thousand tenge (or 446 mln. $US), including for buy the vessels | Republic budget |
| 1.5. Creation of information system for the wrecking based on the use of satellite information and models of emergency oil spills for the correction of data about oil spread on offshore waters taking into account the changes of hydro-meteorological conditions and undertaken measures | Order of MEP | 2009 MEMR, MES, MEP, MTC, national oil companies | Will be determined by the oil companies | Financial means of national oil companies |
| 1.6. Establish at the expenses of oil companies near the oil wells the automatic monitoring stations in order to take necessary measures on time in case of emergency situations | Monitoring stations | 2009-2012 MEP, Kazhydromet |  | Republic budget |
| 1.7. Participation in preparation of draft Protocols to Framework Convention for the Protection of the Marine Environment of the Caspian Sea, concerning: - Regional cooperation in case of oil spills in the Sea; - EIA in transboundary context; - Protection of the Sea from pollution of land sources - Biodiversity conservation | Drafts of Protocols | 2008-2010 MEP, MFA, MES, MoA, MEMR, oil companies |  | UNEP, other donors |
| 1.8. Creation of ship movement control system in according to requirements of the International Marine Organization (IMO) for safety navigation and to meet the requirements of the International Code on Management of Safety Ship Operation and Pollution Warning | Governmental Statement | 2009 MTC, MEP, MEMR, MoA, oil companies | No need |  |
| 1.9. Creation of marine bases for oil spills response in Bautino, Kuryk as well as in a mouth of the river Ural in according to the Complex Plan of a coastal infrastructure development in Kazakhstan sector of the Caspian Sea | Marine bases | 2009 MEMR, MES, MEP, oil companies |  | Oil companies |
| 1.10. To identify the ecological capacity of the Caspian Sea | Scientific assessments | 2009-2010 MEP, MoA, MEMR, Akimats of Pre- Caspian oblasts |  | Republic budget |
| Task 2. To create the monitoring system of environmental contamination |
| 2.1. To create the Caspian Environment Monitoring Center | Information to the Government | 2008-2010 Akimats of Pre- Caspian oblasts, MEP, MoA, MEMR |  | Republic and local budgets |
| 2.2. To improve the state ecological monitoring system in the Caspian Sea. | Information to the Government | MEP, Kazhydromet |  | Republic budget |
| 2.3. Update and recharge of data bank on monitoring the pollution of the Caspian Sea and its coastal zone ecosystem. | Renewed and added data base | MEP, MoA, MEMR, ALR, Akimats of Pre-Caspian oblasts |  |  |
| A priority 2 – Complex planning and management by the coastal zone The purpose: Ensuring of complex and sustainable use of the Caspian Sea coastal zone |
| Task 1. To ensure the liquidation and reduction of historical industrial pollution as well as restoration of degraded coastal areas |
| 1.1. Conservation and liquidation of the flooded oil wells | Report to the Government | 2008-2010 MEMR, Akimats of Pre – Caspian oblasts, oil companies |  | Republic and local budgets, Financial means of oil companies |
| 1.2. Clearing the mazouted areas and liquidation of oil barns with carrying out work on revegetation of soil in the oil fields | Report to the Government | 2008-2010. (I stage) MEMR, Akimats of Pre – Caspian oblasts, oil companies |  | Republic and local budgets, Financial means of oil companies |
| 1.3. Realization of plans of enterprises on reduction of passing oil gas volumes burnt on torches (since 2010 at the expense of enterprises) | Reduction of passing gas emissions | Beginning 2010 (stage by stage) Oil companies |  | Financial means of oil companies |
| 1.4. To develop and realize the coordinated methods of sulfur storage with attraction of the oil-produce companies | Approved methods of sulfur storage. Process of sulfur storage has been started | Beginning 2008 (stage by stage) MEMR, MEP, MoA, MES, ALR, oil companies |  | Financial means of oil companies |
| 1.5. Localization of negative impacts of sewage water evaporation fields, for example, “Tukhlaya Balka” in Atyrau city on the environment (stage by stage). | Project of localization of sewage water evaporation fields | 2008-2009 MEMR, MEP, MIT, Akimat of Atyrau oblast, industrial companies | 30, 0 | Republic budget, financial means of industrial companies |
| 1.6. In Атырау to carry out the introduction of full clearing of industrial and household drains (stage by stage till 2013) | Information to the Government | 2009-2013 Akimat of Atyrau oblast, industrial companies |  | Republic budget, financial means of enterprises |
| 1.7. Construction of new evaporation fields outside of the banks of the river Ural | Information to the Government | 2009-2012 Akimat of Atyrau oblast, industrial companies |  | Republic budget, financial means of enterprises |
| 1.8. Construction of high-quality controllable and equipped ranges for utilization of wastes of oil and gas industries (TengizShevroil, Agip KCO and Atyrau Oil Refining Plant, at the expense of own means). | Ranges for utilization of wastes | 2008-2010 Oil companies and industrial enterprises |  | Financial means of oil companies and industrial enterprises |
| 1.9. Development of the Feasibility Report for construction of the plant on processing the solid domestic wastes in Atyrau | Feasibility Report | 2008 -2010 Akimat of Atyrau oblast |  | Local budget of Atyrau oblast |
| 1.10. Development of the Design Estimates on construction of the range on solid domestic waste burial in Atyrau | Design Estimates | 2008 – 2010 Akimat of Atyrau oblast |  | Local budget of Atyrau oblast |
| 1.11. Development of the Design Estimates for restoration of polluted areas in Atyrau oblast. | Design Estimates | 2008 – 2010 Akimat of Atyrau oblast |  | Local budget of Atyrau oblast |
| 1.12. To develop the Feasibility Study and Design Estimates for the construction of solid domestic waste ranges in all large settlements of Atyrau oblast. | Feasibility Report and Design Estimates | 2008 – 2010 Akimat of Atyrau oblast |  | Local budget of Atyrau oblast |
| 1.13. Realization of projects on reconstruction and restoration of the tailing “Koshkar – Ata” | Tailing restoration | 2007-2009. Akimat of Mangystau oblast | 77,6 mln $US (at 2001) | Local budget of Mangystau oblast |
| 1.14. Stabilization of the level of the tailing “Koshkar –Ata” | Stabilization of water level it the tailing | 2007-2011 Akimat of Mangystau oblast | 77 mln $US (at 2001) | Local budget of Mangystau oblast |
| 1.15. Carrying out of permanent state monitoring for the dusting of radioactive and toxic wastes of the tailing “Koshkar – Ata” | Monitoring of dusting | 2007 – 2011 Akimat of Mangystau oblast | 54 thousand $US | Local budget of Mangystau oblast |
| 1.16. Liquidation of the sunk ships in the bay Bautino and the abandon derricks in coastal strip of the Sea. | Information to the Government | MTC, MEMR, MIT, MEP, ALR, industrial companies, Akimat of Mangystau oblast |  | Republic and local budget, financial means of industrial companies |
| Task 2. To improve the system of coastal zone planning and management |
| 2.1. Assessment of possibility of introduction of the General Plan on Strengthening the Potential on the Environment Protection and the Pollution Control in Atyrau oblast prepared by the Japanese International Cooperation Agency (JICA) | Information to the Government | 2008 MEP, MEMR, MES, Kazhydromet, Akimat of Atyrau oblast | No need |  |
| 2.2. Improvement of the hydro-meteorological observation network in the Pre-Caspian region to ensure the forecasting of storm – surges phenomena and carrying out the environmental pollution monitoring | Information to the Government | 2008-2010 MEP, Kazhydromet |  | Republic budget |
| 2.3. Assessment of seismic danger connected to increase of hydro-carbonic resources production scales and implementation of seismic monitoring in the Pre-Caspian region | Information to the Government | 2008-2010 MEMR, MoES, oil companies |  | Financial means of oil companies |
| 2.4. The organization of underground waters system monitoring in coastal part of the Sea near to oil production areas | Monitoring network | 2008-2010 MEMR, Akimat of Atyrau oblast, oil companies |  | Republic budget, financial means of oil companies |
| 2.5. Development and introduction in practice of forecast methods for the Caspian Sea level fluctuations in view of climate changes | Information to the Government | 2009-2010. MEP, Kazhydromet |  | Republic budget |
| 2.6. Alteration in normative legal acts on prohibition of construction of any objects, except for bridges, moorings, off-takes and etc. in mouth part of the river Ural | Information to the Government | 2009-2010 Akimat of Atyrau oblast | No need |  |
| 2.7. Improvement of navigation regimes on the rivers Ural, Kigach and Safonofka | Order of MTC | 2009-2010 MTC, MEP, MoA, Akimat of Atyrau oblast | No need |  |
| 2.8. Development of the draft for the water-protection zone in river Ural | Standard act | 2009 MoA, Akimat of Atyrau oblast | No need |  |
| Task 3. To decrease the desertification process in the Caspian Sea coastal zone |
| 3.1 The organization of monitoring system for the desertification process | Information to the Government | 2009-20010 MEP, ALR, MEMR, MoA, Akimats of Pre- Caspian oblasts |  | Financial support of donors |
| 3.2 Development and realization of pilot projects on prevention of technical degradations process, rational use and creation of pastures | Pilot projects | 2009-2010 MEP, Akimats of Pre- Caspian oblasts |  | Financial support of donors |
| 3.3. Realization of the project on protection of settlement. Сенек in Mangystau oblast and the station Isatai in Atyrau oblast from barchans coming up. | Information of Akimats of Pre-Caspian oblasts | 2008-2010 Contract organizations |  | Local budgets of Atyrau and Mangystau oblasts |
| Priority 3 – Conservation of biological and landscape diversities of the Caspian Sea and its coastal zone The purpose: Creation of bases for conservation and balanced use of biological and landscape diversity of the Caspian Sea and its coastal zone |
| Task 1. To rehabilitate the degraded water and coastal ecosystems, places of spawning as well as the inhabited places of trade animals |
| 1.1. Carrying out of works on fish- industry reclamation for rehabilitation natural spawning areas of sturgeons on the river Ural (stage by stage) | Information to the Government | 2008-2010 I stage MoA, Fishery Industry Center |  | Republic budget and local budget of Atyrau oblast |
| 1.2. Participation in the international researches on the assessment of the Caspian Sea biological resources status and preparation of anticipatory measures on struggle with Mnemiopsis leidyi (comb jelly) (stage by stage) | Information to the Government | 2008-2010 I stage MoA, Fishery Industry Center |  | Republic budget |
| 1.3. Increase of the areas of saksaul and tugai woods (stage by stage) | Information to the Government | 2008-2010 I stage MoA, Akimats of Pre-Caspian oblasts |  | Republic budget |
| 1.4. Renewal of watering places and organization of crossing places of trade animals through line routes of constructions (stage by stage) | Information to the Government | 2008-2010 I stage MoA, Akimats of Pre-Caspian oblasts |  | Republic budget |
| 1.5. Regulation of the number of some spices of predatory animals | Information of the Akimats of Pre-Caspian oblasts | 2008-2010 I stage MoA, Akimats of Pre-Caspian oblasts |  | Local budgets of Pre-Caspian oblasts |
| 1.6. Creation of natural protected areas in the delta of river Ural | Information to the Government | 2008-2010 MoA, Akimat of Aryrau oblast |  | World Bank, UNDP, local budget of Atyrau oblast |
| Task 2. To create the effective system for the conservation and balanced use of biological resources of the Caspian Sea and its coastal zone biological and landscape diversities |
| 2.1. Implementation of complex of actions on conservation and increase in stocks of sturgeons, including research of status of gene pool of sturgeons and other spices of fishes, measures on conservation and increase in stocks of fishes due to increase in quantity of sturgeons breeding and releasing to the Sea, and also due to commodity sturgeon breeding (stage by stage) | Information to the Government | 2008-2010гг. I stage MoA, Fishery Industry Center, Atyrau Fishery Plant |  | Republic budget |
| 2.2. Strengthening of logistical support and financial insurance of the state bodies on protection of biological resources and natural protection areas (stage by stage) | Local environment protection bodies are equipped with modern devices and equipments | 2008-2010 I stage, MoA, Akimats of Pre-Caspian oblasts |  | Republic budget |
| Task 3. To improve the system of biological and landscape diversities monitoring of the Caspian Sea and its coastal zone |
| 3.1. To create the Center on Biological and Landscape Diversities, equipped with the modern devices and equipments, including those which would allow to determine the reasons of mass mortality of fishes and seals | Specialized laboratory created in Aktau | 2009-2010 I stage Akimat of Mangystau oblast, MoA, oil companies |  | Akimat of Mangystau oblast, oil companies |
| 3.2. Inventory of the Pri – Caspian areas and revealing of areas which have some problems with ecological point of view and also unproductive agricultural areas. | Information to the Government | 2008-2010 MoA, MEMR, ALR, Akimats of Pre-Caspian oblasts |  | Republic budget |
| 3.3. To carry out the study of oil-and-gas industries impacts on biological resources of the Caspian Sea shelf in Atyrau and Mangystau oblasts | Information of Atyrau and Mangystau oblasts | 2008-2009 Contracted organizations |  | Local budgets of Atyrau and Mangystau oblasts |
| A priority 4 – Interaction with the public of the region on managing the Caspian Sea environment The purpose: Support of coastal zone public participation in management of the Caspian Sea environment |
| Task 1. To increase the public awareness about the environmental problems of the Caspian Sea |
| 1.1. Organization of the systematical ecological education of the Pre-Caspian Sea population in the field of the Caspian Sea ecosystem conservation (stage by stage) | Public awareness about ecological problem through mass media | 2008-2010гг. I stage MIc, Akimats of Pre-Caspian oblasts |  | Republic and local budgets |
| Task 2. To support the participation of the regional public representatives in management of the Caspian Sea environment |
| 2.1. Organization of public discussions on social and ecological aspects of development of marine oil-and-gas operations (stage by stage) | Public hearings, publications in mass media | 2008-2010 I stage MEMR, oil companies, Akimats of Pre-Caspian oblasts |  | Financial means of oil companies |
| 2.2. Support of the public access to the decision-making (stage by stage) | Public access to the ecological situation is provided | 2008-2010 I stage All state bodies |  | Republic and local budgets |
| Task 3. To organize the network of ecological tourism about the Caspian Sea |
| 3.1. Preparation and realization of pilot projects in Atyrau and Mangystau oblasts for the ecological tourism development on the Caspian Sea coastal zone | Pilot projects | 2008-2010 MTS, Akimats of Pre-Caspian oblasts |  | Republic and local budgets |
| 3.2. Design of the Ecological Tourism and Amateur Fishery Development Program in Pri – Caspian oblasts | Programs concerning ecological tourism | 2008-2010 MTS, Akimats of Pre-Caspian oblasts |  | Republic and local budgets, investments from donors |

Notes: MEP – Ministry of Environment Protection; MEMR- Ministry of Energy and Mineral Resources; MoA – Ministry of Agriculture; MFA – Ministry of Foreign Affairs; MTC – Ministry of Transport and Communication; MES – Ministry of Emergency Situation; MJ – Ministry of Justice; MIT – Ministry of Industry and Trade; ALR – Agency of Land Resources; MoES- Ministry of Education and Science; MIC- Ministry of Information and Culture; Ministry of Tourism and Sports